## Slide 1: Hyper-Kamiokande: From Construction to Discovery Physics
Jeanne Wilson

## Slide 2: Contents
Why long baseline experiments?
The Hyper-K project
Physics design considerations
IWCD
Far Detector
  Cavern
  Tank
  Instrumentation: 50cm PMTs, mPMTs
  Outer Detector
  Electronics
  Water Systems
  Calibrations
Status
Notes: We expect invited key lecturers to provide talks that contain both, an introduction
for non-experts and also elements which are more result-focused. The character of the
Erice School/Workshop is somewhere between an actual summer school (which it is not)
and a full fledged specialized conference (which it is also not). It is rather
designed to give an overview on a given field - thus the broad topics - in particular
for students and postdocs working in the field."
Thus, please use some time at the beginning for an introduction dedicated
specifically for first-year PhD students, and only then go into details.

## Slide 3: Neutrinos Oscillate
Start with a know source (flavour, flux) of neutrinos
Measure or calculate the flux before oscillations
Does the initial flavour disappear?
Does a different flavour appear?
T2K as an example
Frequency
Amplitude
Disappearance
Appearance
Notes: Assuming mixing matrix is unitary

## Slide 4: 3 flavour oscillations
3 mixing angles
2 mass splittings
+ CP violating phase

## Slide 5: The story without beams
Atmospheric neutrinos (Super-K)
disappearance
and (
Solar neutrinos (SNO Super-K)
disappearance
KamLAND 180km reactor baseline
disappearance
and (
Reactor neutrinos, short baseline (Daya Bay, Double Chooz, RENO)
disappearance
and .
<<

## Slide 6: + Beam neutrinos
Control your source
Measure your source
disappearance and
appearance and
Compare and appearance
  MINOS, K2K
  T2K, NoA
,

## Slide 7: Oscillations measure - how do we know the sign of ?
Matter effects alter the effective and mixing angles in matter compared to a vacuum
- additional potential due to ambient electrons
Effect larger in denser medium, longer baseline, higher energy
Normal Ordering
oscillations enhanced in matter
oscillations suppressed in matter
Inverted Ordering
oscillations suppressed in matter
oscillations enhanced in matter
Notes: If \(\Delta m_{31}^2 > 0\) (Normal Ordering), neutrino oscillations are enhanced in matter while antineutrino oscillations are suppressed.
If \(\Delta m_{31}^2 < 0\) (Inverted Ordering), the situation flips: antineutrino oscillations get the enhancement instead

## Slide 8: Current Status
and matter effects are degenerate
NoA – Nu2026 talk
Baseline = 810km
T2K– Nu2026 talk
Baseline = 295km
Notes: Check up to date plots
T2K plots from
https://indico.global/event/15740/contributions/155587/attachments/72629/140807/2026_06_04_T2K_NEUTRINO_2026.pdf
NoVa plots from
https://indico.global/event/15740/contributions/155585/attachments/72595/140743/202606_Neutrino_NOvA.pdf

## Slide 9: Why we need Long Baseline Neutrino Experiments
Next Generation of Experiments should:
Determine the mass ordering
  Through matter effect
  Long baseline (or atmospheric )
Determine if neutrinos violate CP
  Compare and appearance to probe
Determine if this model is correct – precise parameter measurements
Notes: Overconstrain model with precise measurements of all parameters – test for new physics

## Slide 10: Overview of the Hyper-Kamiokande project
Far Detector (FD)
Water Cherenkov
187kton fiducial mass
1750 m.w.e. overburden
Oscillated , and measurement
Statistics!
Excellent separation
Intermediate Water Cherenkov Detector (IWCD)
870m downstream
Vertically moving Water Cherenkov spans 1.5-4 off-axis angles
110t fiducial mass
cross sections
Neutral current
Near Detectors (ND280)
280m downstream
Magnetised tracking detector
, flux measurement (including wrong sign)
Final state hadrons and interaction cross-sections
Since beginning of T2K, upgraded 2024
JPARC neutrino beam
Provide or beam
2.5 Off-axis narrow energy peak 0.6GeV
Upgrading to 1.3MW beam operation in 2028
Tokai
Kamioka
Notes: IWCD can directly measure the re-
lationship between true and reconstructed neutrino energy
by sampling different off-axis angles [20]. The large tar-
get mass, high precision electron/muon discrimination and
self-shielding property of water also allow IWCD to make
precise measurements of electron neutrino and antineutrino
cross-sections.

## Slide 11: Hyper-Kamiokande Physics
Proton Decay Search
CP violation, oscillation parameters
J-PARC neutrino beam:
Near Detectors
Atmospheric neutrinos:
,
Mass Ordering
Solar neutrinos,
Supernova bursts
Diffuse Supernova Background Neutrinos
High Energy Neutrinos
See Nataly Ospina’s talk this afternoon for more details
Notes: Hyper-K is a multi-purpose, next generation neutrino experiment.
The Hyper-K project as a whole encompasses both the huge water cherenkov far detector, and the neutrino beam from J-PARC.
Together these are needed for one of the major goal of Hyper-K - the measurement of CP violation and precision measurement of oscillation parameters with beam neutrinos, as you will hear about in Patricia Vahle’s plenary talk on Friday morning
But the large volume far detector means we can measure a lot of other non-beam sources. Firstly, atmospheric neutrinos, which I'm not going to cover today as their power is in combination with the beam measurements to address the mass hierarchy - I'll leave that topic for the plenary talk too.
What I will focus on today is:
- Proton decay searches
- Solar neutrino measurements
- Supernova measurements
- and high energy neutrinos of astrophysical origin

## Slide 12: Hyper-Kamiokande Collaboration
~660 members from 23 countries and ～100 institutes

## Slide 13: Hyper-K long baseline strategy
At a 295km baseline, disappearance oscillation maximum corresponds to 600MeV
  Matter effects are sub-dominant (<10%)
  Quasi-elastic interactions dominate at low energy
    Select 1-ring e-like or -like samples in Water Cherenkov
    Reconstruct neutrino energy from basic kinematics
Off-axis beam technique:
  Use kinematics of 2-body pion decay
  Near and Far detectors 2.5 off-axis give neutrino energy peaked at 600MeV
  Intrinsic from decay reduced off-axis
Notes: DO I need to explain what we measure to probe each parameter?

## Slide 14: Long Baseline Oscillation Measurements
survival sensitive to and
appearance sensitive to, and in leading terms
sensitive to in sub-leading terms (different signs)
Plots from HK design report: https://arxiv.org/pdf/1805.04163
1) Need to accumulate of order 103 and signal events at FD to measure CP violation with few % accuracy
3% statistical error
2) Need to control systematic uncertainties
Notes: Especially on the Nu-e and Nu-e-bar cross section ratio

## Slide 15: Beam Event Rates
Expect Protons on Target (POT) per Calendar year
6 cycles of 22 days Beam / year with 87% efficiency at 1.3MW
1:3 FHC to RHC ratio
  Comparable numbers of electron-like events at far detector for CP conservation scenario
  Optimal to break CPV degeneracy with and
Notes: Hyper-Kamiokande is expected to collect statistics from 2.7 ×1021(!! /year) Protons-On-Target (POT) per calendar year,
corresponding to 6 cycles of 22 days with 87% running efficiency at 1.3 MW. We chose a partition of 1/4 of the
exposure in FHC and 3/4 in RHC, considering proper control of systematic uncertainties and direct access to ex-
tensive statistics of both neutrino and antineutrino events for a robust assessment of CP violation. In particular, this
FHC/RHC partition is the optimal one to break the CPV degeneracy with sin2 θ23 and sin2 θ13. Due to difference in the
cross-section and flux of neutrinos and antineutrinos, this partition leads to a comparable number of events in the FHC
and RHC electron-like samples in the case of CP symmetry conservation.
Tab. 2: Expected number of events at Hyper-Kamiokande with 27 ×1021 POT (6.75 ×1021 POT in FHC and 20.25 ×1021
POT in RHC), corresponding to 10 years of accumulated statistics. The first four columns correspond to non-oscillated events
which include electron (anti)neutrinos from the intrinsic beam contamination.

## Slide 16: Far Detector Event Selections

## Slide 17: Other Measurement Key Requirements
Proton Decay
  187kton FV contains order 1035 nucleons to give sensitivity to nucleon lifetime at the level of 1035 years
  Fiducial volume = statistics
  Reconstruction and PID
Atmospheric neutrinos
  Separation of and interactions
Solar neutrinos
  Low energy threshold (<5MeV), low radioactive backgrounds

## Slide 18: Intermediate Water Cherenkov Detector
Additional detector 870m from neutrino production point, same target medium as Far Detector
  Increased cancellation of systematics
  Measure cross-sections from intrinsic in beam
  >10k signal events for each in 10 years
  >4% accuracy on
  Detector moves 1.5-4 off axis
  Neutrino energy varies with position
  Measure relationship between neutrino energy and lepton kinematics
Beam axis
1
2.5
4
Notes: Because we use \nu_\mu \rightarrow \nu_e oscillations to measure CP violation, and measure \nu _\mu fluxes at a near detector to predict the \nu _e at the far detector, any unmodelled asymmetry in the double cross-section ratio would introduce a systematic in the oscillation results.

## Slide 19: IWCD
Inner diameter 9m, high 12m
Construction of the 50m deep shaft has begun
Water Cherenkov Test Experiment (WCTE) performed @CERN

## Slide 20: mPMTs
IWCD will be instrumented with ~400 mPMT modules
Each consists of 19 8cm PMTs in a pressure vessel
  Improved timing (lower TTS)
  Improved granularity
Better event reconstruction
Path lengths ~8m vs ~80m in FD
Considerable event pile-up

## Slide 21: Far Detector Overview
Water systems
LINAC - calibration
Access, safety, comfort!
DAQ
50cm PMTs
mPMTs

## Slide 22: Segesta Acropolis and Amphitheater
56m
21m
10m
63m

## Slide 23: Far Detector Overview
68m
71m

## Slide 24: Cavern
Excavation of world’s largest human-made cavern was completed in 2025
Y. Asaoka et al., Prog. Theor. Exp. Phys 2026, ptag91

## Slide 25: Infrastructure
Access tunnels
Rock disposal
Side cavern for water purification systems
Air-flow, power, water, wifi, transport, safety, toilets, cleanliness ….

## Slide 26: Tank
72m
68m
Start of Water Piping
Magnetic compensation coils
Stainless Steel Lining

## Slide 27: Support Structure
Capacity for 40,000 50cm diameter PMTs, each cell is cm2
Structure built and instrumented at base of cavern and raised into place
Barrel is 93 cells high, 288 cells in circumference.
Aim to install a 4-cell high ring in 3 days

## Slide 28: 50cm PMTs
  20,000 Hamamatsu PMTs
  Improved efficiency, timing, and pressure tolerance
    R&D on shape, manufacturing process
    Box-and-line dynode design
  Purchase complete
  Quality Assurance performed
Notes: Optimised based on identification efficiencies, background rejection power and cost
High-efficiency, high-resolution particularly useful for faint signatures including pi+ and kaons in p-decay modes, pi-0 resolution

## Slide 29: Pressure Tolerance
Bottom of the detector will be under 70m of water = 7 bar of pressure
Stainless steel covers with acrylic faces designed to protect 50cm PMTs from implosion
Implosion tests conducted in the Mediterranean sea.
Production of the covers is underway
Notes: https://lsc-canfranc.es/en/ninth-implosion-test-campaign-for-hyper-kamiokande-pmts-protective-covers-in-collaboration-with-socib/

## Slide 30: mPMTs
Production of 800 mPMTs for installation into the far detector underway
  Multiple production sites
  Some fitted with units with LEDs for calibration
Help to constrain particle dependent energy scale errors
Improve detector calibration by breaking correlations
  Extra directionality and granularity helps separate direct and indirect light
  resolve degeneracies between eg. absorption length and angular response of PMTs
Improve event reconstruction close to the detector wall
  Extend fiducial volume and increase statistics for all physics analyses
https://doi.org/10.22323/1.402.0056

## Slide 31: Hyper-K Outer Detector
The OD is 2m deep in the end-caps and a 1m wide shell in the barrel region.
Maximise the collection of Cherenkov light generated by cosmic muons in this volume
Cosmic muons, 45Hz = ~4 million/day
Background to all physics measurements
3600 photo-sensing modules (8cm PMT + WLS plate)
6 football pitches worth of Tyvek
Notes: Child-hood nightmares

## Slide 32: Underwater Electronics
Readout electronics encapsulated in a waterproof vessel
  Up to 10bar pressure
  No access once water filled – 10s years stable operation
  Underwater cable connections
Route communication fibers to the deck after installation

## Slide 33: Water Systems
Attenuation lengths > 100m required
Radon concentration < 1mBq/m3
  To control radioactive background rate in solar and other low -E measurements
Potential to add Gd (for n-detection) in the future
The FD will hold 250 kilotonnes of water
  equivalent to 100 Olympic swimming pools!
It will take nearly 6 months to fill

## Slide 34: Calibrations
Low level calibration with:
  Light injection
  B-field mapping
  PMT pre-calibration
High level calibration with sources and control samples
  LINAC
  DT
  AmBe
Photogrammetry
  Fixed cameras
  Drone option
Many components tested in the WCTE
Stopping muons
Michel electrons
NCBJ, Poland
Melbourne, Australia
UK groups
See Menai Lamers James’s talk this afternoon for more details

## Slide 35: Status
Hyper-K cavern is excavated and the tank is constructed
Component production and testing is underway
  50cm PMTs, PMT covers, mPMTs, OD units, electronics, DAQ, Calibration systems
Instrumentation installation in the tank next year
Water filling and start of operation planned for 2028

## Slide 36: Backup

## Slide 37: The story so far
Atmospheric neutrinos: disappearance (Super-K): and
Solar neutrinos: disappearance (SNO, Super-K): and
Reactor neutrinos (180km baseline): disappearance (KamLAND): and
Reactor neutrinos (short baseline): disappearance and . (Daya Bay, Double Chooz, RENO):
Beam neutrinos: disappearance (MINOS, K2K): and
Beam neutrinos: , appearance (T2K, NoA): and