## Slide 1: CMOS Monolithic Active Pixel Sensors
M. Deveaux, GSI
Wafer with MIMOSA-5 sensors

## Slide 2
Outline today
What are MAPS and why does a hammer may put them to value.
Hot to improve the time resolution of MAPS without hitting the moon.
Radiation tolerance of MAPS: Why smaller is tougher.
Why telegraphs may cause trouble.
MAPS knocked out: What you should know about Single Event Effects.
Oh oh...
1+1=3

## Slide 3
What do those pictures have in common?
ALICE ITS-2
Soft X-ray spectroscopy (GU Frankfurt)
RNA – sequencing (GU Frankfurt)
J. Cabello, 2007, doi: 10.1109/NSSMIC.2007.4436936.
Tritium autoradiography

## Slide 4
What do those picture have in common?
CMOS Monolithic Active Pixel Sensor
(MIMOSA-26 by IPHC Strasbourg)

## Slide 5
CMOS Monolithic Active Pixel Sensors
What is required to get a MAPS detector?
Mostly a hammer…
…Metal tape…
…and some radiation.
… a Webcam…

## Slide 6: Radioaktivity as seen by a webcam

## Slide 7
The operation principle of MAPS
Reset
+3.3V
+3.3V
Output
SiO2
SiO2
SiO2
N++
N++
N+
P+
P-
P+
Digital camera: ~1000 photons produce one electron each.
Particle detector: One particle produces ~1000 electrons.

## Slide 8
MAPS – the beginning
MIMOSA – 1 (1999)
MIMOSA – 1 (2000)
 | Mi - 1
Pixel size [µm²] | 20 x 20
Pixel number | N x 64 x 64
Readout | Analog
Frame time [µs] | ~104
Dead time | > 50%
MIMOSA 1 paper

## Slide 9
MAPS vs. Hybrid pixels
CMS @ LHC – Hybrid Pixel
~100 µm
~120 µm
Readout - chip
Hybrid:
0.5mm Si
equivalent
Pixel
Pixel
Pixel
MAPS:
~0.05 µm
Si equivalent
Multiple coulomb scattering:
Particle trajectory is manipulated by detector.
Angle scales with

## Slide 10
MAPS – the hope and limitations
Hybrid pixels (LHC / CMS)
 | Hybrid pixels (2001) | MAPS (2001)
Single point resolution | ~ 30 µm | ~2 µm
Material budget | ~ 500 µm Si | ~ 50 µm Si
Time resolution | 25 ns | ~10 ms
Radiation hardness | ~1015 neq/cm² | 1012 neq/cm²
More sensitivity
Massive improvement required.
MAPS Hybrid

## Slide 11
Performance of MAPS today (25µm vs. 50µm thick sensors)
std 25 µm
Dark rate typically <1010/pixel (2 Hz/cm²)
driven by individual hot pixels.
State-of-the-art sensors show spat resolution with <30µm pitch (ALPIDE/MIMOSIS).
May be if charge information is used.
46th CBM collaboration Meeting, Oct. 20-25 2025, Lanzhou, China
p-stop 25 µm
p-stop 50µm
+ 0.5 µm for longer
pixel dimension
Optimal number of fired pixels/particle (about 2.5)
p-stop 50 µm
std 25 µm
p-stop 25 µm
Pitch/5

## Slide 12
MAPS – the hope and limitations
Hybrid pixels (LHC / CMS)
 | Hybrid pixels (2001) | MAPS (2001)
Single point resolution | ~ 30 µm | ~2 µm
Material budget | ~ 500 µm Si | ~ 50 µm Si
Time resolution | 25 ns | ~10 ms
Radiation hardness | ~1015 neq/cm² | 1012 neq/cm²
More sensitivity
More statistics
We need both
Massive improvement required.
MAPS Hybrid

## Slide 13
The need for speed
Time resolution?
Particle rate?
Data bandwidth?

## Slide 14
Speed of MAPS: Limiting factors
Reset
+3.3V
+3.3V
Output
SiO2
SiO2
SiO2
N++
N++
N+
P+
P-
P+
 | Optimized | Traditional
Charge collection time | 1 ns | 100 ns
Signal formation time | few ns | 500 ns
Time resolution |  | 10 000 000 ns
Why the gap?

## Slide 15: Block diagram of MAPS
Externer ADC
Sensor
200'000 fps
=> 1.2 Tbit/s
500k Pixel, 5cm²
8000m/s
3PB/s = 30000m/s
600m/s
What about data compression?
?
3.5h to the Moon.
How much data does a 10m² Detector generate?
About
~3 PB/s.
Should we better start a new pile each hour?
Disclaimer:
Numbers indicative only.

## Slide 16: Data compression
Most pixels (>99.5%) are black.
Only few are white.
Idea: Ignore all black pixels.

## Slide 17
How to readout the pixels?
Pixel array
Output
Chip
FPGA - card
CPU
Rolling shutter readout:
Read pixels sequentially.
Frame time:
ADC
Hit
finder
Column parallel rolling shutter readout:
Read pixels of one column sequentially.
Frame time:
Pixel array
1000 x discriminator
Zero suppression
Outside world
Compress by ignoring dark pixels:
5000 Mbps => 200 Mbps (x25 reduction)
Still – Each pixel is addressed once per frame.

## Slide 18
Why no in-pixel discriminator in 2008-2015?
Reset
+3.3V
+3.3V
Output
SiO2
SiO2
SiO2
N++
N++
N+
P+
P-
P+
15µm
50µm
N+
P
P
In standard CMOS sensors, no PMOS transistors are possible in pixel
=> No high level functions like discriminators … => “slow”
PMOS Transistor

## Slide 19
Quad – Well process (from 2008)
Progress was reached with Quad-well CMOS as provided
by the manufacturer TowerJazz (180 nm, today 65nm).
Reset
+3.3V
+3.3V
Output
SiO2
SiO2
SiO2
N++
N++
N+
P+
P-
P+
15µm
50µm
N+
P
P
deep P-well

## Slide 20
Beyond column paralle readout.
Data-Buffer
01001010010
01001010110
01001011000
On-chip
Off-chip
ALPIDE Sensor.
~ 50 mW/cm²
Human hair (to scale)
~30µm
~30µm
14.5µm
Mimosis Pixel Logic Layout (106 Transistors)
Priority encoder

## Slide 21: Data compression: Efficiency
8000m/s
3PB/s = 30000m/s
600m/s
?
3.5h to Moon.
How much data is generated by a 10m² detector?
~30GB/s = 0.5 m/s
With compression
No compression
Disclaimer:
Numbers indicative only.

## Slide 22
0.3 x 2 cm²
Side band contains:
Data buffers.
Voltage regulators, trim DACs.
Slow control interface.
Temperature sensors.
…
CMOS technology integrates:
Sensors.
Analog electronics.
Digital data processing.

## Slide 23: Toward MAPS Gen. 4
So far “frame readout”:
  Pixels measure for given “frame time”, typically 1-10 µs.
  Results are copied into pixel output buffer.
  Output buffers are read-out by column logic.
+ : No data collisions on column data bus.
- : Time stamping determined by frame time, no matter the pixel performance.
A look to real pixel performance:
Time stamping may be improved by >10x if frame readout
is replaced by “first come, first serve” readout.
Still: Would need a lot of energy for ~10 ns time resolution.
Slew (Signal delay) [ns]

## Slide 24
B. Arnoldi-Meadows
ToT at proprtional seetings: Resolution 42 e
Minimum ToT @ high speed settings: ~3µs
Still not good enough. What about time walk correction?
Time walk correction:
Measure signal amplitude – correct for average delay.
Signal measurement by ADC impossible, what about Time-over-Threshold (ToT)?
Time walk correction may improve sensor performance dramatically.
ToT may
be switched
on and of.
Different setting than previous slide
Inspired by G.A.Rinella et al.,
NIM-A Vol. 1056 (2023) p. 168589

## Slide 25
Time walk correction
DPTS
Start with the DPTS prototype (by ALICE)
2 sensor residual.
~6.3ns single sensor resolution
G. A. Rinella et al., arXiv:2212.08621v4
G. A. Rinella et al., arXiv:2212.08621v4
Time walk correction
As demonstrated in beam (by the ALICE-ITS3 team):
MAPS can reach a time precision of ~6ns (analogue front-end included) with time walk correction.
  Speedup almost 1000x w.r.t MIMOSIS.
DPG conference Erlangen – 16 March 2026
Time-Over-Threshold may provide excellent analogue time stamping with limited energy.

## Slide 26
Going toward faster MAPS – Power consumption
CBM
Data transport cost is non-negligible – needs reduction for lowest power applications.

## Slide 27
Pixel col.
TDC
Position
+ ~10 ns time
Novel sensor concepts (my simplistic understanding)
Downstream logic
Concept of OCTOPUS:
Connect ~20x20µm² pixels individually with readout.
Submit data on raising edge and falling edge each.
Compute Time-Over-Threshold, do time walk correction outside sensor.
=> ~5-10ns time resolution & ~3 µm spatial resolution
First come, first serve.
If collision: Highest spatial priority first.
Asynchronous Priority Arbiter (APA)
More on APA:
https://doi.org/10.1016/j.nima.2024.169663
DPG conference Erlangen – 16 March 2026

## Slide 28
Pixel col.
Fast TDC, e.g. vernier delay line/ring oscillator by
SLAC, IP2I/CPPM
Pixel OR
Coarse TDC
Position
+ ~10 ns time
<1ns time
Novel sensor concepts (my simplistic understanding)
Enable
Enable
Downstream logic
Concept: Use PixelOR for additional time resolution => Needs additional space => 40 µm pixels with four diodes each. Time resolution 1-10ns, spatial resolution 5-10 µm.
Versatile: Aim to tune power vs. performance by slow control.
Pixel structure, APA and much more…: Synergies with OCTOPUS
Asynchronous Priority Arbiter (APA)
More on APA:
https://doi.org/10.1016/j.nima.2024.169663
DPG conference Erlangen – 16 March 2026

## Slide 29
Novel sensor concepts (my simplistic understanding)
Disclaimer: My limited personal understanding.
Trigger
Data (serialized)
Trigger
Data (serialized)
Trigger
Data (serialized)
Data Receiver
TDC
8x8 pixel
Concept:
Build pixel macros with 8x8 or 4x4 tiny pixels (10 or 20µm pitch) => 3µm spatial resolution.
Get time information from “MacroOR”.
Read data in a serialized way.
Best optimized for small pixels and low energy consumption (no ToT by default).
Time resolution <100ns (ALICE3 R&D goal)
ALMIRA

## Slide 30
Finding the best solution: A collapetition…
“People agreed on a common technology. They use it in a
slightly different way.”
OCTOPUS, MANTA and ALMIRA will presumably
Rely on the legacy of ALPIDE/MIMOSIS and ALICE-ITS3/MOSAIX
Differ in column readout in response to complementary optimization.
Share numerous building blocks (e.g. RAM, drivers, …).
Share integration technologies.
Expect substantial synergies in R&D.
GSI is at present involved in all three projects
Coordinated R&D will exploit synergies and to obtain best technologies.

## Slide 31
Radiation tolerance
Will this create signals or damage?
=

## Slide 32
Radiation tolerance
+3.3V
Output
SiO2
SiO2
N++
N+
SiO2
SiO2
P++
P++
P++
GND
GND
+3.3V
Radiation dose
Inititially: Charge collection by diffusion=> slow => Radiation tolerance: 1012 neq/cm²
Idea: Apply electric fields => Speed up
Bulk damage
(Crystal damaged)

## Slide 33
Radiation tolerance: D-MAPS
SiO2
N+
P+
P+
P-
Flat diodes:
Point diodes:
(?)
Max. 1.8V
Max. 1.8V
VBackBias
N+
Improvements
Reduce doping, add back bias, e.g. ALPIDE (hard for >6V).
Extend diodes (H. Pernegger et al., 2017 JINST 12 P06008)
Add AC-Pixel (MIMOSIS-1, see H. Darwish HK 4.5)

## Slide 34
Radiation tolerance: D-MAPS
SiO2
SiO2
N+
P+
P+
P-
Max. 1.8V
Max. 1.8V
Max. 1.8V
Improvements
Reduce doping, add back bias, e.g. ALPIDE (hard for >6V).
Extend diodes (H. Pernegger et al., 2017 JINST 12 P06008)
Add AC-Pixel (MIMOSIS-1, pioneered by IPHC, GU, GSI)
MIMOSIS-1
VBackBias
Flat diodes:
Point diodes:
(?)

## Slide 35
DPTS
TOWER–0.18µm, p-stop (MIMOSIS-1)
TPSCo 65 nm (DPTS)
Going beyond the power wall: Radiation tolerance vs. pitch
DPTS: G. A. Rinella et al., arXiv:2212.08621v4
MIMOSIS-1: H. Darwish et al, proceedings of 20thTrento workshop (2025), under preparation
Others: M. Deveaux, 2019 JINST 14 R11001
MIMOSIS

## Slide 36
Random Telegraph Signal (RTS)
0.35 µm AMS
0.18 µm TowerJazz

## Slide 37
Random Telegraph Signal
My charge is neutral
My charge is positive
Gate
I
t
Symbolic picture:
Measured on photo diode
I
Threshold
A particle…
RTS in diodes: Observed in MAPS since 2004, known radiation damage.
P. Marthin-Gonthier et al. [1], "RTS in small MOSFETs create noise in MAPS"
Check: Noise decreases for bigger MOSFETS in our 0.18µm MAPS [2].
[1] P. Marthin-Gonthier et al., ICECS 2009, Hammamet, Tunisia, 13-16 December 2009. Piscataway NJ : IEEE, 2010, pp. 928-931. ISBN 978-1-4244-5090-9
[2] D. Doering et al., 2014 JINST 9 C05051
Vdd
Load

## Slide 38
0.35 µm AMS
The 180nm noise puzzle
0.18 µm TJazz
Good practice: Transistor as small as possible…
Gate length: 0.35µm
Symbolic picture
Symbolic picture
Gate length: 0.18µm

## Slide 39
Effect of heavy ion hits on electronics
Heavy ions show high dE/dx or LET:
Scales with z² of the projectile => Au = 6200 M.I.P
Bethe Bloch: "Slow" ions create higher LET than relativistic ions.
Minority charge carriers excited by ions may:
Break transistor gates => Gate rupture
Switch digital electronics => Bit flip
Open unwanted conduction paths => Latch-up
(like short cut, extinguish by power cycle)
Macroscopic damage by individual ion: Single Event Effect.
Irreversible destruction
Thermal destruction if ignored
Malfunction if ignored
Latch-up: Vulnerable structure
Unwanted current
Ways to spot SEE:
Gate rupture: Search for permanent failure (not observed).
Bit flip: Write register with known date, read back, compare.
Latch-up: Detect increase of current consumption.

## Slide 40
LET [eV/Å]
500
0
3.3 AMeV Ca
on Si (SRIM)
Not fully to scale
Substrate
ROI
 | M3 @ GSI UNILAC
Energy / ion type | 3.2 A MeV Ca
Beam spot | 1.5 x 1.5 cm² mostly uniform
Beam time structure | 5 Hz pulses of 5 ms
Beam intensity (mean) | ~ 107 Hz/cm²
Beam intensity (pulse) | 400 MHz/cm²
Dosimetry | Dedicated installation
Low beam energy: Sufficient to reach vulnerable structures?
OK
New strategy:
Use masks to isolate building blocks (most sensitive and representative as chosen by the designers)
Test at GSI - M3 beam line

## Slide 41
Beam test UNILAC – heavy ions and SEE
Hits in DAC steering registers confuse sensor.
1-bit flip automatic recovery does not work.
Need power cycle to restart.
No latch-up observed (for LET = 20 MeV cm²/mg).
Sensor withstands 400 MHz/cm² HI (beam impact scenario) w/o damage.
10 s
MIMOSIS-1:
Pulses: Few 106/cm²
No beam
MIMOSIS-1
ROI = DAC
Current [a.u.]
1s
Current [a.u.]
MIMOSIS-2:
Hits in DAC steering registers tolerated.
1-bit flip automatic recovery does work.
May be overwhelmed (2 sync bitflips).
  Observed at fluences ~10² above specs.
  Recovered by reprogramming (most of the time).
Single bit flip recovery circuits now working.
=> Major improvement in robustness (as hoped).
1+1=3

## Slide 42
MIMOSIS prototypes – Tolerance to heavy ion impacts
46th CBM collaboration Meeting, Oct. 20-25 2025, Lanzhou, China
UNILAC ions as seen by MIMOSIS
As results of intense studies: MIMOSIS is considered robust to SEE.
GSI is equipped to do such work for the different communities.

## Slide 43
Summary and conclusion
MAPS are initially derived from digital cameras.
Major advantages: Light material budget and tiny pixels.
Technology being prepared for charged particle tracking since 1999.
  Excellent spatial resolution worked out of the box.
  Improvement was needed on time stamping and radiation tolerance.
Faster time stamping.
  Limited by reading out the pixels and data rates.
  Modern concepts aim for data reduction on pixel level.
  Power may buy time stamping but needs to be provided/cooled.
  Aim: Reach up to ~10 ns and rates up to 100 MHz/cm².
Radiation tolerance:
  Smaller pixels are more tolerant to radiation.
  Single Event Effects are of worry (and GSI is particularly competent to measure them).
  Aim: Reach >1015neq/cm².
  Reducing Random Telegraph Signal and tolerance to SEE remains a continuous task.