## Slide 1: Medical physics appications of CMOS detectors @GSI Biophysics
Daria Boscolo
1st Pixel Platform Workshop (Mar 23, 2026)

## Slide 2
Measurements of charged particle trajectories
MIMOSA-28 sensor
CMOS technology
Active area: ~ 2 × 2 cm2
Pixel size: 20.7 μm
Epitaxial layer: 14 μm
Readout time: 186.5 μs
Spatial resolution: σ < 10 μm
Binary output with high resolution
Developed by PICSEL group,
IPHC Strasbourg
Reconstructed track through the
different clusters and vertex
PhD Thesis of Claire Anne Reidel

## Slide 3
Fluence perturbations due to fiducial markers in ion-beam therapy
CMOS experience @ Biophysics
Three-dimensional fluence distribution from all reconstructed tracks
Quantification of the fluence perturbation due to fiducial markers for particle therapy
Reidel, C. A. et al PMB 2020.

## Slide 4
CMOS experience @ Biophysics
4D-online monitoring of density gradients
CMOS particle trackers that are used to reconstruct the fragment vertices and to verify a treatment delivery
Reidel, C. A. et al Front. Oncol. 2025

## Slide 5
Cluster size distributions to different particles and energies
CMOS experience @ Biophysics
Dependence on the energy loss
Dependence on particle species?
C.-A. Reidel et al., NIMA, 2021

## Slide 6
Characterization of complex scattered fields:
Near-field of 3D-Range-Modulators for in FLASH beam application:
Simeonov et al, PMB, 2017.

## Slide 7
Characterization of complex scattered fields:
Near-field of 3D-Range-Modulators for in FLASH beam application:
50 mm
200 mm
Experiment conducted by Claire-Anne Reidel and Christoph Schuy

## Slide 8
Mini Beam
Characterization of complex scattered fields:

## Slide 9
Or even combining them… PRESTO (EU Pianoforte project)
Characterization of complex scattered fields:
Modulator
Mini Beam
Modulator + Mini Beam

## Slide 10
Ideal applications:
Beam QA for particle therapy
Trackers for monitoring in beam: looking at the phase space
Possibly able to measure dE/dx
Ideal characteristics:
Large area
Operational at high intensities (10^5-10^6 particle per spill)
Compact and transportable
Simple to operate (evtl some routines for clustering, alignment etc..)
Wish list for pixel detectors for medical physics applications

## Slide 11
Claire Anne Reidel
Uli Weber
Christoph Schuy
Andreas Bückner
Marco Durante
Aknowledgments
Thank you for the attention!