## Slide 1: Injector Upgrade for FAIR
W. Barth
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 2: Injector Upgrade for FAIR
Introduction
FAIR-requirements
Status of the Unilac High Current Performance
Further Investigations
  ion source emittance
  RFQ-Matching
  superlens performance
  pulsed gas stripper
High Energy LINAC
  rf-amplifiers
  beam dynamics studies
  accelerator cavity studies
FAIR proton LINAC&UNILAC proton performance
cw-LINAC
Summary&Outlook
W. Barth, GSI - Darmstadt
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 3
The GSI UNIversal Linear ACcelerator
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
High Current Injector (1999)
Alvarez (1975)
Single Gap Resonators (1975)
High Charge State Injector (1991)

## Slide 4
Development of compact, high efficient, (high intensity) heavy ion linac cavities
Delivery of Post-Stripper HILAC (heavy ion linear accelerator) tank on Cyclotron Road (at the horseshoe curve), April 16, 1956.
Mar 1983; Particle accelerator conference; Santa Fe, NM (USA):
238U37+
Very complex ion sources
Ion sources to be optimized for high intensity high charge state beams
Low charge/mass ratio  High field gradient/long accelerating structure
Stripping losses  intensity requirements
Highest linac energy  stripping to the highest possible charge state for max. final beam energy
How to shorten the lenghs of a heavy ion accelerator?
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 5: rf-cavity development -> preparation for the injector linacs
nc-CH-cavity
sc-prototype, 360 MHz
sc-325 MHz
UNILAC-booster cavity
nc-325 MHz
Alvarez
HSI 36 MHz@gsi
HLI 108 MHz@gsi
IH 216 MHz@HIT/Heidelberg
Wideröe
5
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 6
FAIR-Requirements
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 7: UNILAC-Upgrade for FAIR
Front End Upgrade
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 8
Recommendation UNILAC-Review
High Current Injector
Alvarez
Single Gap resonators
Increase of U4+
beam intensity:
Terminal West&
Compact LEBT
- RFQ-Upgrade (rf-sparking)
- KONUS beam dynamics vs. strong periodic focusing -> beam brilliance!
Short
gas-stripper section
- strong periodic focussing -> (ALVAREZ type DTL prefered)
- no performance limitations (vs. costs, length, ...)
- UNILAC as FAIR injector only !!!
Strong performance issues
overall injector strategy?
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 9
Status of the Unilac High Current Performance
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
source+LEBT performance
U28+
Injector per-formance???
38% of the design intensity
(25% of the performance w.r.t. beam brilliance)
Talk of O. Boine-Frankenheim, GSI

## Slide 10: Status Quo
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 11: Terminal West
Dedicated Terminal exclusively for uranium beam
General layout exists
Integrated service area
All power supplies integrated in the Faraday room
No extension within the basement
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
Talk of R. Hollinger, GSI

## Slide 12: Design of LEBT
Measurements of uranium beam emittance@North TerminalEmittance for high current uranium beam (55 mA) , Oct. 2013
 Latest solution: Use existing quartet before RFQ, and a new quartet behind source
9733mm
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 13: Design of a Dedicated Uranium LEBT (long version, allows for three sources feeding the HSI)
iris (U3+ suppression)
98% space charge compensation
magnet field maps used
two charge states
cutting of off-acceptance ions
final
initial
14 mA U4+ inside
220 mm*mrad
C. Xiao
U3+ ~ 20 mA
U4+ ~ 36 mA
220 mm*mrad
13.45 mA U4+ inside ellipse
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 14
RFQ Matching
Data for required advanced beam dynamics simulations (further optimization, upgrade, redesign and development of machine) were collected -> Measurements are complete and self-consistent.
A gain in particle transmission with new QQ settings was confirmed with Ta 4+ (RFQ transmission of 75±2% instead of 51±4%; 4 mA)
Additional tuning of the LEBT, based on dedicated beam dynamics simulations with recently measured beam emittance behind ion source terminal potentially could lead to increased particle transmission for the entire HSI
Further optimization of the whole HSI for high current beam applying new QQ setting is proposed by means of medium ions.
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 15
RFQ-Upgrade
RFQ-Upgrade 2004 (RFQ-Matching, surface quality)
RFQ-Upgrade 2009 (surface quality as well, increase of acceptance, increased field gradient
extensive mixed operation (high duty factor operation m/q=25 (50Ti2+ + short pulse heavy ion beams (m/q=59.5; 238U4+) -> Reduced performance (10% less field gradient): reduced transmission, increased beam emittance
2014: no mixed operation until now -> 96,4% of the design gradient reached.
High probality of ireversible damages of the electrode surface (field emission stimulated by thermal stress, high voltage breakdowns caused by strong particle losses)
New RFQ-rods
tank voltage [a.u.]
tank voltage [a.u.]
Design
5 years of operation
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
Talk of S. Yaramyshev, GSI

## Slide 16
Further Investigations III – MEBT performance
Beamload for a 6.5 mA Uranium beam was appr. 25 kW ( beamload with 2 mA Krypton beam 7.5 kW)
With improved setting for Krypton beam, the measured beamload was reduced to appr. 4 kW.
Beamload caused by a mismatch of the RF-power -> reduced shunt impedance of the resonator (beam is hitting the surfaces).
86Kr2+: 10% higher superlens rf-amplitude & 15% higher quadrupole field strength -> MEBT-transmission increased 75% -> 93%
Recommendation: new quad doublet with increased field strength, trapezoidal shaped superlens electrodes!
(Redesign of the MEBT in discussion)
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 17
Optimization of gas stripper area (1.4 MeV/u)
enlarged apertures
high stripper target density
high current operation (extremely high space charge forces)
full transmission
separation of Uranium charge states
optimum stripping efficiency
less long./transv. emittance growth
max.
40Ar10+
high current
low current
FAIR
high current
(HSI)
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 18
Further Investigations – fast switching gas stripper
How does the gas distribution looks like?
V.P. Shevelko
U4+ + N2; 2,5 ms
U4+ + He; 4 ms
gas cell
25+
27+
reduced average gas pressure
increased target density
pulse to pulse variation
lower gas consumption
 dense noble gas target available
He -> lower (equilibrium) charge state, increased yield
P. Scharrer, et.al.
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 19
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
High Energy LINAC

## Slide 20: Active defects
178 tank-quadrupoles
(leak tightness/water/pre-vakuum, el. properties, ground faults), drift tubes + supports (water& vakuum leaks)
Leak tightness of all tanks
Drift tubes
massive sparkovers beam induced surface defects
Copper surface quality
... inner tank blanket at different positions
Reduced availibility of the focussing system  limited beam intensity and quality, (no) multi beam operation !
Regular and substantial repairing program for all tanks!
High probality of long term-break downs, significant limitations during operation (reduced duty factor, limited rf-voltage, ...)
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 21
High Energy LINAC - rf-amplifiers (2015-2017)
Modularized Upgrade strategy
Exchange of supply and control units
Exchange LLRF, Measurement, interlock
Independent exchange of driver amplifier system (Solid state amplifiers)
Independent exchange of high power amplifiers
  Prototype (THALES) ordered
  Dedicated test area allocated
  Milestone: Successful test operation
  Procurement of series: 2017
  Step by step mounting in shutdowns
Potentially finalized until 2020!
UNILAC rf-amplifier gallery (since 1975)
120m
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 22
Rf-Simulations on Drift Tube Design for
HE-Linac Alvarez-DTL with strong periodic Focusing
present
modified (current status)
Rs = 53 MΩ/m
Rs = 60 MΩ/m
108 MHz, example: Lcell = 200 mm ≙ 2.45 MeV/u
X. Du
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
Rf-Simulations on Drift Tube Design for
HE-Linac Alvarez-DTL with strong periodic Focusing
Interdigital H-Mode cavity: Emittance Growth Reduction for KONUS Beam Dynamics
new: old: UNILAC*:
Transmission: 92% 88% 100%
Emittance growth: ~ 35% ~ 50% 20-40%
*measured
new design (2014)
KONUS beam dynamics features high effective Rs
the price to pay is reduced focusing & periodicity in transv. & long. planes

## Slide 23: The FAIR Proton Injector
Beam Energy Beam Current (design/oper.) Beam Pulse Repetition Rate Frequency Norm. Emittance at output Momentum Spread Beam Loading (peak) RF Power (peak) Klystron (3 MW Peak Power) Solid State Amplifier (50 kW) Total Length (RFQ + CH) | 70 MeV 70 / 35 mA 36 µs 4 Hz 325.224 MHz 2.1 / 4.2 µm ≤ ± 10-3 4.9 MW 2.5 MW 7 3 ≈ 27 m
RFQ
CH-DTL
Klystron
≥2019

## Slide 24
UNILAC proton performance
Chart: Ion current [mA]
Avril 14 (H3-p) | 0.485 | 0.1 | 0.0751 | 0.0598 | 0.0334 | 0.031 | 0.03 | 0.0853
May 14 | 2.1 | 0.64 | 0.55 | 1.43 | 1.21 | 0.91 | 0.92 | 0.67
July 14 | 2.4 | 1.23 | 0.95 | 1.94 | 1.85 | 1.78 | 1.74 | 1.52
October 14 | 3 | 1.5 | 1.26 | 3
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
April 14 (H3p)

## Slide 25
High intensity proton beam@UNILAC
clean ion source&stripper-spectrum
high brilliance beam
parallel operation -> carbon beam operation!
Further development goal: 3emA, improved ion source performance, careful UNILAC-optimization w.r.t. beam transmission
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 26
Chart: FAIR: 15emA, U28+, 1.1 mm*mrad
| stripper section | ALVAREZ | transfer line
Iproton/acc. [%] | 110.5 | 79.9 | 74.2333
UNILAC proton performance
SiS-acceptance (norm.) [pi*mm*mrad] | 1.1
SIS-p-design current | 1,76
SIS-Uranium-design current | 15,0
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 27
High Intensity protons@FAIR
FAIR
p-LINAC
GSI-UNILAC
S. Appel, GSI
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
3emA
2.1e11 (measured)

## Slide 28: Post acceleration of UNILAC p-beam
Beam Diagnostic Test Bench (since 2008)
FAIR-p-LINAC-Prototype (to be tested 2015)
Dump
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
28

## Slide 29: Post acceleration of UNILAC p-beam
Beam Diagnostic Test Bench (since 2008)
FAIR-p-LINAC-Prototype (to be tested 2015)
Dump
24.3 MeV, p
rebuncher
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
29

## Slide 30: Superconducting cw-linac layout
High charge state injector@GSI
Small number of rf cavities and short cavity lengths (1m)
acc. gradient of 5 MV/m  compact linac design
Several cavities, solenoids per cryostat
Very small transverse cavity dimension
GSI/HIM-SHE-progr.
Super Heavy community  High duty factor, 7.5 MeV/u, variable beam energy, heavy ion linac
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
30

## Slide 31: Pushing the limits: cw-heavy ion beams@coulomb barrier
He-reservoir
Advanced Demonstrator
High Charge State Injector
Wkin = 4.6 MeV/u (heavy ions)
Wkin  5.8 MeV/u (medium ions)
Step 1 (2016)
Step 2 (2019)
Power Supplies, rf-amplifiers and controls
7773 mm
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 32
Summary&Outlook (Update!!!)
UNILAC-Upgrade measures:
  Terminal West, Compact LEBT – increased primary beam intensity
  RFQ&MEBT-upgrade and careful beam matching for entire HSI
  No change for stripper section incl. charge separation system  pulsed gas stripper
  Optionally re-design of matching line (depending on DTL solution)
Two to be considered HE-LINAC options: ALVAREZ type DTL (strong periodic focusing) or IH-type DTL: short tanks, triplet focusing scheme
  Design and layout, testing of the major HE-LINAC key components
  Reconstruction of rf-amplifier gallery  preparation for HE-LINAC
FAIR commissioning with upgraded HSI, but existing UNILAC DTL (improved reliability)
Avoiding long duty operation (in particular mixed operation with short pulse heavy ion beams) -> applying UNILAC as injector for FAIR only  cw-LINAC project
UNILAC usefull as a (medium) high current proton injector for the first time  FAIR p-LINAC (longterm option)
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 33: Backup
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 34
28 GHz-ECR ion source
RF injection side
Beam extraction side
Increase pulse intensities for medium and heavy ions by a factor of 10-15!
GOAL:
Higher Charge State  higher energy gain
Higher Charge State  higher beam intensity without stripping
Higher heavy ion beam intensity  cw-/ pulse-mode operation
Compact accelerator  lower cost
low consumption rate -> operation with rare isotope
ECR-projects/developments for heavy ion application:
VENUS (LBNL)
SERSE (INFN)
SUSI (NSCL/MSU) -> FRIB (U33+/34+)
MS-ECRIS@RIKEN (U35+)
SECRAL (IMP-HIRFL) (U41+)
Uranium-Charge state distribution from the RIKEN 28 GHz SC-ECRIS
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 35
Status of the Unilac High Current Performance
March 14: 2.35 emA, U28+@Transfer Line -> Injector performance dropped down (2012)!
U28+
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany

## Slide 36: Beam Diagnostics Test Bench
(enlarged)
quadrupole duplett
hor./vert. slit
profile grid
h/v-steerer
beam-dump
ion current
beam profile
position (correction)
beam emittance
bunch structure (non destructive)
beam energy
High resolution x/y-profile grid
(emittance meas.)
phase probe
(beam position)
beam transformator
(ion current)
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany
36

## Slide 37
Compact-LEBT – Status
Design of the LEBT in progress, optimum solution proposed, other solutions under investigation.
Optimum solution: Length appr. 9.7 m , two focusing magnets up to switching magnet (quadrupole/solenoid not yet decided): Appropriate for various alternative scenarios of RFQ (unchanged or redesigned), adjustable for various beam emittances from ion source.
Measurements at North terminal with Uranium und Tantalum June-October 2013, used for simulations for proposed LEBT-design!
15.10.14
W. Barth, Injector Upgrade for FAIR, ICST, Worms/Germany