## Slide 1
STT News
Peter Wintz (IKP, FZJ)
PANDA Collaboration Meeting, Dec-2013, FAIR

## Slide 2
Recent STT activities
    Workshop summary
    Straw production & straw layout
    Readout systems
    Test system installations
  Beam tests 2014
STT timelines
  STT pre-series test in 2015/16
STT News

## Slide 3
STT Workshop in Oct-2013
STT work packages discussed
Straw and layer-module production (FZJ)
STT general mechanics (LNF)
Gas system (LNF)
Frontend / analog electronics (Krakow, FZJ)
Digital readout (Krakow, FZJ)
Detector control & HV system (IFIN-HH)

## Slide 4
  STT straw layout:
    New straw pitch: 10.12 mm (~ 10 µm gap)
    Straw diameter: ~ 10.05 mm (pressurized)
    Mylar film wall: 27µm
  Straw layer modules
    Determine all straw positions (soon)
    Group straws into 4-layer modules, stereo-layer modules
    Periphery, mounting elements, ..
    Integration in mechanical frame  iteration with Dario
Straw Layout in STT
straw pitch

## Slide 5
Straw production
    final straw film specification, leakage tests successfull
    straw series production started in Oct-2013
    complete straw mass production takes 3-4 years, including ~50% spares
Quality checks
    leakage and wire tension measurement for each straw
    long-term test sample
Straw Productions

## Slide 6
Currently in preparation: large-scale systems
ASIC-ToT + TRBv3:
    new ASIC chip in design, in production soon
    available in (late) Q2/2014, ~ 100chips (8ch)
FADC based readout
    new design amplifiers & cabling, FPGA/FADC architecture
    available in Q2/2014
Electronic Readout Status

## Slide 7
Permanent STT test systems with DAQ in Juelich
PC network (“strawnet“)
ASIC-TRBv3 readout installed last week by Cracow
      3 ASIC-boards, 96 channels
    Greg‘s, Jacek‘s talks
Cosmic ray tests as preparation for next beam tests
      tuning setups, straw electric coupling, HV distribution
      optimise electronic parameters (ASIC shaping)
      define default straw operation settings (gas gain)
      clean tracking  resolution limits
Test System Installations

## Slide 8
Beam time requests for 2014 (COSY)
    1 week in Jun-2014, protons at 3.0, 0.8, 0.6 GeV/c
    1 week in Sep-2014, deuterons at 2.0, 1.3, 1.0 GeV/c
    1 week in Nov-2014, protons at 2.0, 1.3, 1.0 GeV/c
    dE/dx range ~ 10 mips
    aim for prot./deuteron separation
2 straw setups for both readouts
    824 straws and 816 straws
Optional: larger straw setups if
new RO systems available
Beam Tests 2014
2 Straw setups, beam coming from the back (Big Karl area @ COSY)

## Slide 9
M3: TDR approval 1.03.2013
M8: Pre-series test accepted 31.03.2016
M9: Final STT construction, acceptance test 31.03.2018
M10: Shipment to FAIR / approval for installation 30.06.2018
M11: Ready for beam 30.09.2018
M12: Commissioning done / ready for operation 20.12.2018
Official timelines transmitted to FAIR
STT Milestones & Roadmap

## Slide 10
M3: TDR approval 1.03.2013
M8: Pre-series test accepted 31.03.2016
M9: Final STT construction, acceptance test 31.03.2018
M10: Shipment to FAIR / approval for installation 30.06.2018
M11: Ready for beam 30.09.2018
M12: Commissioning done / ready for operation 20.12.2018
Official timelines correlated with money flow
STT Milestones & Roadmap

## Slide 11
One complete STT sector (~ 800 straws)
    final design of straw-layer modules
    mechanical frame
    electronic RO system (800 channels)
    supply system & DCS
Assembly and installation in 2015
Beam test at COSY 2015/16
  Complete! test
STT Pre-Series Test
STT hexagon sector
Beam

## Slide 12
  Tracking + dE/dx measurements
    position calibration by reconstructed tracks
    isochrone + dE/dx calibration methods
    scatter target?  fiber, foil, .. in beam
    final resolution
  Continuous DAQ, (PANDA-DAQ v1?)
    high particle rates ~ 1 MHz
    online tracking
  No magnetic field, straight tracks
Pre-Series Test Program
STT hexagon sector
Beam