## Slide 1
Reconstructing Radiator Plates for the Barrel DIRC
Marko Zühlsdorf1,2
1GSI Helmholtzzentrum für Schwerionenforschung GmbH, Darmstadt
2Goethe-Universität Frankfurt

## Slide 2: DIRC Design Options
use 1 wide plate Instead of 5 bars per segment
  fewer pieces to be polished
  requirements for optical quality of side surfaces less severe due to fewer side reflections
  significant cost reduction
What about PID performance?
30 cm
Synthetic fused silica instead of mineral oil as material for expansion volume
  one prism per DIRC segment
  better optical properties than oil

## Slide 3: Reconstruction via Look-Up-Table
Maria (PANDA CM, Dec12):
radiator
detection plane
Reconstruction gets harder with wider radiator as width contribution to θC-resolution is not negligible anymore
top view
z
x

## Slide 4: Time-based likelihoods
1 GeV/c
140° θ
3.5 GeV/c
22° θ
π+
π+
K+
K+
In 3 dimensions (X,Y,T) hits patterns show differences between particle species
π
K
Probability Density Functions (pdf) can be created
by shooting ~100,000 particles in Monte Carlo with same event parameters

## Slide 5: Likelihood ratio test
:
pdf:
:
:
:
:
Take log-likelihood-difference
:
Separation Power: 4.7σ
π-tested
K-tested
Likelihood for Hypothesis
PDF for Hypothesis
Background distribution
Expected photon number for Signal
Expected photon number for Bg.
Distribution of expected hits (poissonian)
3.5 GeV/c
22°

## Slide 6: Time based likelihood test: Example
1 GeV/c
3 GeV/c
Blue: Kaon hypothesis
Red: Pion hypothesis
loop over all hits and multiply pdf values
take the likelihood ratio for two competing hypotheses
apply cut value to accept or reject hypothesis

## Slide 7: Time based likelihood test
π-tested
K-tested
3.5 GeV/c
22°
SP=4.7σ
π-tested
K-tested
1 GeV/c
90°
SP=6.8σ
π-tested
K-tested
1 GeV/c
140°
SP=8.4σ

## Slide 8: Time based likelihood test
Simulations have been done with 100 ps time resolution.
But what if we don’t have such timing?
100 ps
500 ps
1 ns
1 GeV/c
140°
3.5 GeV/c
22°
PID seems to be quite robust.
Even with a timing worse than 100 ps results can be expected.

## Slide 9: Test Beam Analysis
Greg has told much about the Beam in 2012 but to repeat the essential things:
August 10 – September 3, 2012
Prototype test at CERN PS T9
Tested different design options and varied
many interesting parameters
August 28 – September 1
First plate prototype was tested!
Mainly different lenses were tested with rotating track angle
Few momentum scans without lens

## Slide 10: Test Beam Analysis
Data
10 GeV/c hadron rich beam
Simulation
10 GeV/c pions
dead PMT
trigger missing
on TRB
-> no calibration

## Slide 11: Test Beam Analysis
Simulation
10 GeV/c pions
Data
10 GeV/c hadron rich beam
Further alignment
may be necessary…
Misalignement between
pixels on same PMT

## Slide 12: Test Beam Analysis
Hit pattern in x,y,t look similar to Monte Carlo.
With fiber tracker coincidences picture improves but statistic goes down (1% left).
Simulation does not perfectly describe data
Further alignments have to be done
Photon yields do not match:
18.3 hits per event from sim
47 hits per event from data
Next steps:
Further improve simulation
Use 10 GeV/c runs to calibrate simulation and low momentum runs to perform PID
Fiber Tracker 1
Fiber Tracker 2

## Slide 13: Summary
Outlook
A design based on radiator plates instead of narrow bars would significantly reduce the cost of the Barrel DIRC.
A likelihood based approach shows good results for simple geometries for ‘crucial’ phase space points.
Time resolution of 100 ps may not be necessary.
Test beam plate analysis has started and shows promising conformity with simulated hit patterns
Beam data needs to be further processed before reconstruction can be applied.
Reco method will be applied to beam data from 2012.
Designs with focusing optics will be tested
An analytical approach to calculate pdfs has to be found as there are too much points in parameter space to be covered by MC.

## Slide 14: Strange hadronic processes in Geant4
Summer 2013
now

## Slide 15: Strange hadronic processes in Geant4