## Slide 1
ELOG-RAG
Deep answers from measurement-heavy logbooks.
Finding a needle in the needle stack.
Alexander Warth · SC Magnets & Testing · GSI/FAIR AI Workshop, 31 August 2026
Supported by the GSI Innovation Fund · External industry pilot partner · Runs fully on-premise
Notes: Take RAG as given – the previous talk covered it. This talk is about what happens when the questions are precise and the entries are dense.

## Slide 2
01 THE DATA
Can a system understand this?
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
2
#8796 · 17.08.2026 · QDM-040 · cooldown run CD02 · "Bipolar Cold Run 2"
Performed: %SH_Bipolar%, %SV_Bipolar%, %CS_Bipolar%
** CS ** Bipolar Stability (10 minutes)
1. [16:01:37], -250 A -> 0.000 s -> 250 A -> 0 A -> -250 A,
+1225.0 A/s, -1225.0 A/s --> CS Quench: [No];
** SH + SV ** Bipolar Stability Validation (10 minutes)
Green. [16:14:28], -100 A -> 250 A -> 0 A -> -100 A, +/- 857.5 A/s
--> SH Quench: [Yes @ 16:14:34], SV Quench: [No]; #Mistake
Green. [16:17:07], -100 A -> 250 A -> 0 A -> -100 A, +/- 857.5 A/s
--> SH Quench: [No], SV Quench: [No];
...
ASK-AI "Did SH quench above 800 A/s in cooldown 02 of QDM-040?"
Answer:
….Entry 8796 (Bipolar Stability, 17.08.26): SH + SV Bipolar Stability Validation at 857.5 A/s – one instance showed SH Quench: [Yes @ 16:14:34], but this was flagged as a "#Mistake" and subsequent runs at the same rate were stable….
Dense by construction
Timestamped ramp sequences, currents, ramp rates, quench yes/no with time, operator remarks - several facts per line, in a house notation that never appears in any training corpus.
2,702 entries carry explicit measurements with units
79 authors over twelve years – notation drifts
97 % EN · 3 % DE bilingual, sometimes within one entry
The answer below is the system's, verbatim: it finds the entry, reads the quench, and reads the operator's #Mistake flag right after it.
Notes: Real entry, operator names removed. Point: the information is there, it is just not in a form similarity search can use. Structure has to be extracted at ingest.

## Slide 3
02 THE DATA
8,712 of those. Twelve years of them.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
3
8,712
logbook entries
Series Test Facility ELOG, July 2014 to today: 157 modules, every ramp and quench.
12
years
Reaches back well before the current campaigns. Vocabulary and authors change.
229
cooldown runs
Ramp rates, quench currents, dwell times, module and feedbox IDs, cross-references to earlier entries – per run, per module.
Breadth vs. depth. A shift log spans a whole machine in narrative form. A test-facility log spans one magnet in numbers. The questions people ask it are entity-scoped, numeric and temporal - "which Corrector Magnet of QDM-030 quenched above 230A in any cooldown run?" - and similarity search alone does not answer them.
Notes: Do not compete on volume. Position: different problem class – depth per entry instead of breadth of entries.

## Slide 4
03 THE BASELINE
Where plain RAG breaks.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
4
Chart: Strict accuracy per question group – baseline run R53
| Procedural | Deep research | Test-stand scoped | Exact entry by ID | Core retrieval | All 99 questions | Multi-run / module | Author
Strict accuracy, run R53 | 0 | 0 | 0.25 | 0.33 | 0.48 | 0.59 | 1 | 1
Baseline: vector retrieval, one LLM pass - naive RAG pipeline.
Similarity search finds look-alikes. It is fine for "what happened to module X" and fails outright on everything that needs structure or iteration:
exact counts, totals, most recent entries
procedures assembled from many entries
analyses across several runs or modules
scope limited to one test stand (FB1–FB4)
Fixed question set (99 questions in 13 groups now), re-run after every change.
Ground truth is not hand-labelled - each question carries a SQL recipe that re-derives it from the live database.
Notes: The tactful answer to a single-branch RAG: nothing personal, just the measured failure modes. Everyone in the room asks these question types.

## Slide 5
Supervison
04 THE APPROACH
Classify, route, escalate.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
5
Question
Classify
8 classes · confidence · entities
Resolve
names → canonical IDs
Route
Lane 1 · Single pass
1 LLM call · fast
Lane 2 · Iterative
≤ 6 tool steps
Lane 3 · Deep
plan → gather ∥ → analyze
simple &
confident
complex or
unsure
depth =
deep
Answer
+ sources
escalate: user button, or classifier unsure
Bounded effort at every level: one call, six tool steps, or a plan you can read before it runs. Every answer cites entry IDs; ambiguous names produce a caveat, not a guess.
"qdm050", "magnet 50", CID "02-000050-50-4" → QDM-050 · "last run", "CD03" → run ID · nothing unresolved reaches SQL
Notes: Concept level. Classes exist because each needs a different search strategy. Do not name internal components.

## Slide 6
05 THE RESULTS
0.59 to 0.98 in ten iterations.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
6
Chart: Accuracy on the fixed 99-question set, May – July 2026
| R53 | R54 | R55 | R56 | R57 | R58 | R59 | R60 | R61 | R62
strict | 0.586 | 0.63 | 0.79 | 0.68 | 0.82 | 0.85 | 0.86 | 0.83 | 0.92 | 0.98
pass (minor gaps tolerated) | 0.83 | 0.9 | 0.88 | 0.9 | 0.92 | 0.95 | 0.93 | 0.94 | 0.96 | 0.99
0.98
strict accuracy at R62
What moved the curve
procedural 0.00 → 1.00
deep research 0.00 → 0.83
test-stand scoped 0.25 → 1.00
exact entry fetch 0.33 → 1.00
core retrieval 0.48 → 0.96
Temporal, multi-run and author questions were solid from the start and held. Shown: R53–R62 on the 99-question set;
Notes: R56 dip = fixture change r45/r46, then recovery. The eval set is the thing that cannot be copied from a slide.

## Slide 7
06 IN USE
It reads the logbook so nobody has to.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
7
FB1
1 module
1 active
QDM-040
● Cooldown 02 since 8/11/2026 — last entry 1d ago
COLD-RUN TESTS Cooldown 02 · 5/13 tests
○ Cooldown
✓ Magnet Training
✓ HV Test
○ Sensor Test
○ Heater Test
○ Quench Detection
✓ Heat Load
✓ AC Loss
✓ LCL Steerer
○ Warmup
RECENT ACTIVITIES
Digest 1d ago
Yesterday
Bipolar stability testing revealed an anomaly where an SV power converter crash led to an attempt to restart via DC -250 A, which triggered an SH quench at 250 A. (#8810)
Aug 21
AC loss characterization of the QD magnet was performed with high ramp rates (up to ±22,000 A/s) reaching 10.5 kA without triggering a quench. (#8806)
Aug 20
Fast and slow extraction cycles on correctors (SH, SV, CS) were successfully completed at ±1225 A/s with no quenches recorded. (#8804)
Aug 19
DC endurance test confirmed stability for SH, SV, and CS correctors held at 250 A for over two hours without incidents. (#8802)
Static heat load measurements required manual correction due to sensor QN10KK12_BT01 being out of calibration (reading 5.9 K vs expected ~5.4 K). (#8800)
Autonomous dashboard
Per-feedbox module state, cold-run test coverage and a nightly activity digest with entry IDs - no question needed. Each summary links to its sources; the state on the left is the live one from this morning.
Ask-AI search
Plain-language questions, depth auto or deep, escalation offered on every answer. "Verify against the original" is built into the UI.
Live ingestion from the STF ELOG, containerised, GSI network.
Notes: Rendered from the live dashboard on 27.08.2026 (FB1, QDM-040 CD02). If you can, show the real thing instead.

## Slide 8
07 STATUS & NEXT
Production by year-end. Your logbook next.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
8
Where we are
D1 RAG system with web UI – delivered
D2 GSI integration: live ELOG, on-prem inference, dashboard - delivered
D3 knowledge graph & evaluation - in evaluation, incl. user test against keyword-search baseline
D4 production operation & documentation - Q4. Needs: an on-prem VM, LDAP auth, an ELOG service account
Funded by the GSI Innovation Fund, Mar–Dec 2026
External industry pilot partner on board Searching for further Partners – Industry and Research
Bring your logbook
The pipeline is a template. Any ELOG with structured entries - module, device, run, date - can be onboarded and evaluated with the same harness. Domain-specific parts: one fact schema, one set of relation rules.
What it costs you
read to your ELOG Instance (service account)
Meta Data Structure
What you get
AI Assisted Search - find your Information in the “Needlestack” quickly
>> Next: explicit ontology layer; same pattern on archived settings and observables.
a.warth@gsi.de · +49 6159 71-3044
Notes: Collaboration hook for IT and other departments: shared inference infrastructure, no duplicated cost, portable pipeline.

## Slide 9
Backup

## Slide 10
09 BACKUP
Recovery by question group (R53–R62).
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
10
13 groups, 99 questions
R core retrieval · N numeric/recency · MD module diversity · TQ temporal · DE German-language · MM multi-run · EM exact entry · DR deep research · AG aggregate · EC edge cases · TS test-stand · AU author · PR procedural
Strict = complete answer, every number and ID correct. A single wrong count fails the question. Each record carries expected route, class, entities, source entry IDs and an oracle SQL recipe; a judge rubric scores the rest.
The groups that failed outright at baseline are the ones that need structure and iteration – exactly where the graph and the agent lanes act.

## Slide 11
10 BACKUP
Hybrid retrieval, one query.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
11
QUERY "What is currently done on QDM-040?"
KNOWLEDGE GRAPH
Structural traversal
Exact counts, relations,
current module state
Derived from entry metadata – no LLM
VECTOR SEARCH
Semantic similarity
Embed → cosine → top-k
Finds cases described differently
KEYWORD SEARCH
BM25 full-text
"QDM-040", IDs, part numbers
Exact identifiers never get lost
FUSION & RERANKING deduplicate · merge · rerank · top-k → LLM synthesis with citations
ANSWER + SOURCES #8746 · #8747 · … – structured, semantic and lexical signals fused into one ranked answer.

## Slide 12
13 BACKUP
Topology.
ELOG-RAG · GSI/FAIR AI Workshop · 31.08.2026
14
BACKEND
WEB UI
GSI LLMBot (on-premise)
Open-weight models
Embedding · inference
PostgreSQL + pgvector
8,712 entries · 8,979 chunks
157 modules · 229 cooldown runs
Vectors · facts · graph relations
ELOG-RAG
Ingest · hybrid retrieval
agent lanes · composer
Dashboard
Feedbox & module state
Activity digest with entry IDs
Ask-AI search
Beyond keywords · depth auto/deep
Structured answers, cited sources
STF ELOG
Live ingestion daemon