## Slide 1: Development of novel detector concepts for nuclear physics with rare isotope beams at FRIB
Marco Cortesi Detector Systems Group Leader cortesi@frib.msu.edu
7 September 2026

## Slide 2: Outline
FRIB Overview
Detector Systems Supporting ARIS
  DL-PPAC tracking/ToF, diagnostics suite, beam performance stats
  Discharge Mitigation: Anti-Discharge Unit (ADU)
Focal-Plane Tracking & PID (S800 / Sweeper / HRS)
MPGD R&D Program
  Multi-Layer THGEM (M-THGEM): position sensitive readout for TPC in active-target (AT) mode
  Multi-Mesh THGEM (MM-THGEM): Fission-Fragment Imaging and implementation on the GIRAFFE detector system
Summary & Outlook

## Slide 3
Fantastic Nuclei and Where to Find Them
Facility for Rare Isotope Beams (FRIB)
FRIB Science Drivers • Nuclear Structure and Reactions • Nuclear Astrophysics • Fundamental Symmetries • Societal Benefits and Applications
FRIB is a U.S. DOE Office of Science scientific user facility, one of 28, providing beams of rare isotopes for nuclear science research
Key capability: up to 400 kW beam power at design capacity (currently operating at ~20 kW, 30 kW demonstrated)
Enables experiments with fast beams (~200 MeV/u), stopped (trapped) beams, and reaccelerated beams (0.6–10 MeV/u)
In-flight isotope separation provides access to more than 80% of the isotopes predicted to exist in nature

## Slide 4: FRIB Laboratory Layout
LINAC
Superconducting linear accelerator that boosts heavy-ion beams to energies above 200 MeV/u.
Production Target System
Converts the primary beam into a wide range of rare isotopes via fragmentation or fission.
ARIS
Advanced Rare Isotope Separator — selects and purifies the isotopes of interest for delivery to experiments.
Experimental Areas
BECOLA, N4, ReA, S2, and S3/S800 host precision, reaccelerated-beam, and fast-beam experiments.
LINAC
Production Target Area
ARIS
Experimental Areas
S3/S800
N4
BECOLA
ReA
S2

## Slide 5: Bird’s Eye View of ARIS: Detectors
DB1
(Pre-Separator Focal Plane)
DB2
DB3
DB4
DB5
(Final
Focal Plane)
Pre-Separator Wedge
Critical for momentum compression and transmission
Target
PPAC pair
PPAC pair
Thin Sci
PIN
Thick Sci
A/Q
Z
PPAC pair
Diamond
Thin Sci
PPAC
PPAC pair
Thin
Sci
PIN Stack
HPGe
Multi-stage (two- or three-stage) separation using “wedges”
Selectable optics
  Momentum compression
  High resolution CB1
  Large acceptance CB2
Features
  Particle identification (PID) of individual isotopes
  Production of ions via projectile fragmentation and/or abrasion-fission
Event-by-Event Identification based on Bρ-ΔE-ToF
Notes: Ok, now back to ARIS, detectors. Salvatore just shared a lot about the ARIS detectors, so I will tell you how we use them.

## Slide 6
FRIB hosts a suite of scientific instruments and general-purpose beamlines in support of the user program
Most systems inherited from the NSCL legacy facility (e.g., Sweeper and S800 spectrometers)
New instrumentation currently under development (e.g., High Rigidity Spectrometer)
Reaccelerated Beams
Stopped Beam
Fast Beams
Science Opportunities at FRIB
with Fast, Stopped, Reaccelerated Beams

## Slide 7: State-of-the-art Diagnostics to support ARIS operation
Time of Flight (ToF):
Plastic Scintillator:
EJ232 (0.15 mm – 1 mm)
PMMA Light guide
Hamamatsu H6533-20
Performance:
  Time  <100 ps (σ)
  Rate  up to 1 MHz
Diamond
Area up to 30x30 cm2
Thickness = 100/200 μm
Performance:
  Time  <50 ps (σ)
  Rate  above 1 MHz
Delay-Line PPAC (DL-PPAC)
Various sizes
Delay-line readout
Custom-made two-stage pre-amplifiers
Anti-Discharge Unit implemented
Performance:
  Position  0.5 mm (σ)
  Time  <150 ps (σ)
  Rate  up to 300 kHz
Si-PIN (Micron Semiconductor model MSX25)
ΔE/E measurement
Performance:
  Energy  < 5% (σ)
  Rate  up to a few kHz
Total Kinetic Energy (TKE)
EJ232 (20x20 cm2 single block)
Two PMTs (Hamamatsu H6533-20)
Dedicated QDC-based DAQ
Performance:
  Rate  up to 1 MHz
TKE Si-PINs
(Micron Semiconductor. MSX25)
Thickness  0.3–1.5 mm
CSP  Mesytec MSI-8 (up to 5 GeV)
Performance:
  Energy  <5% (σ), 5.9 MeV α
  Rate  up to a few kHz

## Slide 8: Operating with 20 kW Beam since March 2025 Total 4190 Scheduled Operating Beam Hours at 92.8% Availability in FY2026
Primary Beams
18O
22Ne
28Si
36,40Ar
40,48Ca
58Ni
64,70Zn
82Se
92Mo
124Xe
144Sm
198Pt
208Pb
238U
Experiments since October 2025:
E21023 (238U): 224Th, 213Fr
E21048 (238U): 85Se
E23035 (64Zn): 60Ga, 59Zn, 58Cu
E25506: (64Zn): 62Zn, 60,61Cu
E25058 (28Si): 20Na, 20,21Mg, 22Al
E21004 (124Xe): 106,108Sn
E21021 (124Xe): 99-101Sn, 98-100In, 97,98Cd, 96,97Ag, 95,96Pd
E21066 (70Zn): 54Sc, 52,53Ca, 55Ti
E21039 (92Mo): 77-80Y, 79,80Zr, 82,83Nb
E23005 (40Ar): 21O
E21080 (208Pb): 183Tm, 186-187Yb, 189-190Lu, 188-192Hf, 189-194Ta, 191-196W, 195-199Re,197-203Os,199-203Ir
E23071 (144Sm): 128-129Sm, 125-128Pm, 123-127Nd, 121-128Pr, 119-125Ce, 116-124La,114-122Ba, 112-119Cs, 111-116Xe, 110-114I, 109-112Te, 108-111Sb
E25022 (40Ca): 35Ca, 33Ar, 32Cl, 31S
More than 650 Rare Isotope Beams Have Been Delivered to FRIB Experiments

## Slide 9: Delay-Line Parallel Plate Avalanche Counter (DL-PPAC): Design Overview
Various sizes (10x10cm2, 20x5cm2, 20x10cm2,30x5cm2)
Delay line (33 nH, 3.3 pF  1 ns/mm )
Custom-made two-stage preamplifier (20dB + 10dB).
Dedicated GHS and DAQ (CFD+TDC)
Operation at <15 Torr iC4H10 or C3F8
Provides: Event-by-event momentum vector determination and ToF signals
(-)
(+)
(+)
Used at several locations in ARIS
X-coordinate
Y-coordinate
Electrodes: 150 nm thick metal (Au, Ag, Cr) layer on a 0.75 μm polypropylene foils
Cathode: uniform foils or wires (MWPC)
Cathode

## Slide 10: DL-PPAC: Summary of Performance
Electrons
Ions
Summary Performance:
Uniform gain (>103) across the effective area
Time resolution (ToF) < 150 ps (σ)
Position Resolution ≈ 0.5 mm (σ)
Rate capability up to ≈300 kHz
10x10 cm2 DL-PPAC

## Slide 11: Beam Tests of DL-PPAC and MWPC Demonstrating High Efficiency at Low Z and High Rate
Low Z detector efficiency test with a beam (Z<30) @ 180 MeV/u
  100% efficiency for all fragments achieved under optimal operational conditions
    iC4H10 at 10 Torr
    PPAC bias > 780 V
    MWPC bias > 865 V
High-rate detector efficiency test with U-238 (Z=92) beam @ 194 MeV/u
  Full detection efficiency for rates up to ≈300 kHz
  Improved by a factor of ~60 compared to the old NSCL PPAC readout technology based on resistive chain
S. Di Carlo, M. Cortesi et al., “High-rate heavy-ion tracking using MWPCs and PPACs with an Anti-Discharge Unit”, JINST, vol. 21, P03022, 2026

## Slide 12: ARIS Particle Identification Capability with PPACs
Delay-line PPACs provide:
  Good time resolution
  Reduced thickness vs scintillators
  Lower charge-state production
  No wedge effect in dispersive plane
Trajectory reconstruction provides Bρ
PID from ΔE–TKE, ToF, and Bρ
  ΔE–TKE: PIN telescope
  ToF: DB3-PPAC1 & DB5-PPAC1
  Bρ: PPACs at DB3, DB4, DB5
Z
Z
A/q
Resolution (DB3-DB4-DB5 reconstruction)
(Z) = 0.167 (as average of first 3 PINs)
(q) = 0.093
(A-2q) = 0.105 (mass resolution)
(A/q) = 0.0024
q
A/q
10
40
30
20
50
Z
0
5
10
(A/q-2) Z
Trajectory-reconstructed PID for 228 MeV/u ¹²⁴Xe fragments on 3.5 mm thick Carbon target.
E. Kwan et al., in Proc. HIAT2025, pp. 311-314.

## Slide 13: High-rate, Ion-Feedback, Spark-Mediated Effects
Significant foil aging caused by:
  Loss of polymer mechanical properties due to high absorbed dose
  Electrode demetallization due to ion back-streaming
  Violent streamer discharges
Observed foil damage:
  Localized circular gold etching
  Aluminum-surface corrosion
  Foil rupture from discharges
  Electrical tree-like discharge patterns
Lifetime-extension strategies:
  Radiation-hard materials
  Wire-based electrodes
  Anti-Discharge Unit (ADU)
AGING MECHANISMS
TYPES OF FOIL DAMAGE
Di Carlo et al. NIM A 1071 (2025) 170076

## Slide 14: ADU: Operating Principle and Discharge Mitigation
Streamer
Originally developed by Kumagai-san at RIKEN for PPAC applications
Operating principle: streamer current above threshold triggers a PMOS switch that grounds the anode within tens of ns; bias is restored within a few ms
Purpose: protect cathode foils from energetic discharges
Impact: minor reduction in effective rate capability
Potential mechanism: suppresses streamer-to-spark transition by sensing pulse-height and triggering on pulses above threshold
H. Sato, Expert Meeting @Grand Rapids 2016/8/31
H. Raether, Electron Avalanches and Breakdown in Gases, 1964

## Slide 15: FRIB ADU Operation Principle
HV PMOS
FRIB ADU device:
Installed inside the PPAC vessel
Selectable discharge threshold
Response time: ~25 ns
PPAC ADU dead time: ~15 ms
PMOS switching time < HV trip time (≥100 ms)
Suppresses streamer development
  Protects fragile foils
  Extends PPAC lifetime
Di Carlo et al. NIM A 1071 (2025) 170076
20 μs rest time from the monostable circuit

## Slide 16: General Purpose ADU for Gaseous Detectors
GP-ADU features (NMOS/PMOS switching):
  Reconfigurable for positive or negative HV bias
  Can pull intermediate HV instead of GND
  Maximum operating voltage: 3.3 kV
  External potentiometer for threshold adjustment
  Response time: 50–60 ns
  GP-ADU recovery: ~5 ms + detector capacitance
  Powered through standard 9-pin NIM power
  Optional output signal with CR-112 charge preamplifier
  Prototype testing ongoing
Example of a pulse below threshold
Example of a pulse above threshold
ADU
V1
V3
V5
V6
VC
MPGD-ADU: Operating Mode
Each GEM protected by a dedicated ADU
ADU
ADU
VR6
V4
VR4
V2
VR2

## Slide 17: GP-ADU: Preliminary Results
ADU-on
Dead-Time ≈ 30 ms
Detector Pulses
Detector Pulses
Threshold below spark limit
Threshold reduced to a lower pulse-height
Long-term CRDC test carried out with an SRS-based DAQ
Different thresholds were used to probe the dynamic range and capture discharge events
Effective protection also maintained with the ADU threshold set above the nominal discharge-onset region
48-h endurance test under repeated discharge conditions; no damage to detector components or VMM3a hybrids observed
Tests on GEM, THGEM-like, and Micromegas are ongoing; observed dead time is detector/test-condition dependent
+HV
GND
ADU
GND
S800 CRDC

## Slide 18: The S800: High-Resolution, High-Acceptance Spectrograph
S800 Spectrograph continues to be the main workhorse for nuclear structure and reactions studies with fast beams until High-Rigidity Spectrometer (HRS) is complete
15 m
Spectrometer Focal-Plane Detector functions:
Particle Identification (PID) based on Bρ-ΔE-ToF  (Z, A/Q, Q)
Variable slits  Beam shaping and background rejection
Event-by-event momentum vector determination  Particle Track Position
Z-number Identification  Energy-loss measurement
Timing/triggering  ToF measurement + energy loss (with moderate resolution)
Charge-state separation & isomer tagging  Total Kinetic Energy (TKE) and γ-ray detection
Standard Focal-Plane detector system for heavy-ion PID
Focal-Plane
Cortesi et al. EPJ Web of Conferences 290, 1006 (2023)

## Slide 19: Sweeper Magnet and the Future High Rigidity Spectrometer
Same focal plane detector technology for tracking and PID developed for the S800 Spectrograph
High Rigidity Spectrometer (HRS)
Sweeper Magnet for invariant mass measurement

## Slide 20: Tracking System: Drift Chambers
Provide event-by-event tracking (position and angle) of each fragment that reaches the focal plane
Cathode Readout Drift Chamber (CRDC): 30 years of operation at NSCL/FRIB  single-wire anode readout
Performance:
  Position resolution < 1 mm (FWHM)
  Rate < 5 kHz
  Fast aging
Position (X,Y):
X  segmented readout
Y  electron drift time
1908 Wire Counter (Single wire readout)
(Rutherford and Geiger)
Path Forward: Transition from single-wire readout to Micro-Pattern Gaseous Detector (MPGD) technology to achieve the increased rate handling and dynamic range performance required for high-Z beam operations!

## Slide 21: Micro-Pattern Gaseous Detectors (MPGDs)
MICRO-GROOVE CHAMBER
MICROWIRE CHAMBER
MICRO-PIN ARRAY
MICRO-PIXEL CHAMBER
Bellazini et al.
NIMA 424 (1999) 444
Adeva et al.
NIMA 461 (2001) 33
Ochi et al.
NIMA 471 (2001) 264
FIELD GRADIENT LATTICE DETECTOR
Dick et al.
NIMA 535 (2004) 347
Rehak et al.
TNS 47 (2000) 1426
MICROMEGAS
Giomataris et al.
NIMA 376 (1996) 29
GAS ELECTRON MULTIPLIER
Sauli
NIMA 386 (1007) 531
MICRO-HOLE & STRIP PLATE
Veloso et al.
TNS 49 (2002) 875
…. and many others
MICROWIRE CHAMBER

## Slide 22: MPGDs at FRIB: new Science Opportunities
Applications: position-sensitive readout for low-pressure drift chambers and AT-TPC, fission fragment imaging, exotic decay studies  heavy-ion tracking and TKE/ToF measurement for momentum vector reconstruction and PID
Operational requirements: wide range of operating pressures (0.1–1 atm) and simultaneous detection across a wide range of Z
Different MPGD structures to suit a diverse array of needs!

## Slide 23: Multi-layer THGEM (M-THGEM) Designed for stable operation in pure elemental gases and at low pressures
No charge loss between stages  high gain @ low voltage
Robust avalanche confinement  lower secondary effects
Long avalanche region  high gain @ low pressure
Field geometry stabilized by inner electrodes
2-Layer M-THGEM
3-Layer M-THGEM
AT-TPC & pure gases
Low pressure
Manufactured by multi-layer PCB technique out of FR4/G-10/ceramic substrate
Cortesi et al., Rev. Sci. Instrum. 88, 013303 (2017)

## Slide 24: M-THGEM vs. THGEM: Performance Comparison
M-THGEM exhibits:
  higher maximum achievable gain at all pressures
  Improved stability due to enhanced avalanche confinement
  Reduced photon-feedback effects
  Superior operation in He and light noble gases
Cortesi et al. Rev. Sci. Instrum. 88, 013303 (2017);
He
He

## Slide 25: Hybrid MPGD-Based Readout  Micro-Pattern Drift Chamber
Nov. 2024: first beam commissioning of the new MPDC in the S800
238U+92 beam
~90 MeV/u
Pulse height
60 cm
30 cm
DAQ Based on the SRS electronics
fully integrated into the FRIBDAQ
-) Pulse Height
-) Peak location (time)
M. Cortesi et al., 2020 JINST 15 P03025
M. Cortesi, GSI, September 2026
, Slide 25

## Slide 26: Sweeper MPDC: Tracking + PID Capability
x-Coordinate (mm)
y-Coordinate (mm)
Unreacted beam
Reaction products
IC-ΔE (a.u.)
Al
Mg
Na
ToF (a.u.)
MPDC-ΔE (a.u.)
IC-ΔE (a.u.)
Counts
Counts
Al
Mg
Al
Mg
PID after tracking correction
J. Lois-Fuentes et al. 2026 JINST 21 P07007
IC Z-identification
MPDC Z-identification
position-sensitive readout +
2-layer THGEM
Commissioned for experiments in February 2025; successfully supported two experiments:
Stable operation at gas gain ~10³–10⁴
Clear track separation: <1 mm FWHM resolution
Effective Z-identification with MPDC-ΔE
Example tracking and PID from the first experimental campaign  Cocktail Beam @ 130 MeV/u

## Slide 27: 3-Layer M-THGEM: Consolidated AT-TPC Readout Technology
pAT-TPC
Active volume 25 liters
(L = 50 cm, Ø = 25 cm)
Cylindrical pad plane (~2000 pads)
Full scale AT-TPC
‣ Active volume 200 liters
(L = 100 cm, Ø = 50 cm)
‣ 10,240 triangular pads
‣ Inside 4 Tesla solenoid (SOLARIS)
M-THGEM
Position-sensitive MM
H2 as proton target
D2 as deuteron target
3He as helion target
4He as alpha-particle target
Others: mixtures D2 + C4D10, CF4, CO2, etc.
Filling Gas/Target
Hybrid readout: Micromegas + (3 layers) M-THGEM  GET electronics
Active Target Mode
Gas functions:
Target
Counting Gas
AT-TPC readout architecture

## Slide 28: Low-Pressure Pure-Gas Operation (Active Target Mode): Challenges
Pure-gas (no quencher) operation (Active Target):
  Photon-mediated secondary effect  slow-breakdown mechanism (discharges)
Low Pressure (Heavy ion tracking):
  Long electron mean free path  Large avalanche volume (large spacing between electrodes)
 Avalanche readout performance: low gas gain (instability), spatial/energy resolution, rate capability, …
Micromegas
Reduction of maximum achievable gain:
1) Diminished confinement of the electron avalanche inside the THGEM holes  photo-mediated secondary avalanches initiated at the top electrode.
2) Abrupt shift from proportional mode to streamer (discharge)

## Slide 29: M-THGEM: Asymmetric Mode of Operation
3M-THGEM hole
THGEM hole
E-field strength computed along the hole axis
2M-THGEM hole
Asymmetric biasing:
  Enhances avalanche confinement in lower hole region:
  Potential reduction of e⁻ collection efficiency at the top of the M-THGEM electrodes
  Enhanced reduction of ion backflow into the drift region

## Slide 30: 3-layer M-THGEM: Asymmetric Bias Mode
Strategy  Stop ions in asymmetric setup
Problems: energy resolution? Effective gain?
Performance:
Same maximum achievable gain across different collection configurations
Lower ion backflow at different voltage bias configurations
No measurable loss of electron collection efficiency under tested configurations
FEM Calculation of the electric field
ɛ
Cortesi et al., Rev. Sci. Instrum. 88, 013303 (2017)

## Slide 31: ReA applications: Example Sensitivity Cases
E20009  pure D2 (760 Torr)
10Be(d,p)11Be
The cinnamon roll: 8 MeV p (5 m range)
SOLARIS (up to 4 Tesla)
E20020  pure He (700 Torr)
4  decay of 16O
The big Kraken: 5 -particle tracks
Spokesperson: Clementine Santamaria
Spokesperson: Daniel Bazin
More Tracks
D. Bazin Courtesy

## Slide 32: AT-TPC Particle Identification and Challenges
Acceptance effect of the AT-TPC
  Low energy cutoff at ~500 keV
  Polar angle acceptance effect for θlab<20o and θlab>160o
  Kinematic gap from transverse track reconstruction (θlab=90o)
PID based on magnetic rigidity and energy loss
(a.u.)
Kinematic plot 10Be(d,p)
Bρ/Sin(θ) (Tm)
11Be Excitation spectrum
Counts
10Be(d,p)11Be (10 MeV/u)
(19⁰ <<31⁰)
TKE (MeV)
(deg)

## Slide 34: Love in the time of … MPGDs
Amplification in Meshes
Multi-Mesh THGEM
Hole-like
Multi-layer
Mechanical support
Rui de Oliveira (CERN)
Marco Cortesi (FRIB)
R. De Oliveira and M. Cortesi, 2018 JINST 13 P06019

## Slide 35: Multi-Mesh THGEM (MM-THGEM)
P. Bhattacharya et al., 2015 JINST 10 P09017
Double Micromegas (DMM)  larger gain, lower IBF
Problem: mechanical stability of DMM over large area?
MM-THGEM
Solution
Features:
Geometry:
  Hole  diam = 0.3-0.7 mm, pitch = 1-1.2 mm, rim < 0.1 mm
  Thickness (single FR4), like in THGEM (0.2-1 mm)
Large-area double MM structure (40 x 30 cm2 in this work)
Multiple amplification stages (uniform field geometry)
Expected excellent ion backflow suppression
Mechanically robust
Can be coupled to reflective photocathode (on top of the THGEM)
R. De Oliveira and M. Cortesi, 2018 JINST 13 P06019

## Slide 36: Science Case: Neutron-Rich Heavy-Ion Collisions - Reaction Dynamics
Goal: Assess how entrance-channel properties (N/Z asymmetry, projectile/target magicity) affect quasi-fission, fusion-fission, and evaporation-residue survival, improving our understanding of SHE-synthesis reaction mechanisms.
Experiment: Investigate FF/QF dynamics with rare isotopes (e.g., the ³⁴Si + ²³²Th reaction) using FRIB radioactive beams and fragment kinematic observables.
Reaction identification based on:
-) ToF  FMT vs. Non-FMT
-) MAD  FF vs. QF
FMT = Full Momentum Transfer
MAD = Mass-Angle Distribution
Hinde et al. PRC 88, 054618 (2013)
Detector 1
Detector 2
Mass ratio
Coincidence Fission Fragment Detector System (CFFD)
Courtesy K. Brown Group

## Slide 37: Performance Evaluation of a 10x10 cm2 Prototype
Detector: 10x10 cm2 active area, equipped with a resistive anode (DLC, 10 MΩ/□) and a 2D delay-line readout
MM-THGEM: Hole diam. = 0.5 mm, Hole pitch 1 mm, rim = 0.05 mm,
FR4 layers: 0.4 mm, 0.2 mm, 0.2 mm.
Stable operation at about 103 gas gain for FF and position resolution of about 0.5 mm (σ)
Harca et al. 2024 JINST 19 P05023

## Slide 38: Low Pressure Prototype Detector for Fission Fragments: ToF and Mass Reconstruction
249Cf α source
ToF [ns]
Counts
σ =1 ns
252Cf fission source
Mass Number (A)
Normalized Yield
Summary Performance:
Stable operation in < 10 Torr iC4H10
Uniform gain (>103) across the effective area
Time resolution (ToF) ≈ 1 ns (σ)
Position resolution ≈ 0.5 mm (σ)
Rate capability up to ≈200 kHz
The extrapolated mass resolution computed by ToF is 2.3 amu (FWHM) (A≈100-140)
Good FF detection efficiency
Across MM-THGEM area
Time resolution ≈ 1 ns (σ)
PMT
Harca et al. 2024 JINST 19 P05023

## Slide 39: Large-Area MM-THGEM Imaging Detector
MM-THGEM:
Hole diam. = 0.5 mm
Hole pitch = 1 mm
Hole rim = 0.05 mm
FR4 layers: 0.4 mm, 0.2 mm, 0.2 mm
Scale up the prototype (10x10 cm2) for Fission-Fragment Imaging Study (40x30 cm2)
DLC Anode (10 MΩ/□)
Delay-line Readout
Thin metallized cathode foil
Full Assembly

## Slide 40: Performance Evaluation with α-Particle Source
Typical Bias Configuration: gas gain ~ 103
MM-THGEM bottom mesh
X1 DL signal
all DL signals
40 ns
Large MM-THGEM-based detectors demonstrate performance comparable to that of the small-scale prototype
Operating pressure = 10 Torr i-C4H10

## Slide 41: Large-area MM-THGEM Detector: Position Resolution
Y coordinate [mm]
Y coordinate [mm]
Projection Y
Projection X
< σ > ~ 0.62 mm
< σ > ~ 0.65 mm
~ 7 h 30 min
Measured position resolution across the effective area ≈ 0.63 mm (σ)  Expected coincidence angular resolution of the CFFD system ≈ 4.5 mrad (σ)

## Slide 42: GIRAFFE: The new Gas-Ionizing Reactions Array for Fission-Fragment Experiments
Two large-area position-sensitive MM-THGEM detectors around the target provide complementary θ coverage for binary-fragment detection
Upstream start detector at 0⁰ provides t0 signal for the ToF measurements
Kinematic coincidence reconstruction determines fragment mass ratio (MR) and center-of-mass angle (θ) from position and timing.
Two SBS detectors provide beam monitoring and cross-section normalization
Target ladder enables target changes under vacuum
Detector 1
Detector 2
Detector#2
Detector#1
Target Ladder
2×SBS
SBS = surface-barrier silicon detectors  monitoring Rutherford Scattering events
Start Timing
Detector
Multi-Wire Proportional Chamber (MWPC)
as timing start detector
beam
MWPC
S. Di Carlo et al 2026 JINST 21 P03022
Performance:
  Position  0.5 mm (σ)
  Time  <150 ps (σ)
  Rate  up to 300 kHz

## Slide 43: GIRAFFE First Science Case: 34Si + 232Th (E=5.43 MeV/u)
Reaction identification: Coincident ToF enables identification of Full Momentum Transfer (FMT) reactions (FF/QF) relative to other reaction channels (elastic, quasi-elastic and deep-inelastic collisions)
Mass-angle distribution analysis further disentangles FF from QF
ToF1: Left MM-THGEM – MWPC
ToF2: Right MM-THGEM – MWPC
FMT
Non-FMT
Beam Spot on the MWPC
ToF2 (ns)
ToF1 (ns)
Y-Coordinate (mm)
X-Coordinate (mm)
Preliminary data from 34Si + 232Th  266Rf* (E* ~68 MeV)
April 2026 run
Courtesy K. Brown, V. Zerbach (PhD student – Analysis in progress)

## Slide 44: Summary
FRIB is one of the premier facilities for rare isotope beam production, demanding state-of-the-art diagnostic and detector technologies
A strong R&D program has been established at FRIB to develop novel detectors supporting the nuclear physics user program
Examples of R&D presented in this talk:
  DL-PPAC/MWPC + ADU: high-rate, low-Z efficiency; discharge suppression; generalized to GP-ADU
  S800/Sweeper: mature Bρ-ΔE-ToF PID; MPDC commissioned; HRS underway
  M-THGEM: stable low-pressure, pure-gas operation for AT-TPC
  MM-THGEM/GIRAFFE: scaled to 40 × 30 cm² (≈0.63 mm resolution); first FMT/non-FMT separation demonstrated; FF/QF analysis in progress
This work reflects FRIB's continued investment in detector innovation, and its role within the broader national detector technology community, to meet the next generation of rare-isotope science