## Slide 1: Analysis of proton emission in collisions at HADES Supervisor: Dr. Manuel Lorenz
Vera Schuhmann
Summer Student Report
15.09.2026

## Slide 2: Particle collision

## Slide 3: HADES detector
Detector for heavy-ion collisions in fixed target experiments
(Charged) particle identification through measurement of:
  Trajectory with MDCs before and after magnet → Momentum
  Time-of-flight with START and RPC/TOF detectors → Velocity
  Energy loss with MDCs
Notes: Show RPC and TOF!
Also MDCs and Magnet
RPC = Resistive Plate Chamber
TOF = Time Of Flight
MDC = Magnetic Drift Chamber

## Slide 4: Experimental setup
Pion beam at beam momentum of 612 MeV/c
Carbon target consisting of seven thin disks
Total collision events used: 2,275,591
Goal of the analysis:
Extract the proton yields per event and their kinematic distribution → cross section

## Slide 5: Kinematic distribution:
Particle counts per bin
  Rapidity in beam direction
  Transverse momentum perpendicular to the beam axis
Mass spectrum for each bin → Interactive Plot
Notes: Hopefully works SMOOTH LIKE BUTTER Bins to show:
  Positrons + pions: pt50, y1.0
  Pions: pt100, y0.7
  Protons: pt250, y0.4
  Deuterons: pt500, y0.3
  Deuterons + Tritium: pt500, y0.2

## Slide 6: Kinematic distribution:
Particle counts per bin
  Rapidity in beam direction
  Transverse momentum perpendicular to the beam axis
Mass spectrum for each bin → Interactive Plot
Notes: Bins to show:
  Positrons + pions: pt50, y1.0
  Pions: pt100, y0.7
  Protons: pt250, y0.4
  Deuterons: pt500, y0.3
  Deuterons + Tritium: pt500, y0.2

## Slide 7: Kinematic distribution:
Rapidity and transverse momentum
Notes: Point out: TOF at lower rapidity and higher transv. momentum than RPC, else just squished together

## Slide 8: Kinematic distribution:
Momentum and detector angle
Notes: Point out: TOF at larger polar angles than RPC -> detector geometry
Transition to next slide: how to extract only the protons

## Slide 9: Energy loss
Particle-specific, described by Bethe-Bloch equation
Spectrum divided in momentum slices of
Landau distribution fitted for each slice
  Parameters: most probable value , width parameter
Selected cut: [ ]

## Slide 10: Proton counts
Extraction of proton counts by fitting a Gaussian to the proton peak for each bin
Integration over interval
Bins with no reliable fit for the proton peak were excluded

## Slide 11: Normalized proton yields
Integrated proton counts
Normalized by bin size and number of analysed events
=> Proton yield per event and bin
Notes: Note: rapidity range only 0-1

## Slide 12: GiBUU simulations
The Giessen Boltzmann-Uehling-Uhlenbeck Project
Event generator for collisions
Produced particles tracked through simulated HADES detector
Available data only at beam momentum 700 MeV/c
Total simulated collision events used: 10,861,566
Simulations analysed in the same way as experimental data => reconstructed proton counts per bin
Comparison to true proton counts per bin

## Slide 13: Efficiency & acceptance correction
Comparison to true proton counts per bin
Correction factor for each bin
Detector acceptance and reconstruction efficiency

## Slide 14: Corrected proton yields:
Correction factor for each bin
=> Corrected proton yields
RPC and TOF combined
  RPC: higher , lower
  TOF: lower , higher

## Slide 15: Corrected proton yields:
Correction factor for each bin
=> Corrected proton yields
RPC and TOF combined
  RPC: higher , lower
  TOF: lower , higher
Notes: SMOOTH LIKE BUTTER!!!

## Slide 16: Differential proton yields
distribution for each rapidity interval
Low momentum points extrapolated with linear function between (0,0) and first -point
Notes: No low p_T points because of detector geometry -> small polar angle, no detection Looks like Boltzmann, but doesn’t work

## Slide 17: Proton rapidity distribution
Integration of momentum distribution:
Measurement and simulation show same qualitative shape
  Simulation shifted towards higher rapidity → 700 MeV/c beam in simulation, 612 MeV/c beam in experiment

## Slide 18: Summary & Outlook
Collisions of beam at 612 MeV/c with carbon target
Extraction of proton yields in and bins with normalization on the number of analysed events and the binsize
Proton selection via cuts on energy loss and invariant mass
Correction for detector acceptance and reconstruction efficiency using GiBUU simulations at 700 MeV/c
Proton rapidity distribution by integrating over the -distributions
Improvement possible through
  Simulations at 612 MeV/c
  Rapidity extrapolation for low with GiBUU simulations
  More statistics
Notes: After my analysis: calculate cross section out of differential proton yields (consider trigger efficiency)

## Slide 19: Thank you for your attention!

## Slide 20: Interactive pt-y Plot for RPC
scp –r hadgst03@lxi001.gsi.de:/u/hadgst03/vschuhmann .
Bins to show:
  Positrons + pions: pt50, y1.0
  Pions: pt100, y0.7
  Protons: pt250, y0.4
  Deuterons: pt500, y0.3
  Deuterons + Tritium: pt500, y0.2

## Slide 21: Introduction
Collision in general (picture/animation)
Then mass spectrum with all particles
But no info on kinematic distribution, # per event, detector effects
Goal: extract proton yields (counts per #events) and their distribution, independent of detector

## Slide 22: Mass Spectrum