## Slide 1
Microdosimetry of complex radiation fields
Federica Anastasia Diana
University of Naples ”Federico II”
Tutor: Enrico Pierobon
1

## Slide 2
  Space radiation environment
  Microdosimetry
  Radiation Field and Source Geometry
  Spectrum Conversion
  Geant4 Simulations with the Diamond Detector
  Results
Index
2

## Slide 3
Introduction, a general view of the problem
Space radiation is one of the main risks for astronauts during long-duration space missions.
The radiation environment in space is mainly composed of galactic cosmic rays (GCRs) and solar particle events (SPEs).
Possibility of important health risks
Need for radition field characterization
3

## Slide 4
GCRs provide a continuous background of
highly energetic particles
(protons, heavy ions...)
Dense ionization
tracks in biological tissue
Galactic Cosmic Rays (GCRs)
Chronic exposure during long-duration missions
long-term health risks
Result
4

## Slide 5
SPEs are temporary increases in the flux of energetic
particles produced by solar activity.
Complex radiation field
ACUTE RADIATION EFFECTS
Solar Particle Events (SPEs)
Particle flux and dose rate can increase significantly over a
short period
Ions and protons with broad kinetic energies
We will focus on Solar Particle Events
5

## Slide 6
1989 Solar Particle Event
  Between August and October 1989;
  most of the protons are concentrated at relatively low energies;
  approximately exponential behaviour;
  the spectrum extends well into the high-energy region, with protons reaching energies above 500 MeV (Range in water greater than 1 m).
6

## Slide 7
Microdosimery
This approach provides information about the radiation field
Microdosimetry characterizes radiation by studying the variation of energy deposition in microscopic volumes.
7
mm
Macroscopy Dosimetry
deterministic value
Microdosimetry
mu
stochastic energy deposition

## Slide 8
where is the mean chord length of the sensitive volume and was calculated as
Microdosimery
Given ε, the energy imparted to the diamond sensitive volume, the corresponding lineal energy, , was then calculated as
The resulting lineal-energy distribution was then used to construct the frequency- and dose- weighted distributions, yf(y) and yd(y), respectively.
sensitive volume
surface area of the sensitive volume
The frequency-mean lineal energy:
The dose-mean lineal energy:
f(y) represents the normalized frequency distribution of lineal energy.
8

## Slide 9
An open-source toolkit developed to model the transport and interaction of particles through matter.
At microscopic scales, energy deposition varies from event to event, yielding a distribution of imparted energies
Simulate physical systems and probabilistic processes
A computational method based on repeated random sampling
Monte Carlo simulation and Geant4
What is Monte Carlo?
Why Monte Carlo?
What is Geant4?
9

## Slide 10
Radiation Field and Source Geometry
source geometry: spherical surface
Aim: Reproducing an isotropic radiation field at the detector location
Cosine-law angular emission
10
  Isotropic angular emission from the surface leads to non isotropic fluence in the volume
*Giovanni Santin ESA / ESTEC and RheaTechLtd
Iso vs Cosine-law angular distribution
Full flux
Reduced by a factor cos

## Slide 11
OLTARIS SPE Spectrum
Monte Carlo Simulation
Developed with BLABLADOR + OpenCode
Geant4 GPS-compatible energy distribution
single
particle spectra
Spectrum Conversion
Python Parser
Geant4 Macro Generation
multi particles spectra
VALIDATION
  source geometry
  angular distribution
11

## Slide 12
Comparison of Energy Spectra
Results
Both distributions were normalized to their respective integrals, allowing their spectral shapes to be compared.
12

## Slide 13
Geant4 Simulations with the Diamond Detector
13

## Slide 14
Detectors Simulated
14
  gas-filled detector
  simulates microscopic volumes of biological tissue
  measures the energy deposited by radiation
Diamond Detector
Tissue-Equivalent Proportional Counter (TEPC)
  solid-state detector
  uses diamond as a tissue-equivalent sensitive material
  measures the energy deposited by radiation at microscopic scales
small physical volume → microscopic energy deposition
large gas cavity + low density
→ microscopic tissue-equivalent volume
Reference

## Slide 15
Geant4 Simulations with the Diamond Detector
Diamond detector geometry
It consists of a 100 × 100 array of diamond microdosimeters arranged on a rectangular carbon substrate.
1 mu
5 mu
1 mu
15

## Slide 16
Geant4 Simulations with the Diamond Detector
The diamond microdosimeter was placed inside a spherical aluminum shielding with an areal density of 10 g cm−2
16
World
Source
shielding
detector
light shielding

## Slide 17
Microdosimetric Spectrum
Results
The obtained value of is consistent with the enhanced microdosimetric
response expected for protons approaching the end of their range.
17

## Slide 18
Microdosimetric Spectrum, validation with TEPC
Results
18

## Slide 19
Shielding and without shileding comparison
Results
19

## Slide 20
  The developed codes were able to effectively convert historical SPE data into Geant4 macro files
  This approach can be generalized to different SPEs
  The response of the diamond microdosimeter to the simulated SPE can be characterized through the resulting microdosimetric distributions and lineal-energy quantities, in agreement with the established literature and the TEPC approach.
Conclusion
THE RESULTS SHOW THAT:
20

## Slide 21
Conclusion
  4. The method can be generalized
Data from: Spenvis
Particles: Proton and Helium
21

## Slide 22
THANK YOU FOR YOUR ATTENTION
23

## Slide 23
Geant4 Simulations with the Diamond Detector
Diamond detector geometry
It consists of a 100 × 100 array of diamond microdosimeters arranged on a rectangular carbon substrate.
15
p-diamond
Sensitives volume segmentation
electrode
Epoxy
substrate
1 um
0.5 um
0.10 um
50 um
Intrinsic diamond

## Slide 24
Results
15