## Slide 1: Data analysis of ACTAF
Patrik Doležal
239444@vutbr.cz
Supervisor: Oleg Kiselev
International Summer Student Program at GSI-FAIR
16 September 2026

## Slide 2: Contents
AMBER
ACTAF
DAQ
Signal processing
Alpha-Source vs HV
FFT
Conclusion

## Slide 3: AMBER
AMBER (Apparatus for Meson and Baryon Experimental Research) experiment at CERN, M2 beam line
Main focus: Proton charge radius measurement
  via elastic muon-proton scattering
  Addresses the “proton radius puzzle“
Other phase-1 goals: hadron spectroscopy, Drell-Yan process

## Slide 4: ACTAF in FAIR
ACTAF (ACtive TArget for FAIR) = a TPC (time-projection chamber) built for R3B (NUSTAR), using rare beams from the Super-FRS
Gas itself is both the reaction target and the detection medium
The TPC used in AMBER‘s proton-radius measurement is ACTAF – the same detector
Low momentum transfer
2030?

## Slide 5: Detector geometry
Two anodes planes: uptream and downstream
2 × 64 pads total (128 channels)
Each pad corresponds to a defined detector position
241Am sources inside

## Slide 6: 241Am alpha sources
Five 241Am sources installed in the detector
Alpha-peak position reflects changes in gas quality

## Slide 7: Data acquisition
ACTAF pads
Pre-amplifiers
SIS3316 FADC modules
Recorded waveforms
14-bit ADC
2500 samples/ channel
4-sample averaging
19.44 MHz effective sampling rate

## Slide 8: Signal-processing chain
MAPPED DATA waveform
pad ID
SIGNAL PROCESSING SG filter
baseline
Integration
calibration+cut
CAL DATA
Energy
pad ID
POSITION RECONSTRUCTION (x,y) ←pad, geom.
z, energy ← from cal
HIT DATA x,y,z energy
Data analysis in this work

## Slide 9: Data analysis
Long shutdown at CERN, no beam available
Used this time to go through existing data and check the detector performance
July 2026: dedicated runs without beam
During these runs High Voltage was decresed from 100% to 10%

## Slide 10: Identification of alpha-source pads
Expected pad positions determined from detector geometry
Alpha peaks identified in the pulse-integral spectra
Measured positions with expected mapping
Some signals observed on neighbouring pads
Low source activity can make some peaks difficult to identify

## Slide 11: Alpha-peak fitting
Peak identification: ROOT TSpectrum
Initial Gaussian fit → μ, σ
Final fit performed around the identified peak
Output: peak position + uncertainty
Peak Search
Gauss fit
μ, σ
Gauss + pol1
Mean + uncertainty

## Slide 12: Alpha peak vs. HV
Mean alpha-peak positon determined for each HV setting
Peak position decreses with decreasing HV
Behaviour observed consistently across the investigated pads
Used to study the anode response as a fuction of HV
July 2026 → 241Am runs →HV: 100% to 10% →visible α-peaks→Peak fitting →Mean vs HV

## Slide 13: Interpretation of HV dependence
High drift-field HV
Faster electron drift
Shorter drift time
Less electron attachment
Larger collected charge
Low drift-field HV
Slower electron drift
Higher probability of electron attachment
Smaller collected charge
Observed: approximately exponential decrese of the mean pulse integral with decreasing HV

## Slide 14: Electronic noise
Noise observed in the recorded waveforms
Selected pads showed a pronounced noise component
Noise investigated in the frequency domain using FFT
Several distinct frequency components were observed
Signal
Noise
Observed fluctuations

## Slide 15: Fourier analysis
Raw(Mapped) waveforms transformed into frequency domain
FFT performed using Root TVirtualFFT
Spectra averaged over all events in the run
Several distinct frequency components were observed
Waveform →FFT →frequency spectrum →noise peaks
Pad 122

## Slide 16: Noise and HV dependence
Pad 107 – 80 % HV
Pad 107 – 20 % HV
Three prominent peaks: ~206, 280, 610 kHz, visible on every inspected pad.
~206 kHz peak amplitude decreases with lower HV.

## Slide 17: FFT Map vs Cal data
The same frequency components are present in both Mapped (Raw) and Cal data.
The Savitzky-Golay filter does not fully reduce the noise.
Mapped waveform→FFT→frequency peaks
Mapped waveform →signal processing (SG filer + other steps) →Cal data →FFT →same peaks

## Slide 18: Conclusions
241Am alpha sources provide clear signals for detector monitoring and calibration
Alpha-peak position shows a clear dependence on the applied HV
Electronic noise contains several distinct frequency components
The amplitude of the ~206 kHz component decreases with decresing HV
Further investigation of the noise sources is needed and digital filtering should be concidered

## Slide 19: Thank you!
Member of ACTAF (Another Coffee To Avoid Fatique) in free time:
Member of AMBER (Another Minute Before Early Rising) in free time: