## Slide 1: Time and Energy resolved Photon detection for bunched beam collinear Laser spectroscopy at TRIGA-MAINZ
Helmholtzzentrum für
Schwerionenforschung
Speaker: Simon Kaufmann
Advisor: Prof. Dr. Nörtershäuser

## Slide 2: Outline
collinear laser spectroscopy (cls)
  principle
  Overview of LaSpec – cls at FAIR
TRIGA-SPEC development platform for LaSpec in Mainz
  Overview and Status
  time resolved cls on bunched beams using an FPGA
  first results on cls of bunched ions at TRIGA-SPEC
Outlook

## Slide 3: collinear laser spectroscopy – basic principle
ionsource
high voltage (10-60 kV)
ionoptics
deflector unit
(overlapping ion & laser beam)
Ionoptic
(ion beam shaping)
optical
detection
Laser
scanvoltage
+
+
+
+
charge exchange cell
Dopplertuning
by accelerating the ions, the laser frequency in the ion rest frame is shifted according to the doppler formula:

## Slide 4: collinear laser spectroscopy – basic principle
ionsource
high voltage (10-60 kV)
ionoptics
deflector unit
(overlapping ion & laser beam)
Ionoptic
(ion beam shaping)
optical
detection
Laser
scanvoltage
+
+
+
+
charge exchange cell
E1
E0
E
ΔE ?
cts
UScan

## Slide 5: collinear laser spectroscopy – basic principle
ionsource
high voltage (10-60 kV)
ionoptics
deflector unit
(overlapping ion & laser beam)
Ionoptic
(ion beam shaping)
optical
detection
Laser
scanvoltage
+
+
+
+
charge exchange cell
E1
E0
E
ΔE ?
cts
UScan
Doppler formula

## Slide 6: collinear laser spectroscopy – basic principle
charge exchange cell
ionsource
high voltage (10-60 kV)
ionoptics
deflector unit
(overlapping ion & laser beam)
Ionoptic
(ion beam shaping)
optical
detection
Laser
scanvoltage
+
+
+
+
Funktionsweise
nuclear spin
charge radius
magn. dipole moment
electr. quadrupole moment
groundstate characteristics
short lived exotic isotopes
principle
resonant laser excitation
flourescence detection
dopplertuning
energy levels ion/atom

## Slide 7: collinear laser experiments
D. Rodriguez, et al.: “MATS and LaSpec: High-precision experiments using ion traps and lasers at FAIR”, Eur. Phys. J. Special Topics 183, 1–123 (2010)
2010
Notes: evtl. weglassen

## Slide 8: collinear laser spectroscopy - at FAIR
further information see:
Technical Design Report of MATS & LaSpec:
D. Rodriguez, EPJ Special Topics 183 (2010) 1-123
Notes: FRS= fragment seperator

## Slide 9
RFQ -cooler & -buncher
MR-TOF
MATS
EBIT
laser spectroscopy
dipole-magnet
gas cell
further information see:
Technical Design Report of MATS & LaSpec:
D. Rodriguez, EPJ Special Topics 183 (2010) 1-123
collinear laser spectroscopy - at FAIR
prototype build at the TRIGA facility, Mainz

## Slide 10: TRIGA –SPEC

## Slide 11: TRIGA-SPEC - Overview
common beamline

## Slide 12: TRIGA-SPEC - Overview
common beamline
COLETTE
„cooler for emittance elimination“
used in MISTRAL until 2010 only in cw-mode
axial confinement implemented at TRIGA-SPEC1
cls on bunched beams massively reduces underground2 (straylight of laser)
1T. Beyer, et al.: „An RFQ cooler and buncher for the TRIGA-SPEC experiment“, Appl. Phys. B (2014) 114:129–136
174Hf+
gated (26µs)
ungated
2A. Nieminen, et al. „On-Line Ion Cooling and Bunching for Collinear Laser Spectroscopy”, Phys. Rev. Lett. 88, 094801 (2002)
@IGISOL
Notes: tacc=500 ms und tgate=26 µs
wurde an University of Jyväskylä gemessens

## Slide 13: radio frequency quadrupole - cooling
Ekin≈ 30keV
radial confinemt due to RF on quadrupole rods
  ionguide

## Slide 14: radio frequency quadrupole - cooling
Ekin≈ 30keV
radial confinemt due to RF on quadrupole rods
ions dissipate their energy to buffer gas and are cooled to a circular spot of appr. 1 mm diameter
without buffergas
with gas in ionguide
beamprofile in CW-mode

## Slide 15: radio frequency quadrupole - bunching
Ekin≈ 30keV
segmented rods enable DC potential for axial confinement
„linear Paul-trap“
up to 106 ions can be accumulated

## Slide 16: radio frequency quadrupole - bunching
Ekin≈ 30keV
for extraction last and 3rd last electrodes are switched

## Slide 17: anticollinear laser spectroscopy on bunched ion beams
time
bunch
extracted
bunch
extracted
TOF
bunch
in
optical
detection

## Slide 18: anticollinear laser spectroscopy on bunched ion beams
FPGA – Field programmable gate array
Chip: Virtex-II
1M logic blocks
40 MHz onboard oscillator
  x up to 200 MHz
  typ. 100 MHZ
    10ns time resolution
16-Bit DAC/ADC
  ±10 V
bitfiles compiled via the LABVIEW to VHDL compilers
  flexibility in field of application
FPGA scheme
Notes: we use an fpga to count the signals in coincidence with the bunch. Dann FPGA kurz vorstellen.
das fpga reprogrammierbare Hardware ist nur erwähnen…
heutzutage gibt es den Virtex 7

## Slide 19: anticollinear laser spectroscopy on bunched ion beams
Data Acqusition – in bunched beam cls
gated (26µs)
voltage
not time resolved
easiest way to get in coincidence with bunch is to set a gate and only count pmt events, when gate is open.
but:
User has to set gates and delay in advance
User has to adapt the delay for each isotope
by counting over the whole gate, velocity to time information is lost.
  okay as long as velocity inside each bunch is constant
time
bunch
extracted
bunch
extracted
TOF
bunch
in
optical
detection
Notes: just by gating the

## Slide 20: anticollinear laser spectroscopy on bunched ion beams
Data Acqusition – in bunched beam cls
time resolved
time
bunch
extracted
bunch
extracted
TOF
bunch
in
optical
detection
Count all PMT events and sort them by time relative to extraction. Typical it is useful to use channels with some 10ns width.
Data set will be a matrix containing all pmt-events for each time and voltage
  no time information is lost
  center frequency can be found in projection
  gates can be set afterwards
Notes: just by gating the

## Slide 21
First results with cls on bunched beams at TRIGA-SPEC
Comissioning of the rfq with stable Ca+-Ions

## Slide 22: First results with cls on bunched beams at TRIGA-SPEC
Day 1: Oscillation in velocity observed
frequency:
appr. 3 MHz
oscillation in phase to extraction
countrate is color coded
40Ca+
Notes: this is summation of 100 Bunches
ions are positiv -> positive scan voltage decelerates ions to get in resonance.
ions that must be more decelerated (higher scan voltage) are faster, than ions in resonance at lower scan voltages

## Slide 23: First results with cls on bunched beams at TRIGA-SPEC
Day 1: Oscillation in velocity observed
switching behaviour of last electrode in rfq, observed with oscilloscope
trapping potential
40 V
extraction potential
-250 V
Notes: overswing

## Slide 24: First results with cls on bunched beams at TRIGA-SPEC

## Slide 25: First results with cls on bunched beams at TRIGA-SPEC
changing extraction potential to 0 V
oscillation disappears
bunch is longer
  about 11.74µs

## Slide 26: Outlook
Upcoming Projects at TRIGA-SPEC
Short term:
  repeat the systematic studies on the energy behaviour of the bunches from RFQ
  establish a python based Control System („TRITON“)
  stable Ca+ isotope shift of D2-line (4s 2S1/2 → 4p 2P3/2)
long term:
  plasma ion source in common beamline
    investigation of short lived isotopes which are currently not ionisable with the surface ion source
Notes: Technetium and ruthenium could be one of the first interesting physics cases at TRIGA-LASER, to study the behavior at N=60 where a sudden appearance of deformation was observed on the elements with slightly lower Z.

## Slide 27
Thank you, for your attention!
Questions?

## Slide 28: Kollineare Laserspektroskopie radioaktiver Isotope
Ionenquelle
Hochspannung
Ionenoptik
Deflektor-Einheit
(10° horizontal)
Ionenoptik
(Quadrupol Doublett etc..)
Ladungsaus-tausch-Zelle
optischer
Nachweis
Laserstrahl
(feste Wellenlänge)
Scan-
Spannung
Laser-
strahl
+
+
+
+
Funktionsweise
resonante Laseranregung
Nachweis über Fluoreszenz
Dopplertuning
Energieniveaus Ion/Atom
Kernspin
Ladungsradius
magn. Dipolmoment
elektr. Quadrupolmoment
Grundzustands-Eigenschaften kurzlebiger exotischer Nuklide
universelle Methode

## Slide 29
Vergleich Online vs. Offline
Notes: Fwhm:
Online CW: 184,81389 11,66189
Offline : 90,92702 0,91471

## Slide 32: gasflow variation

## Slide 33: number of Ions

## Slide 34: ions/bunch

## Slide 35: Variation der Kühlzeit
Fläche ist konstant
keine Ionen gehen verloren
Notes: 1V = 17Mhz
Haben kleinere V -> mehr Energie

## Slide 36: Variation der Kühlzeit
Linienlage verschiebt sich
Ionenenergie nach Ausschuss nimmt ab
Notes: 1V = 17Mhz
Haben kleinere V -> mehr Energie

## Slide 37: Vergleich: Spektren an ISCOOL
FWHM: 5,7 V || 100 MHz
30 kV,
rel. Dopperlfaktor: 17,5 MHz
4 µs lange Pulse
ISCOOL
RFQ-Cooler and Buncher an ISOLDE