The Status of the SciTil
Carsten Schwarz, GSI
Motivation
Setup
Mechanics
Readout
Work packages
Status India
Costs
barrel SciTil
EMC
Barrel
barrel DIRC

---
Motivation: Event Timing
Events 1,2,3,4,5,6,7,8... for 50Mhz interaction rate with 6 tracks
Klaus Götzen,Influence of Particle Timing on Event Building
PANDA collaboration meeting March 2011, GSI

---
Motivation: Conversion Detection
Conversion of gammas within the DIRC
can be detected with the SciTil
EMC
1%
17%
SciTil
DIRC
 Relative timing
TOF
TOF
PANDA has no start detector
SciTil important for relative timing and PID

---
SciTil
Quad module
With electronics
8 ch. ASIC
data transfer IC
Readout at two positions
more photons
less light path fluctuations
larger detection efficiency

---
Super-module = 90 quad modules
Total
5760 SciTils
3 x 30 quads
16 super modules
outside of DIRC barrel
Radial thickness
1.8 cm
Cooled by dry air
TOF-PET
ASIC

---
EMC
570 mm
505.5 mm
SciTil
DIRC
476 mm

---
ASIC for SiPM readout
TOF-PET ASIC for PET applications
M.D. Rolo JINST 8 C02050
Per channel:
100 kHz
7 mW
2nd threshold
validation of events (i.e. dark count rejection) and
provision of a second time stamp for TOT
→ development board now commercial available
    (Mach 2014)
12000 tiles: → 84 Watts

---
Results of test beam time in Juelich, Feb. 2014
Ken Suzuki:
With analog SiPM, with a preliminary online analysis, we reached almost
100ps (sigma) intrinsic time resolution.
With a careful offline analysis we’ll probably reach 100ps, one of the goal of the project.
With digital SiPM together with Philips, we reached an
astonishing <50ps (sigma) intrinsic time resolution.
More will be reported at the next PANDA meeting.

---
Work packages
Work package	Interested institutes
Simulation	BARC
Module design	GSI, BARC
Scintillator	Dubna, Gatchina
Silicon PM	EU HP3, BARC, Dubna, Gatchina
Readout design	EU HP3, BARC
Mechanical design	GSI
Prototype production	BARC
construction
R&D
Status:DAE - BRNS Workshop on Hadron Physics – 2011
R&D:	Vienna, Mainz, Erlangen for R&D with test stands
Vienna, GSI, Experiments in beam
Work Package	Interested Institutes
SiPM test facility	BARC
construction

---
R&D
Prototype
Electronic readout (TOF-PET)
Testing and documentation of 12000 sensors
Dark current
Bias
Temperature dependence of bias
>1year
Only few bias lines...
Testing and documentation of 6000 tiles
Material
Coupling of sensors
>1year
Assembly of 6000 tiles
tiles
electronics

---
PANDA – India Present Status
Bidyut Roy
(on behalf of Panda – India collaboration)
Present Members (PANDA-India Collaboration)
BARC, Mumbai
IIT Bombay, Mumbai
AMU, Aligarh
BITS-Pillani, Goa campus, Goa
Gauhati university, Gauhati
IIT Indore, Indore
Sardar Patel univ., Vallabh Vidyanagar,
Sardar Vallabhbhai National Inst. of Tech., Surat
Veer Narmad South Gujrat univ., Surat
P. D. Patel Inst. of Applied Science, Anand
(in Theory Advisory Board)
Membeship applied:
> Visva bharati univ,
> B.R. Ambedkar National Inst. of Technology
On SciTil work:
Gauhati University got DST fund, one JRF has been appointed
AMU Aligarh got BRNS fund + 1 JRF being appointed
Visva Bharati got BRNS fund, 1 JRF being appointed
03/10/14
SciTil Status, B.Roy Mach 2014

---
SiPM / SciTil test facility at BARC
Most of the necessary equipments are purchased and Setup ready, initial R&D work being carried out.
SciTil Status, B.Roy Mach 2014

---
Time resolution ~ 500 ps achieved.
Initial results but very encouraging.
There are ways to minimize the spread/contribution from electronics,
and are being studied. Time resolution ~ 200 ps or better is feasible.
Shifting to a new lab space, which is more or less ready.
Work will resume soon.

---
Costs
		2011		2014
	device	sum	device	sum
Tile	25	140k	25	145k
SiPM	30	330k	90	1060k
Readout	20	220k	50	590k
Mechanics		50k		53k
Total		740k		1848k
Costs driven by SiPM prices in India
SiPM prices in Europe go down

---
Conclusions
R&D / test in beam done by
Vienna, Mainz, Erlangen
100ps is reached
Construction planned in India
SiPM infrastructure is setup at BARC
Critical mass of man power not yet reached
Cost increase due to expensive SiPM in India
Funding?