## Slide 2: Safety in Modern Particle Accelerators: The role of control room operators.
WAO, Mainz 2014 - 26-31 October 2014
Authors: P. Ninin, F. Valentini
Edms: 1422714
Workshop on Accelerator Operations

## Slide 3: Outline
PS Accelerators complex at CERN.
Operators safety tasks overview.
Risks related to Machine Operation.
System Automation for risks mitigation.
Remarks
Edms: 1422714

## Slide 4: PS Accelerators Complex
BEAM ON
ACCESS ON
Medicis
CTF-3
Asacusa

## Slide 5: Safety Tasks Performed by Operators
Access Requests
Handle calls from Access Point. User access rights verification. Verify user safety equipment. Deliver Safety Tokens. Check log of users in zone.
Co-Activities Coordination
Plan/schedule interventions. Verify zone safety conditions. Check specific authorizations.
Hardware Tests
Evaluate operational risks. Establish operational procedures. Filter accesses to the zone. Authorize de-consignation of equipment.
Short Interventions
Plan beam shutdown. Verify safety access conditions. Coordinate intervention phases. Maintain of safety conditions.
Safety Conditions for BEAM
Verify that nobody is in the zone. Execute patrol of the zone. Verify safety conditions for Beam. Execute beam startup sequence.
Safety Conditions for ACCESS
Consignation of safety equipment. Verify safety access conditions.
Edms: 1422714

## Slide 6: Main Critical Points for Machine Operation
Large accelerator facility to be monitored operators.
High volume of user requests to be treated at the same time.
Management/Execution of high number of different operational
procedures.
Heterogeneous user population accessing to dangerous area.
Edms: 1422714

## Slide 7: Main Hazards Related to Machine Operation
ONE OR SEVERAL PERSONS REMAIN INSIDE THE MACHINE WHEN BEAM IS ON.
Main Consequences
C1: Exposition to ionizing radiations (injury), x-rays, activated material.
Initiating Causes
Human Errors:
C2: Exposition to electrical hazards (death).
C3: Accident to be reported to Nuclear Authorities.
Lack of operational procedures.
Violation of procedures.
Work under stress conditions.
Lack of communication.
Insufficient supervision tools.
Particular incident scenarios not handled.
Unclear consigns for operators.
Users not properly trained.
Undisciplined users.
Edms: 1422714
Not adequate PPS tools.

## Slide 8: Main Hazards Related to Machine Operation
Factors Related to Probability Estimation
History of incidents reported for similar installations:
Historical data may likely be incomplete: incidents not documented / unknown.
Quality Measure of existing operational procedures:
Difficult to evaluate if existing procedures are efficient for handling all incident scenarios.
Typology of users operating into the installation:
Common sense of users in respecting rules depends from the subjective risk perception and from the motivations to break rules under certain circumstances.
Costs factors: easy to estimate.
Probability of occurrence: many factors to consider.
Edms: 1422714

## Slide 9: Typical Incident Scenario (1): Unsafe Access
Access Point
1
User call Control Room (CR) for entry permission.
2
CR verifies (via CCTV) authorizations and unlocks
the safety token.
3
User turns the token without extracting it and enters.
4
Another user exiting the zone notices the un-removed token at set it back in safe pos.
Edms: 1422714

## Slide 10: Typical Incident Scenario (1): Unsafe Access
5
Control Room operator verify safety conditions
of the zone for Beam reactivation:
Patrol state OK.
All safety tokens safe inside distributor.
6
Operator set BEAM ON for the zone.
BEAM ON
INCIDENT
 | Safety Barriers
Prevention | Checklist execution / Manual count of users in zone.
Mitigation | Public Address messages before beam injection.
Control Room
Edms: 1422714

## Slide 11: Typical Incident Scenario (2): Intrusion
1
User calls Control Room to request the exit.
2
CR unlocks the door for exit and closes audio/video
connection.
3
User opens the door and leaves the zone.
4
At the same time, an intruder accesses the zone though the opened door: TAILGATING Intrusion.
Access Point inside
Edms: 1422714

## Slide 12: Typical Incident Scenario (2): Intrusion
5
Control Room operator verify safety conditions
of the zone for Beam reactivation:
Patrol state OK.
All Safety Tokens safe inside distributor.
User count in zone = 0.
6
Operator set BEAM ON for the zone.
BEAM ON
INCIDENT
 | Safety Barriers
Prevention | NONE
Mitigation | Public Address messages before beam injection.
Control Room
Edms: 1422714

## Slide 13: System Automation for Risks Mitigation
USERS CONTROL AT THE ACCESS POINT
FRAUDULENT ENTRIES VIA THE ACCESS POINT
CRITICAL TESTING ACTIVITIES COORDINATION
Edms: 1422714

## Slide 14: User Control at the Access Point
Main Covered Risks
Non trained users access. Access without rad dosimeter. User overpassing radiation limits.
Automatic System Verifications
Training validity of the user.
Authorization to access the area.
Authorization to work in the area (IMPACT).
Possession of radiation dosimeter.
Identification via biometry system (eye recognition).
Possession of personnel safety token before accessing the zone.
Count of people in zone and track of Safety Tokens delivered.
Edms: 1422714

## Slide 15: Fraudulent Entries Via the Access Point
Main Covered Risks
Undetected person in zone. Exposition to radiological hazards. Exposition to electrical hazards.
PERSONNEL ACCESS DEVICE
Dynamic weight detection system.
Infrared access detection barrier.
Limitation of the internal space.
Anti-intrusion Detection Systems
Edms: 1422714

## Slide 16: Fraudulent Entries Via the Access Point
MATERIAL ACCESS DEVICE
Human Presence Detection System
FRAME 0
FRAME 1
FRAME DIFFERENCE

## Slide 17: Critical Testing Activities Coordination
Main Covered Risks
Exposition to Electrical Hazards. Beam accidental startup.
Access procedure supervised by the system
(1) Operator authorizes electrical tests in zone by setting a special TEST Mode.
(2) The system verifies that NO beam can be injected in the zone and authorizes the Test mode.
(3) Users entry requests are automatically filtered at Access Point (reduced authorization list): only accepted calls are treated by operators.
(4) The operator unlocks the safety tokens for the validated users.
(5) Access System waits for an additional key confirmation given, locally, by the zone responsible officer.
Edms: 1422714

## Slide 18: Remarks
Deep knowledge of the automation system.
Analyze/Evaluate system actions.
Identify/Handle situations where Safety is bypassed.
Recognize system erroneous behaviors.
Handle risks not covered by the system during specific situations.
Commissioning phases of the machine.
Maintenance periods of Personnel Protection System.
Failures of Personnel Protection System.
In addition of all the automated Safety and non-safety functionalities performed by the Personnel Protection System, the role of the operators is still essential for the operational risks reduction.
In Particular:
Edms: 1422714