## Slide 1: SARAF phase-I status and challenges
Leo Weissman
Soreq Nuclear Research Center
Soreq
Outlook of the talk
Introduction
Status of the accelerator
Recent operation experience
Challenges in operation

## Slide 2: SARAF – Soreq Applied Research Accelerator Facility
To enlarge the experimental nuclear science infrastructure and promote nuclear research in Israel
To modernize the source of neutrons at Soreq and extend neutron based research and applications
To develop and produce radioisotopes for bio-medical applications
Notes: 2

## Slide 3
SARAF vision in 2006
Phase I - 2006
Phase II – 2014
Phase I linac (excluding auxiliaries) was expected to be delivered as a
turn-key by the industrial company, Research Instruments, former ACCEL.
Small local group will participate in the Phase I commissioning and will
receive adequate training from the industrial partner
Phase II built will be lunched after successful commissioning of Phase I
Phase II - 2010
LINAC 2006
176 MHz
DC
2 mA
2 mA
Notes: 3
3

## Slide 4
SARAF today
EIS
LEBT
RFQ
PSM
MEBT
D-plate
targets
Beam dumps
Phase I operational, but not all specifications have been reached
Since 2008 complete decoupling from the industry partners. Commissioning and operation by local team. Local team and its
expertise has grown considerably
Experiments at the temporary beam line
Phase II is under design (in 5 years)
The linac is operated with CW/pulsed protons and pulsed deutrons beams.
For CW proton beam : 1mA at ~3.7 MeV~ 10 hours/trip
2 mA at ~ 2 MeV ~ 2 hours/trip
The accelerator is used to:
  Collecting expertise in the accelerator field
  Study high intensity beam tuning
  Development with high intensity targets
  Basic research in nuclear astrophysics and nuclear medicine
Notes: 4
4

## Slide 5: SARAF Phase I – Upstream View
5
EIS
LEBT
RFQ
MEBT
PSM
A. Nagler, Linac-2006 C. Piel, EPAC-2008 A. Nagler, Linac-2008 I. Mardor, PAC-2009 L. Weissman, Linac-2010
D. Berkovits, Linac-2012
L. Weissman, Rupac-2012
Notes: 5

## Slide 6: Beam lines downstream of the linac
PSM
Beam dump
target

## Slide 7: ECR/LEBT
wire/FC
slits
aperture
ECRIS
8 mA p/d
DC/pulsed
analyzer
magnet
sol1
sol2
sol3
beam
blocker
Notes: 7

## Slide 8
Beam observation in LEBT
Slit is inserted

## Slide 9
Radio Frequency Quadruple injector
Acceleration and bunching is performed
by sophisticated modulation of the rods
4 rods structure traps and transport
the low-energy beam
RFQ works, but ….
built by NTG/U. Frankfurt

## Slide 10
Deuterons CW
Protons CW
RFQ conditioning
Stable operation of deuterons only at low DC(<10%)

## Slide 11: May-June 2014 RFQ conditioning campaign

## Slide 12: Prototype Super conducting Module (PSM)
Houses 6 x 176 MHz HWR (Half Wave Resonator) and 3 SC 6T
Accelerates protons and deuterons from
1.5 MeV/u to 4 and 5.5 MeV
Very compact design
Cavity vacuum and insulation vacuum
are separated
M. Pekeler, LINAC 2006
2500 mm
Beam
The main goal of the prototype cryomodule was demonstration of
acceleration of high current (> 1mA) CW proton/deuteron beams to variable energy up to 4(5.5) MeV
Notes: 12
12

## Slide 13: HWR Microphonics measurements
HWRs are extremely sensitive to LHe pressure fluctuations (60 Hz/mbar)
Detuning signal is dominated by the Helium pressure drift
Detuning sometimes exceeds +/-200 Hz (~ +/-2 BW)
Frequency Detuning
* Performed in collaboration with J.Delayen and K. Davis (JLab)
45 sec
45 sec
BW

## Slide 14: Deterioration of piezo ranges
Chart: Months
| 0 | 0.5 | 3.5 | 6.5 | 10.5 | 11.5 | 17.5 | 18 | 18.75 | 19.75 | 20.5 | 22.5 | 23.596774193548388 | 24.6 | 25.7 | 27.2
HWR6 | 1384 | 1027 | 922 | 701 | 661 | 617 | 1350 | 1373.8 | 1326 | 1278 | 1293.5 | 1382 | 1209 | 1246.8 | 1219.8 | 1271.8
HWR5 | 874 | 822 | 605 | 109 | 165 | 120 | 1380 | 1312 | 1208 | 1375 | 1191.3333 | 1250 | 1144.25 | 1096.4 | 1097.4 | 1073.5
HWR4 | 978 | 614 | 610 | 522 | 100 | 90 | 1300 | 1251.4 | 1232 | 1325 | 1155.5 | 1266.6667
HWR3 | 1013 | 853 | 871 | 850 | 83 | 80 | 1400 | 1198.8 | 1113 | 1141 | 1187 | 1260 | 1164.75 | 1101.4286 | 1135.2 | 1143.6
HWR2 | 780 | 516 | 399 | 360 | 280 | 406 | 1200 | 1091.6 | 1070 | 1094 | 1050 | 1050 | 905.6 | 928.2 | 941.2 | 955
HWR1 | 900 | 977 | 833 | 624 | 696 | 653 | 1150 | 1142 | 1056 | 1002 | 1014 | 940 | 887 | 907.2 | 975 | 985.5
LV PZT
HV PZT
Piezomechanik Gbm
2011
Cavity BW
May 2012
stepping motor
Piezo tuner
beam axis

## Slide 15: Monitoring new piezo ranges
Chart: Months
| 0 | 0.5 | 1.25 | 2.25 | 3 | 5 | 6.096774193548387 | 7.1 | 8.1645161290322577 | 9.6645161290322577 | 11.164516129032258 | 12.1 | 13.164516129032258 | 15.914516129032258 | 18.414516129032258 | 20.378801843317973 | 22.378801843317973 | 24.378801843317973 | 27.3
HWR1 | 1150 | 1142 | 1056 | 1002 | 1014 | 940 | 887 | 907.2 | 975 | 985.5 | 953.5 | 982.1667 | 980.6667 | 962.3333 | 1025.1667 | 995.3667 | 965 | 1030 | 1024
HWR2 | 1200 | 1091.6 | 1070 | 1094 | 978.5 | 1050 | 905.6 | 928.2 | 941.2 | 955 | 939.1667 | 943 | 952.1667 | 931.1667 | 934 | 923.1667 | 824 | 966 | 997
HWR3 | 1500 | 1198.8 | 1113 | 1141 | 1187 | 1260 | 1164.75 | 1101.4286 | 1135.2 | 1143.6 | 1095.5 | 1106.1667 | 1120.8333 | 1097.3333 | 1148 | 1135.9167 | 1106 | 1241 | 1170
HWR4 | 1300 | 1251.4 | 1232 | 1376 | 1155.5 | 1266.6667 | 1160.75 | 1105 | 1074.8 | 1034.3333 | 1067.3333 | 1033 | 1069.8333 | 1032.3333 | 1128 | 1017.1818 | 1008 | 1149 | 1097
HWR5 | 1450 | 1312 | 1208 | 1415 | 1191.3333 | 1250 | 1144.25 | 1096.4 | 1097.4 | 1073.5 | 1045.6667 | 1087.3333 | 1063.1667 | 1069.5 | 1132.2 | 1038.3333 | 961 | 1088 | 1043
HWR6 | 1350 | 1373.8 | 1326 | 1278 | 1293.5 | 1382 | 1209 | 1246.8 | 1219.8 | 1271.8 | 1240.3333 | 1235.3333 | 1232.5 | 1222.6667 | 1344.6 | 1090.3 | 836 | 939 | 853
BW
May 2012

## Slide 16: 4 kW RF power supplies
I. Fishman, LINAC 2012

## Slide 17: RF couplers
Cold window
70OK
Copper strip to
thermal shield for cooling
10-11 mbar
4 0K
Temperature
sensor
Thermal shiled 50OK

## Slide 18
RF on
RF off
RF on
RF off
HWR1
230 kV
HWR2
460 kV
HWR3
460 kV
HWR4
720 kV
HWR5
830 kV
HWR6
425 kV
Coupler warming up during operation (set for 3.9 MeV)
12 hours
T (K)
60
130
77.5
95
112.5

## Slide 19: Implementation - DC bias-T element
1 kV bias
no bias
B. Kaizer LINAC2014

## Slide 20: Production pilot beams

## Slide 21
Acceleration of chopped beam
EIS
LEBT
RFQ
PSM
MEBT
D-plate
VAT
BD
BPM
FFC
chopper
chopper
BD
MEBT BPM
D-plate FFC
The shortest chopped time 200 ns
The rise/fall time better than 10 ns
7 m
RFQ pickup

## Slide 22: Neutron TOF measurements with LiLiT
A 0.5 mA, 4 MeV proton pulses were sent to the liquid lithium target (LiLiT).
Duration of the pulses was 200 ns and frequency 500 Hz.
The TOF spectrum was taken with a plastic scintillator placed at a 5 meters distance upstream from the target
MEBT BPM
RFQ pickup

## Slide 23
Activation VAT copper beam dump
GM counter next to the VAT BD
Original
background
Overflow during
beam operation
Activation after
proton irradiation
The VAT beam dump is made from copper.
3 MeV 1 mA CW protons, ~ 9 hours
We have created ~0.1 mCi source of
65Zn (T1/2=244 d) via 65Cu(p,n)65Zn reaction
Gamma spectrum is dominated
by 65Zn activity
The reaction threshold 2.1 MeV
Ge detector 8 hour after irradiation
L. Weissman et al, JINST 6, 2011, T03001

## Slide 24
Copper beam dump with Ta front
A. Grin
3.9 MeV protons
CW 1 mA
GM 0.5 m distance

## Slide 25
Experience with the Tungsten Beam dump
Visual inspection reveal strong blistering effects
BD #2
BD #3
H2
50 micron Tungsten sheet fused to a water cooled cooper plate.
No activation, low neutron radiation is expected at beam energy up to 10 MeV.

## Slide 26
Tungsten Pin Beam dump
A. Arenstam et al. JINST 8 T07004 (2013)
A 40 mm diameter prototype tested up to
1 kW with 3.7 MeV and
2 MeV beams

## Slide 27
Full scale W pins beam dump
beam
No residual activity up to 10 MeV
Most of the beam power is removed by radiation
Target is always hot (independed on beam current) do implanted hydrogen diffused out very fast
10 deg relative to be axis (copper is shaded by the W pins)
4 mm dia 60 mm long W pin
8” ID vacuum tube
280 W pins
Water cooling channels
Beam diagnostic viewports

## Slide 28: Example of radioisotope production
deuteron beam
I. Silverman et al., NIM B261, 747-750 (2007)
103 Pd production via 103Rh(d,2n)103Pd reaction
Rh foil
filling ports
frame
metal coolant
Notes: 28

## Slide 29
Foil target tests (2011)
25 mm
25 mm SS + 1 mm NaK + 2 mm SS base
Maximum power ~ 1 kW
Maximum irradiation time > 40 hours
Peak dose corresponds to ~ a displacement per target atom (DPA)
I. Silverman et al., ACCAP 2013

## Slide 30: Liquid Lithium Target - LiLiT
Design parameters:
Proton energy: ~2 MeV
Proton current: <3.5 mA
T ≈ 2200C
Tmax ≈ 3500C
Jet: 18 mm x 1.5 mm
Lithium velocity: 20 m/s
Wall assisted lithium jet
Jet chamber
liquid lithium
beam
Notes: 30

## Slide 31: LiLiT - Lithium installed and heated

## Slide 32: Lithium jet circulating (LiLiT)
Measured velocity 7 m/s Maximum e power density 2.0 MW/cm3 @ 4 m/s
S. Halfon et al. App. Rad. Isot. 2011, INS26 2012, CARRI 2012
18 mm

## Slide 33: LiLiT at SARAF beam corridor - 2013
Remote control
Safety measures
“Blind” beam tuning
Nuclear detectors
LiLiT
PSM
RFQ
Ion source
Max beam intensity
~ 1.6 mA
Peak power densities:
3 kW/cm2 and
~ 0.6 MW/cm3

## Slide 34
Protons on Li target
Ethres=1.88 MeV
7Li(p,n)7Be
Application of protons at ~ 1.92 MeV produce spectrum similar to a Maxwelian distribution at ~ kT=30 keV
This distribution mimics stellar neutron spectrum
2 ·1010 n/s/mA
G. Feinberg et al., PRC 2012,
M. Freidman et al., NIM 2013

## Slide 35
Experiments at LiLiT
Experiment | Collaboration | Status
Stellar neutron capture cross section on 94Zr and 96Zr | HeU-SNRC | Finished
Primordial 7Li problem | UCONN-CERN-PSI-HeU-SNRC | First run
Stellar neutron capture cross section for nat.Kr | HeU-SNRC-ANL-UnFrankfurt | First run
Stellar neutron capture cross section on 92Zr | HeU-SNRC-ANL | Planned
Neutron capture cross section for 209Bi | HeU-SNRC-IRMM | Planned
Stellar neutron capture cross section on 90Sr | HeU-SNRC-ANL | Planned
Operation deuteron beam on LiLiT; high energy neutrons | SNRC-WI | Planned

## Slide 36: Boron Neutron Capture Therapy
Sh. Halfon PhD. Thesis

## Slide 37: Research with deuterons natCu(d,x)65Zn
SARAF 2014
65Cu(d,2n)65Zn
63Cu(d,g)65Zn
L. Weissman NIM B 342(2015)7-12.

## Slide 38: Statistics of net operation hours
Type of operation | 2013 | 2014 (October)
RFQ conditioning | 154 | 92
Beam studies | 151 | 61
Accelerator tune | 73 | 155
Beam on targets | 97 | 106
Total operation | 321 | 322

## Slide 39: Items for improvement
Action item | Improvement | Status
A separated target room | 1.5-2 | Designed
The electrical system upgrade | 1-1.5 | Installed
Training of new operator(s) | 1.5-2.5 | In progress
Upgrade of control system | 1.5-2 | In progress
Total | 3-15 | 

## Slide 40: Conclusion(s)
SARAF phase-I is running high intensity CW and pulsed beams on experimental irradiation targets
LiLiT experiments will be the main direction for the next future
However, the facility is not operating at its full capabilities.
Improvement of the operation performance should become the major objective for the next future
This should be done by :
Improving the accelerator subsystem
Improving the facility infrastructure
Expanding the operation team and its expertize

## Slide 41
People involved in phase I/phase II/experiments
(including consulters, students and partially affiliated personal ):
D. Berkovits, A. Arenshtam, Y. Ben-Aliz, Y. Buzaglo, Y. Eisen,
I.Eliyahu, I. Gertz, A. Grin, S. Halfon, D. Har-Even, Y. Haruvy,
D. Hirshman, T. Horovits, B. Kaizer, A. Kreisel, D. Kijel, Y. Luner, J. Rodnizki, G. Shimel, A. Shor, I. Silverman, S.Vaintraub, L. Weissman
+ support from general Soreq technical and logistical services
+ support from the users
Total ~ 20 PPY (Persons Per Year)
Operation/support phase I ~ 6-7 PPY

## Slide 42
Backup slides

## Slide 43: Pin Beam dump as a diagnostic tool

## Slide 44: Pin Beam dump; one of high power tests
1.7 mA of 3.5 MeV proton beam
Beam dynamics analysis shows that beam was over
focused in one direction
Prompt neutron radiation ~ 10 mrem/h at 1 m
No residual activity

## Slide 45: Experiment with dummy LiLiT nozzle
Pulse was red from the left and right plates
and effect of beam steering on temperature
was studied.
It was demonstrated that temperature reading
is adequate for beam diagnostics
The dummy system operated robustly at
1 mA CW beam

## Slide 46: Use radiation detectors for current monitoring
NaI spectrum
Peak power densities:
3 kW/cm2 and ~ 0.6 MW/cm3

## Slide 47
High power targets

## Slide 48: Lithium florescence
LiLiT screen
a few W
LiLiT, 2 kW beam
Light ON Light OFF

## Slide 49: Lorentz detuning and microphonics
The cavities are sensitive to Lorentz detuning. Intense ponderomotive oscillations appear at certain power on the high frequency side. These oscillations significantly hinder locking of the cavities at high RF power values.

## Slide 50: HWR – parameters
176 MHz | Frequency
0.09 | Geom. β
0.15 m | Lacc=βλ
5.5 MV/m 840 kV | Eacc Vacc
>4.7x108 | Q0@Eacc
~1.3x106 ~130 Hz | Qext Loaded BW
< 10 W @Emax | Cryo load
The main goal of the prototype cryomodule is demonstration of
acceleration of high current (> 1mA) CW proton/deuteron
beams to variable energy up to 4(5.5) MeV
Notes: 50
50

## Slide 51: First experience with accelerated deuterons
Water flow
4.7 MeV d beam
Fast neutrons
150 mm LiF layer
109 n/sec
Isotropic distribution
Fast neutrons up to 20 MeV
Chart: E(MeV)
T. Hirsh PhD. Thesis

## Slide 53
LEBT aperture
50 mm
5 mm
25 mm
15 mm
10 mm
Manipulating beam size, current and emittance using the LEBT aperture
p
Aperture diameter (mm)
5
10
15
20
25
50
norm rms emit ( mm mrad)
Transmission (%)

## Slide 54: Rutherford Scattering monitor
Beam
Beam
Si det
Si det
target ladder
drive
target change
chamber

## Slide 55
New instrumentation LEBT
New beam blocker/collimator
Grin
New RFQ entrance flange
Rodnizki

## Slide 56
X-ray detectors
RFQ

## Slide 57
DC breaker for RF coupler

## Slide 59: Beam characterization:
1. Total current (slow FC)
2. Beam position monitor (beam position monitor, 50 Ohm strips)
3. Beam emittance (x-y slits/wires)
4. Bunch phase measurement ( phase probes,
capacitive pick up rings, allows to obtain energy from TOF
5. Longitudinal profile measurements, Fast FC
( C. Deibele et al , SNS)
6. Beam current monitoring
( Modular Parametric Current Transformer, MPCT)
7. Halo measurements (halo monitor)
Most of the measurements will be performed at reduced beam
of 200 W power using pulse mode of the ion source and RFQ (duty cycle ~1/100)
SNS design
Bergoz Instrumentations
Soreq

## Slide 60
Testing RGM from GANIL
* E. Gueroult et al. , JINST 8, T0805 (2013)
RGM
Wire profiler

## Slide 61
Use of commercial VAT beam dump
PSM
D-plate
VAT-BD
Tungsten-BD
Due to logistics constrains we used the commercial VAT beam dump during the tests with
3 MeV 1mA proton beam. VAT beam dump water cooled copper plate, up to 6 kW.
N
S
beam blocker
Ta collimator
suppressor
permanent
magnets
VAT-BD

## Slide 62
Tuning accelerator
300 mg/cm2 gold foil
glued on graphite frame
Pulser peak
resolution 6.6 keV
Typical spectrum without cavity voltages (RFQ only)
1.5 MeV peak
used for calibration
Probably doubly
scattered particles
Rutherford Scattering technique
Measurements provide calibration of asynchronous phase and resonator voltage
L. Weissman, DIPAC2009

## Slide 63
HWR6 0 kV
HWR6 200 kV
HWR6 400 kV
HWR6 600 kV
HWR6 1000kV
L
LLRF RFQ
L
LLRF HWR
~
~
176 MHz
176 MHz
Δf
Resonator calibration

## Slide 64
Prototype of the Beam Loss Monitor system

## Slide 65: Challenges of LiLiT experiment
Impossible to read current as lithium jet is grounded
Limited tools for tune and monitoring (radiation monitoring,
temperature of the side plates)
Demand for accurate set of beam energy
Developed a special diagnostic station
Efforts on energy calibrations
Test with dummy LiliT nozzle
Beam calibration with radiation detectors
Actions items:

## Slide 66
Use of quartz viewer
Use of combination quartz and Ta viewers
Quartz < 1 W beam power
Ta foil < a few 10 W beam power

## Slide 67
Chart: Arb. time (s)
fast valve
target
Vacuum protection

## Slide 68
Radiological test, tungsten beam dump
Radiological test:
3.5 MeV ~ 1mA, 4 hours
CR-90 radiation tags
(fast, thermal neutrons and gammas)
Results:
No sign of fast neutrons
5 mrem thermal neutrons
15 mrem gamma in contact downstream
450 mrem gammas in contact upstream
No residual activation
The beam dump
50 micron Tungsten sheet fused to a water
cooled cooper plate.
Up to 10 MeV, no activation, low neutron
radiation is expected.

## Slide 69: Neutron flux and profile
sx =6 mm
s = 6 - 6.5 mm
sy =5.5 mm
Total neutron rate: ~2×1010 n/s/mA
Autoradiography
2 cm

## Slide 70: Be-7 production
7Be: half-life of 53 days, 478 keV gamma radiation.
Annual irradiation with 4 mA, 2 MeV proton beam, will produce the following dose rate, 30 cm from the system.
Solutions:
Most of the Be-7 will be accumulating at the cold trap and heat exchanger area[1]. The temperature in the loop and in the cold trap should be set to 190°C according thermodynamic analysis of 7Be in molten lithium.
The area will be shielded (2 cm of Pb).
The irradiation periods were calculated in advance in order to control the radiation levels.
[1] M. Ida et. al., Fusion Engineering and Design 82 (2007) 2490-2496.
Notes: 70

## Slide 71
7Be dose rate around LiLiT

## Slide 72
Example of accelerator operation
two weeks in 2012
9 days of continuous operation of two experiment
This is the mode we would like to work at SARAF
However, this approaches to the limit of operation with a single operator
Training of 1(2) operator(s) will increase availability by
a factor of 2

## Slide 73
Control system: work in progress
1. Migration to new Labview version
2. Migration to new control computers and new Window systems
3. New data base system
4. New control system server
5. Replacement of outdated hardware
6. Improvement of network infrastructure
7. Improvement of Labview applications
8. Improvements in the control cabinets
Huge front of work.
Only one control engineer.
This work will effect beam availability in the next future
Eventually increase of availability by a factor of 1.5

## Slide 74
Temporary beam line
Increase of availability
by a factor of 2

## Slide 75
Chart: 2012
 | 4 | 1 | 1 | 2 | 6 | 12 | 9 | 7 | 3 | 5 | 0
Chart: 2011
 | 4 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 2 | 1 | 2
New UPS operational
in 2014
Increase availability by
a factor of 1.5
Poor electricity quality

## Slide 76
s-only
64
76
70
80
82
86
87
88
He-burning stage:
13C(α,n)16O
22Ne(α,n)25Mg
T≈350 MK
~ 30 keV
G. Feinberg PhD thesis

## Slide 77
Big Bang Li production problem
Measure destruction rate of 7Be
via the 7Be(n,α)α reaction
M. Gai et al

## Slide 78: 94Zr experiment
94Zr(n,g) activation:
  Measured: 28.6 mb
  Literature: 27.7 mb
Neutron fluence according to gold activation:
6.85 1013 neutrons (0.83 mA-h at 1.913 MeV)
gold
Zr
M. Tesler M Sc. Thesis

## Slide 79
Cavity | Acceleration voltage (kV) | Phase (deg) | Energy (MeV)
HWR 1 | 213 | -90 | 1.536
HWR 2 | 0 | 0 | 1.536
HWR 3 | 646 | -10 | 2.003
HWR 4 | 493 | -15 | 2.416
HWR 5 | 697 | -35 | 2.971
HWR 6 | 544 | 10- | 3.501
Cavity | Acceleration (voltage (kV | Phase (deg) | Energy (MeV)
HWR 1 | 212 | -95 | 1.5
HWR 2 | 552 | 30 | 1.86
HWR 3 | 646 | -25 | 2.36
HWR 4 | 493 | -10 | 2.81
HWR 5 | 552 | -10 | 3.31
HWR 6 | 544 | -20 | 3.82
Accelerator tunes
from Arik Kreisel
Chart: Distance PSM (cm)
| 0 | 50.8 | 77.8 | 124.1 | 142.1 | 188.4 | 215.4
 | 1.5 | 1.536 | 1.536 | 2.003 | 2.416 | 2.971 | 3.5
Type 1
Type 2
Chart: Distance PSM (cm)
| 0 | 50.8 | 77.8 | 124.1 | 142.1 | 188.4 | 215.4
 | 1.5 | 1.5 | 1.86 | 2.36 | 2.81 | 3.31 | 3.82
HWR6
HWR5
HWR6
HWR4
HWR3
HWR1
HWR2

## Slide 80
Use neutrals for tune LEBT
x-x’
y-y’
Idipole=38.65 A
Idipole=38.95 A
Idipole=38.80 A
L. Weissman et al.
TUP74 LINAC 2010

## Slide 81: ANL conceptual design (2012)
The ion source and LEBT are in the original position
New (RFQ) MEBT and superconducting linac
176 MHz b=0.09 and b=0.16 Half Wave Resonators
Total superconducting linac = 19.47 m
7 low-β HWR operating at 1 MV and 21 high-β HWR operating at 2 MV
  Beam dynamics study at [B. Mustapha et al. IPAC 2012, J. Rodnizki et al. LINAC12]
Total (static and dynamic) power dissipation ~ 350 W @4K
P. Ostroumov et al. LINAC12
5mA, 40 MeV p/d

## Slide 82: Target Hall (2019)
2001 2010
2014 2019
diffractometer
Phase II linac :
40 MeV 5 mA
two proposals :
ANL and CEA
Thermal n source
40 m
radiography
R&D
Thermal neutrons
Radiopharmaceutical
Physics ?
Notes: 82

## Slide 83: Effect of Proton Beam Energy
For 1905 keV (instead of 1915 keV)
we would get 71% of neutrons less

## Slide 84: 13C(p,g) resonance at 1.751 MeV
Chart: Ge spectrum
Chart: NaI spectrum

## Slide 85: Proton energy tune and verification
Time of Flight and
Rutherford Back Scattering
Neutron counting rate as function of proton “energy”