## Slide 1: UNILAC: Review follow-up and upgrade plans
W. Barth

## Slide 2: UNILAC: Review follow-up and upgrade plans
Introduction
FAIR-requirements
Recommendation UNILAC-Review
Status of the Unilac High Current Performance
Further Investigations
  ion source emittance
  RFQ-Matching
  superlens performance
  pulsed gas stripper
UNILAC proton performance
28 GHz-ECR ion source
High Energy LINAC
  rf-amplifiers
  beam dynamics studies
  accelerator cavity studies
Aiming FAIR Uranium intensities (strategy)
Schedule
W. Barth, GSI - Darmstadt

## Slide 3
The GSI UNIversal Linear ACcelerator
High Current Injector
Alvarez
Single Gap Resonators

## Slide 4: Active defects
178 tank-quadrupoles
(leak tightness/water/pre-vakuum, el. properties, ground faults), drift tubes + supports (water& vakuum leaks)
Leak tightness of all tanks
Drift tubes
massive sparkovers beam induced surface defects
Copper surface quality
... inner tank blanket at different positions
Reduced availibility of the focussing system  limited beam intensity and quality, (no) multi beam operation !
Regular and substantial repairing program for all tanks!
High probality of long term-break downs, significant limitations during operation (reduced duty factor, limited rf-voltage, ...)

## Slide 5
FAIR-Requirements

## Slide 6: UNILAC-Upgrade for FAIR
Front End Upgrade

## Slide 7
Recommendation UNILAC-Review
High Current Injector
Alvarez
Single Gap resonators
Increase of U4+
beam intensity:
Terminal West&
Compact LEBT
- RFQ-Upgrade (rf-sparking)
- KONUS beam dynamics vs. strong periodic focusing -> beam brilliance!
Short
gas-stripper section
- strong periodic focussing -> (ALVAREZ type DTL prefered)
- no performance limitations (vs. costs, length, ...)
- UNILAC as FAIR injector only !!!
Strong performance issues
overall injector strategy?
injector requirements w.r.t MTI ?

## Slide 8
Status of the Unilac High Current Performance
March 14: 2.35 emA, U28+@Transfer Line
U 28+
Injector per-formance???
source+LEBT performance

## Slide 9
Status of the Unilac High Current Performance

## Slide 10: Status Quo

## Slide 11
Status of the Unilac High Current Performance
max. U27+-beam intensity  5.5 emA (0.200 pmA) (2007)
max. U73+-beam intensity  2.7 emA (0.037 pmA) (2007)
max. U28+-beam intensity  4.5 emA (0.161 pmA) (2007)
max. U40+-beam intensity  6.0 emA (0.150 pmA) (2010/11)
intensity/transmission data confirmed after RFQ-upgrade (2009)
30% design intensity
Injector performance dropped down in 2012 ?!
High current emittance measurement performed in 2007
25% of the design performance w.r.t. beam brilliance
Last emittance measurements (2012) for 0.8mA only -> tbd. 10/2014

## Slide 12: Design of LEBT
Latest solution: Use existing quartet before RFQ, and a new quartet behind source
(Alternatively: existing sc solenoid could be used, additional simulations...)
Measurements of uranium beam emittance@North Terminal, Oct. 2013
Results of emittance measurements@North Terminal for medium and high uranium currents (35 mA, 55 mA)
9733mm

## Slide 13: Terminal West
Dedicated Terminal exclusively for uranium beam
General layout exists (LOIS)
Integrated service area
All power supplies integrated in the Faraday room
No extension within the basement, only ground floor

## Slide 14: Design of a Dedicated Uranium LEBT (long version, allows for three sources feeding the HSI)
iris (U3+ suppression)
98% space charge compensation
magnet field maps used
two charge states
cutting of off-acceptance ions
final
initial
14 mA U4+ inside
220 mm*mrad
C. Xiao
U3+ ~ 20 mA
U4+ ~ 36 mA
220 mm*mrad
13.45 mA U4+ inside ellipse

## Slide 15
RFQ Matching
Data for required advanced beam dynamics simulations (further optimization, upgrade, redesign and development of machine) were collected -> Measurements are complete and self-consistent.
A gain in particle transmission with new QQ settings was confirmed with Ta 4+ (RFQ transmission of 75±2% instead of 51±4%; 4 mA) and with U 4+ (77±7 instead of 74±1% ;10 mA) – even with a lower RFQ-voltage.
Typically this effect is higher for medium and low beam current
Additional tuning of the LEBT, based on dedicated beam dynamics simulations with recently measured beam emittance behind ion source terminal potentially could lead to increased particle transmission for the entire HSI
An optimization of the whole HSI for high current beam applying new QQ setting is proposed by means of medium ions (e.g. Argon or Xenon beam).

## Slide 16
RFQ-Upgrade
RFQ-Upgrade 2004 (RFQ-Matching, surface quality)
RFQ-Upgrade 2009 (surface quality as well, increase of acceptance, increased field gradient
extensive mixed operation (high duty factor operation m/q=25 (50Ti2+ + short pulse heavy ion beams (m/q=59.5; 238U4+) -> Reduced performance (10% less field gradient): reduced transmission, increased beam emittance
2014: no mixed operation until now -> 96,4% of the design gradient reached.
High probality of ireversible damages of the electrode surface (field emission stimulated by thermal stress, high voltage breakdowns caused by strong particle losses)
New RFQ-rods
tank voltage [a.u.]
tank voltage [a.u.]
Design
5 years of operation

## Slide 17
Further Investigations III – MEBT performance
Beamload for a 6.5 mA Uranium beam was appr. 25 kW ( beamload with 2 mA Krypton beam 7.5 kW)
With improved setting for Krypton beam, the measured beamload was reduced to appr. 4 kW.
Beamload caused by a mismatch of the RF-power -> reduced shunt impedance of the resonator (beam is hitting the surfaces).
86Kr2+: 10% higher superlens rf-amplitude & 15% higher quadrupole field strength -> MEBT-transmission increased 75% -> 93%
Recommendation: new quad doublet with increased field strength, trapezoidal shaped superlens electrodes!
(Redesign of the MEBT in discussion)

## Slide 18
Optimization of gas stripper area (1.4 MeV/u)
enlarged apertures
high stripper target density
high current operation (extremely high space charge forces)
full transmission
separation of Uranium charge states
optimum stripping efficiency
less long./transv. emittance growth
max.
40Ar10+
high current
low current
FAIR
high current
(HSI)

## Slide 19
Further Investigations – fast switching gas stripper
How does the gas distribution looks like?
V.P. Shevelko
U4+ + N2; 2,5 ms
U4+ + He; 4 ms
gas cell
25+
27+
reduced average gas pressure
increased target density
pulse to pulse variation
lower gas consumption
 dense noble gas target available
He -> lower (equilibrium) charge state, increased yield
P. Scharrer, et.al.

## Slide 20
UNILAC proton performance
Chart: ion current [mA]
| LEBT | RFQ | HSI | Gasstripper | Alvarez | Single Gap Resonators | Transfer line | Emittance @ Transfer line
 | 2.1 | 0.64 | 0.55 | 1.43 | 1.21 | 0.91 | 0.92 | 0.67

## Slide 21
High intensity proton beam@UNILAC
clean gas-stripperspectrum
high brilliance beam
main limitations: ion source performance, rf-controls
parallel operation -> carbon beam operation!
Further development goal: 2emA, improved ion source performance, careful UNILAC-optimization (transmission)

## Slide 22
High Intensity protons@FAIR
E [MeV] | 70 | 11,4 | 11,4 | 15 | 15
I [mA] | 35 | 1 | 2 | 1 | 2
Ex,y (phys. 4*rms) [mm mrad] | 7/8 | 7/8 | 7/8 | 6/7 | 6/7
gamma | 1,07 | 1,01 | 1,01 | 1,02 | 1,02
beta | 0,37 | 0,15 | 0,15 | 0,18 | 0,18
beta**2*gamma**3 | 0,17 | 0,02 | 0,02 | 0,03 | 0,03
Space charge limit (N) | 5,8E+12 | 8,6E+11 | 8,6E+11 | 1,1E+12 | 1,1E+12
SIS100 output (particles/cycle) | 1,7E+13 | 1,2E+12 | 2,3E+12 | 1,2E+12 | 2,3E+12
SIS100 output (relative) | 100% | 7,1% | 13,5% | 7,1% | 13,5%
FAIR
p-LINAC
GSI-UNILAC
S. Appel, GSI

## Slide 23
28 GHz-ECR ion source (to be ordered 2014!)
RF injection side
Beam extraction side
Increase pulse intensities for medium and heavy ions by a factor of 10-15!
GOAL:
Higher Charge State  higher energy gain
Higher Charge State  higher beam intensity without stripping
Higher heavy ion beam intensity  cw-/ pulse-mode operation
Compact accelerator  lower cost
low consumption rate -> operation with rare isotope
ECR-projects/developments for heavy ion application:
VENUS (LBNL)
SERSE (INFN)
SUSI (NSCL/MSU) -> FRIB (U33+/34+)
MS-ECRIS@RIKEN (U35+)
SECRAL (IMP-HIRFL) (U41+)
Uranium-Charge state distribution from the RIKEN 28 GHz SC-ECRIS

## Slide 24
High Energy LINAC - rf-amplifiers (2015-2017)
Modularized Upgrade strategy
Exchange of supply and control units
Exchange LLRF, Measurement, interlock
Independent exchange of driver amplifier system (Solid state amplifiers)
Independent exchange of high power amplifiers
  Prototype (THALES) ordered
  Dedicated test area allocated
  Milestone: Successful test operation
  Procurement of series: 2017
  Step by step mounting in shutdowns
Potentially finalized until 2020!
UNILAC rf-amplifier gallery (since 1975)
120m

## Slide 25
Emittance Growth Reduction for KONUS Beam Dynamics
KONUS beam dynamics features high effective Rs
the price to pay is reduced focusing & periodicity in transv. & long. planes
for time being KONUS lattices were designed manually wrt emittance growth reduction
efforts were put to establish a semi-empirical procedure for providing a quasi-periodic lattice & per. matching
but, straight forward recipe for periodic KONUS lattice design still missing
keep constant C1/C2
find individual per. solution for each section
try to match between them
scan for first section
A. Orzhekhovskaya
alfa
new: old: UNILAC*:
Transmission: 92% 88% 100%
Emittance growth: ~ 35% ~ 50% 20-40%
*measured
new design (2014)

## Slide 26
Rf-Simulations on Drift Tube Design for
HE-Linac Alvarez-DTL with strong periodic Focusing
mod. geometry promises higher Rs per surface field
(varied through changing Lgap/Lcell from 0.15 to 0.35)
Curve Length [mm]
Epeak @ Ugap=1V [V/m]
homogeneous distribution of surface field
present
modified (current status)
Rs = 53 MΩ/m
Rs = 60 MΩ/m
108 MHz, example: Lcell = 200 mm ≙ 2.45 MeV/u
X. Du

## Slide 27
Aiming FAIR Uranium intensities (strategy)
Terminal West., Compact LEBT – increased primary beam intensity
RFQ-upgrade (new rods as a copy of existing, medium range)
Avoiding long duty operation (in particular mixed operation with short pulse heavy ion beams) -> applying HSI as injector for UNILAC only
MEBT-upgrade
Careful beam matching for entire HSI (may be additional quadrupole PS for individual set up)
High current beam diagnostic (beam position monitors, online transmission, BIF monitors)
no change for HSI-IH-DTL focusing scheme
no change for stripper section incl. charge separation system
Optionally re-design of matching line (depending on the DTL solution)
Two to be considered alternatives: ALVAREZ type DTL (strong periodic focusing) or IH-type DTL: short tanks, triplet focusing scheme – avoiding emittance growth driven by strong space charge forces! -> further beam dynamics studies!
Design and layout, testing of the major key components: rf acceleration cavity, (may be) focusing lenses (until 4/2017)
FAIR commissioning with upgraded HSI, but existing UNILAC DTL (improved reliability)
UNILAC usefull as a (medium) high current proton injector for the first time!
Reconstruction of rf-amplifier gallery -> prepare for HE-LINAC (to be installed >2020!)

## Slide 28
Time schedule I (Ion source, LEBT, HSI-Upgrade)

## Slide 29
Time schedule II (UNILAC-rf system)

## Slide 30
Time schedule III (UNILAC-availibility)

## Slide 31: Backup

## Slide 32
Compact-LEBT – Status
Design of the LEBT in progress, optimum solution proposed, other solutions under investigation.
Optimum solution: Length appr. 9.7 m , two focusing magnets up to switching magnet (quadrupole/solenoid not yet decided): Appropriate for various alternative scenarios of RFQ (unchanged or redesigned), adjustable for various beam emittances from ion source.
Measurements at North terminal with Uranium und Tantalum June-October 2013, used for simulations for proposed LEBT-design!

## Slide 33
Emittance Growth Reduction for KONUS Beam Dynamics
Transmission 88 %
Emittance growth ~ 50 %
Transmission 92 %
Emittance growth ~ 35 %
old design (2012)
new design (2014)
G. Clemente
A. Orzhekhovskaya