## Slide 1: Marina Dolinska 28th August , 2014
Stochastic Cooling:
Approaches for studies

## Slide 2: Cooling methods
Electron (SIS18, ESR, RESR, NESR, HESR)
Stochastic (ESR, CR, RESR, HESR)
Laser (ESR ??, HESR ??)
.....other

## Slide 3
Aim of cooling is reduction of emmitances (transverse and longitudinal)
Increase the phase space density of particles
Why do we need cooling ?

## Slide 4: Outline
Basic principle of stochastic cooling
- Time domain approach
Other approaches (short overview)
Cooling at CR (preliminary results of simulations)

## Slide 5: Stochastic cooling system
Pickup – detect the beam parameters
Electronics – transfer signal, filter, amplify
Kicker – correct
These devises are places in storage ring, which parameters are important for stochastic cooling system

## Slide 6: Basic principle of stochastic cooling
Measure position and apply a correction.
One particle consideration:
One particle passing with maximal position at PU
Requirement: particle crossing the reference orbit at kicker with maximal angle
Trajectory of not ideal particle
Closed orbit of the ring
(trajectory of the ideal particle)
ΔX‘=gXs,
g – normalized gain
[0<g≤1]
Kicker eliminates angle deviation

## Slide 7
Center of gravity of one sample Position with respect to the reference orbit. Pick-up detects the value of this displacement and forms the signal.
samples
Mean value of sample
Basic principle of stochastic cooling
The coasting beam is sampled. The number of samples and its time length
is defined by frequency range [f1 ; f2] of SC. Bandwidth W=f2-f1
Nominal value for the CR of W=2-1=1 GHz

## Slide 8: Basic principle of stochastic cooling
A sample of particles passing the kicker gets correction of the mean position.
The individual particle coordinate is reduced by the mean value of ensemble. After one turn one has not full cooling.

## Slide 9: Mixing
All particles migrate from one sample to another one. This particle migration is called “mixing”.
Because of mixing the new mean value of sample is formed.
At the next turn the pick-up detects this value and then the kicker corrects it again
mean value evolution of one sample
mean value appears

## Slide 10: Theoretical study
This process is repeated turn by turn and cooling takes place.
For quantitative description of this process the time domain consideration can be used. It gives more better understanding of cooling process and parameters of SC system.
The special computer code is developed, where the time domain approach is applied.

## Slide 11: The main ideas of time domain approach
The beam dynamic is calculated by particle tracking in a ring a turn by turn
Beam sampling (or binning) is applied.
- Complete pick-up, electronic and kicker characteristics, which are defined in the frequency domain, are introduced via inverse Laplase transformation to define the kicker response, which acts on particles.

## Slide 12: Time domain approach
Lattice and SC system parameters
Particle generation
Analyses of distributions ( Δp/prms and εrms )
Pick-up action
Mixing on the way Pick-up – Kicker
Kicker action
Mixing on the way Kicker – Pick-up
Stop after N turns
one turn

## Slide 13: Particle generation
The ensemble of N particles is generated in 6D phase space.
Each particle has the six coordinates (x, x‘, y, y‘, Δp/p, t)
Number of particles N > 104
transformed to normalized phase space
simulation becomes simpler

## Slide 14: Sampling
The particles are generated in a certain time-window: Tw=nsts
Number of samples must be ns > 5
The momentum spread is distributed over this time.
Additionally each particle is assigned to certain bin (or sample).
The time-window of one bin ts is defined by a frequency bandwidth W
of the stochastic cooling system
Revolution time
Tw
W=Wmax-Wmin=109 Hz
ts=0.5 ps
Example of CR
Tw

## Slide 15: Pick-up action
At Pick-up the each sample is analyzed.
The average value of each sample is calculated
s - sample number (max ns)
Ns – number of particles in some sample

## Slide 16: On the way from Pick-up to Kicker
On the way from Pick-up to Kicker mixing takes place.
The particles migrate from sample to sample, which means the time coordinate of each particle is changed by Δt
bad mixing
D(s) - dispersion function
ΔL – path length
ρ – bending radius of dipole
-0.011 (pbar optics)
0.18 (RIB optics)

## Slide 17: On the way from Pick-up to Kicker
Betatron oscillation
The particle coordinate is changed due to betatron oscillation in the ring.
In the normalized transversal phase space it is simple rotation
The phase advance Pick-up→Kicker must be close

## Slide 18: Kicker action
At the kicker correction is applied. All particles of sample get the kicker correction and energy change
g – is normalized gain [0 < g ≤ 1]

## Slide 19: On the way from Kicker to Pick-up
Mixing takes place. The particles migrate from sample to sample, which means the time coordinate of each particle is changed by Δt
good mixing
Here Δµ can be any
In transverse plane the coordinates are recalculated

## Slide 20: cooling effect
The procedure is repeated from turn to turn. Due to such repetition the cooling effect takes place. One can see evolution of particle distribution in transverse and longitudinal spaces
The rms values of amplitudes distribution are calculated.

## Slide 21
Δp/p
Cooling time
εx,y
Evolution of the Rms values of the Emittances and Momentum spread during SC
Rms Emittance
cooling effect

## Slide 22: cooling effect in time domain treatment
cooling effect in ideal case is calculated by simple formulae:
In reality one has to take into consideration the pick-up-kicker loop geometry
with specific frequency characteristic of all components of SC.
Then the given formulas must be modified according to this SC system .
Let‘s look how the signal is proceed in the SC system.
Palmer method
Mixing:

## Slide 23: Noise of signal
δnoise
Noise in the time domain treatment
is still a subject of study :
how to calculate δnoise
Up to now the analytical approach is used

## Slide 24: Noise of signal
noise-to-signal ratio :
damping factor α is introduced
D.Möhl, Stochastic Cooling of particle beams, Springer-Verlag 2013.
λ – sensitivity of SC system. Many construction details are hidden λ

## Slide 25: Kicker response
inverse Laplase transformation

## Slide 26: Kicker response
s(t)
1
the normalized gain is transformed according to shape of signal in the kicker.
s(t) – is formalized function (max is 1)
inverse Laplase transformation
signal shape at kicker

## Slide 27
These formulae for calculation of cooling in time domain approach
cooling effect in time domain treatment

## Slide 28: Other approaches (short overview)
Analytical formulae
Solution of Fokker Plank equation

## Slide 29: Analytical formulae
Momentum spread and emittance evolution are calculated by
Here the cooling rates 1/τ are calculated by formulae

## Slide 30: Analytical
W, g, N – const
W – bandwidth [Hz]
g – normalized gain factor [0 - 1]
N – number of particles
M, B, U – parameters. Here the parameters of hardware are included.
M – mixing factor [1 - ∞ ]
B – parameter of signal shift [0 – 1]
U – noise to signal ratio [0 - ∞ ]

## Slide 31: Analytical
M - the mixing factor.
for the Gaussian distribution
for the homogenous distribution
For analytical formula it is an average value, because Δp/p is not constant
In reality M = M(t) is time dependent function.

## Slide 32: Fokker-Plank equation
ψ - Probability Density Function (PDF) is calculated
X =Δp/p, εx εy
In general, the FPE is very complicated and can not be solved analytically, therefore one has to use numerical algorithms. Most simplest way is one dimensional FPE (only dp/p, or εx or only εy )
The general Fokker-Planck Equation (FPE) for Nv variables X = (x1; x2; : : : xN ):
Fi - drift vector
Dij - diffusion tensor

## Slide 33: Fokker-Plank equation (1D)
Ψ=ψ(z,t)=ΔN/Δz - particle density
z=Δp/p
F=F(z,t) - cooling force (cooling)
D=D(z,t) - diffusion term (heating)
Δp/p

## Slide 34: Fokker-Plank equation (1D)
Coefficients F and D include
parameters of Stochastic Cooling
Coherent effect (cooling)
Incoherent effect (heating)
F
D

## Slide 35
Fokker-Planck equation 2D
t=0
t=5 s
x1=Δp/p, x2=εx
dp/p
emittance
emittance
dp/p

## Slide 36: Codes for simulations
Computer codes for numerical simulations
FOPLEQ-1D (Fokker-Planck one dimension)
FOPLEQ-2D (Fokker-Planck two dimensions)
MPT-6D (TIME-Domain approach six dimensions, still under development)

## Slide 37
MPT-6D code
Notch filter
TOF, Palmer
Instead of inverse Laplase transformation
simple analytical approximations are used
ts=
ts
ts
turn by turn the coordinates are recalculated
Noise
s(t) – kicker response
N=104 macro-particles
ns= 5 samples
g – normalized gain [ < 1]

## Slide 38
Benchmarking of MPT-6D
Measured emmitance and Δp/p at ESR using PALMER method
MPT-6D calculations
Argon beam : 36Ar18+,
E=400 MeV/u
W=0.8 GHz
η = 0.31
gain g and parameter of noise α are adjusted
F. Nolden, et. al. Proceedings of EPAC 2000,conference

## Slide 39: Cooling of ions at CR
Palmer method
System bandwidth W= 1 GHz
Uranium beam 231U92+
Energy 740 MeV/u
η=0.17

## Slide 40: Cooling of ions at CR
N=104 macro-particles
ns=5 number of samples
MPT-6D and analytical calculation of cooling with Palmer method

## Slide 41: Cooling of antiprotons at CR
System bandwidth W= 1 GHz
Antiprotons
Energy 3000 MeV/u
η=0.011
Notch filter method

## Slide 42: Cooling of antiprotons at CR
Gain parameter is varied to find optimal value
2.5x10-4
1.2 mm*mrad
Still the noise parameter must be more correct interpreted
Kicker response should be calculated via inverse Laplase transformations

## Slide 43: Cooling of antiprotons at CR
N=104 macro-particles
ns=5 number of samples
MPT-6D code and analytical formulae are used for calculation of cooling

## Slide 44: Conclusion
Time domain approach is more advanced method
(simpler, multi-dimension, mixing simulation close to reality, other effects can be easy integrated, simulation time is reasonable (10-30 min depending on N)
Next steps:
Kicker response
Frequency characteristic of electronics
Plunging of electrodes
Combination of different methods (Palmer + Filter for ions)
Other effects can be included (IBS, target effect, RF-cavity (bunch rotation, barrier bucket), other...?).