## Slide 1: FPGA Helix Tracking Algorithm for PANDA
Yutie Liang, Martin Galuska, Thomas Geßler, Wolfgang Kühn,
Jens Sören Lange, David Münchow, Björn Spruck, Milan Wagner
II. Physikalisches Institut, JUSTUS-LIEBIG-UNIVERSITÄT GIESSEN
09.09.2014

## Slide 2
Outline
1. Introduction to the PANDA Straw Tube Tracker (STT)
2. Road finding and momentum calculation
Performance study with C++
Implementation with VHDL
5. Summary and outlook

## Slide 3
Straw Tube Tracker (STT)
4636 Straw tubes
23-27 planar layers
15-19 axial layers (green) in beam direction
4 stereo double-layers for 3D reconstruction,
with ±2.89 skew angle (blue/red)
From STT : Wire position + drift time

## Slide 4
Tracking Algorithm -- Road Finding
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Tube_ID
Layer_ID
Hit: Seg_ID(3 bits) + LayerID(4 bits) + Tube_ID (6 bits) + Arrival time
1: Start from inner layer
2: Attach neighbour hit to tracklet layer by layer
Boundary between two segments.
Number of neighbor:
4 in axial layer; 6 in stereo layer

## Slide 5
Known : xi , yi , di
Question: To determine a circle,
x2 + y2 + ax + by + c = 0
Method: Minimize the equation
E2 = ∑(xi2 + yi2 + a xi+ b yi + c)2 (1/di)2
Sx = ∑xi …
Sxx = ∑xixi …
Sxxx = ∑xixixi …
Tracking Algorithm -- helix parameters calculation
1) Circle para.
2) Track quality.
x
y
xc, yc, R

## Slide 6
To Improve the Momentum Resolution -- using a 2nd iteration
Pt(input) 1st iteration 2nd iteration
0.2GeV/c : 0.195 ±0.0068 0.195±0.0068
0.5GeV/c : 0.5 ±0.0212 0.5 ± 0.0164
1.0GeV/c : 0.99 ±0.0595 1.0 ± 0.0317
2.0GeV/c : 1.85 ±0.213 2.0 ± 0.073
Pt(GeV/c)
Pt(GeV/c)
1st iteration
2nd iteration
x
y
xc, yc, R

## Slide 7
Event #4
Event #4
Black dashed line: track by MC truth
Red line: recon. track
Blue: recon. using outer layers
drift circles belong to current event (Red) or other events (Green)
T0 information: current event(Red) or other events(Green)
Performance Study -- realistic events, time-based

## Slide 8
Event #1
Event #1
Black dashed line: track by MC truth
Red line: recon. track
Blue: recon. using outer layers
drift circles belong to current event (Red) or other events (Green)
T0 information: current event(Red) or other events(Green)
Assign Track to Correct Event

## Slide 9
Pz reconstruction
1: The radius, the position of the helix center in the XY plane are determined.
2: Φ = kZ + Φ0
z
y
x
One cylinder the helix lies in.
Based on Pt determined before
One straw tube
Track need to be tangent to the crossing ellipse.
Crossing points
(ellipse)
Gianluigi Boca and Panda Collaboration, Panda STT TDR, 2012

## Slide 10
Pz reconstruction
Known : zi , Φ i , di
Question: To determine a line,
Φ + kz + Φ0= 0
Method: Minimize E2 = ∑(Φi + kzi + Φ0)2 (1/di)2

## Slide 11
Pz reconstruction
Pt = 0.5 GeV/c
Pz(input)
0.25 GeV/c : 3.7 %
0.50 GeV/c : 4.0 %
1.00 GeV/c : 4.3 %
Pt = 1.0 GeV/c
Pz(input)
0.5 GeV/c : 3.1 %
1.0 GeV/c : 3.8 %
2.0 GeV/c : 4.2 %
Pt = 2.0 GeV/c
Pz(input)
1.0 GeV/c : 3.7 %
2.0 GeV/c : 4.8 %
4.0 GeV/c : 5.2 %

## Slide 12
VHDL Implementation
VHDL: Very-high-speed integrated circuits Hardware Description Language.
Square root : Look-up table
(1-2000)  1-4 4-16 16-64 64-256 …
Division: Look-up table
a/b = (a*2^n) / (b*2^n) b*2^n in (0.5-1)

## Slide 13
Performance at FPGA
2: Time per event:
Pz calculation not finished yet.
1: Device Utilization Summary:
For one event with 100 hits (6 tracks):
100 clock cycles (cc) (2) 50 cc * 6 (3) ~200cc * 6 /(3 or 4)
Previous:
(1) 100 clock cycles (cc) (2) 50 cc * 6 (3) ~50cc * 6
34%
1%
42%
1%
58%
96%
Previous design

## Slide 14
Tracking at FPGA -- at low event rate
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 15
Tracking at FPGA -- at low event rate
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 16
Tracking at FPGA -- at low event rate
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 17
Tracking at FPGA -- 20 MHz
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 18
Tracking at FPGA -- 20 MHz
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 19
Tracking at FPGA -- 20 MHz
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 20
Summary and Outlook
5 μs/event , 100 FPGA @ 20MHz interaction rate
Next to do:
Optimize the VHDL code.
Include MVD points
Test with PTDAQ.
 | C++ | VHDL
Pt 1st iteration | √ | √
Pt 2nd iteration | √ | √
χ2 calculation | √ | √
Pz 1st iteration | √ | On going
Pz 2nd iteration | √ | On going

## Slide 21
Thank you

## Slide 24
VHDL implementation
2D Mapping
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
ToT
T0
T0
Ring Buffer
Input Interface
T0
Tracking module
5
4
8
6
7
2
3
1
..
..
..
9
Calc Mom
Form tracklet
Index

## Slide 25
The Compute Node (CN)

## Slide 26
Hardware Description Language
VHDL, Verilog, SystemC
VHDL: Very-high-speed integrated circuits Hardware Description Language.
It’s a dataflow language, unlike procedural computing languages such as C++ which runs sequentially, one instruction at a time.
A
B
A1
A2
A3
A4
B1
B2
B3
B4
Signal A3_B1 …;
Signal A4_B2 …;
A3 <= A3_B1;
B1 <= A3_B1;
A4 <= A4_B2;
B2 <= A4_B2;

## Slide 27
PC as data source and receiver.
Ethernet.
Optical link (UDP by Grzegorz Korcyl )
(not integrated yet)
FPGA
FIFO
Tracking algorithm
Ethernet via
Optical Link
Setup and Test
FIFO

## Slide 28
Event #2
Event #2
Black dashed line: track by MC truth
Red line: recon. track
Blue: recon. using outer layers
drift circles belong to current event (Red) or other events (Green)
T0 information: current event(Red) or other events(Green)
Assign a track to the correct event

## Slide 29
0.2GeV
0.5GeV
2GeV
1GeV
Performance study – single track
x(cm)
y(cm)
x(cm)
y(cm)
x(cm)
y(cm)
x(cm)
y(cm)

## Slide 33
Pt = 0.5 GeV/c
Pz(input)
0.25 GeV/c : 3.7 %
0.50 GeV/c : 4.0 %
1.00 GeV/c : 4.3 %
Pt = 1.0 GeV/c
Pz(input)
0.5 GeV/c : 3.1 %
1.0 GeV/c : 3.8 %
2.0 GeV/c : 4.2 %
Pt = 2.0 GeV/c
Pz(input)
1.0 GeV/c : 3.7 %
2.0 GeV/c : 4.8 %
4.0 GeV/c : 5.2 %
Pz reconstruction