## Slide 1: The PANDA Experiment
| Tobias Stockmanns

## Slide 2: PANDA Detector
13 m
p
p

## Slide 3: PANDA — Event Reconstruction
Mitglied der Helmholtz-Gemeinschaft
Continuous read out
  Novel feature
  Background & signal similar
  No hardware trigger based on few sub-detectors, but online event reconstruction using full detector information
(Reject background events, save interesting events)
Reduction
Amount:
Time:
~1/1000
50 ns/evt
Storage space for offline analysis
3 PB/y
Event:
Raw data:
2 × 107/s
200 GB/s
Rate

## Slide 4: Event Selection
Channel | TRK | NEUT | Excl. | mult | PID | p | E | ang. | inv M | dist cut | veto | 4C | Vtx C | Mass C | Sig Eff[%]
J/psi pi+ pi- | 4 | 0 | x |  | e, pi |  |  |  | x |  |  |  | J/psi pi+ pi- |  | 30
J/psi pi0 pi0 | 2 | 4 | x |  | e |  | g |  | x |  | J/psi eta pi0 | x | J/psi |  | 17
chi_c1,2 gam | 2 | 2 | x |  | e |  | g |  | x |  |  | x | J/psi |  | 30
J/psi gam | 2 | 1 | x |  | e |  |  |  | x |  |  | x | J/psi |  | 40
J/psi eta | 2 | 2 | x |  | e |  |  |  | x |  |  | x | J/psi |  | 40
h_c -> 3gam | 0 | 3 | x | 3n |  |  | g | h_c | x |  |  | x |  |  | 8
h_c -> 2phi gam | 4 | 1 | x |  | K |  | g |  | x |  | pi0 | x |  |  | 8
D+ D- | 6 | 0 | x |  | ? | D |  |  | x | z(D) |  | x | D+- |  | 8
D*+ D*- | 6 | 0 | x |  | ? | D* |  |  | x | z(D*) |  | x | D0 | D0 | 14
eta_c1 eta | 2 | 7 | x |  | e |  |  |  | x |  |  | x |  | chi, pi0, eta | 7
eta_c1 eta | 4 | 8 | x |  | K, pi |  |  |  | x |  | >1 comb/ev | x | K pi | D0, D0*, eta, pi0 | 5
J/psi omega | 4 | 2 | x |  | e, pi |  |  |  | x |  |  | x | J/psi pi+pi- | J/psi, pi0 | 15
f2(2230) -> 2phi | 4 | 0 | x |  | K |  |  |  | x |  |  | x | phi |  | 20
Ds Ds(2317) | 3 | 0 |  |  | K, pi |  |  | K | x |  |  |  | Ds, phi |  | 20
Xi- Xi+ pi0 | 6 | 2 | x |  | p, pi |  | g |  | x | d(IP-Xi) | >1 comb/ev | x | Lam,Xi+- | Xi Xi pi0 | 16
Lam Lam | 6 | 0 | x |  | p, pi |  |  |  | x | d(IP-Xi) |  |  | Lam |  | 11 ... 23
Xi- Xi+ | 6 | 0 | x |  | p, pi |  |  |  | x |  |  |  | Lam, Lam pi |  | 19
Selection criteria used in the Physics Report Analyses
a lot of fitting!
March 8, 2012
few kinematic cuts
(except mass)
PID!
no
multiplicity cuts
K.Götzen

## Slide 5: Selection Criteria
Physics Book criteria:
J/psi ( base for many charmonia)
  Invariant Mass: Tracking/Momentum
  Electron ID: Tracking, cluster energy, track/cluster match
  Muon ID: Tracking, Muon detector information
  Vertex: Tracking
D/Ds Mesons
  Pi0s: EMC clusters
  Inv. Mass: Tracking
  Kaon, Pion ID: dE/dx, DIRC info (w/ track match), ToF (track match)
  Vertex: Tracking
Baryons
  Inv. Mass: Tracking
  proton, pion ID: DIRC info (w/ track match)
  Vertex: Tracking
Full events: 4C fitting
Tracking & momentum
→ key information

## Slide 6: Event structure in PANDA
Beam structure in HESR quasi-continuous over 1.6 µs then 0.4 µs gap
Mean time between events 50 ns in high luminosity mode
Distribution of events follows Poisson statistics  high probability of short time between events
Time resolution of detectors very different:
  MVD: < 10 ns
  STT: < 250 ns
  GEM: < 10 ns
  SciTil: < 1 ns (but far outside > 1 m)

## Slide 7: PANDA DAQ
continuous sampling DAQ
flash ADC
self-triggered
detector front-end
front-end feature extraction
(signal amplitude, shape, …)
each signal get a time stamp (160 MHz)
high quality clock distributed
EMC pile-up waveform

## Slide 8: Time-based Simulation

## Slide 9: Data Path
Event-Generation
Simulation
Digitization/ Det. Data
Local Reco
Global Reco
Event Building
Analysis
Selection
Event-based
Time-based sub detector level (clusterization, hit reco)
Time-based global level (global tracking, PID)
(Reco)Event-based

## Slide 10: Digi Data randomized
Digi Data Stream
Digi Index
Same color = same event

## Slide 11: Digi Data randomized
TimeStamp of Digi vs Index
Digi Index
Time Stamp [ns]

## Slide 12: Digi Data Sorted
Digi Data Stream
Digi Index
Same color = same event

## Slide 13: Digi Data Sorted
Digi Index
Time Stamp [ns]
TimeStamp of Digi vs Index after sorting

## Slide 14: PANDA – Event Simulation

## Slide 15: Event Display
Event selected by MVD via time gap
STT hits matching to MVD time

## Slide 16: Time-Based Event Reconstruction

## Slide 17: Data packaging
Select data packages according to time gaps between digi clusters
Works very well for detectors with precise time measurement
Example: GEM Digis
MC Truth
Packages
R. Karabowitcz

## Slide 18: GEM Tracking Efficiency
87% for primaries with |p|>1GeV/c,
compared to ~95% in event-based reconstruction
R. Karabowitcz

## Slide 19: GEM Event Building
Use the tracks’ start-time
• Tracks with start-time closer than 3 ns end up in one event (3ns come from the tracks start-times correlation), with event time set to a mean of constituent tracks’ start times
• Even one track can form an event
• Compare reconstructed event times with MC event times, if the difference is smaller than 5 ns the MC event is considered to be reconstructed
R. Karabowicz

## Slide 20: Event Builder
R. Karabowicz

## Slide 21: Event Builder
R. Karabowicz

## Slide 22: Event Builder
R. Karabowicz

## Slide 23: Event Builder
R. Karabowicz

## Slide 24: GEM Event Reconstruction
10000 DPM events
simulated
• 8165 events with reconstructable track in GEM tracker
• 7536 events Reconstructed (92.3%)
• 139 ghost events (1.8%)
R. Karabowicz

## Slide 25: Event Building Model
SciTil
Data Buffer
Find Events
Track Buffer
Store Event Data
MVD Track
Find Events
Store Event Data
GEM
Track
Track Buffer
Find Events
Track Buffer
Store Event Data
Global
Find Events
Store Event Data
Events
Event Buffer
Build Event
Work in progress
R. Karabowitcz

## Slide 26: Track Finding + FItting

## Slide 27: STT — Drift Tubes and t0
Mitglied der Helmholtz-Gemeinschaft
Particle ionizes gas atoms in drift tubes
Resolution without t0: 𝒪(0.1 cm) Resolution with t0: 𝒪(0.015 cm)
Usual HEP experiment: t0 by trigger
But PANDA has no trigger…
Electrons drift to anode wire, ions to wall
Signal only when electrons arrive at wire
No information about drift duration!
For that, start time (t0) needed:
t0 - tarrival ≈ tdrift
vdrift = const → tdrift • vdrift = risochrone
risochrone

## Slide 28: Event Structure -- pile-up
20 MHz
2000 ns revolution time
400 ns gap
TMean between 2 events: 50 ns
Drift time: ~250 ns
Wrong T0  Wrong drift circle  bad track quality
Event pile-up
Y. Liang

## Slide 29: Hitstream Display: 15 GeV/c DPM, 50 ns Mean Time
XY-View
  DPM Benchmark: Realistic event rate and structure, continuous operation
M.Mertens
Triplet
Isochrone early
Isochrone early & skewed
Isochrone close
Isochrone late
MVD hit
Track timed out
Track current

## Slide 30: Cell Track Finder

## Slide 31: CellTrackFinder
1. Generation of tracklets in STT
  Primary tracklets: use of cellular automaton
  Combination of tracklets: use of Riemann Fit
  Faulty: Fit to center of the tubes
  Add remaining hits to best fitting Track
 TrackletGenerator
 HitCorrector
2. Correction of STT-Hits based on event time
  Correct points for Riemann Fit by calculating tangents to the isochrones

## Slide 32: 1. TrackletGenerator Cellular Automaton
Abstract discrete model for dynamic systems
Definition by:
  Cell
  Neighborhood relations
  Discrete number of states
  Transition rules for states
  Simultaneous changes

## Slide 33: 1. TrackletGenerator Cellular Automaton - Apply to STT

## Slide 34: 1. TrackletGenerator Cellular Automaton – Apply to STT
1
2
> 2
Number of Neighbours:
unambiguous
ambiguous

## Slide 35: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 36: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 37: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 38: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 39: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 40: 1. TrackletGenerator Cellular Automaton - Apply to STT
15
7
1
10
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 41: 1. TrackletGenerator Cellular Automaton - Apply to STT
1/10 7/15
7/15
1/10
7/15
1/10
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 42: 1. TrackletGenerator Cellular Automaton - Apply to STT
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 43: 1. TrackletGenerator Riemann fit
Points to be fitted
Add z-dimension
Map onto paraboloid

## Slide 44: 1. TrackletGenerator Riemann fit
Fit Plane
Normal vector  Circle parameters
quadratic  linear
explicit solution
already implemented in PandaRoot
Advantages

## Slide 45: 1. TrackletGenerator Result of the combination
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15

## Slide 46: 1. TrackletGenerator Example – Unambiguous hits

## Slide 47: 1. TrackletGenerator Example – First tracklets

## Slide 48: 1. TrackletGenerator Example – Combined tracklets

## Slide 49: Road Finder

## Slide 50: Tracking Algorithm -- Road Finding
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Tube_ID
Layer_ID
Hit: Seg_ID(3 bits) + LayerID(4 bits) + Tube_ID (6 bits) + Arrival time
1: Start from inner layer
2: Attach neighbour hit to tracklet layer by layer
Boundary between two segments.
Number of neighbor: 4
Y. Liang

## Slide 51: Two iteration circle fit
x
y
xc, yc, R
Pt(input) 1st iteration 2nd iteration
0.2GeV/c : 0.195 ±0.0068 0.195±0.0068
0.5GeV/c : 0.5 ±0.0212 0.5 ± 0.0164
1.0GeV/c : 0.99 ±0.0595 1.0 ± 0.0317
2.0GeV/c : 1.85 ±0.213 2.0 ± 0.073
Pt(GeV/c)
Pt(GeV/c)
1st iteration
2nd iteration

## Slide 52: Performance Study
Event #4
Event #4
Black dashed line: track by MC truth
Red line: recon. track
Blue: recon. using outer layers
drift circles belong to current event (Red) or other events (Green)
T0 information: current event(Red) or other events(Green)

## Slide 53: Beyond CPU

## Slide 54: VHDL Implementation
VHDL: Very-high-speed integrated circuits Hardware Description Language.
It’s a dataflow language, unlike procedural computing languages such as C++ which runs sequentially, one instruction at a time.
Y. Liang

## Slide 55: Tracking at FPGA -- 20 MHz
Data flow: Hit information at PC  FPGA, extract helix para.  PC
Y. Liang

## Slide 56: Performance at FPGA
2: Time per event:
1 burst, 20 MHz, 40 events
 260 μs
Only 1st iteration is implemented in VHDL
1: Device Utilization Summary:
Y. Liang

## Slide 57: New compute node

## Slide 58: GPU Algorithms

## Slide 59
Mitglied der Helmholtz-Gemeinschaft
Algorithms #1
Hough Transform
Riemann Track Finder
Triplet Finder

## Slide 60: Algorithm: Hough Transform
Mitglied der Helmholtz-Gemeinschaft
Idea: Transform (x,y)i → (α,r)ij, find lines via (α,r) space
Solve rij line equation for
  Lots of hits (x,y,ρ)i and
  Many αj ∈ [0°,360°) each
Fill histogram
Extract track parameters
i: ~100 hits/event (STT)
j: every 0.2°
rij: 180 000
x
y
x
y

## Slide 61: Hough Transform — Granularity
Mitglied der Helmholtz-Gemeinschaft
Choice of α granularity determines resolution
α = 0°, 2°, 4°, …
α = 0°, 2°, 4°, …

## Slide 62
1800 x 1800 Grid
PANDA STT+MVD
Mitglied der Helmholtz-Gemeinschaft
68 (x,y) points
r
α
Algorithm: Hough Transform

## Slide 63: Hough Transform — Remarks
Mitglied der Helmholtz-Gemeinschaft
Two Implementations
Thrust (CUDA‘s STL)
  Performance: 3 ms/evt
  Reduce to set of standard routines
    Fast (uses Thrust‘s optimized algorithms)
    Inflexible (hard to customize)
    Not yet at performance maximum
Plain CUDA
  Performance: 0.5 ms/evt
  Built completely for this task
    Fitting for PANDA; customizable
    A bit more complicated at parts
Peakfinding challenging

## Slide 64: Hough Transform — Remarks
Mitglied der Helmholtz-Gemeinschaft
Hill Climber
Iterative Maximum Deleter
Peakfinding challenging
current research

## Slide 65
Mitglied der Helmholtz-Gemeinschaft
Algorithms #2
Hough Transform
Riemann Track Finder
Triplet Finder

## Slide 66: Riemann Track Finder — Method
Mitglied der Helmholtz-Gemeinschaft
Idea: Don‘t fit lines (in 2D), fit planes (in 3D)!
Create seeds
  All possible three hit combinations
Grow seeds to tracks Continuously test next hit if it fits
  Use mapping to Riemann paraboloid (+ s-z fit, det. layer)
x
x
x
x
y
z‘
x
x
x
y
x
x
x
x
y
x
More on: Seeds; Growing
1
2

## Slide 67: Riemann Track Finder — GPU Adaptations
Mitglied der Helmholtz-Gemeinschaft
CPU
GPU
100 × faster than CPU version: ~0.6 ms/event
Still needs merging into PandaRoot
3 loops to generate seeds serially
for (int i = 0; i < hitsInLayerOne.size(); i++) {
for (int j = 0; j < hitsInLayerTwo.size(); j++) {
for (int k = 0; k < hitsInLayerThree.size(); k++) {
/* Triplet Generation */
}
}
}
Needed: Mapping of inherent GPU indexing variable to triplet index
int ijk = threadIdx.x + blockIdx.x * blockDim.x;
1
2
Port of CPU code; parallelism on seed base
Only easy computations; e.g. 3x3 matrices

## Slide 68
Mitglied der Helmholtz-Gemeinschaft
Algorithms #3
Hough Transform
Riemann Track Finder
Triplet Finder

## Slide 69: Triplet Finder
Mitglied der Helmholtz-Gemeinschaft
More
http://www.fz-juelich.de/ias/jsc/nvlab
Idea: Use only subset of detector as seed
  Don’t use STT isochrones (drift times
  Calculate circle from 3 points (no fit)
Features:
  Fast & robust algorithm, no event time needed
  Many tuning possibilities

## Slide 70: Triplet Finder — Display
Mitglied der Helmholtz-Gemeinschaft
Triplet
Isochrone early
Isochrone early & skewed
Isochrone close
Isochrone late
MVD hit
Track timed out
Track current

## Slide 71: Triplet Finder — Times
Mitglied der Helmholtz-Gemeinschaft
K20X
in publication

## Slide 72: Triplet Finder — Optimizations
Mitglied der Helmholtz-Gemeinschaft
Bunching Wrapper
  Hits from one event have similar timestamps
  Combine hits to sets (bunches) which occupy GPU best
Hit
Event
Bunch
𝒪(N2) → 𝒪(N)

## Slide 73: Triplet Finder — Clock Speed / GPU
Mitglied der Helmholtz-Gemeinschaft
K40 3004 MHz, 745 MHz / 875 MHz
K20X 2600 MHz, 732 MHz / 784 MHz
Memory Clock
Core Clock
GPU Boost
in publication

## Slide 74: FAIR MQ

## Slide 75: FairMQ in PANDA - FPGA
FPGA to FairMQ: Used as fast transport layer in test beam
FE
FPGA
pull
push
State Machine
Storage
Mux
pull
pub
Monitor
sub
Backup
sub
Control
push
push
push
push
Storage
4 x

## Slide 76: FAIR MQ in PANDA - GPU

## Slide 77: Summary
Event reconstruction in real time challenging enterprise in PANDA
Time-based simulation exists to simulate data stream
Event building scheme and algorithms under development
Most challenging: tracking
Different tracking algorithms tested
Implementations for FPGAs and GPUs exist but still a lot of work necessay
New concept of FairRoot for concurrent processing under study
Open Issues:
  Global event building
  Alignment and calibration
  Online analysis and selection

## Slide 78: PANDA — Read Out Scheme
Mitglied der Helmholtz-Gemeinschaft
Requirements to Online Tracking
Fast
Sophisticated algorithms possible; reprogrammable
Parallelism beyond single devices
Fast
Limited precision ok
GPUs

## Slide 79: Event Time
Signal Event
Signal and Background Events

## Slide 80: Digi Time
MVD Digi Pixel Time

## Slide 81: Reco Hit Time
Reco Hit Time