## Slide 1: FPGA Helix Tracking Algorithm -- VHDL implementation
Yutie Liang, Martin Galuska, Thomas Geßler, Wolfgang Kühn,
Jens Sören Lange, David Münchow, Björn Spruck, Milan Wagner
II. Physikalisches Institut, JUSTUS-LIEBIG-UNIVERSITÄT GIESSEN
Dec. 09. 2014

## Slide 2
Outline
1. Introduction to the STT
Road finding and momentum calculation
Implementation with VHDL
4. Summary and outlook

## Slide 3
Straw Tube Tracker (STT)
4636 Straw tubes
23-27 planar layers
15-19 axial layers (green) in beam direction
4 stereo double-layers for 3D reconstruction,
with ±2.89 skew angle (blue/red)
From STT : Wire position + drift time

## Slide 4
Tracking Algorithm -- Road Finding
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Tube_ID
Layer_ID
Hit: Seg_ID (3 bits) + LayerID (4 bits) + Tube_ID (6 bits) + Arrival time
1: Start from inner layer
2: Attach neighbour hit to tracklet layer by layer
Boundary between two segments.
Number of neighbor:
4 in axial layer; 6 in stereo layer

## Slide 5
Known : xi , yi , di
Question: To determine a circle,
x2 + y2 + ax + by + c = 0
Method: Minimize the equation
E2 = ∑(xi2 + yi2 + a xi+ b yi + c)2 (1/di)2
Sx = ∑xi …
Sxx = ∑xixi …
Sxxx = ∑xixixi …
Tracking Algorithm -- helix parameters calculation
1) Circle para.
2) Track quality.
x
y
xc, yc, R

## Slide 6
Pz Reconstruction
1: The radius, the position of the helix center in the XY plane are determined.
2: Φ = kZ + Φ0
z
y
x
One cylinder the helix lies in.
Based on Pt determined before
One straw tube
Track need to be tangent to the crossing ellipse.
Crossing points
(ellipse)
Gianluigi Boca and Panda Collaboration, Panda STT TDR, 2012

## Slide 7
Known : zi , Φ i , di
Question: To determine a line,
Φ + kz + Φ0= 0
Method: Minimize E2 = ∑(Φi + kzi + Φ0)2 (1/di)2
z(cm)
Φ
Pz Reconstruction

## Slide 8
VHDL Implementation
VHDL: Very-high-speed integrated circuits Hardware Description Language.
Square root : Look-up table
(1-2000)  1-4 4-16 16-64 64-256 …
Division: Look-up table
a/b = (a*2^n) / (b*2^n) b*2^n in (0.5-1)

## Slide 9
Square Root Operation
384 bins in the range of 1 ~ 4, error ~ 0.4%
sqrt_array_dyn(0) <= "00000001000000000000000000000000"; -- 1.00000
sqrt_array_dyn(1) <= "00000001000000001111111110000000"; -- 1.00390
……
sqrt_array_dyn(383) <= "00000001111111110111111111110000"; -- 1.99805
(Xc, Yc)  R
C++ VHDL
Xc: 0.7286 0.7278
Yc: 161.153 161.138
R: 161.155 160.624 (0.33%)
Zi:
C++ VHDL
29.4 ±5.0 20.0 ±5.1
17.0 ±8.1 7.7 ±8.1
Black: C++
Red: VHDL
z(cm)
Φ

## Slide 10
Square Root Operation
C++ VHDL
Xc: 0.7286 0.7278
Yc: 161.153 161.138
R: 161.155 161.167 (0.01%)
Zi:
C++ VHDL
29.4 ±5.0 29.23 ±5.1
17.0 ±8.1 16.93 ±8.1
384 bins in the range of 1 ~ 4, error ~ 0.4%
Linear extrapolation, precision improves
z(cm)
Φ

## Slide 11
Hit reading
For one event with 100 hits (6 tracks): 14 μs
Road finder
Pt extraction
Pz extraction
Performance at FPGA
(100 cc)
(50 cc X 6)
(120 cc X 2 X 6)
(60 cc X 2 X 6)

## Slide 12
Performance at FPGA
For one event with 100 hits (6 tracks): 7 μs
Hit reading
Road finder
Pt extraction
Pz extraction
(100 cc)
(50 cc X 6)
(120 cc X 2 X 6)
(60 cc X 2 X 6)

## Slide 13
Tracking at FPGA -- at low event rate
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 14
Tracking at FPGA -- 20 MHz
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 15
Summary and Outlook
σ_pt : ~ 3.2% σ_pz : ~ 4.2%
7 μs/event (6 tracks) , 140 FPGA @ 20MHz
 | C++ | VHDL
Pt 1st iteration | √ | √
Pt 2nd iteration | √ | √
χ2 calculation | √ | √
Pz 1st iteration | √ | √
Pz 2nd iteration | √ | √
Next to do:
Optimize the VHDL code.
Include MVD points
Test with PTDAQ.

## Slide 16
Thank you

## Slide 18
VHDL implementation
2D Mapping
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
ToT
T0
T0
Ring Buffer
Input Interface
T0
Tracking module
5
4
8
6
7
2
3
1
..
..
..
9
Calc Mom
Form tracklet
Index

## Slide 19
The Compute Node (CN)

## Slide 20
Hardware Description Language
VHDL, Verilog, SystemC
VHDL: Very-high-speed integrated circuits Hardware Description Language.
It’s a dataflow language, unlike procedural computing languages such as C++ which runs sequentially, one instruction at a time.
A
B
A1
A2
A3
A4
B1
B2
B3
B4
Signal A3_B1 …;
Signal A4_B2 …;
A3 <= A3_B1;
B1 <= A3_B1;
A4 <= A4_B2;
B2 <= A4_B2;

## Slide 21
PC as data source and receiver.
Ethernet.
Optical link (UDP by Grzegorz Korcyl )
(not integrated yet)
FPGA
FIFO
Tracking algorithm
Ethernet via
Optical Link
Setup and Test
FIFO

## Slide 22
Event #2
Event #2
Black dashed line: track by MC truth
Red line: recon. track
Blue: recon. using outer layers
drift circles belong to current event (Red) or other events (Green)
T0 information: current event(Red) or other events(Green)
Assign a track to the correct event

## Slide 23
0.2GeV
0.5GeV
2GeV
1GeV
Performance study – single track
x(cm)
y(cm)
x(cm)
y(cm)
x(cm)
y(cm)
x(cm)
y(cm)

## Slide 27
Pt = 0.5 GeV/c
Pz(input)
0.25 GeV/c : 3.7 %
0.50 GeV/c : 4.0 %
1.00 GeV/c : 4.3 %
Pt = 1.0 GeV/c
Pz(input)
0.5 GeV/c : 3.1 %
1.0 GeV/c : 3.8 %
2.0 GeV/c : 4.2 %
Pt = 2.0 GeV/c
Pz(input)
1.0 GeV/c : 3.7 %
2.0 GeV/c : 4.8 %
4.0 GeV/c : 5.2 %
Pz reconstruction

## Slide 29
To Improve the Momentum Resolution -- using a 2nd iteration
Pt(input) 1st iteration 2nd iteration
0.2GeV/c : 0.195 ±0.0068 0.195±0.0068
0.5GeV/c : 0.5 ±0.0212 0.5 ± 0.0164
1.0GeV/c : 0.99 ±0.0595 1.0 ± 0.0317
2.0GeV/c : 1.85 ±0.213 2.0 ± 0.073
Pt(GeV/c)
Pt(GeV/c)
1st iteration
2nd iteration
x
y
xc, yc, R

## Slide 30
Pz reconstruction
Pt = 0.5 GeV/c
Pz(input)
0.25 GeV/c : 3.7 %
0.50 GeV/c : 4.0 %
1.00 GeV/c : 4.3 %
Pt = 1.0 GeV/c
Pz(input)
0.5 GeV/c : 3.1 %
1.0 GeV/c : 3.8 %
2.0 GeV/c : 4.2 %
Pt = 2.0 GeV/c
Pz(input)
1.0 GeV/c : 3.7 %
2.0 GeV/c : 4.8 %
4.0 GeV/c : 5.2 %
z(cm)
Φ