## Slide 1
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015
Photosensor
APD
Preamplifier
APFEL (GSI)
Data Concentrator
16-ch
ADC
64-ch, 14-bit
80-MSPS
ADC for EMC
- PANDA EMC Readout System
Photosensor
VPTT
Preamplifier
Basel
3,600
11,952
47,808
14400
Ca. 1,000
Compute Node
Compute Node
Compute Node
65

## Slide 2
2008
16-ch, 12-bit
160 MSPS ADC
Used for the first tests, sold to WIENER
2010
16-ch, 2GBit/s
Optical Data Concentrator
Used in many experiments including WASA, KLOE2
2011
16-ch, 14-bit
125 MSPS ADC
Virtex-5
Used for evaluation of DSP algorithms
2012
32-ch, Dual-range, 14-bit
80 MSPS ADC
Virtex-6
Used for first data taking and durability tests
2013
64-ch, 14-bit
80 MSPS ADC
Kintex-7
Close-to-final prototype
ADC for EMC
- SADC development for PANDA
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 3
ADC for EMC
- ADC_64K
ADC Model | ADC_32DR | ADC_64V |  | ADC_64K
No. of channels | 32 (64) | 64 |  | 64
Sampling rate | 80-125 MSPS |  |  | 
Input coupling | DC, positive, negative, diff |  |  | 
Resolution (ampl) | 14-bit dual range | 14-bit |  | 
Input Connector | uFL | Samtec |  | 
Baseline | 0V |  |  | 
Input range (dual) | ±1.0V, ±60 mV | ±1.0V, ±100 mV |  | 
Noise | 100uV |  |  | 
Data retention/ch. | 25us |  |  | 
Input filter | Active-filter/Amplifier |  | CR-passive | Active filter/Amplifier
Interface | Optical, SFP, LC-type, 2 Gbit/s |  |  | 
Feature extraction: |  |  |  | 
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 4
ADC for EMC
- ADC_64K_2
ADC_64K_2
List of recent changes/improvements
Overall error correction
Input can be galvanically de-coupled from the ground
Improved analog/digital ground separation
All low-voltage power supplies can be distributed via backplane connectors
Space optimization
Baseline shifting (?)
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 5
ADC for EMC
- Common Platform
uTCA Carrier board
AMC Connector
FMC Mezzanine Board
FPGA
(XC7KU040)
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
SFP+
uTCA Carrier board
AMC Connector
Custom Mezzanine Board
16-ch. ADC
(8 * AD9250)
16-ch. AMP/SHP
(16 * LTC6403)
PLL
(LMK
04806)
FPGA
(XC7KU040)
SFP+
Optical
Data Concentrator
Shashlyk
250 MSPS
14-bit ADC
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 6
ADC for EMC
- Data Concentrators
VME64x
AMC (uTCA)
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 7
ADC for EMC
- Stacked SFP cages
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 8
ADC for EMC
- Data Concentrators
Stand Alone
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 9
ADC for EMC
- Schedule
 | 2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
EMC SADC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ADC tests |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final version production |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Firmware development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Radiation immunity test |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
First production batch |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Batch testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Batch burn-in |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Partial assembly |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Second production batch |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final implementation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EMC Data Concetrators |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DC design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DC testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototype production |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Batch production |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
System testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 10
ADC for EMC-Endcap
- Manpower
Manpower
Uppsala
Hardware design - Pawel Marciniewski
System integration - Postdoc
Stockholm
Firmware - PhD
KVI Groningen
Firmware - Peter Schakel
Uni Bonn
Firmware/Integration - PhD (Johannes Muellers)
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015

## Slide 11
ADC for EMC-Endcap
Thank You !
Pawel Marciniewski, PANDA DAQ Workshop, GSI 19.02.2015