Hardware AFCK
Wojciech M. Zabołotny
Institute of Electronic Systems, Warsaw University of Technology
Based on materials provided by Grzegorz Kasprowicz (IES WUT)

---
Requirements for DPB boards
- The Data Processing Boards are intended to be an important component of the CBM readout chain and control system
- They should concentrate and possibly preprocess data received from the front-end electronics, before sending them via long optical links to FLES
- They should provide control (both fast and slow) for FE electronics
- They should distribute reference clock and timing to the FE electronics

---
CBM Data Flow (ASIC based FEE)
CBM Data Flow (ASIC based FEE)
15-30m
~700m
on/near Detector
CBM ‘Bunker’
'Green Cube'
HUB
GBT
FLIB
FLES
DPB
ASIC
'opto'
Data&
Control
Clock &
Data &
Control
Data
clock
ECS
TFC
Author: W.F. Mueller
DCS
DCS
Clock &
Sync
Cu
optical
Ethernet
Control
DCS
STS,TRD,MUCH,…

---
Requirements for DPB boards
- The Data Processing Boards are intended to be an important component of the CBM readout chain and control system
- They should concentrate and possibly preprocess data received from the front-end electronics, before sending them via long optical links to FLES
- They should provide control (both fast and slow) for FE electronics
- They should distribute reference clock and timing to the FE electronics
- From the above requirements we can see, that the DPB boards should provide quite complex communication capabilities
- For prototyping we needed versatile board, allowing to check and verify different concepts, related to possible solutions of communication interfaces and associated firmware

---
MTCA.4 (for Physics) as DPB platform
- Micro TCA Carrier Hub 1 (MCH1) with clocking, Ethernet switch is standard interface.
- 12x custom AMC with FPGA and 6 QSFP optical transceivers. On mid-height AMC.0 double-width board, one can fit 24 + 8 optical links into it. Optionally, one of AMC implements WR core and acts as a timing source. 8 GTX ports are routed to the RTM connector.
- Rear Transition Module (RTM) can be used to further extend number of optical links
- JTAG Switch Module. Used to communicate between MCH1, MCH2 and 12 AMCs for remote debugging (chipscope) and FPGA upgrade
- MCH2 - optional, redundant carrier hub with White Rabbit switch, crosspoint switch, low jitter clock distribution circuit and JTAG master port. WR management port can be connected to the general Ethernet network
- Optional AMC with 5 White Rabbit ports (SFPs). In this configuration, the crate may also perform function of WR switch
- MTCA.4, 8U crate with JTAG module (JSM), redundant power supply module and dual fan tray. VT811 from Vadatech is recommended.
- Optional AMC CPU with x86 Intel processor, connected do all AMCs using PCIe interface via MCH PCIe switch
- Optional RTM modules with SFP+ or QSFP connectors

---
Existing AFC board
- There was existing Open Hardware AMC FMC Carrier (AFC) board
- Artix based, flexible board in MTCA standard
- After replacement of Artix FPGA with bigger and faster Kintex, and adding even more flexible clocking and communication functionalities it was converted to AFCK, which may be used for development of DPB

---
AFCK board
- Available as Open Hardware solution on OHWR website
- Ready to work in the MTCA crate, but usable also in stand alone mode
- This is a prototyping platform, not a final DPB solution!

---
Programmable resources
- Module Management Controller (MMC) - LPC1764FBD100 – software may be modified by the user
- Xilinx Kintex 7 325T FFG900 FPGA
  - 326080 logic cells (50950 slices)
  - 840 DSP slices
  - 890 1kb BRAMs, 10 CMTs, 1 PCIe, 16 GTX

---
Memory resources
- 2 GB(16 Gb) of DDR3 SDRAM with 32-bit interface and 800 MHz clock – for huge amount of data requiring relatively slow access
- SPI Flash for FPGA configuration (accessible from MMC)
- SPI Flash for user data storage
- EEPROM with MAC and unique board ID
- 16020 kb of data in FPGAs BRAMs – for data requiring high speed parallel access

---
High speed communication capabilities
- 2 HPC connectors for 2 single width FMC or one dual width FMC
  - Up to 4 GTXs may be routed to each FMC
  - In the prototype: GTXs in FMC1 are proven to work at 10 Gbps, while GTXs in FMC2 up to 5 Gbps (in next revision higher speed in FMC2 should be achievable)
- GTXs available in FMC connectors may be optionally routed to the RTM connector
- Another 8 GTX transceivers are available at AMC FP ports
  (in MTCA backplane)

---
Other connectivity functions
- Mini USB connector connected to MMC
- Mini USB with UART converter connected either to FPGA or to MMC
- SATA connector connected to AMC PORT 2 and 3, which may be routed to FPGA GTX

---
Flexible clocking
- Why do we need flexible clocking?
- Different clock domains:
  - GBT-FPGA – 120MHz or 40MHz
  - 1 Gbps Ethernet/WR – 125 MHz
  - 10 Gbps Ethernet – 156.25 MHz
- Clock distribution circuit compatible with White Rabbit
  - Based on CDCM61004RHBT and Si57X
- Jitter cleaner allowing to use clock recovered from GTX receiver to drive GTX transmitter
- Clock crossbar with 16 inputs and 16 outputs

---
Other functions
- Flexible JTAG
  - The JTAG chain uses the TI SCANSTA JTAG switch, allowing to access either main FPGA or FMC cards
- Monitoring capabilities
  - Temperature measurement: FMC1, FMC2, power supply, FPGA core, DDR memory
  - Monitoring of voltage and current in all FMC buses

---
1
2
3
4
FMC1_IPMI
FMC2_IPMI
IPMI
IPMI.SchDoc
HeightUnderFMC
FPGA_RESETn
HeightRuleRoom1.9mm.SchDoc
I2C_CPU
i
i
FPGA_RESETn
I2C
CP U _ I 2C:
OK
UPDATEn
1010
111
MCP-EEPROM
UPDATEn
RESETn
FTG1
FTG2
1101
111
MCP-RTCC
RESETn
I2C1
ADD
I2C1
ADDRESS
1001
111
TEMP_ADC0
1001
110
TEMP_ADC1
FTG3
FTG4
MISC1
IPMB
MISC1
IPMB
1001
101
TEMP_ADC2
I2C2
PM
1001
100
TEMP_ADC3
I2C2
PM_control
1001
011
Cross-point
MISC2
FTG5
FTG6
A
MISC2
A
1001
000
MAX6642
RTM_CON
I2C_Si57
SCN_ENn
I2C_Si57
ENABLE#
100 0
000
INA_ADC0
RTM_CON.SchDoc
FTG7
FTG8
100 0
001
INA_ADC1
EN_RTM_JTAG
TCLK_A_C_SEL
100 0
010
INA_ADC2
UUART
SCN
RTM_SDA
RTM_SDA
SCN
100 0
011
INA_ADC3
USB_UART.SchDoc
100 0
100
INA_ADC4
RTM_SCL
RTM_SCL
100 0
101
INA_ADC5
FSPI
RTM_PS#
RTM_PS#
SPI_FPGA
TxD
SDRAM
FTMP
FPGA_I2C
FPGA_THERM
RxD
SDRAM.SchDoc
ASATA
AMC_CON
FPGA.SchDoc
FPGA
AMC-SATA.SchDoc
AMC_Connector.SchDoc
RTM_MP
SDRAM
FPGA_I2C
FPGA_THERM
FDDR
JTAG
SDRAM
SPI_FPGA
ADDRESS
PORT3_LVDS
PWRA
RTM_FPGA_CLK1
RTM_FPGA_CLK1
PORT3_LVDS
PORT3_LVDS
IPMB
PORT2
PWRB
RTM_FPGA_CLK2
RTM_FPGA_CLK2
PORT2_MGT
PORT2_MGT
PORT2
PORT2
PORT3
RTM_IO[13..0]
RTM_IO[13..0]
PORT3_MGT
PORT3_MGT
PORT3
PORT3
SFP_GTP
SFP_GTP
SFP_GTP
ENABLE#
RTM_LVDS
TxD
RTM_LVDS
RTM_LVDS
RxD
RTM_SYNC_CLK
PORT0
PORT0
PORT0
HPC1
FPGA_RESETn
PORT1
FPGA_RESETn
PORT1
PORT1
FMC_connector.SchDoc
B
FABRIC_CLK
B
DP1
MISC
DP
DP1
TELECOM_CLK
LA1
PIPE1
I2C
LA
LA1
FAT_PIPE1
FAT_PIPE1
HA1
PIPE2
3P3VAUX
HA
HA1
FAT_PIPE2
FAT_PIPE2
HB1
GND
GA0
HB
HB1
AMC_P2P
AMC_P2P
GBT1
GND
GA1
GBT_CLOCK
GBT_CLOCK1
LVDS_PHY
VREF1
VREF
VREF1
M - L V DS
PHY.SchDoc
CLKS1
MLVDS_F
MLVDS_A
FMC1_P3V3
P3V3
FMC_CLOCKS
MLVDS_FPGA
MLVDS_FPGA
MLVDS
MLVDS
JTAG1
PVADJ1
VADJ
JTAG
POWER
AJTAG
JTAG
HPC2
CLK_MGT
Clock_management.SchDoc
FMC_connector.SchDoc
TCLK_A_C_SEL
DP2
PLL_CTRL
MISC
DP
DP2
PLL_CTRL
PLL_CTRL
LA2
FPGA_CLK
I2C
LA
LA2
FPGA_CLK
FPGA_CLK
HA2
FMCC1
3P3VAUX
HA
HA2
FMC1_FPGA_CLK_IN
FMC1_FPGA_CLK_IN
R124
3P3VAUX_R
HB2
FMCC2
GA0
HB
HB2
FMC2_FPGA_CLK_IN
FMC2_FPGA_CLK_IN
1%
GBT2
MGT
0
C
GND
GA1
GBT_CLOCK
GBT_CLOCK2
MGT_CLK
MGT_CLK
C
VREF2
VREF
VREF2
FABRIC_CLK
FJTAG
FPGA_JTAG
TELECOM_CLK
FMC2_P3V3
P3V3
FMC_CLOCKS
FMC1_CLOCKS
RESETn
PVADJ2
VADJ
JTAG
RESETn
JTAG_Configuration.schdoc
JTAG_CONF
POWER
FMC2_CLOCKS
UPDATEn
FMC_JTAG1
JTAG
UPDATEn
Copyright
CNPEM
2012.
I2C_Si57
RTM_JTAG
I2C_Si57
JTAG2
I2C_CPU
FMC_JTAG2
FPGA_JTAG
I2C
Thi s
d ocument at ion
describes
Open
Hardware
and
i s
licensed
under
the
CERN
O HL
v.1.1.
You
may
redi st ri but e
and
m odify
this
EN_RTM_JTAG
SCN
RTM_SYNC_CLK
document at io n
under
the
terms
o f
the
CERN
OHL
v.1.1.
(http://ohwr.org/CERNOHL).
This
documentation
is
distributed
WITHOUT
ANY
EXPRESS
OR
IMPLIED
WARRANTY,
PWR_MGT
INCLUDING
OF
MERCHANTABILITY,
SATISFACTORY
POWER_Management.SchDoc
QUALITY
AND
FITNESS
FOR
A
PARTICULAR
PURPOSE.
I2C_CPU
Please
see
t h e
CERN
O HL
v.1.1
for
applicable
conditions.
I2C
POWER2
POWER2
POWER1
POWER1
PM_control
RTM_MP
RTM_PWRA
Title
D
D
RESETn
RESETn
Size
Number
Revision
CLKS2
A4
Date:
2014-12-13
Sheet
of
File:
D:\Users\..\AMC_FMC_Carrier.SchDoc
Drawn
By:
1
2
3
4

---
Modes of operation
- The AFCK board may be used in two modes:
  - In the standard MTCA crate
  - In the stand alone mode. In this case only a single 12V power supply is necessary.

---
Firmware done up to now
- IPbus core successfully ported – control of board via Ethernet is working
- Transmission via 4 10 Gbps links through FMC1, using the FADE protocol done
- Porting of the FPGA-GBT core to AFCK board done
- Porting of the WR core to the AFCK board – in progress
- STS-XYTER protocol tester (which includes significant parts of future DPB firmare) – developed on KC705, porting to AFCK – in progress

---
Thank you for your attention!