## Slide 1
Status of the PANDA Barrel DIRC
1GSI Helmholtzzentrum für Schwerionenforschung GmbH, Darmstadt
2Goethe-Universität Frankfurt
Marko Zühlsdorf1,2
for the PANDA Cherenkov Group
5th HIC for FAIR Physics Day Expert Group 3
Outline
PANDA DIRC introduction
Resolution requirements
Optical components
Electronic components
Summary

## Slide 2: AntiProton ANnihilation at DArmstadt
12 m
Hadron physics experiment at FAIR
Cooled antiprotons up to 15 GeV/c on a fixed target
Wide range of fields (e.g. charm physics, exotics, hypernuclear physics, …)
Target spectrometer and forward spectrometer for almost 4π coverage
target
p

## Slide 3: AntiProton ANnihilation at DArmstadt
Hadronic PID required over large momentum and angular range
Hadronic PID in the target spectrometer covered by two DIRC detectors
Barrel DIRC
  for polar angle range 22° - 140°
  pion/kaon separation up to 3.5 GeV/c
Endcap Disk DIRC
  for polar angle range 5°/10° - 22°
  pion/kaon separation up to 4 GeV/c
PANDA Target Spectrometer
Cumulative kaon phase space coverage for reactions with antiproton momenta 6 GeV/c < p < 15 GeV/c

## Slide 4
Detection of Internally Reflected Cerenkov Light
Condition for Cherenkov radiation:
If always some Cherenkov photons are totally internally reflected for
Propagation to the readout end of the radiator bar
Focused on readout plane
Radiator material: synthetic fused silica
Radiator shape: long rectangular bars
Sensors: single photon sensitive

## Slide 5
PANDA Barrel DIRC
Barrel DIRC is based on the successful BaBar DIRC with important improvements:
Focusing optics Compound lens system for a better Cherenkov angle resolution
Compact photon detectors Smaller expansion volume Better spatial resolution
Fast photon detection Better background reduction Chromatic dispersion correction New reconstruction methods
2.4 m
5 m
PANDA
BaBar
5 m
̴2 m

## Slide 6
Tracking resolution, multiple scattering
Single photon Cherenkov angle Resolution
Number of detected photons
Contribution from image of radiator thickness
Contribution from image of pixel size
Cherenkov angle spread (chromatic)
Barrel DIRC Resolution
At 3.5 GeV/c:
Expected performance:
mrad;

## Slide 7
PANDA Barrel DIRC
Baseline Design (based on BaBar)
80 radiator bars, synthetic fused silica
Bar dimensions: 1.7 cm × 3.2 cm × 240 cm
Focusing optics: lens system
Expansion volume:
  30 cm depth
  Mineral oil
15k channels of MCP-PMT
Photon detection with good time resolution
Radiator
Design Options
Baseline design provides technical solution for PANDA
Alternative designs to improve performance and reduce cost
Readout
Expansion
volume
Focusing optics

## Slide 8: Radiator Requirements and Options
Radiator Quality:
DIRCs have tight mechanical requirements on flatness, squareness, and parallelism of the radiator surfaces
  Surface roughness 10 Å rms
  Squareness 0.5 mrad
  Total thickness variation 25µm
Production difficult, potentially expensive
Using 1 wide plate instead of 5 narrow bars per segment would reduce number of pieces to be polished by factor 5
Worked with vendors in Germany, Russia, USA, and Japan to produce a number of radiators using different fabrication techniques.
125 cm

## Slide 9: Radiator Quality Studies
Autocollimator
Surface studies
Squareness, parallelism studies

## Slide 10: Geometrical Reconstruction
5 narrow bars, unfocused (MC Simulation)
3 wider bars, unfocused
bars
detection plane
20° track polar angle 140°
20° track polar angle 140°
10 mrad 30
10 mrad 30
track azimuth angle
track azimuth angle
Geometrical reconstruction uses location of bar and pixel to determine photon vector in the radiator.
Combinatorial background due to ambiguous solutions.
inspired by BaBar DIRC
plate
detection plane
Works well for narrow bars but fails for wide plates.
Width of radiator not negligible anymore.
side view
top view

## Slide 11: Probability Density Functions
Probability density functions (pdf) can be generated with ~100k Monte Carlo tracks with same parameters and saved in histograms.
22° polar angle
p = 3.5 GeV/c
π
K
In 3 dimensions (x, y, t) hit patterns show differences between particle species
π
K
PMT map, with 5 x 3 sensors, 64 pixels each
x
y
normalized PDF for a specific pixel
π sample
K sample
Inspired by Belle II TOP
MC
Simulation
Likelihood ratio test lnLK-lnLP

## Slide 12: Radiator Shape Studies
Wide plate Narrow bar
1.7 GeV/c pion beam @ GSI 2014
CERN 2012
log(LK )-log(Lπ)
Likelihood ratio test
pions
kaons
Mixed hadron beam, 1.5 GeV/c < p < 10 GeV/c
Beam data
σ = 13 mrad

## Slide 13: Expansion Volume Shape
30 cm
Compact expansion volume using fused silica instead of oil
Better optical properties
Fewer readout sensors/channels needed
Optically independent segments

## Slide 14: Focusing Optics
Simulation
Beam data
Beam data
Fused silica
N-LaK33
Different types of lenses were tested

## Slide 15: Photon Sensors
Requirements:
Single photon sensitivity, low dark count rate
High photo detection efficiency
Fast timing: 100 ps
Operation in magnetic field (1T)
Long lifetime: 0.5 C/cm²/yr
Best candidates: MCP-PMTs
Ongoing ageing tests show
breakthrough in
MCP-PMT lifetime
(Photonis Planacon)
Situation in 2011

## Slide 16: FEE Concept
Trigger Readout Board
TRBv3
NINO Card; PADIWA Card
MCP-PMT connector
4 FPGAs programmed as TDC
<10 ps RMS time precision
700 kHz max trigger rate
67 MHz max hit rate
Close cooperation with CBM RICH group
Amplifier and discriminator card
NINO card, developed in Mainz NINO ASIC
PADIWA, developed at GSI FPGA

## Slide 17: Summary and Outlook
Summary
The Barrel DIRC is a key component of the PANDA particle identification system.
Baseline design with narrow bars and high-refractive lens meets PANDA PID goals.
Cost optimization identified design alternatives (wide plate, solid fused silica camera, compound lenses), validated with simulation and prototype tests.
QA tests of radiator surfaces, validation of different lenses and radiator shapes are ongoing.
Readout electronic is produced and tested in prototype test, using synergies with the HADES DAQ and CBM RICH group.
Outlook
Measure PID performance of design options in mixed hadron beam at CERN in summer 2015.
Decision on a design and PANDA Barrel DIRC TDR (due in early 2016).
The PANDA Cherenkov Group
1