Pattern Recognition FTS
@Cracow University of Technology
work in progress
status report
Jerzy Jaworowski, Krzysztof Korcyl, Mateusz Michałek, Joanna Płażek,
Piotr Poznański

---
Four methods
evaluation of methods:
  1. Pattern Matching
  2. Hough Histogram
  3. Circle-Line-Tangent Filter
  4. Circle-Tangent Region
Final solution may consist of a combination of those

---
Pattern Matching Method

---
Segments and Data Organisation
- FT 1, 2 layers : 1, 2, 7, 8 & 9, 10, 14, 15 (2D)
- Pair (Key, Data) - stored in hash table
  (log2n search time)
- Key: 16 segments (16 bytes - 2 bytes per layer)
- 1 segment – relative tube index on layer (0-131)
- Data: double[2] - a,b (slope-intercept from of linear equation, x=a*z+b)

---
Pattern Generation
- precision 0.01 mm step
- for FT1 segment – 19102 patterns (will reduce < 16000)

---
Pattern Matching
1. If exact pattern found – stop.
2. If not, return first pattern with key not less than searched one (‘close’ pattern).
3. Evaluate mean-square distance between event and close pattern (two different distance measure algorithm’s tested : Levenshtein and custom one).
4. Repeat step 3 for enclosing keys to determine local minimum

---
Hough Histogram Method

---
Segments and Histo Generation
- Implemented for FT 1, 2, 5, 6 (2D)
- using drift circles
- lexical-distance based maxima search

---
Segments and Histo Generation
- TBDaTY:
  - FT3 and FT4 (conformal transformation vs 3D Histogram)
  - 3D (3-4D Histogram?)
  - check efficiency using straw centers instead of drift circles

---
Circle-Line-Tangent Filter Method

---
Method Description
- Method is global FT1 – FT6 (2D)
- Steps:
  1. Choose (any combination of) 3 points from FT3, FT4
  2. Create circumcircle over choosen points
  3. Use filters to verify created circle
- FtsPointZ and FtsPointX used as input by now
- aiming at: using straws centers

---
Filters
1. radius within range <50,5000> cm
2. center far away from beam pipe
3. circle passes through 6 hits
4. circle has tangent in FT5, FT6 which passes through 6 hits
5. circle has tangent in FT1, FT2 which passes through 6 hits

---
Execution in numbers
34 hits generate 5984 and after filtering 84 circles
  1. radius filter droped 3543 circles
  2. circle center filter droped 1840 circles
  3. six point circle (0.010cm cutoff) filter droped 480 circles
  4. FT56 tangent filter (0.800cm cutoff) droped 37 circles
  5. FT12 tangent filter (0.800cm cutoff) droped 0 circles
single threaded, Intel Core i5 M520@2.40GHz 10.18ms

---
Circle-Tangent Region Method

---
Method Description
- Implemented for FT 1, 2, 5, 6 (2D)
- Using most external layer hits in a segment, create paths, where other hits are searched for.

---
issues encountered
(showstopers)
Errors in simulation data:
- wrong straw numbers
- wrong geometry (z-coordinate value mismatch with FTS desciption)

---
Further Investigations
- add 3D (take into account skewed straws)
- add FT3, FT4
- evaluate applicability combination of methods
- once the issue of test data sorted-out will adjust methods and test efficiency
- optimisation and parallelisation