## Slide 1
The PANDA Barrel DIRC with wide radiator plates
GSI Helmholtzzentrum für Schwerionenforschung GmbH, Darmstadt
Goethe-Universität Frankfurt
Marko Zühlsdorf

## Slide 2: Motivation for Plates
Baseline design working solution for PANDA
Alternative designs to improve performance and reduce cost
Radiator
One wide plate instead of 5 narrow bars per segment
Fewer pieces to be polished
Less strict requirements for optical and mechanical quality of side surfaces
Potential significant cost reduction
Expansion volume (camera)
One synthetic fused silica prism per segment instead of oil tank
Better optical properties
Smaller detection surface
Fewer photon sensors needed
Less readout channels
30 cm
125 cm

## Slide 3: Geometrical Reconstruction
radiator
detection plane
20° track polar angle 140°
20° track polar angle 140°
10 mrad 30
10 mrad 30
track azimuth angle
track azimuth angle
Geometrical reconstruction uses location of bar and pixel to determine photon vector in the radiator.
Works well for narrow bars but fails for wide plates
Width of radiator not negligible anymore
5 narrow bars, unfocused (MC Simulation)
3 wider bars, unfocused
inspired by BaBar DIRC

## Slide 4: Geometrical Reconstruction
X-Z projection
many more ambiguities from dispersion
Y-Z projection
4 ambiguities in the prism
4 ambiguities in the bar
z
y
x
Cherenkov angle is reconstructed
but with bad signal/background ratio

## Slide 5: Probability Density Functions
Probability density functions (pdf) can be generated with ~100k Monte Carlo tracks with same parameters and saved in histograms.
22° polar angle
p = 3.5 GeV/c
π
K
In 3 dimensions (x, y, t) hit patterns show differences between particle species
π
K
PMT map, with 5 x 3 sensors, 64 pixels each
x
y
normalized PDF for a specific pixel
π sample
K sample
Inspired by Belle II TOP
MC
Simulation
Likelihood ratio test lnLK-lnLP

## Slide 6: 2014 Prototype Test
122.5 cm
Pion beam
1.7 GeV/c
Prototype
Beam time at GSI; 5 weeks in summer 2014
2014 prototype is similar to a module of the final detector
5 x 3 Planacon MCP-PMT
960 pixels (in total >1200 readout channels)
Wide plate w/ and w/o focusing lens
Narrow bar with different lenses

## Slide 7: Plate Data Analysis
Wide Plate
Simulation:
Geant 4
Radiator plate
Cylindrical lens
120° polar angle
1.7 GeV/c pions
pixelated:
true locations:

## Slide 8: Plate Data Analysis
Wide Plate Data:
Occupancies with cuts on timing and event multiplicity
Simulation predicts
~20 hits/track
Simulation:
120°
Beam data:

## Slide 9: Plate Data Analysis
70° with lens
PiLas time peak positions for
hit time alignment
unaligned:
aligned:
simulation:

## Slide 10: Plate Data Analysis
70° with lens

## Slide 11: Plate Data Analysis
Likelihood Ratio test
T0-fit:
Use the simulated pion data with different
time offsets and perform a Maximum Likelihood fit
on the beam data
Pions Kaons
Photon Yield (no lens)
* * * Data
-- -- Sim
Problems:
Time resolution again worse than expected
High noise/PADIWA oscillations
Discriminator thresholds not determined correctly

## Slide 12: Analytical PDF
Problem:
Can PDF be created efficiently via simulation for each point in track parameter space?
Momentum, hit position, polar angle, azimuth, particle species
High dimensional parameter space, each PDF requires ~100k × 5 simulated particles for hypothesis tests
Without analytical (and fast) generated PDF approach not feasible.
p = 3.5 GeV/c
θ = 22°

## Slide 13: Analytical PDF
All ambiguities from geometric reconstruction are calculated and enter the PDF (after cuts)
→ tj
The widths σj are determined by the propagated uncertainties of refraction index, calculated Cherenkov angle, and track parameters.
Normalizations Aj are proportional to the fraction of φC entering the ambiguity and the number of created Cherenkov photons
Sim
Sim
Calc
Calc
Calc
Calc
Pixel

## Slide 14: Summary and Outlook
Summary
Baseline design of the Barrel DIRC with narrow bars and high-refractive lens meets PANDA PID goals.
Cost optimization identified two design alternatives (wide plate, solid fused silica camera), to be validated with simulation and prototype tests.
Prototype data from the 2014 beam time at GSI shows promising results for radiator plate.
First version of analytically derived probability density functions is finished and feasibility is proven.
Outlook
Beam time scheduled for may and june 2015.
PADIWA noise “features” have to be understood in order to set thresholds properly and achieve good time resolution.
Extensive angular scan with plate will be performed to determine performance.
Thank you