## Slide 1: Electron Beam Profile Monitor measurements of the Montague Resonance in the SNS Ring
W. Blokland*, R. Potts#, S. Cousineau#
* Diagnostics
# Beam Dynamics
Beam Dynamics meets Diagnostics Workshop
4-6 November 2015
Convitto della Calza, Florence, Italy

## Slide 2: Spallation Neutron Source Accelerator
945 ns
Current
1 ms macro-pulse
Current
1ms
Accumulated in the Ring
16.6ms
Current
670 ns
RTBT
Ring
Linac
Spallation Neutron Source (SNS)
  Materials research with neutrons through spallation of protons in mercury
Power on Target | 1.4 MW at 1.0 GeV
Pulse on Target | 1.5 E14 protons (24 µC) in 670 ns
Macro-pulse in Linac | 1000 mini pulses of ~24 mA average over 1 ms at 60 Hz

## Slide 3: Beam Dynamics meets Diagnostics
Beam Dynamics:
  Define and execute experiment
  Simulate experiment
  Benchmark simulation with experiment
Diagnostics:
  Knows how to setup diagnostics devices for measurements
  Knows how obtain beam parameters from raw data
  Provides application to acquire data and generate results
What the..?
Problem:
  Beam profiles are found to be coupled under certain conditions
   Setup to get right beam size on target more complicated

## Slide 4: Beam Dynamics: Space Charge Effects
Hill’s equation with space charge as driving force:
Nominal tune point without space charge
Tune spread due to space charge effects particles differently based on local density
with
Simulation of space effect on tune

## Slide 5: Beam Dynamics: Resonances
Characteristics:
  Sensitive to intensity: stronger with more space charge
  Sensitive to tune-split: stronger with closer tunes
  Observe exchange of RMS widths between planes
Montague Resonance:
2x-2y=0
Turn
Second Order Beam Moments
Vertical
Horizontal
Simulation of space charge effect on RMS width

## Slide 6: Experiment
Conditions SNS Ring:
  Different tune-splits with different beam intensities and stored turns
Required Data:
  Profiles (RMS width) during accumulation and storage
Device | Location | Each Injection | Stored turns | Resolu -tion | Time@1Hz | Time per set*
Wire Scanner | RTBT | Profile point extracted | Adjust ring | 50 -100 pts | 100-200 s | 160 min
Harp | RTBT | Full profile extracted | Adjust ring | 30 pts | 1 s | 40 min
Electron Scanner | Ring !!! | Full profile slice any turn | No adjustment | 50 -100 pts | 5 - 40 s | 30 min
The electron scanner can take a set of data unattended (requires offline analysis)
The wire scanner has the best signal to noise ratio, the harp has lowest resolution
Only the electron scanner can measure directly (no extraction kicker, lattice, etc)
*1 min per profile to setup extraction for RTBT measurements

## Slide 7: Electron Scanner Principle
dy
dx
Quadrupoles
Deflector
Look at the deflected projection of a tilted sheet of electrons:
  Neglect magnetic field (small displacement of projection)
  Assume path of electrons is straight (they are almost straight)
  Assume net electron energy change is zero
Electrons 
Multiple scans
Proton beam
   take the derivative of curve to get the profile

## Slide 8: Electron Scanner Hardware
Electron scanner now covered with magnetic shield
Quadrupoles
Dipoles
Deflector
Electron Gun
Ring Beam Pipe
Screen
HV Transformer
Camera

## Slide 9: Electron Scanner Capabilities
Parameter | Range | Implementation | Dependency
Beam Intensity | 50 nC-25 µC (1*600ns) 10’s mA – 10’s A | 10-100 keV | Geometry (deflection)
Beam Potential | Up to ~20kV | Requires 100 keV electrons | Electron momentum
Bunch Length | > 10’s ns < 10’s ns | Deflector single shot profile Cavity or step per position | Amount of electrons to screen
Beam size | > 5 mm < 5 mm | Parallel projection & screen diverging projection & MCP | Geometry
Rep Rate | < 10’s Hz | Screen and Camera | Fluorescent Tc and power supply
The SNS Ring presents a good operational spot for the electron scanner:
A lower kV setting requires better magnetic shielding
A higher beam potential requires higher kVs (expensive)
Shorter bunch lengths require faster scans e.g. cavity and result in less electrons
A smaller beam size requires lower electron emittance and projection and better sensor resolution and/or diverging projection
A faster rep rate requires a more expensive electron gun HV supply

## Slide 10: ES: Profile generation
Setup of accelerating voltages, cathode current, deflector voltages, dipoles, quadrupoles, and timing.
Images
Take derivative to generate profile
Multi profiles show bunches in the ring during accumulation
But for beam dynamics more is needed:
Automatic acquisition of defined turns and slices
Offline quantitative analysis
Visualize large amounts of data
Find the curve

## Slide 11: ES: Offline analysis
  Handle large amount of data
  Analyze images in stages for quick re-analysis
    Image to profile (most time-intensive), profile to accumulated profile, profile to RMS
  Visualize and export analysis results
    Results plotted vs. turns
    Verify operation of electron scanner and data

## Slide 12: Electron Scanner imperfections
This is a prototype:
Projection not through center of quads:
  Beam pipe of vertical ES not straight
  Projection is not a straight line when no beam
Aperture is too small
  Need to extend analysis beyond marker
  Rotated vertical deflection
Artifacts interfere with image
  Blobs of un-deflected electrons
  Background of lower momentum electrons
  New HV power supply to be installed
These imperfections make the setup (~1 hr. for new conditions) and analysis more time-consuming and also restrict beam conditions (width)
Before
After
background
blobs
Deflection past markers
Increased aperture between markers by rotating the deflectors

## Slide 13: Analyzing: Image to Profile
Find curve in image then take derivative to find profile:
  Use spline fit to reduce noise but not predispose to a certain profile shape
  Shows slope
  Show effect of gap in trace due to marker
Marker
Slope
  ~1.2µC beam

## Slide 14: Analyzing the data: Composite Profile
From profile slice to composite profile:
  Shows slope
    Subtract base trace
  Show effect of gap in trace due to marker
    Exclude if no deflection
Animation of analyzing all profiles in this data set (40 turns with each 40 slice profiles of ~1.2µC total accumulation)

## Slide 15: Analyzing the data: display
The Electron Scanner shows the evolution of transverse profile during the accumulation (and even profiles within the bunch)
Qualitative idea of what is going on. But we need additional quantitative results for beam dynamics
  Checking the electron scanner profiles
Beam accumulation for the first 100 turns

## Slide 16: Calibrating the scale
Convert image pixels to mm in the profile
  Horizontal projection isn’t quite at 45 degrees  small correction
  Vertical deflector intentionally rotated  large correction

## Slide 17: Checking the obtained profiles
Integrate profile to obtain charge
  we clearly see the linear increase in charge up to turn 100 and the charge matches beam accumulation even as profiles are changing (whole profile is captured)
Track centroid through accumulation and storage
  Centroid is stable
Calculate RMS width

## Slide 18: Analyzing the data: Numerical results
Plot the charge, centroid, and RMS width for both planes in same plot
Allow user to view evolution of profile

## Slide 19: Ring coupled beam study: Initial results
1.2 µC
0.7 µC
0.4 µC
Split tune does not show RMS oscillation
1.2 µC
Case | Hor Tune | Ver Tune | dTune
Equal | 6.19944 | 6.19781 | 0.00163
Split | 6.20898 | 6.16860 | 0.04038

## Slide 20: Ring coupled beam study: initial results
Damped oscillator: check its period changes vs charge
Fit to function:
a*exp(-f*x)*sin(b*x +c)+d
 Lower charge seems to have longer and stronger exchange of RMS
1.2 µC
0.7 µC
0.4 µC
1.2 µC
Split tune

## Slide 21: Beam Dynamics initial conclusions
Probably not Montague Resonance because coupling stronger at lower intensities
Looks like linear lattice coupling, but this was corrected before experiment started with skew quads
Investigation ongoing…. (e.g. mapping profiles from RTBT to Ring, simulations, verifying calibration)

## Slide 22: Beam Dynamics meets Diagnostics
Good example of how to use a complex diagnostic
Has advantages over wire scanner
  Can handle high intensity
  Scans faster
  Not interceptive  No beam losses
The Beam Dynamics experimental needs pushed the development of the electron scanner software
  Manage many turns of data for acquisition and display
  Further verification of analysis
At SNS, the Beam Dynamics and Diagnostics meet every day (Espresso!)