## Slide 1
Single Particle Detection
with a Resonant Cavity
Markus Steck, GSI Darmstadt

## Slide 2: The GSI Accelerators: UNILAC, SIS18 and ESR
SIS18
UNILAC
ESR
Ion sources
SIS-18
upgrade
for FAIR
beams to SIS100
IH structure
2
FRS

## Slide 3
Storage of stable ions and RIBs in the energy range 3-550 MeV/u
Stochastic cooling (  400 MeV/u)
Electron cooling ( 3 - 430 MeV/u)
Internal gas jet target
Deceleration (down to 3 MeV/u)
Fast and slow extraction
Beam accumulation
Multi charge state/ multi component operation
Schottky mass spectrometry
Isochronous mode
The ESR Storage Ring

## Slide 4
from GSI Scientific Report 1995
standard capacitive Schottky pick-up
broad band ( 1-150 MHz)
resonant circuit (30-80 MHz)
Single Particle detection in ESR
single 182W ion
cooled by electron cooling  recombination 74+  73+
Interacting with internal target  ionization 73+  74+
Schottky signal power P = N (Qe)2 f02

## Slide 5
Schottky Mass Spectrometry
Injection of cocktail rare isotope beam from fragment separator FRS
Cooling (stochastic pre-cooling + final electron cooling)
Achieved momentum spread (p/p = 510-7, f/f = 210-7)
Two single ions !
broad band spectrum
narrow band spectrum

## Slide 6
Radioactive Decay of a Single Particle
low signal to noise ratio
time resolution is limited
averaging over many seconds
from GSI scientific report 2000/2001
frequency/Hz - 59950000
Schottky noise signal of rare isotopes after stochastic and electron cooling

## Slide 7
Design Considerations for a Schottky Resonator in the ESR
increased sensitivity to single ions
faster detection of single ions
UHV compatibility
decoupling of the resonator from the beam at high intensity
variable resonant frequency
frequency band width up to one percent
choice of frequency larger sensitivity <=> better time resolution (lower frequency) (higher frequency)
mechanical dimensions of cavity

## Slide 8
Pillbox Type Cavity
resonant frequency  244 MHz, radius 30 cm
TM010 mode
cylindrical symmetry
coupling to the longitudinal electric field generated by the particle
SUPERFISH
simulation
CST-MAFIA
simulation
magnetic field

## Slide 9: Signal to Noise Ratio of a Single Particle
Qunloaded = 1130
Rs(=0.7 ) = 40 k
P (q=1) = 1 × 10-21 W
f/f = 10-6 (extremely cool beams, single particle)
dPnoise/df = -173 dBm = 5 × 10-21 W/Hz
Pnoise < P(q)  q > 31
single particle power on resonance:

## Slide 10: Basic Resonator Design
flanges for frequency tuning
ceramic gap
dismountable assembly
two resonator halves,
air filled
flange for coupling loop

## Slide 11
New Schottky Resonator
noise floor
Transit time factor
(sensitivity vs velocity )
Frequency 244  2.5 MHz
Quality factor (unloaded) 1130
Quality factor calc. 1940/3837
R/Q exper. 50.7 
T =

## Slide 12
Dielectric losses in ceramics
Losses in stainless steel inside vacuum chamber
Partially exposed construction steel surface
no problem, as larger band width is requested anyhow
Reduction of Quality Factor

## Slide 13
142 59+
Pm
142 59+
Nd
142 59+
Pm
Nd
142 59+
Old Schottky
Pick-up
Stripline electrode
with resonant circuit at 30th harmonic
of revolution frequency
New Resonator Cavity
(pill box type)
124th harmonic
of revolution fequency
New Schottky Resonator

## Slide 14
Measurement of Cooling Process
time 32ms/u
frequency 31.25 Hz/u @ 244 MHz
Electron cooling
Stochastic cooling
+
Electron cooling
Electron cooling
Cooling of
142Pr59+ at 400 MeV/u

## Slide 15
Measurement of Radioactive Decay
Stochastic cooling
no cooling
Electron cooling
142Pm59+
142Nd59+
time 32ms/u
frequency 31.25 Hz/u @ 244 MHz
Electron cooling

## Slide 16
Measurement of Electron Capture Decay
142Pm60+ + e-  142Nd60+ + e
isotropic emission of neutrino  transfer of energy 90 eV to daughter ion

## Slide 17
e
recoil
Beam
direction

CM
pR cos()
f = ± 3.91 kHz
(120 ch)
e emitted forward
e emitted backward
Three Parent He-Like 142Pm Ions

## Slide 18
Revolution Frequency Difference f of the Recoils just after Decay: f = fdec - fcool
Vd
↓
Vd
↓
decay at f = fd (cool)
decay at
f = fp(cool)
From vd and md one gets the momentum of the
(monochromatic) neutrino: (pc)d = md cvd = (pc)
From mp and md one gets its energy: E = (mp – md) c2 and then β = E /(pc)
For a (longitudinally) unpolarized beam the
distribution should have a rectangular shape
For a (steadily controlled) polarized beam the distribution would provide the helicity of the neutrino

## Slide 19
Stability of Revolution Frequency
variations of revolution frequency over one week:   310-6
stability of magnet power converters
stability of electron beam (energy)
frequency variation over one week determined from the peak position
FFT of temporal variation

## Slide 20
Analysis of Cooling Process
forward emission (daughter 2)
 deceleration
backward emission
(daughter 1)
 acceleration
142Nd59+ 400 MeV/u

## Slide 21
Analysis of Cooling Process
Chart: time [s]
| 0 | 4.2000000000000003E-2 | 8.4000000000000005E-2 | 0.126 | 0.16800000000000001 | 0.21000000000000002 | 0.252 | 0.29400000000000004 | 0.33600000000000002 | 0.378 | 0.42000000000000004 | 0.46200000000000002 | 0.504 | 0.54600000000000004 | 0.58800000000000008 | 0.63 | 0.67200000000000004 | 0.71400000000000008 | 0.75600000000000001 | 0.79800000000000004 | 0.84000000000000008 | 0.88200000000000001 | 0.92400000000000004 | 0.96600000000000008 | 1.008 | 1.05 | 1.0920000000000001 | 1.1340000000000001 | 1.1760000000000002
Daughter1 | 2598.778 | 2241.148 | 1883.518 | 1573.572 | 1358.994 | 1025.206 | 834.47 | 667.576 | 548.366 | 405.314 | 333.788 | 238.42 | 166.894 | 119.21 | 71.526 | 71.526 | 47.684 | 23.842 | 0
Daughter2 | 1597.414 | 1358.994 | 1096.732 | 810.628 | 619.892 | 476.84 | 262.262 | 190.736 | 143.052 | 95.368 | 95.368 | 47.684 | 23.842 | 0
Chart: g2Dv [m/s]
| 7382.507141 | 6280.8903250000003 | 5298.654227 | 4428.7003999999997 | 3663.9304000000002 | 2997.2457829999998 | 2421.5481020000002 | 1929.738914 | 1514.7197739999999 | 1169.392235 | 886.65785500000004 | 659.4181873 | 480.57478739999999 | 343.02921049999998 | 239.68301159999999 | 163.43774579999999 | 107.1949683 | 63.856234129999997
Daughter1 | 3.51 | 3.14 | 2.79 | 2.46 | 2.16 | 1.87 | 1.61 | 1.37 | 1.14 | 0.944 | 0.766 | 0.609 | 0.474 | 0.36 | 0.267 | 0.196 | 0.147 | 0.118
Daughter2 | 2.9 | 2.52 | 2.16 | 1.83 | 1.52 | 1.25 | 0.992 | 0.766 | 0.565 | 0.391 | 0.243 | 0.121
force F =
relative velocity 2v =
theoretical cooling force

## Slide 22
Analysis of Cooling Process
Chart: g2Dv [m/s]
| 24457.807499999999 | 23609.693190000002 | 22736.18304 | 21840.410179999999 | 20925.507750000001 | 19994.60888 | 19050.846699999998 | 18097.354340000002 | 17137.264940000001 | 16173.71162 | 15209.827520000001 | 14248.74577 | 13293.59951 | 12347.521849999999 | 11413.64594 | 10495.10491 | 9595.0318889999999 | 8716.5600080000004 | 7862.8224 | 7036.9521960000002 | 6242.0825299999997 | 5481.3465319999996 | 4757.8773339999998 | 4074.8080690000002 | 3435.2718679999998 | 2842.4018639999999 | 2299.3311870000002 | 1809.1929700000001 | 1375.120345 | 1000.246444 | 687.70439850000002 | 440.62734030000001
Mother1 | 2.52 | 2.6 | 2.67 | 2.73 | 2.79 | 2.83 | 2.87 | 2.89 | 2.91 | 2.91 | 2.91 | 2.89 | 2.87 | 2.84 | 2.8 | 2.75 | 2.69 | 2.62 | 2.54 | 2.45 | 2.35 | 2.24 | 2.12 | 2 | 1.86 | 1.72 | 1.56 | 1.4 | 1.22 | 1.04 | 0.846 | 0.644
Mother2 | 3.49 | 3.46 | 3.43 | 3.39 | 3.34 | 3.28 | 3.22 | 3.15 | 3.07 | 2.99 | 2.9 | 2.8 | 2.69 | 2.58 | 2.46 | 2.33 | 2.2 | 2.06 | 1.91 | 1.75 | 1.59 | 1.42 | 1.24 | 1.06 | 0.864 | 0.665
Mother3 | 2.18 | 1.83 | 1.5 | 1.21 | 0.958 | 0.737 | 0.549 | 0.395 | 0.274 | 0.188 | 0.135
Mother4 | 1.56 | 1.37 | 1.19 | 1.02 | 0.87 | 0.734 | 0.613 | 0.506 | 0.415 | 0.338 | 0.276
cooling force depends on initial
parameters of the ion (single particle emittance)
ions start with different relative velocities (longitudinal and transverse)
Chart: time [s]
| 0 | 4.2000000000000003E-2 | 8.4000000000000005E-2 | 0.126 | 0.16800000000000001 | 0.21000000000000002 | 0.252 | 0.29400000000000004 | 0.33600000000000002 | 0.378 | 0.42000000000000004 | 0.46200000000000002 | 0.504 | 0.54600000000000004 | 0.58800000000000008 | 0.63 | 0.67200000000000004 | 0.71400000000000008 | 0.75600000000000001 | 0.79800000000000004 | 0.84000000000000008 | 0.88200000000000001 | 0.92400000000000004 | 0.96600000000000008 | 1.008 | 1.05 | 1.0920000000000001 | 1.1340000000000001 | 1.1760000000000002 | 1.218 | 1.26 | 1.302 | 1.3440000000000001 | 1.3860000000000001 | 1.4280000000000002 | 1.4700000000000002 | 1.512 | 1.554 | 1.5960000000000001 | 1.6380000000000001 | 1.6800000000000002 | 1.7220000000000002 | 1.764
Mother1 | 8702.33 | 8392.384 | 8106.28 | 7700.966 | 7367.178 | 7033.39 | 6699.602 | 6437.34 | 6103.552 | 5745.922 | 5435.976 | 5054.504 | 4768.4 | 4458.454 | 4100.824 | 3719.352 | 3385.564 | 3051.776 | 2813.356 | 2479.568 | 2217.306 | 1931.202 | 1621.256 | 1406.678 | 1192.1 | 977.522 | 810.628 | 619.892 | 476.84 | 333.788 | 262.262 | 214.578 | 190.736 | 143.052 | 71.526 | 23.842 | 0
Mother2 | 7414.862 | 6961.864 | 6580.392 | 6055.868 | 5722.08 | 5412.134 | 5006.82 | 4625.348 | 4220.034 | 3910.088 | 3576.3 | 3290.196 | 2980.25 | 2622.62 | 2241.148 | 1931.202 | 1692.782 | 1454.362 | 1192.1 | 1072.89 | 858.312 | 691.418 | 500.682 | 381.472 | 262.262 | 190.736 | 143.052 | 95.368 | 71.526 | 0
Mother3 | 1192.1 | 953.68 | 715.26 | 572.208 | 452.998 | 381.472 | 286.104 | 238.42 | 214.578 | 166.894 | 143.052 | 119.21 | 119.21 | 95.368 | 71.526 | 23.842 | 0
Mother4 | 1049.048 | 858.312 | 667.576 | 596.05 | 500.682 | 381.472 | 309.946 | 214.578 | 166.894 | 143.052 | 95.368 | 71.526 | 47.684 | 23.842 | 0
142Pm59+ 400 MeV/u

## Slide 23
the ion velocity vion in many cases exceeds the electron velocity ve (due to the spread of the ion distribution)
for single ions this contribution vanishes and allows measurements of the cooling force for well controlled ion parameters
vion  10-6  v0  2×102 m/s
ve  103 – 105 m/s
Analysis of Cooling Force
Parkhomchuk formula of electron cooling force:
longitudinal
transverse

## Slide 24
Xe54+ 15 MeV/u
with internal gas target operation
dp/p=110-3
High Sensitivity Measurement of Interaction with Matter
dp/p=110-5
40 s
deceleration in residual gas
deceleration in internal target
Measurement of single ions allows the measurement of target effects without the uncertainty introduced by the beam spread
time

## Slide 25
Isochronous Mode of the ESR for Mass Measurements of Short-lived Isotopes
operation at transition energy:
negative dispersion in straight section
makes revolution frequency
independent of the beam momentum
 = 0 (  = t, transition energy t )
measurement of
transition energy
by variation of beam energy
energy
frequency
 < t
 = 0  = t
 > t
from PhD thesis O.Kovalenko

## Slide 26
ion is lost after a few thousand turns due to energy loss in foil,
 a few milliseconds of storage
ToF Detector
= - =
time / µs
voltage / a.u.
(if  = t)
passage of single ions
a Schottky detector with millisecond measuring time should be competitive or even superior

## Slide 27
(fLo = 245924.5 kHz)
Resonator Measurement in Isochronous Mode
decay
detection of the decay of a radioactive ion in the isochronous mode
injected with a momentum spread of  0.2  (no cooling)
m/m = 1.88 10-5 f/f=1/t2 m/m = 9.2  10-6
 f = 2.3 kHz

## Slide 28
Resonance frequency : 173MHz (TM010)
Tuning range : ±1.5MHz
Shunt Impedance Rsh : 161kΩ
Quality factor Q0 : 1880
Ceramic tube size: 290mmΦ, 15mm thick
from COOL‘15:
Y. Yamaguchi et al.
Commissioning of the Rare-RI Ring
at the RIKEN RI Beam Factory
Schottky Resonator at the RIKEN Rare-RI Ring
deceleration in the residual gas of a single ion in isochronous mode
78Kr36+ 168 MeV/u

## Slide 29
SIS100: intense, primary heavy ion beams up to 2.7 GeV/u
SuperFRS: RIB production
CR: isochronous mass measurements of RIBs with energies 400-740 MeV/u
CRYRING@ESR: low energy ions and RIBs from ESR
p-linac
SIS18
SIS100
UNILAC
pbar target/ separator
HESR
SuperFRS
FAIR - Modularized Start Version (MSV)
CR
ESR
CRYRING @ESR

## Slide 30: Schottky Resonators in the Collector Ring of FAIR
Schottky resonators for isochronous mass measurements
will also be useful for highly sensitive diagnostics of
antiprotons

## Slide 31
Position Sensitive Schottky Resonator
position dependent shunt impedance  Schottky noise signal power P(x)
rectangular cavity
elliptic cavity
= - =
horizontal position in dispersive section is related to particle velocity (momentum)
correction for deviations  = t +  by measurement of p or v
(normalization to normal cavity signal)
beam pipe offset from cavity center
X. Chen, PhD thesis, supported by EU-contract No. PITN-GA-2011-289486

## Slide 32
thanks to my colleagues
X. Chen, P. Hülsmann, Y. Litvinov, F. Nolden, C. Peschke, P. Petri, S. Sanjari, I. Schurig, J. Wu