## Slide 1
High Intensity Effects on Tune Observables in the Synchrotron SIS18
- A Beam Diagnostics View -
R. Singh, P. Forck, P. Kowina, GSI
with contributions by:
O. Boine-Frankenheim, O. Chorniy, R. Haseitl, W. Kaufmann, K. Lang, GSI & M. Gasior, CERN
Workshop ‘Beam Dynamics meets Diagnostics’, Florence, November 5th, 2015
High Intensity: Q 0.05 space charge tune spread & coherent tune shift
measurements at SIS18 with up to 1013 charges
Observables: Tune spectra, time resolved bunch oscillations, chromaticity
modifications by in-coherent tune spread & coherent tune shift
Point-of-view: Results of measurements & usage for operation at SIS18
Main work & original talk performed by Rahul Singh,
but he can’t participate in this workshop

## Slide 2
Outline
Outline of the talk:
Motivation: Vision of tune measurement for operational usage
Hardware: BPM system and excitation method
Theoretical expectation: Tune spectra including space charge
Measurements and interpretation: Tune spectra for high intensity beams
Measurement: Quadrupole oscillations
Conclusion

## Slide 3
GSI Heavy Ion Synchrotron SIS18 (B=18Tm): Overview
Important parameters of SIS-18
Circumference | 216 m
Inj. type | Multiturn
Energy range | 11 MeV → 2 GeV
Acc. RF | 0.8 → 5 MHz
Harmonic | 4 (= # bunches)
Bunching factor | 0.4 → 0.08
Ramp duration | 0.06 → 1.5 s
Ion range (Z) | 1 → 92 (p to U)
injec-
tion
extrac-
tion
acceleration
Ion range (Z) | 1 → 92 (p to U)
Circumference | 216 m
Injection type | Horizontal multi-turn
Energy range | 11 MeV/u → 2 GeV/u
Ramp duration | 0.1 → 1.5 s
Acc. RF | 0.8 → 5 MHz
Harmonic | 4 (= # bunches)
Bunching factor | 0.4 → 0.08
Tune h/v | 4.2 or 4.4 / 3.4
Trans. size h / v |  10 / 5 mm injection
Important parameters of SIS18
extrac-
tion
injec-
tion
acceleration
Dipole, quadrupole,
rf cavity 0.8 < f < 5 MHz
electron cooling
acceleration
Upcoming FAIR:
SIS18 used as booster
high intensities up to ‘space charge limit’
precise control of beam parameter for emittance conservation & low losses
BPMs: 12 regular + 5 for special purpose
+ stripline exciter

## Slide 4
Online display for
tune measurement
during acceleration
Excitation with
band-limited noise
Time resolution:
4096 turns  20 – 4.5 ms
Variation during ramp:
triplett to duplett focusing
Result:
Online display for user
Sufficient signal strength
with moderate excitation
Minor emittance growth
Tune Determination at SIS18: Online Display in Control Room
P. Kowina et al., Proc. BIW’10; R. Haseitl et al., Proc. DIPAC’11, G. Jansa et al., Proc. ICALEPCS’09
Beam parameter:
1010 Ar18+ , 11  300 MeV/u
within 0.7 s
tune variation by
imperfect focusing ramp
2 mm
5 mm
Tune versus time
horizontal
vertical
Working Diagram
Tune at fixed time
vertical
horizontal
horizontal
vertical
Maximum Position Variation
 Qy  0.020
 Qx  0.015
2 mm
5 mm
0.05
0.05
time [ms]
0
200
500
700
0
200
500
700
time [ms]
time [ms]
time [ms]
hori. frac. tune Qx
vert. frac. tune Qy
vert. Qy
hori. Qx
horizontal tune
vertical tune
Position of maximum in spectrum

## Slide 5
Parameter | Typical Value
Circumference | m
Beam current | charges
Injection energy | MeV/u (
Betatron tune | 4.31 or 4.17 & 3.28
Synchrotron tune | ( kHz)
Trans. size x & y | 6...10 & 3...5 mm
Parameter | Typical Value
Circumference | 
Beam current | 
Injection energy | 
 | 4.31 or 4.17 & 3.28
Trans. size x & y | 6...10 & 3...5 mm
Low current: Tune spectra has symmetric sidebands due to synchrotron motion.
Relevant GSI SIS18 parameters
Higher current: The „global“ peak moves to the left. The symmetry of the spectrum is broken.
Tune Spectra at SIS18: Beam Intensity Modification
General questions:
Why is the tune spectrum modified at increasing beam current ?
Very practical: Which peak is the coherently shifted tune ?
What can we learn from this modification for further beam parameters ?
Most measurement and tests at prolonged injection flat-top with highest Q performed.

## Slide 6
Outline
Outline of the talk:
Motivation: Vision of tune measurement for operational usage
Hardware: BPM system and excitation method
Theoretical expectation: Tune spectra including space charge
Measurements and interpretation: Tune spectra for high intensity beams
Measurement: Quadrupole oscillations
Conclusion

## Slide 7
General functionality:
The beam is excited by band-limited noise or sweep
Broadband amplification & oversampling of bunches
Position value for each bunch
Fourier transformation gives the non-integer tune Q f
Mainly spectrum in baseband i.e. Q f < 1/2
R. Singh (GSI) et al., Proc. HB’10, U. Springer et al., Proc. DIPAC’09
Digital Electronics
(LIBERA from I-Tech):
ADC with 125 MSa/s
9 effective bits
FPGA: position evaluation etc.
Remark: For FAIR-SIS100 12 eff. bits ADC
Linear cut BPM:
Size: 200 x 70 mm2, length 260 mm
Position sensitivity:
Sx = 0.44 %/mm, Sy = 1.6 %/mm
Tune , Orbit & POsition System TOPOS  Oversampling
Different excitations:
noise or sweep

## Slide 8
Example: One turn = 4 bunches @ 35 MeV/u
Tune , Orbit & POsition System TOPOS  Oversampling
General functionality:
The beam is excited by band-limited noise or sweep
Broadband amplification & oversampling of bunches
Position value for each bunch
Fourier transformation gives the non-integer tune Q f
Mainly spectrum in baseband i.e. Q f < 1/2
Different excitations:
noise or sweep
R. Singh (GSI) et al., Proc. HB’10, U. Springer et al., Proc. DIPAC’09
Steps for digital processing:
Baseline restoration
Integration of bunches
 position for each bunch
Tune: FFT on position of
same bunch turn-by-turn i.e.1 of 4 per turn
From raw data: bunching factor,
synch & head-tail bunch shape
Uright
Uleft

## Slide 9
The beam is excited to betatron oscillation by band-limited noise or chirp:
The beam position is determined by analog manner via peak detector measured
Filtering of base-band component deliver the non-integer tune Q f
System designed by M. Gasior (CERN) and honored by Faraday Cup Award, see e.g. BIW’12
‘Quadrupolar’ BPM:
Size: 200 x 70 mm2, length 210 mm
Position sensitivity:
Sx = 1.4 %/mm, Sy = 2.1 %/mm
Base-band Tune system BBQ analog Peak Detection
BBQ design: M. Gasior BIW’12; GSI measurements; R. Singh (GSI) et al., Proc. HB’12 and DIPAC’13
or DAQ: ADC + FFT calc
Different excitations:
noise or sweep

## Slide 10
BBQ design: M. Gasior BIW’12; GSI measurements; R. Singh (GSI) et al., Proc. HB’12 and DIPAC’13
Base-band Tune system BBQ analog Peak Detection
Steps of analog processing:
Peak detection
Amplification of the difference
Filtering
Feeding to spectrum analyzer or DAQ
 weighted folding of spectrum to baseband
The beam is excited to betatron oscillation by band-limited noise or chirp:
The beam position is determined by analog manner via peak detector measured
Filtering of base-band component deliver the non-integer tune Q f
System designed by M. Gasior (CERN) and honored by Faraday Cup Award, see e.g. BIW’12

## Slide 11
BBQ spectrum
TOPOS spectrum
Ni7+ beam:
11 MeV/u
2  1010 ions
k = 0
k = 1
k = -1
Comparison BBQ versus TOPOS
TOPOS:
Oversampled digitization of the BPM signals
Full time domain information
Versatile data processing possible
e.g. picking 1 of 4 bunches, filtering ...
Results: Position, tune, longitudinal profile
synchrotron frequency s
 versatile due to full information stored
Remark: Improved algorithms in preparation
based on linear regression fit
(presently only as offline version)
BBQ:
Peak detection using analog circuit
i.e. no further treatment possible
High dynamic range
Result: tune with higher sensitivity
 ‘Easy-to-use’ device
R. Singh et al., IBIC’15
Amplitude
tradition: integration & y  /
(presented data)
novel: linear fit i versus i
Same raw data but different algorithms
vertical
5 x higher signal-to-background + higher resolution
+ better common mode suppression
Notes: TOPOS is the position and orbit measurement system, and tune is calculated from the FFT of the position across the whole cycle, when the beam excitation is also applied. The technical system, and implementation in FPGA and huge data acquisition was part of a separate 3-4 year project which was almost completed when I joined.
My initial contribution to the TOPOS was to use it, and face problems in its operation. Over the period of time, I understood the problem areas in the algorithm, and came up with an alternate position calculation algorithm, thus I will briefly explain it.
Compare the baseline restoration algorithm to the regression fit, pros and cons.
Another contribution was to understand the noise sources in the BPM.

## Slide 12
Outline
Outline of the talk:
Motivation: Vision of tune measurement for operational usage
Hardware: BPM system and excitation method
Theoretical expectation: Tune spectra including space charge
Measurements and interpretation: Tune spectra for high intensity beams
Measurement: Quadrupole oscillations
Conclusion

## Slide 13
Envelope shifted!
Sideband amplitude given by
Bessel-function Jk of order k
Frequency of harmonics m & mode k
b betatron freq. 0 rev. freq. a bunch length,
Basic of Tune Spectrum: Non-interacting Particle Model
Basis of single particle movement:
Dipole moment d(t) comprises betatron = amplitude x(t) & synchrotron = phase I(t) modulation
Finite chromaticity  modifies sideband’s heights !

## Slide 14
Non -zero chromaticity  intra-bunch movement
Rigid oscillations for zero chromaticity
Eigen-functions:
Example: five consecutive turns
Turn 1 2 3 4
Time Domain Mode Structure: Non-interacting Particle Model
Time  / ns
Time  / ns
Time  / ns
Time  / ns
Chromatic tune freq.
SIS18 injection:
Q0 = 3.27,  = 0.92
Bunch center-of-mass
1
2
3
4
5
 = 0
 = 1
 = 2
k = 0
k = 1

## Slide 15
Space charge parameter
qsc includes effect of longitudinal oscillations
Incoh. tune spread
Coherent tune shift
Transvers impedance
Simple Formulas: coherent Tune Shift and incoh. Tune Spread
Model assumptions: round constant beam & pipe radius, constant or KV distribution, constant synchrotron tune ...
Relation
beam radius
pipe radius
b pipe radius, R synchrotron radius,
A ion mass, q ion charge
N number of ions, Bf bunching factor, Q0 bare tune
W0 kinetic energy per nucleon,  velocity,  Lorentz factor
a beam radius,  transverse emittance
Notes: So, how do the space charge effects, modify the tune spectra?
First the more challenging and interesting effect, which was the prime motivation of all these detailed examples.
The distance between the head-tail modes change in a characteristic way, explained by certain theoretical and numerical studies, and our measurements match with the prediction quite well, and rather beautiful interpretation of tune spectra is obtained.
These are the examples of the theoretical curves, and the spectrum on the side for the given beam conditions exactly show, how the characteristic modification occurs.

## Slide 16
M. Blaskiewisz: Fast head-tail instabilities with space charge, Phys. Rev. Acc.. Beams 1, 044201, (1998)
A. Burov, Head-tail modes for strong space charge, Phys. Rev . Acc. Beams 12, 044202, (2009)
O. Boine-Frankenheim et .al., Transverse Schottky noise spectrum for bunches with space charge, Phys. Rev .Acc.. Beams 12, 114201, (2009)
Low intensity: spacing of sidebands:
Findings:
it is i.e. value of shifted bare tune as of importance for operating
k > 0, head-tail modes come closer
k < 0 almost constant slope (but larger Landau damping  broader and lower spectral lines)
Assumption of analytical description of head-tail modes by M. Blaskiewicz (1998):
Transverse phase space: KV-distribution
Longitudinal ‘airbag’ phase space: phase  constant momentum only two velocities vs =  vs0
 synchrotron tune: Qs =  vs0 /(R 0 a)
Analytical Model: Space Charge Modification of Tune Spectra
Qc = 0.06 Qsc
High intensity: spacing of sidebands:
Qsc incoherent tune spread
Qc coherent tune shift
Example for SIS18 parameter
Notes: So, how do the space charge effects, modify the tune spectra?
First the more challenging and interesting effect, which was the prime motivation of all these detailed examples.
The distance between the head-tail modes change in a characteristic way, explained by certain theoretical and numerical studies, and our measurements match with the prediction quite well, and rather beautiful interpretation of tune spectra is obtained.
These are the examples of the theoretical curves, and the spectrum on the side for the given beam conditions exactly show, how the characteristic modification occurs.

## Slide 17
Outline
Outline of the talk:
Motivation: Vision of tune measurement for operational usage
Hardware: BPM system and excitation method
Theoretical expectation: Tune spectra including space charge
Measurements and interpretation: Tune spectra for high intensity beams
Measurement: Quadrupole oscillations
Conclusion

## Slide 18
Measurement of all relevant beam parameters
to calculate for horizontal and vertical direction, respectively:
Current Transformer
Presented tune spectra are measured
by BBQ or TOPOS
Ionisation Profile Monitor
TOPOS
Longitudinal Schottky
Parameter | Symbols | Value | Value
Beam | A Ion q+ | 238 | 14
Energy |  | MeV/u | MeV/u
No. of particles |  |  | 
Emittance |  | mm-mrad | mm-mrad
Tune |  |  | 
Bunching factor |  |  | 
Synchrotron tune |  |  | 
Chromaticity |  | set | 1 meas.
Parameter | Symbols | Value | Value
Beam | A Ion q+ |  | 
Energy |  |  | 
No. of particles |  |  | 
Emittance |  |  | 
Tune |  |  | 
Bunching factor |  |  | 
Synchrotron tune |  |  | 
Chromaticity |  |  | 
Measurements: Overview of Beam Parameters
effective emittance
TOPOS or BBQ

## Slide 19
Red lines: predicted lines using measured beam parameters:
Measured spectra
R. Singh et al., Interpretation of transverse tune spectrum in a heavy-ion synchrotron, Phys. Rev. Acc. Beams 13, 034201 (2013)
Measurements: Moderate Space Charge Parameter
Beam: U73 +, 11.4 MeV/u, (1 ... 12)  108 ions,
Fractional horizontal tune Qfx
Qc = 0.06 Qsc

## Slide 20
Predicted spectra : red lines
Measured spectra
Measurements: Strong Space Charge Parameter
Beam: N7+, 11.56 MeV/u, (3 ... 15)  109 ion,
(smaller transverse size than U73+ beam)
R. Singh et al., Interpretation of transverse tune spectrum in a heavy-ion synchrotron, Phys. Rev. Acc. Beams 13, 034201 (2013)
Qc = 0.14 Qsc

## Slide 21
Slope
Comparison of predicted and measured Space Charge Parameter
General trend well reproduced i.e. reason for modified tune spectra was found
Significant deviation for higher values of qsc (as expected from analytic model)
 Does a better model with high prediction power exists ?
Can such model be applied to SIS18 parameter providing a plots of tune spectra ?
The values qsc from the depicted measurements with U73+ and N7+
Measurement of all parameters:
Predicted
Measured based on the distance between lines
of modes and :  qk 0 1
Findings:
R. Singh et al., Interpretation of transverse tune spectrum in a heavy-ion synchrotron, Phys. Rev. ST Acc. Beams 13, 034201 (2013)

## Slide 22
Measurements: Determination of coherent Tune Shift Qc
The coherent tune shift Qc from the depicted N7+ spectra and further spectra with Ar18+
For k = 0 : = i.e. value of coherently shifted bare tune as of importance for operating
Results:
Expected linear scaling coherent tune shifts versus peak beam current
For value of slope the resistive, effective impedance Z can be determined
 estimation of effective beam pipe radius mm & mm
R. Singh et al., Interpretation of transverse tune spectrum in a heavy-ion synchrotron, Phys. Rev. Acc. Beams 13, 034201 (2013)

## Slide 23
11 consecutive turn-by-turn center-of-mass recordings:
Time Domain Identification of Head-tail Modes
Frequency sweep allows the observation of bunch center oscillations i.e. head-tail modes
Beam parameter: 15  109 N7+ at 11.5 MeV/u, Qy = 3.75,  = -2.1
Tune spectrogram during sweep:
Results:
Sweep excitation allows excitation of individual head-tail modes
The mode-structure verifies the spectra interpretation
Remark: Eigen-functions for high intensities could be determined, if it of interest
Notes: The head tail modes were further identified in time domain, to indeed confirm that the negative modes could not be excited, and the left most mode is actually k=0 mode. On top of that, the mode structure could be used to calculate other beam parameters such as chromaticity.
These are some of the first clean measurements of excited head-tail modes. Normally they occur, when some of them cross their instability thresholds.

## Slide 24
Bold lines: measured bunch center
Dotted lines: least squares fit with
chromaticity  as fit parameter
Determination of Chromaticity from Head-tail Oscillations
Fit of measured head-tail modes to the classical (i.e. without space charge) eigen-functions
Beam parameter: low current 15  109 N7+ at 11.5 MeV/u
Results:
Precise determination of chromaticity 
SIS18: Deviation between set & actual value
& coupling to tune due to uncorrected closed orbit
 Reliable method but only for offline analysis
Fit result:  set = 1.19  meas + 0.80
R. Singh et al., Interpretation of transverse tune spectrum in a heavy-ion synchrotron, Phys. Rev. Acc. Beams 13, 034201 (2013)
Longitudinal bunch position /s
Transverse center-of-mass /
Notes: The eigenmodes have exclusive dependence on Chromaticity. (Inspired by O.R. Jones measurements)
All the measured modes were fitted according to the analytical prediction for a square-bag model.
Chromaticity measured in both planes. Comparision with traditional method
NOW:
Chromaticity measurements were performed based on the head-tail mode structure.
The coupling between the planes due to improper alignment of the quadrupoles, or the skew components was also measured.
All this due to proper understanding on the two complimentary systems. Now systems in regular operation.

## Slide 25
During acceleration:
transverse emittance decreases
synchrotron tune Qs decreases
 qsc > 1 i.e. relevant modification of spectrum
R. Singh et al., PRST-AB 2013 and IBIC’13
acceleration of 1010 Ar18+
Measurement: Head-tail Modes at higher Energies
Parameter | SIS18 | SPS | RHIC | ANKA
Ipeak / |  |  |  | 
 / |  |  |  | 
Lorentz fac. |  |  |  | 
Tune spr. |  |  |  | 
Synch. tune |  |  |  | 
SC para. |  | 7 |  | 
Parameter | SIS18 | SPS | RHIC | ANKA
Typical values at other synchrotrons at injection:
-
-

## Slide 26
Comparison to advanced theoretical Predictions
Theoretical investigations by other groups
as seen by a beam diagnostics person:
Head-tail modes discussed for instabilities
Eigen-frequencies predicted as a function of qsc
Landau damping stronger for negative modes
Bunch length influences Qs(bunch )  changes in spectrum
Chromaticity influences the peak height and width
But: Seldom plotted in terms of beam observables
 Prediction missing for height & width for SIS18
M. Blaskiewisz: Fast head-tail instabilities with space charge, Phys. Rev. Acc. Beams 1, 044201, (1998)
A. Burov, Head-tail modes for strong space charge, Phys. Rev. Acc. Beams 12, 044202, (2009)
O. Boine-Frankenheim et .al., Transverse Schottky noise spectrum for bunches with space charge, Phys. Rev. Acc. Beams 12, 114201, (2009)
M. Blaskiewicz, V.H. Ranjbar Transverse beam transfer functions via Vlasov equation, Proc., PAC2013, Pasadena p. 1427 (2013).
Example: PIC spectrum by code PATRIC (Boine-Frankenheim et al.)
M. Blaskiewicz,
V.H. Ranjbar, PAC’13
reactive BTFrea
resistive BTFres
0
1
2
3 = k
k = 0
k = 2
k = 1
k = -1
Example: Plot of calculated BTF(qsc )
Measured tune spectrum:
P() = BTF2rea() + BTF2res()
qsc = 5
Qc = 0.15Qsc
a = 0.4 b
conclusion

## Slide 27
Outline
Outline of the talk:
Motivation: Vision of tune measurement for operational usage
Hardware: BPM system and excitation method
Theoretical expectation: Tune spectra including space charge
Measurements and interpretation: Tune spectra for high intensity beams
Measurement: Quadrupole oscillations
Conclusion

## Slide 28
Quadrupole Oscillations with Tune Shift
Envelope oscillation results in a time dependent quadrupole moment of the beam
Occurrence: E.g. injection mismatch by wrong transfer line focusing called ‘beta mismatch’
Beam’s quadrupole moment:
BPM signal: four plate combination
Offset & size oscillations:
y
Shift of quadrupole lines for coasting beam KV-distribution:
Tune without space charge contribution Qsc = 0:
&
Tune with space charge contribution Qsc  0:
 Qsc can be determined from Qcoh,1 & Qcoh,2
y
x
beam
cross section
y
x
beam
cross section
W. Hardt, On the incoherent space charge limit for elliptic beams, CERN/ISR/Int. 300 GS/66.2 (1966)
I. Hofmann, Stability of anisotropic beams with space charge, Phys. Rev. E 57 (4), 4713 (1997)
M. Chanel, Study of beam envelope oscillations.by measuring the Bema Transfer function with quadrupolar pick-up and kicker, EPAC’96,
Ur
Ub
Ut
Ul

## Slide 29
Quadrupole Oscillations with Tune Shift
Example: Horizontal tune spectra (coasting beam)
horizontal beta-mismatch:
Ibeam = 6 mA
Result: in-coherent tune spread Qsc measurable
Technical realization:
uses BBQ setup as for tune
but analog combing (UR + UL ) and (UT + UB ), resp.
presently: no quadrupole exciter available
Beam parameter:
N7+ at 11.4MeV/u,
x (2) = 32 µm, y (2) = 51 µm, Qx0 = 4.2, Qy0 =3.3
Result:
Qsc shifts with beam intensity
approximately according to expectation
Example: Variation of beam current:
1024 turn FFT
256 turn FFT
R. Bär et al., NIM A, 415, 460 (1998), R. Singh et al., Proc. IBIC’14
BBQ

## Slide 30
Summary and Outlook
Experimental finding:
System for online tune measurement realized, excitation with acceptable emittance growth
Measurement of all beam parameters required for correct interpretation of tune spectrum
Tune spectra: Eigen-frequencies significantly shifted for qsc 0.5 by head-tail modes
Coherently shifted tune Qc at k = 0 mode  this value is right number for operation !
However, k = 0 mode is not always the highest peak
 spectrum must be interpreted e.g. by recording the mode structure of bunches !
Estimation of tune spread Qsc available  usage for operation and MD-times ?
Comparable findings see e.g. V. Kornilov et al., PRST-AB 15, 114201 (2012)
General understandings and outlook:
Estimation of spectrum modification required
Interpretation of in-coherent Qsc required for usage during accelerator operation
Extension to realistic beam e.g. with Gaussian distribution desired
Possible improvement from beam dynamics community: plots of typical beam observables
 desired for tune spectra: Prediction for height & width for actual accelerator setting
Thank you for your attention !

## Slide 31
Extra slides

## Slide 32
Beam parameter:
15  109 N7+ at
11.5 MeV/u
Measurement: Tune Spectra for different chromaticities 
Chromatic phase:
i.e. dependence on  & bunch length Am
Comparison of expectation by Bessel-functions Jk(f )
to height of measured modes
Tune spectra for different chromaticities  :
Obvious result:
Amplitude of different modes depend on 
 k = 0 is not always the highest peak
Head tail oscillations k = 0:
Bunch shape for different 
for 3 consecutive turns:

## Slide 33
Resolution and Noise Reduction of Tune Spectra
R. Singh et al., Proc. HB’10
Resolution of tune spectra: Variation of FFT length for 40960 turns
either short FFT length and many averages
or longer FFT and less averages
2  109 ions at 11.4 MeV/u, vertical tune spectrum
Beam: 2  109 ions at 11.4 MeV/u, vertical tune spectrum

## Slide 34
Position Determination: Integration versus least square Fit
Example: One turn @ 35 MeV/u
Novel: Ordinary least square fit algorithm:
1. Creation of window of a single bunch with N samples
2. Calculation of sum and difference for each sample:
and for i = 1...N
‘Plotting’ i versus i
3. Assumption: From 
with a=xS and b as fit parameter
 Least square fit of i as a function of i
General solution for fit parameter a :
&
with average value &
4. Position i.e. from fit value from diff-over-sum
Advantage:
No baseline reconstruction required
Robust against offset etc. (here fit parameter b)
i.e. high common and differential mode suppression
Easy to implement
For closed orbit: window over many bunches
Traditional: Integration
1. Creation of window for
one bunch of N samples
2. Determine baseline values Bl/r
3. Subtraction Ui,L/r – Bl/r for i = 1...N
4. Integration of bunch signal
5 .Position:
S is the position sensitivity

## Slide 35
Tune Spectra for different experimental Parameter
Variation of excitation power:
Result:
signal-to-noise varies
general tune spectrum remains
Beam parameter:
5108 U73+ at 11.4 MeV/u
Variation of excitation type:
Result: No significant difference
Spectrum of
band limited
noise:

## Slide 36
The model allows analytical solution of the Vlasov equation including space charge forces

Real bunch
Model
(Airbag distribution)
longitudinal profile
voltage
Synchrotron tune
distribution
time
voltage
time
momentum distribution
THEORY : M. Blazkiewicz, Fast head tail instability with space charge, Phys. Rev ST Accel. Beams 1, 044201, (1998)
SIMULATIONS : O. Boine-Frankenheim and V. Kornilov, Transverse Schottky noise spectrum for bunches with space charge,Phys. Rev ST Accel. Beams 12, 114201, (2009)
Analytical Theory : High Intensity Effects