## Slide 1: Using Stripline BPMs to Measure the Longitudinal Twiss Parameters in the SNS linac
Andrei Shishlo
ORNL
SNS Project
Florence, Italy
November 2015

## Slide 2: Outline
Physics picture description
Harmonics analysis
Short RF cavity +drift+ BPM
Algorithm
SNS Results
Conclusions

## Slide 3: Longitudinal Bunch Distribution from Stripline BPMs. Is it possible?
If v=c the signal will be proportional to ρ(z)
Our case v<c and r0 <<R
There is now direct way to interpret the stripline BPM signal as the bunch density
Bunch usually too short for the frequency bandwidth of the existing electronics
No, it is not possible!
What can we do?
2R
r0
From Alex Chao’s book
“Collective Instabilities in Accelerators”
signal
signal

## Slide 4: Amplitude of Particular Harmonic
J. H. Cuperus, Nucl. Instrum. Methods 145, 219 (1977)
MONITORING OF PARTICLE BEAMS AT HIGH FREQUENCIES
- Harmonics of sum of electrodes BPMs signal at frequency
- Fourier harmonics of the longitudinal density distribution
- radius of the beam pipe
- relativistic parameters
Let’s assume this for easy interpretation
Citation: “The response to higher harmonics is limited, and measurement of the bunch form is not possible.”
We are not going to use the higher harmonics

## Slide 5: Harmonic of Gaussian Distribution
Gaussian Longitudinal Distribution
BPM harmonic after Fourier transformation
- Longitudinal bunch size in deg.
Problem: for short bunches
results are useless
For long bunches
BPM is an analog of a Wire Scanner for the longitudinal size

## Slide 6: SNS Linac Structure
Length: 330 m (Superconducting part 230 m)
Production parameters:
Peak current: 38 mA
Repetition rate: 60 Hz
Macro-pulse length: 1 ms
Final Energy: 940 MeV (1000 MeV design)
Average power: 1.4 MW
SNS H- linac
Important for us Linac Diagnostics:
BPM - Beam Position and Phase Monitors

## Slide 7: Longitudinal Twiss Analysis
CCL4
BPM1
BPM2
…
BPM{n}
…
n – number of BPMs
or we can do n measurements with one BPM
Standard LSM Problem

## Slide 8: SCL Entrance Longitudinal Twiss Analysis
CCL4
BPM1
BPM2
…
BPM{n}
All SCL RF are OFF
Statistics:
40 measurements
13 BPMs
Does not work!
Errors are too big!

## Slide 9: RF Cavity as Measuring Device
CCL4
BPM1
BPM2
…
BPM{n}
SCL
RF
dE
φ
dE
φ
dE
φ
…
RF Kick
Drifting
Maximal debunching
z
σφ
Over-focusing in RF
RF cavity position
RF transforms longitudinal phases space
We have good models for short RF cavities
The RF transport matrix is known

## Slide 10: Longitudinal Twiss Analysis with SCL RF
CCL4
BPM1
BPM2
…
BPM{n}
SCL
RF
We can include a controllable element in the lattice and get more data
The Twiss errors should be reduced. For 5 deg step, matrix will be (72x14)x3.
Results (XAL units):
Alpha = 0.56 +- 0.02
Beta = 5.33 +- 0.13
Emitt = (0.928 +- 0.012)*10-6
Defocusing
Over focusing
A. Shishlo, A. Aleksandrov,
Phys. ST Accel. and Beams 16, 062801 (2013).

## Slide 11: SCL Twiss for CCL4 Phase Scan
We want to verify our method with something different
Studies performed on 09.22.2012
Simultaneous BSM-410 measurements
Peak beam current 35 mA
CCL4
BPM1
BPM2
…
BPM{n}
SCL
RF
BSM
CCL4 Phase Scan
-20 ↔ +40 deg
Design phase = 0 deg
SCL01a Phase Scan
For Long. Twiss

## Slide 12: CCL Bunch Length for Two Methods
Results are very close. It proves the applicability of the new method.
Limitations: assumption of Gaussian distribution in the bunch.
If we are far from the matched case (design) the bunch could be non Gaussian.
Design

## Slide 13: Longitudinal Twiss along SCL (1)
We can use each cavity in SCL as the measuring point for the longitudinal Twiss
Data were collected in April, 2013
Only cavities in the first 12 cryomodules were scanned (34 cavities)
The BPM amplitude calibration was calculated by using the same scan data, so only about half of BPMs were calibrated properly.
For the first cavity we used the analysis described, but for all downstream cavities we assumed a constant normalized emittance. It means we fitted α, β Twiss parameters only and un-normalized BPM amplitudes.
BPM1
…
BPM{n}
SCL
RF
01a
SCL
RF
01b
SCL
RF
01c
BPM2
SCL
RF
02a
SCL
RF
02b
SCL
RF
02c

## Slide 14: Longitudinal Twiss along SCL (2)
We have measurements at the entrance of each cavity, and we can calculate Twiss by using Online Model and the initial Twiss
Results are in a good agreement
The existing discrepancies grow with the distance from the beginning. Probably OM is not very good for very unmatched beams.
In longitudinal direction we have a very unmatched beam. The matching will be done in the future.

## Slide 15: Results of “Z” Twiss Analysis 2014
2014.08.10
Longitudinal beam size
Peak current 24 mA
Production beam
Beam un-matched longitudinally
Agreement Model/Measurements is good.

## Slide 16: Conclusions
A non-invasive method of measurements of Longitudinal Twiss parameters with stripline BPMs is developed
The method was validated on SNS SCL linac

## Slide 17: Latest Attempt J-PARC

## Slide 18: J-PARC BPMs’ Signals
BPM’s Length
Beam
t
T
bunch
T
t
A
B
Signal from
A end
Signal from
B end
Signal from the B-end is late because it takes time for the bunch to reach this end and time for signal to go back.

## Slide 19: Bunch Length and Amplitude of Harmonic
- constant defined by the BPM geometry
- total bunch charge
- RMS bunch length
(*)
Formulas (1) and (2) give us the ability to calculate the RMS bunch length if we know the Const and have the BPM waveform.
It means we need a calibration!

## Slide 20: J-PARC BPM ACS21B:BPM Signals
All ACS Cavities are OFF
All ACS Cavities are ON
J-PARC BPMs’ show the energy dependency in the peak positions
It is not exactly an expected time shift: probably termination is not perfect
Correction factors are needed