## Slide 1: Measurement of 6D Beam Distributions at Low Beam Energy
A. Aleksandrov
Oak Ridge National Laboratory,
USA

## Slide 2: Outline
Introduction
  What
  Why
  How
  Challenges
Practical Implementation
  SNS Integrated Test Stand Facility
  6D distribution measurement tools
Status and Plans

## Slide 3: We will measure charge distribution function in 6D beam phase space
- coordinates in phase space
- 2D distribution function
- 4D distribution function
- 6D distribution function
sometimes called 6D but
except for special case of no any correlations between degrees of freedom

## Slide 4: Example:
‘K - V like’ distribution

## Slide 5: Realistic initial distribution is needed for PIC simulation of beam dynamics in linac
End-to-end simulation starting from ion source plasma surface
  No comments
4D distribution measurement after ion source + PIC simulation through RFQ
  Accurate 4D measurement at RFQ entrance is difficult
  Beam dynamics simulation in RFQ is most challenging part of linac simulation: strong space charge, many cells, no diagnostics
6D distribution reconstruction from 2D emittances measured after RFQ
  Absence of correlations between degrees of freedom is assumed without experimental validation
  Dedicated experiment (LEDA) did not support this approach
Direct measurement of 6D distribution after RFQ

## Slide 6: 2D distribution measurement (emittance) using slit-slit technique
SLIT_Y_1
SLIT_Y_2
FARADAY CUP
BEAM
L

## Slide 7: 4D distribution measurement using four slits arrangement
FARADAY CUP
SLIT_X_1
SLIT_Y_1
SLIT_X_2
SLIT_Y_2
BEAM

## Slide 8: 6D distribution measurement arrangement
SLIT_X_1
SLIT_Y_1
SLIT_X_2
SLIT_Y_2
dxdy
BEAMLET
dxdydx´dy´
BEAMLET
SLIT_X_4
SLIT_X_3
RF deflector
BENDING MAGNET
Magnetic spectrometer for energy determination
RF deflector or other time resolving device for temporal degree of freedom
FARADAY CUP
Looks simple, why don’t we see it everywhere?

## Slide 9: “Curse of dimensionality” problem
High-dimensional spaces have very large volume: V
  Large scan time
  Low charge density
  Large data sets
Same setup can measure all lower dimension projections
  x - x’
  x – y
  x - φ
  x - w
  x’ - y - x
  x’ - φ - x
  x’ - w - x
  ….

## Slide 10: Scan time estimate
1 2 …….. m
Total number of bins
Number of steps per degree of freedom
dimensionality
For
Total scan time at
Total scan time at
Tens of hours total scan time

## Slide 11: Signal strength estimate
For
current after all 6 slits
Number of particles in
beam pulse is
Number of particles after 6 slits: at the distribution center
at
at
at
at
at
at

## Slide 12
Many hours of beam time allocated for single experiment
is big challenge for any large scale accelerator facility
Only feasible at a dedicated facility

## Slide 13: SNS Integrated Test Stand Facility (ITSF)
Ion Source
RFQ
MEBT
Particles | H-
Energy | 2.5 MeV
Current | < 50 mA
Pulse width | < 1 ms
Rep rate | < 60 Hz
Power | < 7.5 kW

## Slide 14
ITSF Diagnostics Beam Line Layout
BUNCH SHAPE MONITOR
90-DEG. BENDING MAGNETS
MEBT BEAM STOP WITH RADIATION SHIELDING
VIEW SCREEN AND FARADAY CUP
QUADROUPOLES
MOVABLE SLITS

## Slide 15: ITSF MEBT

## Slide 16: X-Y Slit arrangement
200-by-200 μm aperture

## Slide 17: Simulated scan of ‘K - V like’ distribution

## Slide 18: Equipment for E-φ degrees of freedom measurement to be installed
90⁰ bending magnet
‘RF deflector’ type longitudinal profile monitor, aka ‘Feschenko device’

## Slide 19: Status
Ion Source operational
RFQ operational
Straight beam line operational
Safety systems, documentation in progress
DOE approval eventually
90⁰ bend beam line spring 2016

## Slide 20: Speeding up W-φ plane measurement
magnet
energy selection slit
time selection slit
Faraday Cup
RF deflector
magnet
view screen
imaging camera
RF deflector
magnet
imaging camera
view screen
φ
W
~10 times faster
~10 times faster
2D optical readout has advantages and disadvantages
  faster
  smaller dynamic range of charge-to-light-to-charge conversion

## Slide 21: Detector modification is simple
Slit mounted on this flange
to be replaced
with view screen
SEM and Faraday Cup
to be replaced
with digital camera

## Slide 22: Research goals
Optimize 6D phase space measuring system for maximum resolution and dynamic range
Develop algorithm for generating particle distributions for loading to PIC codes
Search for high-dimensional correlations in the measured distribution
Develop and verify methods of generating 6D distributions from low-dimensional projections
Repeat LEDA beam dynamics experiment with newly developed diagnostics

## Slide 23: US National Science Foundation Grant with University of Tennessee (Sarah Cousineau is PI)
Proposal highlights:
  Direct 6D phase space measurement.
  Study halo formation in FODO structure.
  Benchmark codes (community resource), evaluate diagnostics.
  Funding for 1 postdoc, 1 graduate student, 3 undergraduates for 3 years beginning in September 2015.
RFQ
IS
MEBT-1
FODO
4-D emittance
existing
future
LEDA style beam dynamics experiment
To be designed, built and commissioned at ITSF

## Slide 24: Thank you for your attention!