## Slide 1: Status of the PandaRoot simulation of the Forward RICH
Konstantin Beloborodov
Budker INP, Novosibirsk, Russia
Novosibirsk State University, Russia
PANDA LIII. Collaboration Meeting
Uppsala, Sweden
Budker INP
8-12 June 2015

## Slide 2: Outline
Geometry
Aerogel
Simulation
Reconstruction

## Slide 3: Forward RICH
RICH | 
Main goal | PID information for higher level triggers
π/K-separation | up to ~10 GeV/c
Radiator | Focusing aerogel
Refractive indices | ~1.05
Radiator thickness | 4 cm
Placement | Between FT5 and FT6
Vertical angle | ±5°
Horizontal angle | ±10°
FT5
FT6
RICH
TOF
ECAL
HCAL
Dipole magnet

## Slide 4: Geometric requirements
Placement along beam axis: between forward trackers 5 and 6
Angular acceptance: dimensions are the same or close to forward trackers dimensions
Aerogel radiator: multi-layer
Mirror: simple shape (flat, round, spheric)
Geometric efficiency: all Cherenkov photons should be detected if it possible
Photon detector: less sizes as it possible (due to cost optimization)
Shape of Cherenkov “ring” on the photodetector surface: simple (circle, ellipse)
…
flat
round
spheric
LHCb

## Slide 5: Mirror parameters optimization
Geometric efficiency:
Lower Č photon hits PhDet
Upper Č photon hits PhDet
All other Č photons automatically do the same
Photo detector width:
w( z, l1, l2, l3, … ) → wmin
Six segments flat mirror
(as an example)
First segment has major influence on PhDet size!

## Slide 6: Optimal mirror configurations
1 segment
2 segments
3 segments
4 segments
6 segments
10 segments
Round

## Slide 7: Some features of flat and round mirrors
feature | 3 segments | Round
PD width, cm | 67.5 | 58.5
Mirror focusing | no | yes
Aerogel focusing | yes | no
combinatorial background | yes | no
Cherenkov “ring” shape on PD surface | elliptical | complicated
Number of parts | 3 | 1
round mirror
Aerogel plate size = 60 cm (half height)

## Slide 8: Multi-layer aerogel: parameter optimization
1.05 − δn
1.05 + δn
1.05 − δn
1.05
1.05 + δn
Two layers
Three layers
Software: FairSoft – apr13, PandaRoot – scrut14

## Slide 9: Multi-layer aerogel: optimal parameter
Two layers
Three layers
n = 1.05
δnopt = 1.03·10-3
δnmin = 0.76·10-3
δnmax = 1.36·10-3
n = 1.05
δnopt = 1.23 ·10-3
δnmin = 0.96 ·10-3
δnmax = 1.47·10-3
Three segments mirror and three layer aerogel were used in further simulations

## Slide 10: Events simulation and reconstruction
X, cm
X, cm
X, cm
Y, cm
Y, cm
Y, cm
φC, rad
θC, rad
Reconstruction methods:
on photodetector surface (template)
photon track reconstruction (in order to obtain cherenkov angles for each hits)
θC = acos(1/n)

## Slide 11: Refraction on the surface of the aerogel
θc, rad
φc, rad
θc = f( φc; β, n, α )
φc − azimuthal angle
β − velocity of the charge particle
n − refraction index of the aerogel
α − polar angle of the charge particle

## Slide 12: Fit result
μ
p = 10 GeV/c
β = 0.99994
βFIT = 0.99912

## Slide 13: Simulated effects
Simulation
  Geometry description
    RICH position
    Aerogel (size, number of layers, refraction index)
    Mirror geometry (round, flat)
  Materials properties for Cherenkov photons
Digitization
  Pixelation
  Quantum efficiency of photodetector
  Photodetector noise
  Dead time of photodetector
  Photodetector time resolution
  Crosstalks (not done)
Reconstruction (simple mode)
  Hit preselection
  Fit θ(φ) dependence
PID (not done)
  Probability calculation

## Slide 14: Hit selection for fit
TA, ns
θC, rad
1000 events

## Slide 15: π/K-separation: first result
2 GeV/c
4 GeV/c
6 GeV/c
8 GeV/c
10 GeV/c
K
K
K
K
K
π
π
π
π
π

## Slide 16: Conclusions
Geometry optimization for flat and round mirrors has been done
Optimization of refractive indices for two and three layers aerogel has been performed
First PANDAroot sim/digi/reco code for the Forward RICH has been created
Events with single K and π mesons (FairBoxGenerator) going directlyto FRICH are simulated
First and simple reconstruction of particle velocity has been realized
First results on π/K separation has been obtained

## Slide 17: …

## Slide 18: …