## Slide 1: Beam dynamics of Super-FRS and MM requirements
John Winfield
GSI Helmholtzzentrum für Schwerionenforschung GmbH

## Slide 2: Introduction
Super-FRS normally used as coupled two-stage Br-DE-Br separator (“achromatic” mode).
Also used as part of 0° (energy-loss) spectrometer, dispersive & other modes - see, e.g., “Physics Case for Super-FRS Collaboration”.
Field measurement programme is based mostly on experience with predecessor, FRS.
Larger aperture of magnets for the Super-FRS must be taken into account.

## Slide 4: Ion optics: Low Energy Branch (Main Separator)
X
Y
MF1
MF2
MF3
LF2

## Slide 5: Dispersion-matched mode
M. Yavor, H. Geissel; 2003
Applied to give high-resolution momentum measurements in combination with secondary reaction studies. Also done for HEB-R3B(H. Geissel 2014-15)

## Slide 6: Field measurements – some issues
First magnet of type, Series magnets.
Number of magnet excitations (current), range (max, min)
Extent of fringe field, step size
Number of vertical planes (dipole)
Harmonic analysis (quadrupole)
Embedded octupole with and without quad excited.

## Slide 7: Dipole
For “1st of kind”: Complete field map incl. fringe fields.
  Transform field map to ion-optical transfer matrix for COSY/GICOSY/Mirko. E. Kazantseva at TU-Darmstadt & Martin Berz’s group at MSU working on this.
  Check field quality (SAT).
Many excitations: Aim is to set magnets more reliably. Usually, many Bρ settings during expt  want to spend as little time as possible. (FRS experience).
Several vertical planes:. Field near pole faces could differ from that at mid-plane. Difficult to extrapolate reliably from mid-plane (Lazzaro NIM A 570 (2007) 192, Manikona PhD thesis, MSU)

## Slide 8: Quadrupole
Both entrance and exit fringe fields ( effective length of magnet) should be measured for all quadrupoles, at many field excitations. (FRS experience: 6th order polynomial fits were made).
FRS quadrupoles: effective length can vary >3% depending on current excitation.
Fields vary according to focusing requirements.

## Slide 9
Chart: Quadrupole field gradients for 20 Tm beam
HEB | 7.398 | 8.6784 | 7.7962 | 3.4036 | 6.7545 | 5.7689 | 5.3447 | 7.3158 | 4.0504 | 7.5466 | 8.8914 | 8.8582 | 8.8571 | 8.8895 | 7.546 | 4.1009 | 7.4907 | 5.5003 | 5.6352 | 6.6535 | 3.4178 | 5.3122 | 6.7172 | 6.3893

## Slide 10: Enge coefficients
In ion-optics programs, magnet fringe field fall-off typically represented by six parameter Enge function:
where z is distance perpendicular to EFB (for multipoles it coincides with reference trajectory),
D is the full aperture, and a1 through a6 are the Enge coefficients. These coefficients are fit to the measured fringe field data.

## Slide 11: Current dependence of Enge coefficients (Q1000)
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a1in 2006 | -0.18515 | -0.18369 | -0.18415 | -0.17366 | -0.15546 | -0.12319 | -0.08524 | -0.055657 | -0.051084 | -0.056051 | -0.068106 | -0.080286 | -0.09162 | -0.10182
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a2in 2006 | 4.6345 | 4.6308 | 4.6191 | 4.6056 | 4.5511 | 4.4769 | 4.3769 | 4.3079 | 4.265 | 4.2588 | 4.2627 | 4.2715 | 4.2782 | 4.2922
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a3in 2006 | -0.36815 | -0.37856 | -0.3703 | -0.35001 | -0.21707 | -0.02667 | 0.23082 | 0.44865 | 0.44857 | 0.51785 | 0.55608 | 0.58557 | 0.60493 | 0.62366
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a4in 2006 | 0.97074 | 0.92844 | 1.0016 | 0.90603 | 0.84269 | 0.66652 | 0.45167 | 0.21653 | 0.24152 | 0.24428 | 0.26984 | 0.29573 | 0.32377 | 0.34265
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a5in 2006 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.23337 | 0.16524 | 0.14484 | 0.13403 | 0.17497 | 0.18069
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a6in 2006 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.072478 | 0.047836 | 0.034978 | 0.028199 | 0.048973 | 0.046092
From: H. Takeda, RIKEN, Expert meeting on in-flight separators, 2010. Entrance side
Q current (A)
Q current (A)
Q current (A)
Q current (A)
Q current (A)
Q current (A)
a1
a2
a3
a4
a5
a6

## Slide 12: Current dependence of Enge coefficients (Q1000)
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a1out 2006 | -0.1317 | -0.12668 | -0.12081 | -0.11448 | -0.092777 | -0.065535 | -0.02196 | 0.00095965 | 0.011629 | 0.0015434 | -0.0077567 | -0.019347 | -0.030045 | -0.044497
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a2out 2006 | 4.5963 | 4.6048 | 4.6025 | 4.5908 | 4.5434 | 4.4767 | 4.386 | 4.3218 | 4.2753 | 4.2663 | 4.2742 | 4.2813 | 4.2924 | 4.3046
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a3out 2006 | -0.20199 | -0.24106 | -0.25533 | -0.23048 | -0.10516 | 0.070057 | 0.31129 | 0.51368 | 0.49103 | 0.55007 | 0.59558 | 0.62958 | 0.64914 | 0.67323
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a4out 2006 | 1.1876 | 1.02 | 1.0005 | 0.90762 | 0.83101 | 0.65298 | 0.42624 | 0.20534 | 0.28159 | 0.27906 | 0.30017 | 0.32117 | 0.36118 | 0.38101
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a5out 2006 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.28615 | 0.27074 | 0.20802 | 0.20078 | 0.23527 | 0.23479
Chart: 
| 20 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
a6out 2006 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.086131 | 0.085448 | 0.05698 | 0.051594 | 0.063604 | 0.06022
From: H. Takeda, RIKEN, Expert meeting on in-flight separators, 2010. Exit side
Q current (A)
Q current (A)
Q current (A)
Q current (A)
Q current (A)
Q current (A)
a1
a2
a3
a4
a5
a6

## Slide 13: Harmonic analysis
Harmonic Analysis

## Slide 14: Alexander Kalimov’s design
Specifications and calculation results
 |  | Type 3 quad
Eff. length, L | m | 0.8
Gradient range G. |  | 1.0-10 T/m
Gradient quality |  | <±8∙10-4, below 8 T/m
Useable horizontal aperture | mm | ±190
Useable vertical aperture | mm | ±120
Embedded octupole (B''') | T/m3 | 105
Harmonics must be obtained at several fields, incl. highest excitation.

## Slide 15: Simulation programs
Simulation and prediction programs such as MOCADI and LISE++ use matrix elements from ion-optics codes, which in turn are more reliable when based on actual magnet field measurements.

## Slide 16: Summary

## Slide 17: Backup slides

## Slide 18: Hysteresis
FRS procedure: before fields are set, magnets are “ramped” by powering them from 0 to nominal current several times.

## Slide 19
Standard approach to extrapolate field far from mid-plane inaccurate: needs high-order differentiation  v. sensitive to errors in mapping.
Better: measure in several planes & interpolate  3D vector field, analytical & differentiable. Use DA to get high order transfer maps.