## Slide 1: Super-FRS multiplet field

## Slide 2: Outline
Multiplets
Magnet Configurations in Multiplets
Requirements on axis and angles
Magnetic field simulations
  Quadroples
  Coupling Quadrupole-Sextupole
Conclusions

## Slide 3
General Design of SC Multiplet
25 long multiplets + 8 short multiplets
Cold, laminated iron yoke (> 40 tons),
Warm beam pipe (38 cm inner diameter)
Common helium bath (~ 1300 liter helium)
1 pair of current leads per magnet
max. current < 300 A for all magnets
~ 7 m long, > 60 tons
1 x long quadrupole (LQ)
2 x short quadrupole (SQ) equipped with octupole (O) coil
3 x sextupole (S)
1 x steering dipole (ST)
(longest multiplet system)
SQ+O
SQ+O
LQ
S
S
S
ST
short multiplet

## Slide 4
Configurations of magnets in 33 multiplets
28 standard configuration, 5 special configurations

## Slide 5: Maximum standard configuration

## Slide 6
Special configurations

## Slide 7: Magnet parameters
 | Quadrupole Type 3 | Quadrupole Type 4 | Sextupole | Steerer
Number of Magnets | 46 | 34 | 41 | 14 (13v/1h)
Effective length | 0.8 m | 1.2 m | 0.5 m | 0.5 m
Gradient/ Field Range | 1.0-10 T/m | 1.0-10 T/m | 4-40 T/m2 | 0-0.2 T
∫gdl | 0.8-8 T/m*m | 1.2-12 T/m*m | 2-20 T/m2*m | ≥ ± 0.1 T*m
Field Quality | For g< 0.8 gmax ±1·10-3 For g > 0.8 gmax ±6·10-3 | For g< 0.8 gmax ±1·10-3 For g > 0.8 gmax ±6·10-3 | ±5·10-3 | ±8·10-3
Usable aperture | Ø 380 mm | Ø 380 mm | Ø 380 mm | Ø 380 mm
Embedded Octupole | 105 T/m³ Int. 84 T/m3×m |  |  | 
Magnets are operated (DC) at all field levels between minimum and maximum !

## Slide 8: Tolerances/accuracy
Axes tolerances of position, pitch yaw and roll of each single magnet in a multiplet in relation to the best multiplet axis which is represented by the references outside the Multiplet cryostat.
Maximum allowed total error between position of magnetic axis and mechanical axis (related to outside references of the cryostat) | ±0.2 mm
Tolerance on pitch and yaw (related to outside references of the cryostat) | ±0.29 mrad
Tolerance on roll (related to outside references of the cryostat) | ±1.15 mrad
Alignment only possible with regards to common best multiplet axis

## Slide 9: Tolerances/accuracy
Accuracy (difference of the integrated flux density between two magnets which are identical in construction and powered with the same current)
Quadrupoles | ≤ 0.25 %
Sextupoles | ≤ 0.4 %
Steerer | ≤ 0.4 %

## Slide 10: Coordinate system (Technical Guideline)
not fixed: origin of coordinate system

## Slide 11: Magnetic field simulations All field caculations by A. Kalimov (St. Petersburg)
Quadrupoles

## Slide 13: Coupling Quadruple-Sextupole
Variation of distance between yokes from 500 mm to 200 mm

## Slide 14: Coupling Quadruple-Sextupole
500 mm 250 mm
200 mm

## Slide 15: Coupling Quadruple-Sextupole
250 mm distance was chosen as compromise between space limit and field distortion

## Slide 16: Strayfield

## Slide 17: Conclusions
28 standard multiplets (long and short)
5 special configurations
Measurements at different field levels are required
Alignment only possible with regards to common axis of a multiplet
For given distance some cross-talk between magnet is expected