## Slide 1: Creating / accessing detector geometry
Thursday, July 30
2

## Slide 2
Structure of a macro for ROOT geometry creation
Accessing geometry parameters in the analysis

## Slide 3: Create geometry file
Geometry in TGeo format (ROOT)
Macros for all detectors are in: r3broot/macros/r3b/geo/*.C
Generated files are in r3broot/geometry/*.root

## Slide 4
Documentation:
https://root.cern.ch/drupal/content/root-users-guide-534
chapter 18 - “Geometry”

## Slide 5: Structure of the macro
void create_tof_geo(const char* geoTag)
{
// ------- Load media from media file -----------------------------------
FairGeoLoader* geoLoad = new FairGeoLoader("TGeo","FairGeoLoader");
FairGeoInterface* geoFace = geoLoad->getGeoInterface();
TString geoPath = gSystem->Getenv("VMCWORKDIR");
TString medFile = geoPath + "/geometry/media_r3b.geo";
geoFace->setMediaFile(medFile);
geoFace->readMedia();
gGeoMan = gGeoManager;
// --------------------------------------------------------------------------
// ------- Geometry file name (output) ----------------------------------
TString geoFileName = geoPath + "/geometry/tof_";
geoFileName = geoFileName + geoTag + ".geo.root";
// --------------------------------------------------------------------------

## Slide 6: Create materials
// ----------------- Get and create the required media -----------------
FairGeoMedia* geoMedia = geoFace->getMedia();
FairGeoBuilder* geoBuild = geoLoad->getGeoBuilder();
FairGeoMedium* mAir = geoMedia->getMedium("Air");
if ( ! mAir ) Fatal("Main", "FairMedium Air not found");
geoBuild->createMedium(mAir);
TGeoMedium* pMed2 = gGeoMan->GetMedium("Air");
if ( ! pMed2 ) Fatal("Main", "Medium Air not found");
FairGeoMedium* mTof = geoMedia->getMedium("plasticForTOF");
if ( ! mTof ) Fatal("Main", "FairMedium plasticForTOF not found");
geoBuild->createMedium(mTof);
TGeoMedium* pMed34 = gGeoMan->GetMedium("plasticForTOF");
if ( ! pMed34 ) Fatal("Main", "Medium plasticForTOF not found");
// --------------------------------------------------------------------------

## Slide 7: Create top volume
// -------------- Create geometry and top volume -------------------------
gGeoMan = (TGeoManager*)gROOT->FindObject("FAIRGeom");
gGeoMan->SetName("TOFgeom");
TGeoVolume* top = new TGeoVolumeAssembly("TOP");
gGeoMan->SetTopVolume(top);
// --------------------------------------------------------------------------

## Slide 8
Create keeping volume
TGeoVolumeAssembly *ptof = new TGeoVolumeAssembly("TOF");

## Slide 9: Shape and volume
Create shape and then volume by assigning material to it
// Shape: TOFBox type: TGeoBBox
dx = 94.450000;
dy = 73.450000;
dz = 0.500000;
TGeoShape *pTOFBox = new TGeoBBox("TOFBox", dx,dy,dz);
// Volume: TOFLog
TGeoVolume *pTOFLog = new TGeoVolume("TOFLog",pTOFBox, pMed34);

## Slide 10: Add to keeping volume
Repeat multiple times with different position / rotation and copy number (in case of complex geometry)
TGeoCombiTrans *t0 = new TGeoCombiTrans("t0");
ptof->AddNode(pTOFLog, 0, t0);

## Slide 11: Add keeping volume to top
Here the global position and rotation are defined
dx = -417.359574;
dy = 2.400000;
dz = 960.777114;
TGeoRotation *gRot = new TGeoRotation();
gRot->RotateX(0.);
gRot->RotateY(-31.000000);
gRot->RotateZ(0.);
TGeoCombiTrans* pMatrix2 = new TGeoCombiTrans("", dx,dy,dz,gRot);
top->AddNode(ptof, 0, pMatrix2);

## Slide 12
Test the geometry and write it to output file
// --------------- Finish -----------------------------------------------
gGeoMan->CloseGeometry();
gGeoMan->CheckOverlaps(0.001);
gGeoMan->PrintOverlaps();
gGeoMan->Test();
TFile* geoFile = new TFile(geoFileName, "RECREATE");
top->Write();
geoFile->Close();
// --------------------------------------------------------------------------

## Slide 13: Sensitive (active) volumes
In the corresponding detector class R3BTof.cxx
Implement virtual function, which checks the name of a volume
Bool_t R3BTof::CheckIfSensitive(std::string name)
{
if (TString(name).Contains("TOFLog"))
{
return kTRUE;
}
return kFALSE;
}
Name assigned in the geometry macro

## Slide 14
Accessing geometry (simulation)

## Slide 15
Fix in your FairSoft installation (missing geant3 data files)
  cd FAIRSOFT_BUILD/share
  mkdir geant3
  cd geant3
  cp -r FAIRSOFT_SOURCE/transport/geant3/data .
  cd R3BROOT_BUILD
  . ./config.sh
  cmake ../r3broot

## Slide 16: Run the standard simulation
cd BUILD_DIR
. ./config.sh
cd SOURCE_DIR/macros/r3b
root -l r3bsim.C
[..] .q

## Slide 17: Implementation in macro
{
// Open parameter file
TFile *file = new TFile("r3bpar.root");
// Get the complete geometry created during simulation
FairGeoParSet *par = (FairGeoParSet*) file->Get("FairGeoParSet");
// Get the volume with specific name
TGeoVolume *toflog = gGeoManager->FindVolumeFast("TOFLog");
// Get its shape
TGeoBBox *box = (TGeoBBox*)toflog->GetShape();
cout << endl << " half-width x = " << box->GetDX() << " cm" << endl;
}

## Slide 18: Implementation in the code (analysis task)
#include “FairRuntimeDb.h”
#include “FairGeoParSet.h”
#include “TGeoVolume.h”
In the SetParContainers() member-function
  FairRuntimeDb *rtdb = FairRuntimeDb::Instance();
  fgeopar = (FairGeoParSet*) rtdb->getContainer(“FairGeoParSet”);
In the Init() member-function
  TGeoManager *geo = fgeopar->GetGeometry();
  TGeoVolume *toflog = geo->FindVolumeFast(“TOFLog”);
  …