## Slide 1: V Stancalie1, M. Zamfirescu1, J. Rothardt3,4, M. Letsinski2, Z. Adelcovic2,R. Klas3,4, M. Tschernajew3,4, T. Kühl2,3, T.Stöhlker2,3 1National Institute for Laser, Plasma and Radiation Phys.,077125 Magurele-Ilfov, Romania 2 GSI Helmholtzzentrum für Schwerionenforschung, 6429 Darmstadt, Germany 3 Helmholtz Institute Jena, 07743 Jena, Germany 4Institute of Applied Physics, Friedrich-Schiller-Universität Jena, 07743 Jena, Germany
Coupling of lasers to the UHV of storage rings

## Slide 2
OUTLINE
Motivation & Introduction INFLPR in-kind contribution to SPARC@FAIR
The UNIT Summary of the most important technical parameters of the XUV-storage-ring coupling unit
Physics related Summary of theoretical and experimental works performed at the INFLPR in support of SPARC@FAIR
Outlook

## Slide 3
MOTIVATION
The Technical Design Report: SPARC@HERS: Instrumentation, approved by the Expert Committee Experiments (ECE) on 22 Jan 2016, establishes a large group of Institutes, including the National Institute for Laser, Plasma and Radiation Physics (INFLPR), distributed over the subjects Laser Spectroscopy, Intense Laser/Ion Interaction and Laser Cooling.
More than 70 researchers, including the INFLPR researchers are listed as participants for these subjects. The INFLPR in-kind contribution is dedicated to design work on the laser beam transport and interaction chamber for the HESR.
The INFLPR scientific collaboration within different SPARC working groups started in 2006 ( DR and MPI studies)
WP 1.2. High Intensity Laser; WP 3.11. Implementation of a Laser Setup; Theory working group
Time | PSP code 1.3.1.3.11 |  |  | Costs
Construction 2007 - 2012 | Investment | Experiment Infrastructure | Laser set-up | 200 kE
 | Development of an X-ray laser | Test Experiments at the Reinjection Beam Line | Laser System with High Repetition rate, Installation of Components | 200 kE /2005

## Slide 4
The development of new lasers with novel sources like soft-X-ray lasers or high average power XUV-lasers require specific technical design for the coupling module to the storage ring and for the corresponding differential pumping stages (including the turbo pumps).
In collaboration between the Institute of Applied Physics (FSU&HI Jena) and the INFLPR, existing data in conjunction with new experimental tools will be used to establish technical issues and requirements, and workout the design of an appropriate optical experiment coupling the new XUV source and the storage ring.
As a next step we will carry out the commissioning of the experimental setup and configuration which will be the XUV-storage ring coupling unit.
Preliminary technical specifications and requirements of an appropriate solution for coupling of lasers to UHV storage ring are presented here.
INTRODUCTION

## Slide 5
THE UNIT
Vacuum chambers
Vacuum pumps and controllers incl. security shut down system
Mechanical support frame for mounting at beam height
Pressure measurement system for all chambers
Adjustment system for below mounted in-flange tubes
Heater blankets

## Slide 6
Turbo-pump
Pre pump
70 cm
60 cm
20 cm
Pre pump
HHG chamber
Tube d=5mm,
L=100mm
Gas nozzle
Turbo-pump
Pre-pump
Opposite
nozzle
Ar
GIPs
XUV mirrors
30 cm
Mirror chamber
THE UNIT: Concept of the XUV source

## Slide 7
Turbo-pump
Pre pump
4xDN63 CF
x
z
y
70 cm
mirror chamber
(angular, chamber)
60 cm
20 cm
15 cm
Pre pump
Fast shutter valve CF 100
30 cm
(round chamber)
Pinhole
10-3 mbar
10-6 mbar
10-11 mbar
Cleanest Space
Gas jet
1. option:
Apertures
Pump
Pump
Pump
Pump
Pump
Pump
Aperture 10mm
Turbo-pump
THE UNIT: Concept of the XUV source

## Slide 8
Pre pump
4xDN63 CF
x
z
y
60 cm
Filter
20 cm
15 cm
Pre pump
Fast shutter valve CF 100
Pinhole
10-3 mbar
10-6 mbar
Coupling unit / differential pumping unit
10-11 mbar
Cleanest Space
T=5% (each filter)
Needs to be improved!
Gas jet
2. option:
Filter foils
Turbo-pump
70 cm
mirror chamber
(angular, narrow chamber)
30 cm
(round chamber)
Turbo-pump
THE UNIT: Concept of the XUV source

## Slide 9
Turbo-pump
Pre pump
4xDN63 CF
70 cm
mirror chamber
(angular chamber)
60 cm
20 cm
15 cm
Pre pump
Fast shutter valve CF 100
30 cm
(round chamber)
Tube d=5mm,
L=100mm
10-6 mbar
10-11 mbar
Gas nozzle
1. option:
Apertures
Pump
Pump
Pump
Pump
Pump
Pump
Aperture 10mm
Turbo-pump
CRYRING
Pre-pump
10-3 mbar
Opposite
nozzle
THE UNIT: Concept of the XUV source

## Slide 10
Turbo-pump
CRYRING
NEG-pump
NEG-pump
Fast shutter
valve CF 100
Tubes d=10mm,
L=100mm
Pre pump
30 cm
Diff. pumping stages 1 -3
THE UNIT: Concept of the XUV source

## Slide 11
Diff. pumping stages: concept of the movable apertures
in the connection flanges
+- 2°
+- 10 mm
+- 10 mm
CF40 flange
Flexible
bellow
Tube holder
Tube
THE UNIT: Concept of the XUV source

## Slide 12: THE UNIT: Concept of the XUV source

## Slide 13
THE UNIT: TECHNICAL SPECIFICATIONS
Input pressure : < 10-6 mbar, mainly Argon or Krypton
Outlet pressure: < 10-11 mbar
Max. heating temperature of whole system: 300 oC
Chamber material : corresponding to the requirements of 10-11 mbar
Surface quality: idem
Clear aperture diameter for XUV beam : 10mm adjustable to the beam axis
Max size: length < 1.2 m (as short as possible)., height < 0.5 m, depth < 0.5 m
Max weight 500kg
Max electrical power consumption: 5kW
Max cooling water heat load: 2KW
Coupling unit and XUV source setup for tests: mid of 2017
Whole system ready for experiments at CRYING: end of 2017

## Slide 14
Physics related/ Expertise/INFLPR
Theory &simulation
(Collaboration with QUB, ISM (former LIXAM), ITM Kyoto Univ, Inst Adv. En.)
Selected bibliography: contributors V Stancalie, G Buica, V Pais, C Iorga
ADNDT 2016(a,b), PRA 2015, AIP Adv 2015, EPJD 2012 - 2014, POP 2005(a,b), PRA 2006, PRA 2005(a,b), LPB 2006, 2007, 2009, Can J Phys 2015, RRP 2015
Structure calculation for ITM-TF:
(RMATX II, GRASP,DARC,ICFT, BPRM)
Photon and Electron interactions with atoms and ions (RMF, TDSE)

## Slide 15
Physics related/Expertise/INFLPR
XRL Experiments. Collaboration with GSI, ENSTA, IPFN, LaserLab
Selected bibliography: contributors D.Ursescu, G Cojocaru, R Banici, R Ungureanu, L Ionel
Optics Express 24, 2016, LPB 32, 2014, Optics Express, 22, 2014, Optics Letters 40, 2015,Optics letters, 37, 2012, Optics Letters, 39, 2014(in collaboration),EPL 94, 2011
Refine the XRL experiments @ GSI
Experiments at shorter XRL wavelengths @ CETAL
Experiments with multiple pulses pumping @ LASERLAB facilities

## Slide 16
Planned activities 2017
Atomic data for HCI ( Li-like and Mg –like)
state-selective photo recombination process in highly charged ions
derivation of an analytical formula for DCS in inelastic electron-hydrogen scattering by a circularly polarized laser field: polarization effects in laser assisted inelastic electron-atom scattering (Buica, PRA2015)
Provide the optimized design of the HHG XUV laser beam –HESR coupling unit
Coupling unit and XUV source setup for tests: mid of 2017
Evaluation of the performances of a coupling unit prototype and perform tests at CRYRING –end 2017. Whole system ready for experiments at CRYING: end of 2017

## Slide 17
Thank you for your attention!
Thank you for you attention!