## Slide 1
J-PARC Slow Extraction
Slow Extraction Workshop (Darmstadt)
2016.06.01
KEK/J-PARC
Masahito Tomizawa

## Slide 2
Contents
J-PARC Slow Extraction History
J-PARC Slow Extraction Schemes
Extraction Devices
Present Performances of the Slow extraction
Issues
Future Plan

## Slide 3
J-PARC Slow Extraction Brief History
•First Slow Beam Jan., 2009
•East Japan Earth Quake March, 2011
•Slow Beam Operation resumed in Jan. 2012
•Radiation leakage incident at the experimental hall
in May, 2013
•Slow Beam Operation resumed in April, 2015
SX-RUN
2015 4/24-5/7、 6/4-6/26、10/15-12/18、
2016 5/27-(6/29)

## Slide 4
Schemes for Very High Extraction Efficiency (low beam loss)
◎Electrostatic Septum (ESS) QF-QF high b (small a) 40m
-> large step size (20mm)
◎dispersion free at ESS + low horizontal chromaticity
-> Separatrix is independent of Dp/p
depends on tune (constant resonant sextupole)
1/3 resonant extraction

## Slide 5
Tune is approached linealy to 22.333 resonance by 48-QFNs in the arcs

## Slide 8
Electro Static Septa (ESS1,2)

## Slide 9
Low field magnetic septa (SMS11,12)
Mid field magnetic septa (SMS21-24)
High field magnetic septa (SMS31,32)
High field magnetic septa (SMS33,34)

## Slide 10
Resonant Sextupoles (RSX1-8)
Bump Magnets (sbmp1-4)

## Slide 11
residual radioactivity improvement by SX collimator
900mSv/h -> 150mSv/h @downstream quadrupole duct (on contact, 4hr. cooling)
Slow Collimators
scrape beam hallo produced by hitting on the ESS ribbons

## Slide 12
RQ P.S.
EQ P.S.
EQ-1
RQ
Beam Spill Feedback System
A beam intensity monitor is placed in external beam line.
Uniform beam spill shape is obtained from tune modulation by quadrupoles EQ
Tune ripples are compensated by quadrupole RQ (and EQ)
A DSP processes EQ and RQ current values from the monitor signal

## Slide 13
Bump
DSP unit
D/O
O/A
SBMP P.S.
Spill
DSP unit
digital
spill monitor
DCCT
to RQ P.S.
to EQ P.S.
gate
optical
AMP
fixed bump
Dynamic bump parameters are processed by
a DSP from QFN pattern and real time EQ currents
Dynamic Bump System
efficiency 98.3%
efficiency 99.5%
real time dynamic bump
Loss -> 1/3.4

## Slide 14
Transverse System (D1 strip line kicker)
500W AMP
500W AMP
500W AMP
500W AMP
combiner
Transverse RF System (D3 strip line kickers in series)
3kW AMP
3kW AMP
matched load
matched load
0.1-100MHz
0.01-200MHz
solenoid(+)
combiner
matched load
matched load
solenoid(-)
1kW
1kW
solenoid(+)
suppress
multipactering
DLC coating
to suppress multipactering
length 1.5m
Length 0.7m

## Slide 15
Mixing
noise width = 62.5 kHz
(/frev = 0.327)
252.5KHz
Transverse RF setting example
1KHz
47.47139057MHz
19steps
Noise width 1KHz
frev=0.191167307692307MHz
D1 strip line kicker
D3 strip line kicker

## Slide 16
Spill DSP
EQ P.S.
Resonant Sextupole P.S.
Dynamic bump DSP
I set
I mon
I set
Stop signal
Stop signal
Present SX Abort System
4 magnets currents are proportionally decreased to zero.
Target
SX BLM
Others
Acc.
Fast MPS
System
OR
QFN correction coil ramping Power Supply
Stop signal
From PLC
Stop signal

## Slide 17
SX Abort Example
SX Beam Study BLM76 (ESS1) beam loss count increase
2015/11/25 12:07 run65 #109878
ESS beam loss
SX Abort
Fast Extraction
To dump
Slow Extraction
Present MR can not abort beam at any timing
Very useful to protect the slow devices and targets from a high intensity beam

## Slide 18
◎Beam Deceleration during debunch process
by RF cavity impedances
present cure -> beam loading compensation by RF feed forward
◎beam loss at Injection period and beginning of acceleration
space charge tune shift or transverse instability
present cures -> tune, chromaticity adjust and BxB F.B.
◎Instability during debunch process
•vacuum pressure rise in the whole ring
•electron cloud
•beam loss in debunch and slow process
present cures -> chromaticity, longitudinal dipole oscillation
Beam Intensity dependent phenomena

## Slide 19
Global offset -19 deg
Global offset -19 -> +21 deg
(after 11/5 RF No5 Gap Open -> Short)
Wall Current Monitor
150ms
w/o dipole oscillation
w/ dipole oscillation
38kW
151106_34,35
151106_14,15
38.7kW
37.7kW

## Slide 20
Global offset -19 deg
#136953
Global offset +21 deg
#137110
Vacuum pressure rise has been suppressed by the dipole oscillation
w/o dipole oscillation
w/ dipole oscillation
37.7kW
38.6kW
Electron cloud monitor ↓
Electron cloud monitor ↓
Electron cloud has been suppressed by the dipole oscillation

## Slide 21
Global offset -19 deg
#136968 37.7kW
Eff. 99.1%
Global offset +21 deg
#137009 38.7kW
Eff. 99.4%
Instability occurred during debunch process
Instability suppressed by dipole oscillation
(after No5 cavity gap short)
(after No5 cavity gap short)
w/o dipole oscillation
w/ dipole oscillation
debunch -> Slow
(Qx’,Qy’) = (-6.0,-7.1) -> (-0.67,-2.4)
debunch -> Slow
(Qx’,Qy’) = (-5.0,-7.1) -> (-0.67,-2.4)

## Slide 22
Upper limit determined from target heat capacity
#110023 (RUN65)
Efficiency 99.52%
Duty 42%
Spill length 2.1s
•dipole oscillation
•Dynamic bump
•ESS1（rotation）,ESS2(parallel、rotation) position tuning
•SMS1(parallel） position tuning
Beam loss distribution at slow region
DCCT
Beam loss distribution In the whole Ring
Beam loss Intensity during extraction
ESS-SMS region
Collimator
(Before Linear Acc)
Red signal x8
41.6kW User Operation Performances
5.52 cycle 2.93s flat top

## Slide 23
41.6kW User Operation Performances
Duty Factor in a Spill
Beam Spill
Large tune ripple produced
by BM and Q current ripple
Av. Duty 42%
Spill length 2.1s
New Result 5/29 Study Duty 58%

## Slide 24
24.5hours
Extraction Efficiency Trend
RUN65
41.6kW (4.8x1013ppp)

## Slide 25
Position and width trends of beam delivered at target
Thanks for Hadron Group

## Slide 26
Trends of Beam Power and its Integration After Recovery
Alanine dosemeter
Total absorption dose so far (2900kWdays)
ESS1 feedthrough port 28kGy
ESS2 feedthrough port 3.6kGy
41.6 kW
Chart: Ave. power (kW)
24 kW
@resumption
1kWday=1.81x10^16 p

## Slide 27
Q076 U
>10 , 1.8
4.0 , 0.8
- , -
- , -
ESS1 D
- , -
7.0, 0.6
- , -
1.8 , 0.2
ESS1 U
- , -
2.0, 0.3
- , -
- , -
Q077 U
- , -
1.0, 0.3
- , -
- , -
SXCol D
5.0 , 0.5
1.7, 0.25
- , -
- , -
Q078 U
- , -
1.0, 0.25
- , -
- , -
aisle
0.27
0.08
0.05
0.018
ESS2 U
- , -
1.4, 0.46
- , -
1.8 , 0.2
SMS1 U
3.0 , 0.5
1.1 , 0.2
- , -
- , -
SMS1 D
- , -
1.0 ,0.25
- , -
- , -
SMS2 U
- , -
0.3 ,0.05
- , -
- , -
SMS31 U
- , -
3.6 , 0.4
- , -
- , -
SMS33 U
- , -
0.85 , 0.1
- , -
- , -
Q082 U
- , -
2.0, 0.25
- , -
- , -
aisle
0.12
0.01
0.015
0.009
Residual Radioactivity
12/18 4hours on contact, 30cm
12/25 on contact, 30cm
01/20 on contact, 30cm
03/09 on contact, 30cm
The 42kW SX beam stopped 12/18 9:00
Unit: mSv/h

## Slide 28
•intra-bunch F.B. --- the instability at the beginning of the acceleration
•(dipole oscillation and) 2nd harmonic cavities
RF bucket is miss matched -> reduces peak current
•longitudinal VHF cavity (2018)
large dp/p and lower peak current
•Repetition rate will go up for a higher beam power
Power supply for BM and QM will be replaced for Nu operation (2018)
5.52 s -> 3.93s (2.63 s flat top)
Beam power gain x 1.4 under discussion
Plans for a higher beam power

## Slide 29
Development of titanium ESS
◎ titamium chamber、yoke、endplates
to reduce residual radioactivity
140 kV achieved (operating voltage 104.4kV)
◎Feedthrough
•titanium ring and flange
•electric field gradient
•fluorinert circulation
◎Planned RF contact

## Slide 30
Future ESS
○ scatterer
○ low-Z septum material
Carbon wire ESS R&D
High voltage test will be planed after finishing titanium ESS job
φ120-150mm (φ7mm fibers are twisted)
CNT
φ125mm (three φ50mm)
φ80-90mm

## Slide 31
COMET
(COherent Muon to Electron Transition)
COMET beam line and building
has been constructed.
Phase-I
Phase-II
Beam power 3.2kW
Sensitivity <10-14
Beam cond. 2018〜
DAQ 100days
Beam power 56kW
Sensitivity <10-16
Beam cond. 2022〜
DAQ 1 year

## Slide 32
8GeV Acceleration Study for COMET (w/o Slow)
V-rms-e 0.68p
H-rms-e 0.62p
Measure profiles at the end of flat top
Measured extinction v.s. RF voltage
8 GeV Acc. and Fast extraction
8GeV Slow Extraction Test and Extinction Measurement will be planned

## Slide 33
SX-Stretcher Design Study
Neutrino RUN and SX RUN compete for beam time
A SX stretcher has a great advantage.
During slow extraction (2-3s), beam can be delivered to Neutrino.
Base line design
Hybrid: SC-quadrupole magnets
and combined function transmission line superferric magnets
MR (One arc module)
Hybrid lattice ring (One arc module)
C= 1567.5m
(Qx,Qy)=(22.295,20.75)
Transition γ 31.6i
C= 1567.5m
(Qx,Qy)=(22.295,20.75)
Transition γ 21.7
Collaboration with TRIUMF A.Konaka
KEK Low Temp. Center T. Ogitsu G