## Slide 1: Interface model for SIS18 and UNILAC
Sabrina Appel, Primary Beams Division, Beam Physics Department, GSI, Darmstadt

## Slide 2: Optimization of a complex system
Define main optimization parameters; Separation into subsystems; Modeling
Injection
Extraction
SIS18
Performance goal:
max. N/s
Experiment or SIS100
UNILAC
  Maximum intensity per second (N/s)
  Reference beams: p, A18+, U28+, U73+
  Simple scaling laws
  Numerical optimization
Optimization of the ion production chain:
Modeling:
  One attempts to find simplest model & fastest algorithms which contain the necessary physics

## Slide 3: Optimization of a complex system
Intensity limitations (for N/s)
N
N,η
UNILAC
Light ions: Space charge
SC
DV
Intermediate charge states: Dynamic vacuum
Understanding of limitations; Define interface parameters and conditions
SIS18
Perf. goal:
max. N/s
Experiment or SIS100
UNILAC
Injection
Extraction
Multi-turn injection
(Liouville)

## Slide 4: Numerical Optimization
The optimization problem is multi-objective
The criteria can be contradicting:
Improving one criterion means worsening others
Pareto front:
Find set of a optimal solutions instead of a single solution
Scan
Gradient
Traditional:
Gradient-based methods or parameter scans
Darwin Finches
J. Gould,
Voyage of the Beagle
New methods:
Genetic algorithms, particle swarms, …

## Slide 5: Intensity limitations: Space charge (SC)
Analytical model
Analytic solution of the Poisson equation for a 2D Gaussian (tune spread and particle amplitude)
(Max. tune shift)
z
x
y
Concept:
Space charge is the inter-particle Coulomb force.
In the beam frame SC force be evaluated with the Poisson’s equation.
Space charge effects:
SC limited or/and determine beam parameters and accelerator components (CERN LHC injector chain + FAIR)
Gauss
Qx
KV
Qy
Qx
SC tune shift from 2D Poisson solver
Particle In Cell algorithms
1-3D self-consistent tracking codes allow detailed investigation
Simple scaling law
Notes: detailed investigation

## Slide 6: Intensity limitations: Dynamic vacuum (DV)
Intermediate charge state:
Large cross sections for electron stripping/capture
Pressure run away initiated by ion loss
Beam lifetime reduction
Initial pressure bump due to injection loss
No Simple scaling law but fast numerical algorithms
P. Spiller, Review, Nov 2013
STRAHLsim: Accurately predict of the dynamic vacuum evolution (local model)
Global model for SIS18 ”transmission”

## Slide 7: Multi-turn injection into SIS
Parents
Reproduction
Offspring
Selection
Genetic algorithm
Better OPT results
Dependence of interface parameter
Optimization goal
x
x’
Septum
Acceptance
Liouville’s theorem: Injected beams only in free space
Loss should be as low as possible
Many beamletts as possible into machine acceptance
Analytically description, but the model is underrepresented
Notes: dependence

## Slide 8: Interface: UNILAC and SIS18
N
N,η
UNILAC
Multi-turn injection
SC
DV
allows to define a frame, in which the required beam parameter can be matched at best for a high performance
Dependence of interface parameter