## Slide 1: The Silicon Tracking System of the CBM experiment at FAIR
  Anton Lymanets1,2 for the CBM collaboration
DPG Frühjahrstagung
14 - 18 March 2016
Technische Universität Darmstadt
1 GSI, Darmstadt, Germany
2 Institute for Nuclear Research, National Academy of Sciences, Ukraine

## Slide 2: Facility for Antiproton and Ion Research
GSI
FAIR
existing
facility
under construction
SIS-100
protons: 30 GeV
Au: 11 GeV/nucleon
SIS 100

## Slide 3: QCD phase diagram
СВМ
nuclear matter formation at high baryon density and temperature
models predict 1st oder phase transition with formation of mixed and exotic phases
existence of critical end-point
10 GeV/nucleon

## Slide 4: Probing the dense fireball
p, Λ, Ξ+, Ω+, J/ψ
Ξ-, Ω-, φ
ρ → e+e-, μ+μ-
π, K, Λ, ...
resonance decays
Au+Au collision at 10.7 GeV/nucleon as simulated in the UrQMD transport code
Leptonic and hadronic signals from all stages of nucleus-nucleus collisions
Rare probes: multistrange hyperons, low mass vector mesons, charmonium, strange dibaryons, hypernuclei.

## Slide 5: CВМ experiment
HADES:
p+p, p+A
A+A (low mult.)
Micro
Vertex
Detector
Dipole magnet
Silicon Tracking System
Time-of-flight detector
Projectile
spectator
detector
Transition
radiation
detector
Muon detector
Ring
imaging
Cherenkov
detector
Online event selection on a computing farm
Vertexing: MVD
Tracking: STS, MUCH, TRD, ToF
Particle ID: RICH, TRD, ToF
Calorimetry: ECAL, PSD

## Slide 6: Tracking challenge
central nucleus-nucleus collision
~700 charged particles

## Slide 7: Experimental requirements
105 - 107 Au+Au collisions per second.
secondary vertex determination (σ≈50 µm)
track reconstruction from hadron and lepton probes
fast and radiation tolerant detectors
self-triggering front-end electronics
fast data acquisition system + online event selection on a computing farm
4D track reconstruction

## Slide 8: Online data flow
First-level Event Selector

## Slide 9: Silicon Tracking System
8 tracking stations in the magnet aperture
double-sided silicon microstrip detectors
Acceptance: 2.5˚< 𝜃 < 25˚
Active area: 4 m2

## Slide 10: STS integration concept
8 tracking stations
ladder
mechanical unit
1 m
material budget for station 8
896 detector modules including:
1220 double-sided microstrip sensors
~ 1.8M readout channels
~ 16 000 readout chips
~ 16 000 ultra-thin readout cable stacks
X/X0, %

## Slide 11: Detector module concept
896 modules required
4-5 modules per ladder
Modules comprises:
sensor
ultra-thin mirocables
front-end board

## Slide 12: Silicon microstrip sensors
double-sided
1024 channels per side
58 µm pitch
300 µm thick
stereo angle 7.5˚(р-side)
dimensions: 6×2 cm2, 6×4 cm2, 6×6 cm2, 6×12 cm2
2nd metallization to interconnect short corner strips
Layout STS5 and 6

## Slide 13: Silicon microstrip sensors
6×12 cm2 sensor design with readout pads in the middle of the sensor (in production by Hamamatsu)
two daisy-chained sensors with 6×6 cm2 size each

## Slide 14: Charge collection studies
Irradiated sensors:
𝛷 = 2e14 neq/cm2
(twice maximum
fluence for CBM
lifetime)
90Sr
Irradiated sensors show reduction in charge collection efficiency of up to 20%
CCE confirmed in a 2 GeV proton beam test at COSY

## Slide 15: Microcables
Material budget per cable stack: 0.228 X0 (equivalent to 213 µm Si)
meshed spacer
signal layer: 64 Al lines of 116 µm pitch, 10 µm thick on 14 µm polyimide, lengths up to 55 cm

## Slide 16: STS-XYTER ASIC
STS-XYTER ASIC
channels | 128, polarity +/-
noise | 1000 e– at 30 pF load
ADC range | 16 fC, 5 bit
clock | 160 MHz
power | < 10 mW/channel
timestamp | < 5 ns resolution
out interface | (1..5)×320 Mbit/s LVDS
data driven architecture
fast branch: time-stamp
slow branch: signal digitization
double-threshold discrimination: time stamp is vetoed if ADC produced no signal
CBM-NET
(v1.0 )
GBT (V2.0)
LSB veto
ts = 30 ns
ts = 80 ns
r/o logic
CSA + PSC
SLOW SHAPER
FAST SHAPER
FAST DISCRIMINATOR
5-BIT FLASH ADC
READOUT/TEST CONTROL LOGIC
Noise performance with STS-XYTER v1 is ~1800 e− (chip + two daisy-chained sensors with 62 mm strips + 30 cm cable)
Significant improvements expected after redesign
ENC vs channel number

## Slide 17: Detector module assembly
1. TAB bonding of microcables to ASICs
3. TAB bonding of microcables to sensors on both sides
2. Wire bonding ASICs to front-end boards + bond protection (glob top)

## Slide 18: Current engineering studies
Front-end Electronics Boards
Read-out Boards, Power Boards
Cooling plate
cabling
cooling
FEB stack 200 W
Bi-phase CO2 cooling system
STS electronics total power dissipation: 42 kW
cooling plate with integrated channels
TRACI XL: 1 kW cooling prototype

## Slide 19: Radiation environment
FLUKA calculation of non-ionizing dose for 10 AGeV Au+Au collisions at SIS100 and the CBM experiment in electron-hadron configuration.
Radiation load per typical operation year
Non-ionzing dose: 1013 neq/cm2 (worst case)
Ionizing dose: <100 kRad
Operation conditions:
1 month of running at 109 ions/s on a 1% X0 target
neq/cm2
neq/cm2

## Slide 20: STS performance simulation
Track reconstruction efficiency
Momentum resolution
realistic detector model
CbmRoot simulation framework
Cellular Automaton track finder
Kalman Filter track fitting

## Slide 21: Feasibility studies at SIS-100
5×106 central Au+Au events 10 GeV/nucleon, using TOF PID
1011 central Ni+Ni events 15 GeV/nucleon, using TOF PID
Operation scenario: from pA (up to 30 GeV) to AuAu (2–11 GeV/nucleon) systems
𝛆4𝜋 = 1.7%
𝛆4𝜋 = 16.5%
Tue, 17:45 HK 25.5
Tue, 16:30 HK 24.1

## Slide 22: Summary
STS system concept has been presented
Progress with prototyping and engineering
Sensor prototypes delivered, radiation hardness is under investigation
Current activity is module assembly and system integration
Full-size module mockup has been produced
System engineering: mechanical structure, mounting of electronics, cabe routing. Close to completion.
Feasibility for physics measurements demonstrated
Production readiness in 2017

## Slide 23: Institutions participating in STS
Germany
Darmstadt, Germany, GSI Helmholtz Center (GSI)
Karlsruhe, Germany, Karlsruhe Institute of Technology (KIT)
Tübingen, Germany, Eberhard Karls University (EKU)
Poland
Krakow, Poland, AGH University of Science and Technology (AGH)
Krakow, Poland, Jagiellonian University (JU)
Warsaw, Poland, Warsaw University of Technology (WUT)
Russia
Dubna, Russia, Joint Institute for Nuclear Research (JINR)
Moscow, Russia, Moscow State University (SINP-MSU)
Ukraine
Kharkov, Ukraine, LED Technologies of Ukraine Ltd (LTU) * Partner
Kiev, Ukraine, Kiev Institute for Nuclear Research (KINR)

## Slide 24: CBM STS assembly flow

## Slide 25: STS related presentations at DPG 2016
Mon, 14:45 HK 8.3 Grigory Kozlov Time-based cluster and hit finding for the STS detector in the CBM experiment at FAIR
Mon, 15:00 HK 7.4 Evgeny Lavrik Optical quality assurance procedures for the sensors of CBM STS Detector
Mon, 15:15 HK 7.5 Maksym Teklishyn Quality assurance tests of the CBM Silicon Tracking System sensors with an infrared laser
Mon, 16:30 HK 14.1 Hanna Malygina The detector response simulation for the CBM Silicon Tracking System as a tool for hit error estimation
Group talk Mon, 16:30 HK 15.1 Anton Lymanets The Silicon Tracking System of the CBM Experiment at FAIR
Mon, 17:00 HK 15.2 Iaroslav Panasenko, Pavel Larionov Quality assurance of the silicon microstrip sensors for the CBM experiment
Tue, 15:00 HK 21.4 Ievgeniia Momot Radiation tolerance of microstrip sensors for the CBM Silicon Tracking System
Tue, 18:00 HK 29.7 Adrian Rodriguez Rodriguez The CBM-STS front-end electronics
Wed, 18:30 HK 45.9 Carmen Simons, Daniel Soyk, and Robert Visinka The workflow of CBM-STS silicon strip sensor module-assembly
Poster Wed, 18:30 HK 45.20 Evgeny Lavrik Bi-Phase CO2 cooling of the CBM STS detector
Poster Wed, 18:30 HK 45.63 Oleg Vasylyev, W. Niebur Mechanical integration of the detector components for the CBM Silicon Tracking System
Thu, 17:45 HK 60.6 Jörg Lehnert, David Emschermann The read-out chain of the CBM STS detector