## Slide 1: Tracking

## Slide 2: Motivation
Why tracking?
  Distinguish charged from neutral particles
  Determine the charge of a particle
  Determine the absolute momentum
  Determine the direction of momentum
  Determine the production/decay point
  See the full story

## Slide 3: AntiProton Annihilation at Darmstadt
13 m

## Slide 4: Magnet System
Solenoid magnet to measure pt Helix approximation
Dipol magnet to measure pl for forward tracks Parabola approximation

## Slide 5: Spurdetektoren

## Slide 6: Tracking Detectors
Micro Vertex Detector
Straw Tube Tracker
Forward Tracking Stations
Luminosity Detector
GEM Detector

## Slide 7: PANDA Event Simulation

## Slide 8: PANDA Event Simulation

## Slide 9: Procedure
Full track reconstruction happens in various steps:
  Group the hits which belong to the same track
  Fast evaluation of the track parameters
  Precise fitting of the track parameters
  Propagate track parameters to the point where they are needed
  pattern recognition / track finding
  pre-fit
  Kalman fit
  propagation / extrapolation

## Slide 10: The Data
The following objects contain the tracking information
They “live” in pnddata/TrackData
  PndTrackCand
    Collection of hits inside a track
    Output of track finder
  PndTrack
    Parameters of track
    Output of prefit and Kalman fit

## Slide 11: PndTrackCand
Is a collection of hits
Each hit is represented by a PndTrackCandHit which is a FairLink(detId, hitId) plus a sorting parameter rho.
detId is the branch ID of the detector who generated the hits
hitId is the position in the TClonesArray
Rho is an sorting parameter of a hit along the track
No fixed rule how to calculate rho

## Slide 12: PndTrackCand - Rho
Possible candidates for Rho
  Distance from vertex (not a good one)
  Time (but time resolution usually not sufficient)
  Length along track (arc length for helix)
  Secondaries: Where is the start of the track?

## Slide 13: PndTrack
This is the hypothesis of a track
  Identified by the momentum, charge and position at the first and last hit
  PndTrackCand accessible via PndTrack
  Why two times the track information?

## Slide 14: Data Summary
We have two objects to describe a track:
PndTrackCand which contains the list of hits in the track
PndTrack which contains the parameters of the track
Why two objects instead of one?

## Slide 15: Data Summary
We have two objects to describe a track:
PndTrackCand which contains the list of hits in the track
PndTrack which contains the parameters of the track
Why two objects instead of one?
  PndTrackCand can be used by different algorithms or different particle hypotheses

## Slide 16: Track finding

## Slide 17: Track Finding Strategies
local
  operates on the data of one sub-detector
  finds all possible tracks in this sub-detector
  tracks in different sub-detectors are combined via their track parameters
  refit of complete track at the end
global
  operates on the data of more then one sub-detector at once
  finds a complete track

## Slide 18: Track Finding Strategies
local vs. global
  local
    optimized algorithms for each sub-detector
    no need to wait until data from all sub-detectors is available
    several different algorithms needed (for each sub-detector and to combine the data)
    how to handle tracks with insufficient hits in one sub-detector?
  global
    all information at hand from the beginning
    just one (but big) algorithm
    treatment of different kind of data difficult (straws vs. pixel)

## Slide 19: Track Finding Strategies
Additional considerations:
All at once  Iterative
Online  Offline
  Performance vs. speed
Primary  Secondary
  Primary: coming from the interaction point
  Secondary: all the rest
  Primary tracks more easy to find
  Secondaries important e.g. for hyperon physics

## Slide 20: Track Finding
Considerations
  Finite number of planes
  Often only one coordinate per plane
  Interactions with material (multiple scattering, energy loss, Bremsstrahlung for e-)
  Detector imperfections (inefficiency, limited spatial resolution, alignment)
  Extra hits from noise, pileup, low momentum particles…

## Slide 21: Track Finding
Conflicting Demands
  High efficiency find all true tracks relevant for the physics
  High purity minimize incorrect assign- ment of hits to a track, that reduces the resolution
  Low ghost rate do not find fake tracks
  Speed often online tracking is needed as part of a trigger decision (limited time (latency) and resources).

## Slide 22: Track Finding with 1D Detectors
Tracking in space (generally needs many layers)
  Combine layers to get a 3D space point,
  do 3D tracking with these points
Tracking in projections (generally needs more CPU)
  find 2D track candidates, then
  combine projections (here each line in 2D is a plane in 3D)

## Slide 23: Local Method: Track Following
Follow track through layers
  Define initial track segment (track seed)
  Use track model to extrapolate to next detector layer
  Define search window around expected position, depends on resolution and amount of material
  If hit found, add it to the track candidate and iterate to next layer
    Detector inefficiency: if no hit found go to next layer, allow several missing layers
    Allow for combinations, if more than one hit in window follow all paths concurrently, decide later what is correct
Kalman-filter, will be discussed later

## Slide 24: Global Method: Histogramming
For circular tracks (homogeneous B-field (usually solenoid))
Conformal mapping (transformation: circles to lines)
Compute angle F
Make a histogram of F
Find peaks in F histogram
Transforms a 2D problem to 1D
If tracks don’t come from (x,y)=(0,0)
  Line is offset, and washed out peak in 1D histogram
  Solution: x’=x-x0 and y’=y-y0 where (x0,y0) is e.g. the innermost point on the track

## Slide 25: Histogram Method
Coordinate space Transformed space
As you see, the histogram binning is not arbitrary, it is related to the resolution. Too fine: then the hits don’t make a peak Too coarse: then the peaks overlap, and the resolution gets worse.

## Slide 26: Hough Transformation
Histogramming technique based on coordinate transformation
Transform point (image space) to parameter space
Hit in image space becomes a trajectory in parameter space
Hits from the same track  trajectories cross in param. space
Binning of parameter space (histogram) (bin size: tradeoff between resolution, efficiency and speed)
Find peaks in histogram  track candidate
Very fast for simple track models (straight line, circle)
Well suited for parallel processing  fast online trigger

## Slide 27: Offline PANDA Examples

## Slide 28: Global pattern recognition
default global PR
Contains: MVD + STT + GEM
Starts from MVD and STT stand alone track finders
Extrapolates STT to MVD and vice versa
New track candidate of MVD and STT is refitted
Refitted track extrapolated to GEM stations
Only primary tracks
No refit with GEM stations because magnetic field in GEMs not homogeneous enough for helix assumption
PndSttMvdTrackFinder / PndSttMvdGemTrackFinder

## Slide 29: Global pattern recognition 2
Alternative global PR
Does not start at any specific detector
Treats MVD, STT and GEM hits equal
Looks for correlation in xy plane
Tries to gather z information when possible
Hit mixing to avoid unphysical correlations
Only primary tracks
PndBarrelTrackFinder

## Slide 30: Online PANDA Examples

## Slide 31: Riemann Track Finder
The Riemann Track Finder is based on a fast circle fit using a Riemann surface:
  The 2D points in xy-plane are projected on a paraboloid (w = x2 + y2)
  A fast fit of a plane through the new 3D points give you the plane parameters which can be bijectively mapped to the radius and the origin of the circle
  In a second fit one plots the arc length of the hits on the circle versus their z-position which should be a straight line
The method is very fast if you neglect energy loss and multiple scattering
Both can be implemented which leads to very good accuracy but then it is slower than a standard Kalman fit
Riemann fit was implemented by Sebastian in pandaRoot but without error treatment

## Slide 32: Riemann Track Finder
Points to be fitted
Add z-dimension
Map onto paraboloid

## Slide 33
Calculation of plane through 3D points simple eigenvalue determination

## Slide 34: Riemann Track Finder
Find all (reasonable) combinations of three points
Calculate Riemann plane
Calculate distance of all hits to plane
If below threshold add them to plane
Recalculate plane at the end (or in between?)
Take only those planes (circles) with more than 3 hits
Linear fit or arc length vs. z-coordinates of hits for z-Dimension

## Slide 35: CA Track Finder

## Slide 36: Cellular Automaton as Track Finder
Build short track segments
Connect according to track model, estimate a possible position on a track
Tree structures appear, collect segments into track candidates
Select best track candidate

## Slide 37: Cell Track Finder

## Slide 38: CellTrackFinder
1. Generation of tracklets in STT
  Primary tracklets: use of cellular automaton
  Combination of tracklets: use of Riemann Fit
  Faulty: Fit to center of the tubes
  Add remaining hits to best fitting Track
 TrackletGenerator
 HitCorrector
2. Correction of STT-Hits based on event time
  Correct points for Riemann Fit by calculating tangents to the isochrones

## Slide 39: 1. TrackletGenerator Cellular Automaton
Abstract discrete model for dynamic systems
Definition by:
  Cell
  Neighborhood relations
  Discrete number of states
  Transition rules for states
  Simultaneous changes

## Slide 40: 1. TrackletGenerator Cellular Automaton - Apply to STT

## Slide 41: 1. TrackletGenerator Cellular Automaton – Apply to STT
1
2
> 2
Number of Neighbours:
unambiguous
ambiguous

## Slide 42: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 43: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 44: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 45: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and one or two neighbours
Rule: Compare your status with the status of your neighbours and take the smallest one

## Slide 46: 1. TrackletGenerator Cellular Automaton - Apply to STT
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 47: 1. TrackletGenerator Cellular Automaton - Apply to STT
15
7
1
10
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 48: 1. TrackletGenerator Cellular Automaton - Apply to STT
1/10 7/15
7/15
1/10
7/15
1/10
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 49: 1. TrackletGenerator Cellular Automaton - Apply to STT
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
Cell: Straw with hit and more than two neighbours
Rule: Copy the status of all your neighbours into your status

## Slide 50: 1. TrackletGenerator Riemann fit
Fit Plane
Normal vector  Circle parameters
quadratic  linear
explicit solution
already implemented in PandaRoot
Advantages

## Slide 51: 1. TrackletGenerator Result of the combination
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15

## Slide 52: Circle Hough

## Slide 53: Idea
(0,0)
STT Isochrone

## Slide 54: Idea
Track (circle) tangent to isochrone

## Slide 55: Idea
Track (circle) tangent to isochrone
Goes through (0,0)

## Slide 56: Idea
Track (circle) tangent to isochrone
Goes through (0,0)

## Slide 57: Idea

## Slide 58: Idea

## Slide 59: Idea

## Slide 60: Idea

## Slide 61: Idea

## Slide 62: Idea
Calculate possible circles for all hits
Fill circle centers into xy-histo
Find peaks
Hits in peaks are part of a track
Calculate track parameters from circle centers

## Slide 63: DPM Example 2

## Slide 64: DPM Example 2

## Slide 65: DPM Example 2

## Slide 66: DPM Example 2

## Slide 67: Kalman Filter

## Slide 68: Track Parametrization
In vacuum the trajectory is defined by the initial parameters or state vector.
5 parameters are necessary and sufficient
Each point along the trajectory, describe with a 5-component state-vector (and its 5x5 covariance vector)
Should be continuous to small changes, approx. Gaussian errors, linear approximation to track propagation
Best parameterization depends upon B-field and detector geometry: e.g. detector surface normal to z-axis surface=beam pipe (collider)
✧ DELPHI barrel: x = (Φ, z, θ, β = φ − Φ, 1/R)
✧ DELPHI forward: x = (x, y, θ, φ, 1/R)
✧ CMS global: position, momentum, charge
✧ CMS local: x = (q/p, dx/dz, dy/dz, x, y)

## Slide 69: Panda Track Parametrization
The physical path of a particle of assigned mass m and momentum p is a six-fold entity of parameters: x, y, z, px, py, pz (+ q)
Track is defined as set of points in detectors, corresponding to the intersection of the physical path of a particle with the detector planes  among six parameters one is fixed by the measurement plane
FairTrackPar/FairTrackParP/FairTrackParH

## Slide 70: Track Model
Track Model describes how the state vector at one surface depends on the state vector at a different surface. (describes particle trajectory)
xk = fk|i(xi)
fk|i is the track propagator from surface i to surface k.

## Slide 71: Track Model
  No magnetic field, no material: straight line
  Homogeneous magnetic field: helix (2D circle)
  Analytic calculation only for simple cases (like above)
  Inhomogeneous B-field, material (energy straggling, small angle scattering): iterative numerical extrapolation of track segments over short distances
    Many tracks, many extrapolation steps, need high computing speed
    Simplest: Newton iteration, or describe each segment as a parabola
    Better: numerical integration like “Runge-Kutta”

## Slide 72: Measurement Model
The measurement model describes the functional dependence of the measured quantities on the state vector at the detector surface:
The vector of measurements mk usually collects the measured coordinates, but may contain also other quantities, e.g. measurements of direction or even momentum.
Error on measurement assumed to be Gaussian which is not always true!

## Slide 73: Kalman Filter
Iterative LS estimation of the state vectors in all measurement layers (or even material layers).
Two steps are repeated:
  Prediction: extrapolate the state to the next layer, add up multiple scattering, subtract energy loss
  Update: combine the predicted state with the current measurement
A good initial state (seed) is important. Its weight should be small.

## Slide 74: Prediction stage of Kalman Filter

## Slide 75: Update stage of Kalman Filter

## Slide 76: Smoother
The last estimate xn of the filter contains the full information.
The full information can be propagated back to all previous estimates.
This can be done by another iterative procedure, the smoother.
The smoother runs in the opposite direction to the filter.

## Slide 77: Smoother
The smoother can also be realized by combining two filters.
One filter runs from m1 to mn: forward filter .
One filter runs from mn to m1: backward filter .
The smoothed states are the weighted mean of the predicted states one filter and the updated states of the other filter.
This is numerically more stable.
The smoothed state x0|n is the best linear estimate and therefore the same as the usual Least-Squares estimate x

## Slide 78: Kalman Filter
The Kalman filter can therefore be used for track finding.
Generate a track seed.
Iterate the following sequence:
  Extrapolate and look for compatible measurements.
  If there is none, go on.
  If there is one, take the most compatible one and make an update.
  If no compatible measurements can be found in several layers, drop the track candidate.

## Slide 79: Kalman Filter in PandaRoot
Genfit
Originally started as part of PandaRoot as a generic fitting package written by TU Munich
Now independent external package
Exists (at the moment) as two implementations: Genfit 1 and Genfit 2
Genfit 1 is a very old version of Genfit using GEANE as track propagator
Genfit 2 is a more up-to-date version using a Runge Kutta track propagator  change to recent Genfit 2 planned for next release
Tests of performance are ongoing in PandaRoot

## Slide 80: Genfit
Offers different track fitters:

## Slide 81: Usage of Genfit in PandaRoot
PndRecoKalmanTask* recoKalman = new PndRecoKalmanTask();
recoKalman->SetTrackInBranchName("SttMvdGemTrack");
recoKalman->SetTrackOutBranchName("SttMvdGemGenTrack");
recoKalman->SetBusyCut(50); // CHECK to be tuned
//recoKalman->SetIdealHyp(kTRUE);
//recoKalman->SetNumIterations(3);
recoKalman->SetTrackRep(0); // 0 Geane (default), 1 RK
//recoKalman->SetPropagateToIP(kFALSE);
fRun->AddTask(recoKalman);

## Slide 82: Usage of Genfit2 in PandaRoot
PndRecoKalmanTask2* recoKalman = new PndRecoKalmanTask2();
recoKalman->SetTrackInBranchName("SttMvdGemTrack");
recoKalman->SetTrackOutBranchName("SttMvdGemGenTrack");
recoKalman->SetBusyCut(50); // CHECK to be tuned
//recoKalman->SetIdealHyp(kTRUE);
//recoKalman->SetNumIterations(3);
//recoKalman->SetTrackRep(0); // 0 Geane (default), 1 RK
//recoKalman->SetPropagateToIP(kFALSE);
fRun->AddTask(recoKalman);

## Slide 83: Track Propagation - GEANE

## Slide 84: GEANE
Track follower / propagator
Simplified geant3 tracking algorithm + error propagation
Original Code is in Fortran
Distributed with geant3 by CERN
Part of FairRoot
It extrapolates both the mean values of the parameters and their covariance matrices
It uses the MC geometry
It takes into account:
  material effects
  magnetic field
  physical effects
Different reference frames
Different kinds of propagation

## Slide 85: Geane Interface
In geane you will find:
FairGeane: this is the task reading in the physics cuts and the physics effects to take into account
This task has to be added to your macro otherwise GEANE will not work!
FairGeanePro: contains the propagation stuff
In trackbase you will find
FairTrackPar/ParP/ParH: track representations of GEANE
FairGeneUtil: frame transformations from to MARS, SC, SD, SP (C++ translation of FORTRAN methods)

## Slide 86: How to use it
First define the start plane:
Define the end position:
Do the propagation:
Back propagation:
Bool_t PropagateToPlane(TVector3& v0, TVector3& v1, TVector3& v2);
Bool_t PropagateToVolume(Tstring VolName, Int_t CopyNo,Int_t option);
Bool_t PropagateToLength(Float_t length);
Bool_t PropagateToPCA(Int_t pca, Int_t dir);
Bool_t PropagateFromPlane(TVector3& v1, TVector3& v2);
Bool_t Propagate(FairTrackParH* TStart, FairTrackParH* Tend, Int_t PDG)
Bool_t Propagate(FairTrackParP* TStart, FairTrackParP* TEnd, Int_t PDG)
Bool_t setBackProp()

## Slide 87: How to use it
First define the start plane:
Define the end position:
Do the propagation:
Back propagation:
Bool_t PropagateToPlane(TVector3& v0, TVector3& v1, TVector3& v2);
Bool_t PropagateToVolume(Tstring VolName, Int_t CopyNo,Int_t option);
Bool_t PropagateToLength(Float_t length);
Bool_t PropagateToPCA(Int_t pca, Int_t dir);
Bool_t PropagateFromPlane(TVector3& v1, TVector3& v2);
Bool_t Propagate(FairTrackParH* TStart, FairTrackParH* Tend, Int_t PDG)
Bool_t Propagate(FairTrackParP* TStart, FairTrackParP* TEnd, Int_t PDG)
Bool_t setBackProp()

## Slide 88: Track Propagator
Additional track propagators:
  FairRKPropagator
    4th order Runge-Kutta propagator
    not used
  PndHelixPropagator
    much faster than GEANE
    but no energy loss
    no varying magnetic field

## Slide 89: Tracking QA

## Slide 90: Introduction
Various different tracking algorithms
Common basis needed to compare and improve tracking algorithms
Common development of Lia Lavezzi and me
Idea:
  Have a set of macros which work on any tracking algorithms which produces PndTrack and PndTrackCand
  Set of identical simulation and digitization files for all tracking algorithms

## Slide 91: Criteria
Track efficiency
  How many MC tracks have been found by track finder
Hit efficiency
  How many hits of a MC track have been found by the track finder
Purity
  Belong all hits of one found track belong to one MC track
Clones
  How often was a track found by the track finder
Ghosts
  How many hits not belonging to an MC track have been found

## Slide 92: Criteria
Partially found
  Not all hits belonging to one track have been found but all hits belong to one MC track
Spurious found
  > 70% found hits belong to one MC track
Fully found
  100 % of MC hits have been found and no other hits are part of the track
Clone
  A MC track was found more than once
Ghost
  A reconstructed track not matching to an MC track

## Slide 93: Efficiency
To determine the efficiency of a track finder a basis is needed:
  All tracks? What about neutral particles or tracks without hits?
  Only tracks with hits? How many hits?
  A barrel track finder cannot find tracks in the forward region
Different criteria defined:
  At least three hits (minimum for circle determination)
  Possible Track:
    Definable by user via functor (who knows what a functor is?)
    Some predefined in PndTrackers/PndIdealTrackFinder/PndTrackFunctor.h

## Slide 94: Efficiency
Predefined functors:
  StandardTrackFunctor:
    MVD > 3 or MVD+Stt+GEM > 5
  FtsTrackFunctor
    FTS > 5
  NoFtsTrackFunctor
    FTS == 0 and StandardTrackFunctor
  Some more specific for certain track finders
    OnlySTTFunctor, RiemannMvdSttGemFunctor, …

## Slide 95: Implementation
Macros in /macro/trackingQA
sim, digi and par files provided in folder
reco_complete.C(TString prefix)
  Does the tracking. Your tracking code has to go here!
  In addition runs an ideal track finder to compare with
  Usage:
    Add prefix to identify which data you want to run on
    root reco_complete.C"(\"dpm_G4_7G0_1000\")"

## Slide 96: Implementation
trackingQA_complete.C(TString prefix, TString branch, Int_t nEvents=0):
  Compares tracking algorithms with ideal tracking
  Usage
    Add the same prefix as in reco_complete.C
    Add the branch name with the final results of your tacking code (has to be of type PndTrack)
    Optional add the number of events you want to run on
    root trackingQA_complete.C"(\"dpm_G4_7G0_1000\", \"SttMvdGemTrack\")"

## Slide 97: Implementation
plot_trackingQA(TString fileName)
  Plots the generated histograms of trackingQA in a nice way
  Usage:
    Give the complete file name of the trackingQA.root file
QA_histos(TString prefix, TString trackBranch)
  Generates a large set of extracted histograms
  Usage:
    Give prefix and branchName
comp_recoqa(TString ,fn TString fn2, int picpercan, …)
  Combines the histograms of two different tracking algorithms
  New feature pictures per canvas

## Slide 98: Hit Efficiency

## Slide 99: Momentum Resolution

## Slide 100: Performance

## Slide 101: Overview Performance

## Slide 102: Overview of Track Finder