## Slide 1: UNILAC requirements for BIOPHYSICS research
M. Scholz, T. Friedrich, K.-O. Voss

## Slide 2
Experimental questions  Variation in radiation quality
Broadbeam experiments (X6)
Microbeam experiments (X0)
Summary: Requirements

## Slide 3: Energies of interest
Jakob et al., Int. J. Radiat. Biol. 2002
Stopping Power
(Radiation Action)
Depth in water
FAIR
SIS
UNILAC
The coexisting availability of beams covering the entire energy range
and ion species under otherwise equal conditions is a prerequiste for systematic biophysics experiments – and unique @GSI.

## Slide 4: UNILAC experiments
sample holder
Jakob et al., Int. J. Radiat. Biol. 2002
C
Bi
Repair of DNA damage depends
on damage density / complexity
Typically: 2-3 d beamtimes, moderate intensities, parasitic mode, irradiation in air

## Slide 5: UNIversal Linear ACcelerator
Goal: Variation of damage density by variation of dE/dx
Tool: Choice of ion species for given energy
He – U: Mechanisms of radiation action
He – C: Radiation protection, Radon project
He – Ne: Radiation therapy
Energies: Broadbeam (X6): min. ~6 MeV/u for light ions (He – C)
Broadbeam (X6): min. ~8 MeV/u for heavier ions (Ar – U)
Microbeam (X0): optimal ~ 5 MeV/u (C – U)

## Slide 6: UNILAC Facilities: Broadbeam (X6)
IC
Exit Window
~Air gaps + foils: 100mm H2O-equivalent thickness
Air Gaps
Mylar foils

## Slide 7: Requirements for Emin
Material in front of sample
Required remaining range
Potential improvements:Reduce material in beam

## Slide 8: Typical broadbeam experiments
Irradiate sample by sample...
Fluences: min. 103/cm2 (~104 particles)
max. 108/cm2 (~109 particles)
Variation: x 20 within sample series (sec)
Variation: x 105 from series to series (~15 min)
Macropulses: To compensate statistical fluctuations, irradiation with more than one macropulse required. Not too high intensity tolerated.
High variation in time averaged particle flux needed
Goal: Cover high flux range without complicated operator intervention
Parameter: Irradiation time (< ~ 5 - 60 s)
Particles per macropuls (change requires new dosimetry)
Macropulse length
Duty cycle
Flexibility in these parameters needed

## Slide 9: Example: Change of time averaged flux
50Hz / 5msec
I
t
5Hz / 1msec
I
t
Required flexibility: Duty cycle: 1-10 Hz
Pulse lengths: 0.5-5 ms

## Slide 10: UNILAC Facilities : Microbeam (X0)
Exit Window: 200nm Si3N4, 1mm2
Distance in air: <300µm
4µm Polypropylen foil in front of cells

## Slide 11: Optimal energy for microbeam irradiation
Limited magnetic rigidity
Limited range in cells
m/q = 8 (z.B. Au 25+)  E_max = 8.5 MeV/u
m/q = 6 (z.B. C 2+)  E_max = 11.4 MeV/u
Rigidity limit of magnetic lense: ~ 5 A
Potential improvements:
higher charge state / stripping
thicker lense

## Slide 12: Impact of pulse structure at the microbeam
Irradiation time for 0.1 ms dead time / ion (calculated for carbon)

## Slide 13: Summary: Requirements
 | Broadbeam | Microbeam
Ion species | p – U (All) | C and heavier
Energies | 3 – 8 MeV/u (3 – 6.5 MeV/u) | ~ 5 MeV/u (ab 1.4 MeV/u)
particles / macropulse | 104-109 | 108 – 109
Pulse length | 0.5 – 5 ms (0.5 – 2 ms) | 0.1 – 5 ms (0.1 – 2 ms)
Repetition rate | 1 – 10 Hz (1 – 5 Hz) | 3 – 50 Hz
...and: - Immediate flexibility in pulse length / repetition rate - Delivery in parasitic mode highly efficient (parallel sources & experiments / parallel to SIS injection)  Optimized experimental throughput
Flexibility, variability and redundancy in beam parameters and beam availability should be kept as much as possible!

## Slide 14: Open questions
For existing / optimized UNILAC:
  Maximum tolerable duty cycle for high current source
  Energy/Ion dependence of duty cycle
  Realistic operating scenarios
  Parallel operation of ion sources
For additional CW-Linac:
  Range of ion species / source availability
  Maximal energy
  Pulse structure / frequency
  Dynamic intensity range
  Pulse structure / frequency
  Parallel operation to FAIR-injector
General:
  Overall time schedule?