IPM profile reconstruction using Neural network
IPM Workshop 2017
R. Singh, M. Sapinski, D. Vilsmeier
GSI

---
Outline
IPM profile distortion
Correction measures or parameter estimation
Introduction to Artificial Neural networks
Training procedure of ANNs
Application to LHC IPM distortion
Summary and references

---
Profile distortion in IPM
Ideal case
Particles are moving on straight lines towards the detector
Real case
Particle trajectories are influenced by initial momenta and by the interaction with the beam field
… instrumental effects such as camera tilt, optical point-spread-functions, point-spread functions due to multi-channel plate granularity come on top!

---
Distortion because of ...
… interaction with the beam field
- While particles are close to the beam they “feel” the beam fields and their movement is influenced accordingly resulting in possible displacements
- This effect occurs for large beam fields ↔ great charge densities, great beam energies
- Can be simulated with reasonable assumptions
… initial momenta
- While particles are moving towards the detector they also move along the profile that is measured
- This effect is significant for small extraction fields / small beam sizes
- Reliable models not available for all energies, projectiles,targets
… instrumental effects such as camera tilt, optical point-spread-functions, point-spread functions due to multi-channel plate granularity

---
IPM Profile Correction
- Using higher electric and magnetic fields (Expensive, sometimes impractical)
- Deconvolving out the cause of distortion using simulations and postprocessing
- Electric and magnetic fields : Sieve method (deconvolve with PSF of radius of Gyration)
  [Dominik Vilsmeier, Bachelor Thesis, CERN]
- Electric fields only: Several calibration/correction attempts.
  Latest: Assumption on input beam distribution (Generalized Gaussian) and iterative procedure for input reconstruction from distorted profile using the data generated from simulation tool
  [Jan Egberts, PhD Thesis, CEA Saclay]

---
IPM Profile Correction
Physical process
Actual profile
Particle number
f'
Measured IPM profile
- Actual profile is replaced by its sigma (strong assumption of Gaussian beam)
- Assuming that such a “target” function exists, use neural network for its approximation usually referred as “learning”.
Bunch length
Energy
Measured IPM profile
f
Particle number
Actual profile
Bunch length
f != f'^{ -1}
Energy
f
Statisticians: Learning is statistical inference

---
Artificial Neural Networks
The question 'What is a neural network?' is ill-posed.
                                                            - Pinkus (1999)
- Biologically inspired → Brain cells -> neurons, computation via connections and thus Networks
- The basic node of ANNs is “Perceptron”
- Only supervised learning discussed
Input Layer
W_1
x_1
Output Node (Perceptron)
o = g(sum from { { k = 0 } } to { N } { {x_k W_k+b} })
x_k
W_k
x_N
W_N
b
Perceptron parameters
Weights from the inputs and bias
is the activation function, a step function with a threshold
"g"
[https://www.wired.com/2016/03/took-neuroscientists
-ten-years-map-tiny-slice-brai/]

---
Artificial Neural Networks
Not linearly separable
Output Layer
Input Layer
Hidden Layer
x2
XOR
W_jk
W_ij
x_1
o_1
x_2
a_1
o_i
a_j
x_k
o_L
x_N
x1
a_M
Each hidden layer and output layer node is a perceptron
o_i = g left( sum from { j = 0 } to { M } {W_ij} (g left(sum from { k = 0 } to { N } {x_k W_jk} +b_j right))+b_i right)
W_k
Minsky & Papert (1969)
Perceptrons can only represent linearly separable functions.
Good news: Adding “hidden” layer(s) allow non-linear target functions to be represented -> Multi-layer Perceptron

---
Multi-layer perceptron (MLP)
Perceptron: No hidden layer
One hidden layer
Two hidden layers
Carla P Gomes, Lecture Notes CS 4700: Foundations of Artificial Intelligence
Universal approximation theorem:
Every bounded continuous “target” function can be approximated with arbitrarily small error, by network with single hidden layer [Cybenko 1989; Hornik et al. 1989]
Any “target” function can be approximated to arbitrary accuracy by a network with two hidden layers [Cybenko 1988]
If we have any unknown function, ,it can be approximated by,
y = f (x)
o_i = g left( sum from { j = 0 } to { M } {W_ij} (g left(sum from { k = 0 } to { N } {x_k W_jk} +b_j right))+b_i right)
Issue: For any particular network structure, it is harder to characterize exactly which functions can be represented and which ones cannot.

---
Training the MLP network
Output Layer
Input Layer
Hidden Layer
1. Supervised learning of target function of : approximate from training data
2. Minimize the objective function as a function of weights and biases
W_jk
y = f (x)
f
W_ij
x_1
(x,y)
o_1
x_2
a_1
o_i
a_j
x_k
E = sum from { { i = 0 } } to { L } { ({y_i - o_i})² }
o_L
x_N
E
a_M
Target function y approximated by MLP
W_13
W_12
o_i = g left( sum from { j = 0 } to { M } {W_ij} (g left(sum from { k = 0 } to { N } {x_k W_jk} +b_j right))+b_i right)
https://www.r-bloggers.com/multivariable-gradient-descent/
Many optimization routines for solving non linear optimization problem
Gauss Newton, Levenberg-Marquardt, Backpropagation with Gradient Descent (Simplest, discussed here)
Activation function “g” should be differentiable, “tanh” or “sigmoid” typically used

---
Back-propagation with gradient descent
Back-propagation: Propagate the error from the output layer to the hidden layers.
The back-propagation process emerges directly from a
derivation of the overall error gradient.
Output Layer
Input Layer
Hidden Layer
W^2_{jk}
W^1_{ij}
x_1
o_1
E = sum from { { i = 0 } } to { L } { ({y_i - o_i})² }
x_2
a_1
Err_i=y_i-o_i
o_i
a_j
x_k
Hidden to output layer weight gradients
{%delta E} over {%delta W^1_ij}= a_j Err_i g'({inp}_i)
o_L
x_N
a_M
Input to hidden layer weight gradients
o_i = g left( sum from { j = 0 } to { M } {W_ij} (g left(sum from { k = 0 } to { N } {x_k W_jk} +b_j right))+b_i right)
{%delta E} over {%delta W^2_jk}= x_k g'({inp}_j) sum from{j=0} to {M} W_ij Err_i g'({inp}_i)
W(t+1) = W(t) + %alpha {%delta E} over {%delta W}
Gradient Descent

---
Artificial Neural Networks (Overview & Jargon)
- Supervised learning, unsupervised learning, reinforcement learning
- Batch learning, incremental learning
- Functions: Activation function, Target function, Objective or error function
- Optimization: Gradient descent, Levenberg-Marquardt, Epoches, Learning rate, Momentum
- Generalization: Cross validation, regularization, early stopping
Approximate target function
o_i = g left( sum from { j = 0 } to { M } {W_ij} (g left(sum from { k = 0 } to { N } {x_k W_jk} +b_j right))+b_i right)
Solve optimization problem with training data
E = sum from { { i = 0 } } to { L } { ({y_i - o_i})² }+ %lambda sum from { { j = 0 } } to { M }sum from { { k = 0 } } to { N }( W_{ij} )²
STOP
Calculate gradient, update weights
For more: How could a Kangaroo climb Everest?
ftp://ftp.sas.com/pub/neural/kangaroos
{%delta E} over {%delta W_ij}= a_j Err_i g'({inp}_i)
W_{ij}(t+1) = W_{ij}(t) + %alpha {%delta E} over {%delta W}
Validate with other data, “validation data” to
check the generalization or “learning”
If not, change the number of units or architecture

---
Conditioning inputs and initial weights
Tanh activation function
- Weights initialization: Generate random initial weights [-1,1] and divide each of these random weights by the square root of the number of units in the larger layer
- Inputs and targets to be standardized according to the used activation function , else some perceptrons will remain saturated (difficulty in learning)
Rules of thumb: Start with two hidden layers with number of hidden units equal to (Input_num + Target_num)/2 and avoid overfitting by regularization
If simple MLP is not good enough for the application, look further into literature!

---
Neural network Zoo
Source: Fjodor Van Veen, Asimov Institute, Utrecht

---
Training data
0.35mm,0.4mm,
1.05 ns, 1.25e11
Training “grid” (375 points)
0.29, 0.31, 0.33, 0.35, 0.37 (mm)
%isigma_x
0.4,0.45,0.5,0.55,0.6 (mm)
%isigma_y
IPM Sim
N_p
1.1e11, 1.25e11, 1.40e11, 1.55e11, 1.7e11
0.9, 1.05, 1.2 (ns)
%isigma_l
0.29mm,0.4mm
1.05 ns, 1.55e11
Output of supervised learning:
A list of weights and biases
ANN
and
%isigma_x
%isigma_y
N_p
and
along with
%isigma_l
Inputs to ANN
Targets
Supervised Learning

---
Validation Data
Training “grid” (375 points)
Validation “grid” (128 points)
4 validation data sets (inputs and outputs) created:
1% off the training grid in each dimension (within in grid)
25% off the training grid in each dimension
50% off the training grid in each dimension
100% off the training grid (the next point outside the grid)
0.29, 0.31, 0.33, 0.35, 0.37 (mm)
%isigma_x
0.4,0.45,0.5,0.55,0.6 (mm)
%isigma_y
N_p
1.1e11, 1.25e11, 1.40e11, 1.55e11, 1.7e11
0.9, 1.05, 1.2 (ns)
%isigma_l
Validation grid is to validate the target function is learned or generalized NOT memorized
Validation is sometimes used during training as a stopping criterion
%isigma_l
%isigma_x

---
Results with Matlab NN Toolbox
- Input: horizontal profile, 3000 points (1 um spacing)
- Decimated to 300 (more noisy) or averaged (less noisy) + normalized to maximum value of each profile
- Nprotons (1 number, normalized to 1.7e11) + longitudinal sigma (1 number, normalized to 1.2e-9s)
  - sample 1: training data – 375 points,
  - sample 2: validation_data_1_percent_off – 128 points
  - sample 3: validation_data_25_percent_off – 128 points
  - sample 4: validation_data_50_percent_off – 128 points
  - sample 5: validation_data_outside_region – 80 points
- Sample 1 used for training and sample 2-5 for validation
- Targets/Outputs: single or both transverse sigmas i.e.
N_p
%isigma_l
%isigma_y
%isigma_x

---
Results with Matlab NN Toolbox
Output Layer
Hidden Layer 2
Hidden Layer 1
Input Layer
i= 1 to Num_outputs
j = 1 to H2
k = 1 to H1
l = 1 to Num_inputs
1 or 2
30
30
302
- Activation function → tanh
- Optimization algorithm → Batch learning, Levenberg-Marquardt
- Total parameters : 302*30+30*30+30*2+ 92 = 10112
- Usually converges is 8-9 Epoches

---
 ANN30301 → In-grid validation data
1% validation data
25% validation data
50% validation data
Bias = 0.5 %, Std. Dev. = 1.2% for validation data inside grid

---
 ANN30301 → Out-grid validation data
Outside region validation
Training data
Bias~ 0.5%
Std.dev ~ 5%

---
Summary and error rates
ANN-MLP: 60,30,1
ANN-MLP: 30,30,1
Red points are the training points, blue points are validation data
Neural network with more nodes gave worse results! (Actually the stopping condition was more relaxed since the optimization problem was bigger)

---
Neural network: a black box?
W_jk
W_ij
x_1
o_1
x_2
a_1
o_i
a_j
x_k
o_L
x_N
a_M
Mean and std. deviation of input to first hidden layer weights for all inputs
Hints on relative importance of each input
Shoulders seem of have the most information concerning the width and distortion

---
Other observations
If noise is expected in measured data, train the network with noise

---
Predicting from horizontal profile ANN30302
%sigma_y
%sigma_x
%sigma_y
- Neural network was trained with both transverse plane widths (sigmas) as the target
- Width estimation in both planes were obtained with validation data

---
Common
Results with Tensor Flow Library
TensorFlow library (Keras interface)
- Input: horizontal profile, 3000 points (1 um spacing)
  Averaged to 300 points + normalized to maximum value of each profile
- Nprotons (1 number, normalized to 1.7e11) + longitudinal sigma (1 number, normalized to 1.2e-9s)
  - sample 1: training data – 375 points,
  - sample 2: validation_data_1_percent_off – 128 points
  - sample 3: validation_data_25_percent_off – 128 points
  - sample 4: validation_data_50_percent_off – 128 points
  - sample 5: validation_data_outside_region – 80 points
- Sample 1 used for training and sample 2-5 for validation
- Targets/Outputs: single or both transverse sigmas i.e.
N_p
%isigma_l
%isigma_y
%isigma_x

---
case 1: model
Tensor Flow MLP parameters
model = Sequential()
model.add(Dense(lindata, input_dim=302, activation='relu'))
model.add(Dense(60,activation='sigmoid'))
model.add(Dense(30, activation='softplus'))
model.add(Dense(2, activation='softplus'))
model.compile(optimizer='rmsprop', loss='mean_squared_error', metrics=['accuracy'])
Layer (type)                     Output Shape          Param #     Connected to
====================================================================================================
dense_1 (Dense)                  (None, 302)           91506       dense_input_1[0][0]
____________________________________________________________________________________________________
dense_2 (Dense)                  (None, 60)            18180       dense_1[0][0]
____________________________________________________________________________________________________
dense_3 (Dense)                  (None, 30)            1830        dense_2[0][0]
____________________________________________________________________________________________________
dense_4 (Dense)                  (None, 2)             62          dense_3[0][0]
====================================================================================================
Total params: 111,578
Trainable params: 111,578
An order of magnitude more parameters, yet roughly same time of computation!

---
case 1: validation
Validation
average: mean=0.0040, 0.4±0.8 %
(12 runs) std=0.0081 overestimation
on samples 2,3,4,5

---
case 1: validation without out-of-region
Validation without out-of-region data
on samples 2,3,4,5
average: mean=-0.0050, -0.05±0.7 %
(12 runs) std=0.0071 underestimation
[Speaker Notes: fitted histogram binning is not optimized]

---
Network trained with less parameters
Trained with ANN 60301 in tensor flow, few minutes
Results similar to NN toolbox, slightly worse

---
Summary
Multi layer perceptron (simplest ANN architecture) with two hidden layers can represent any of unique mapping/function between input and target
The number of perceptrons (units) in hidden layers should be enough to represent the hidden mapping or function. Too many units might lead to overfitting but OK with good regularization schemes. Rules of thumb exist in literature
IPM profile width estimation from the distorted profile due to space charge (for LHC parameters) with MLP (supervised learning) using two different libraries (NN toolbox in Matlab and TensorFlow)
Training “grid” was placed with a spacing of ~6% in each input dimension. Generalization error with validation input was (0.7-1.5)% in variance and 0.5-2.0% bias. Tensor flow library gave (slightly) better results but with larger hidden layers.
For training of Neural networks, good description of the system to be modeled is needed → Good simulation tools for generating training and validation data or alternative measurements: Promising first results.
References
Carla P Gomes, Lecture Notes CS 4700: Foundations of Artificial Intelligence
Excellent Reference to all ML questions: ftp://ftp.sas.com/pub/neural/FAQ.html

---
Art and science of ANNs
Lets try our hand at sketching and see if machine recognizes
https://quickdraw.withgoogle.com
The next pop star could be a neural network (album coming out soon)
http://www.flow-machines.com/ai-makes-pop-music/
Or Bach
http://www.asimovinstitute.org/analyzing-deep-learning-tools-music/
Modern (or futuristic) art anyone?
http://nerdist.com/why-are-googles-neural-networks-making-these-brain-melting-images/
Other boring things like economics, Geosciences, Football, …..
https://www.intechopen.com/books/artificial-neural-networks-application
ftp://ftp.sas.com/pub/neural/FAQ7.html#questions

---
Single output, N30301

---
case 1: training 1+4
case 2: training 1+4
- on sample 1+4
- shuffle=True, nb_epoch=100, batch_size=4
- loss function: 0.003->0.0006 (typically)

---
case 1: validation of training 1+4
case 2: validation of training 1+4
average: mean=-0.0019, -0.2±0.7 %
(12 runs) std=0.0074 underestimation
on samples 2,3,5

---
case 1: training 1+5
case 3: training 1+5
- on sample 1+5
- shuffle=True, nb_epoch=100, batch_size=4
- loss function: 0.003->0.0006 (typically)

---
case 1: validation of training 1+5
case 3: validation of training 1+5
on samples 2,3,4
average: mean=0.0001, -0.01±0.8 %
(12 runs) std=0.0080 underestimation

---
IPM Profile Distortion
- Detector issues → Excluded
- Initial velocity Put Mariusz slides → start and conclusion
- Space charge → was seen as the major issue, profile distortion as a function of beam intensity and charge density. Could be simulated well if initial velocities do not play a role.