## Slide 2
Future Circular Collider Study
Goal: CDR For the European Strategy Update 2018-2019
International FCC collaboration
(CERN as host lab) to study:
• pp-collider (FCC-hh)
→ main emphasis, defining infrastructure requirements
16 T → 100 TeV pp in 100 km
• 80-100 km tunnel infrastructure in Geneva area, site specific
• e+e- collider (FCC-ee), as potential first step
• p-e (FCC-he) option, integration one IP, FCC-hh & ERL
• HE-LHC with FCC-hh technology

## Slide 3
Future Circular Collider Study
The FCC study is necessary to propose a credible project for the period after the exploitation of the High-Luminosity LHC, i.e. 2035-2040.

## Slide 4
Future Circular Collider Study
Feasibility study of the new tunnel: FCC fits in CERN area
Injection options:
SPS → LHC → FCC
Injection energy 3.3 TeV from LHC
SPS (upgraded) → FCC
Injection at 1.5 TeV from SPS equipped with fast-cycling SC magnets, 6-7 T, 1 T/s ramp.

## Slide 5
FCC-hh Parameters

## Slide 7
1.8K – 166 W
4.5K - 65.7 W
20K – 14 W
77K - 2.9 W
Per Tw = 300 K
For low T:
300
10
5
2
Minimum power (Carnot) needed to remove 1 W from a cold surface.
Typical efficiency with respect to Carnot cycle : 0.3
Temperature of the cold surface [K]
Cold mass 1.9 K
Cold bore
Beam

## Slide 8
What does it mean to transfer 30 W/m from 1.9 K to 300 K in FCC?
Paluel (F) Nuclear Power Plant 5.5 GW

## Slide 9
The required beam gas density is ~5 times lower that the one for the LHC: from 1015 to 2x1014

## Slide 10
Ph. Lebrun, L. Tavian, V. Baglin
Beam screen temperature:
To have saturated vapour density much lower or much higher than 2x1014 m-3, the temperature ranges 20-40, 60-100, 120-200 should be avoided.
To reduce resistive impedance, temperature lower than 60 K are required.
The chosen temperature is around 50 K for copper co-laminated stainless steed beam screens.
Cu

## Slide 11
The FCC-hh beam screen model
As a consequence of the higher SR power density:
The mass flow of gas in the cooling channel must be increased. The diameter of the channel has to be increased to avoid too high pressure drop.
The beam screen temperature must be increased in the range 40 to 60 K, as compared to the 5 to 20 K in LHC, to reduce the needed cryogenic power. The higher temperatures have large repercussions on the vacuum due to higher equilibrium vapour pressures.
There is an increased photo-desorption due to an higher number of photons (x6 above cut-off at 4 eV). Higher effective pumping speed is needed.
In addition, from the early design, we want to integrate an ecloud suppressor method.
Consequence: The present LHC beam cannot be adapted/copied to the FCC-hh.

## Slide 12
FCC-hh beam screen geometry evolution
Lower impedance
Symmetrical design
Pumping holes hidden by the screen
Better heat transfer
Cold thermal sprayed copper coating on the outer side
Improved pumping
Larger pumping holes (no impedance constraint)
Easier manufacturing
Polygonal shape of the screen
Improved heat transfer
Increased He cooling channel
Cold thermal sprayed copper coating on the outer side
March 2015
May 2015
August 2015
January 2016

## Slide 13
April 2016

## Slide 14
Orsay 09/2015
3rd WP4 meeting
Geneva 06/2016
4th WP4 meeting
Barcelona 11/2016
5th WP4 meeting
Improve pumping speed
Optimize thermal and mechanical behaviour
GOALS

## Slide 15
Synchrotron light distribution, including absorber: Power
W/cm2
Ribs
32.9%
Reflectors
Cold bore
Inner copper
29.3%
0.007%
6.56%
End absorber
12.6%
% of Total BM Power, 502W
Drift space
8.1%
68% of the incident power is reflected on the reflector
Credit: I. Bellafont, ALBA, EuroCirCol Meeting, 7/11/2016, Barcelona
SYNRAD+ ray-tracing simulation code

## Slide 16
Synchrotron light distribution, including absorber: Power
Credit: I. Bellafont, ALBA, EuroCirCol Meeting, 7/11/2016, Barcelona
END-RADIATION ABSORBER
S. steel, welded to the BS and brazed to the Cu
22mm long, 12.8o slope
Possible absorber location
Beam direction
Present LHC Interconnect

## Slide 17
Synchrotron light distribution, including absorber: Power
Credit: I. Bellafont, ALBA, EuroCirCol Meeting, 7/11/2016, Barcelona
END-RADIATION ABSORBER
W/cm2
61 W (12.6% Tot.P.)
800W/cm2 max`
For an ideal beam, this end absorber can reduce the maximum power density more than 4 times on the slope area, reducing the possibility to have a thermomechanical failure
Redirecting as much SR as possible to the absorber, not only the cooling efficiency improves, the total outgassing is also decreased. It can be done changing the reflector’s shape or reducing its roughness
Carnot efficiency of refrigerators
Beam direction

## Slide 18
Synchrotron light distribution, including absorber: Flux
Credit: I. Bellafont, ALBA, EuroCirCol Meeting, 7/11/2016, Barcelona
Photons/s/cm2
Ribs
29.6%
Reflectors
Cold bore
Inner copper
21.4%
0.27%
4.9%
End absorber
12.8%
% of Total BM Flux, 2.1E18 ph/s
Drift space
5.9%
78% of the incident flux is reflected by the reflector

## Slide 19
Synchrotron light distribution, including absorber: Flux
Credit: I. Bellafont, ALBA, EuroCirCol Meeting, 7/11/2016, Barcelona
MISALIGNMENT STUDY
To perform an approach to the real geometry conditions, a misalignment study has been carried out, moving the beam 1mm upwards
The leaked power is slightly lower, while the molecular density is slightly higher
The radiation is directed forward with a narrower angle, increasing the power on the end absorber.
W/cm2
Molecular density @72h
Cold bore power
Absorber power
Aligned
9.88·1013 H2/m3
0.034 W
63 W
Misaligned
9.93·1013 H2/m3
0.032 W
86 W
Inner copper power
3.3 W
3.7 W
Ribs power
165 W
73 W
Stretching the sharp point of the reflector can produce the same effect in ideal conditions

## Slide 20
Gas density distribution: Molflow+ Simulations
9.88·1013 H2/m3
Pumping Holes length
10mm
Holes area coverage
67.6 %
Reflector roughness
σ/T = 0.0032
Average arc density
Conditioning Time
72h
Average arc pressure
6.56 ·10-10 mbar
Main slot aperture
5mm outwards
Beam direction
Drift space between dipoles
1.43m
Bending magnet 14.3m
PSD data
Bk. 316 SS H2 293K 4 keV
Ribs
60K
Main reflector
Cold bore
Inner copper
60K
1.9K
47K
Other areas
50K
End absorber
100K
Temperatures
4.97·10-6 mbar·l/s
Outgassing per BM
Molecular density
profile; only PSD H2
Credit: I. Bellafont, ALBA, EuroCirCol Meeting, 7/11/2016, Barcelona
14.3 m-long Dipole
1.5 m-long Drift

## Slide 23
This 3D simulation has been carried out taking into account ‘Joule effect’ coupling magnetic field and temperatures ().
x
z
Electric current,
Mechanical Design
Magnet quench
Variation of magnetic field at quench produces currents all along the beam screen.
These currents produce Lorentz forces that have to be correctly withstood by the beam screen.
x
z
y

## Slide 24
Max stress: 1500 MPa
The maximum stress reached at highest Lorentz force (0.008 secs) is 1500 MPa (Yield strength at 50 K: 1350 MPa), so the material will plastify during magnet quench.
Mechanical Design
Stress analysis
Max displacement: 0.467 mm

## Slide 25
Latest news
Von Mises Stress (MPa)
0
1300
0.2 mm gap
0 mm gap
Present design
Design optimisation
Design modification
Design evolution
Behaviour during a magnet quench
Present design
Design optimisation
Design modification
 Significant improvement by the design modification and potentially easier to manufacture

## Slide 26
Beam screen development (2)
Design of the supporting system ongoing
0.3 mm thick
0.2 mm displacement
Von Mises stress
21 mm
Contact pressure: ~ 360 MPa
Contact force: ~ 11 N
1.7 mm height
( pre-stress 0.2 mm)
Welding points (4 per ring)
0
500
Total heat load transferred:
~ 0.03 W/support
Temperature profile
Mechanical analysis
Thermal analysis
Preliminary design promising
Mechanical behaviour acceptable

## Slide 27
1.5 mm
Thermal load to cold bore
Electron cloud effect
Total thermal load transferred to cold bore: 99.73 mW/m
1
5
6
3
2
4
4
1
2
3
4
4
5
6
Max power allowed: 100 mW/m
Nuclear scattering: 46 mW/m
Synchrotron radiation: 2.4 mW/m
Thermal radiation: 2.33 mW/m
Beam screen supports: 49 mW/m
Image currents

## Slide 28
1250 MPa
BS comparative
44 K
47 K
1500 MPa
Change on deflector gap produces higher Lorentz forces and lower inertia moment, so that, stresses are higher.
Amount of copper reduced 70%.
Inner copper layer temperature reduced 3K thanks to the isolation produced by bigger pumping slots.

## Slide 29
Ecloud mitigation integrated in the design: Present baseline
Laser treatment, just above the ablation threshold, of the top and bottom beam screen surfaces (ASTeC-STFC and Dundee University).
The morphology of the surface is strongly modified
20 mm
Very low SEY is achieved
Studies in progress:
Morphology optimisation
Impedance
Dust generation
Effect of magnetic field
Very efficient to reduce photon reflectivity

## Slide 30
Configuration
Slit height: 5 mm
External copper rings:
~ 6 mm * 0.5 mm
Pitch: 11 mm
Probably no coating in the middle of the beam screen
Fixed point
Cooling circuit
Cooling channel: 316L
Beam screen wall:
304L, 1.5 mm
copper electrodeposition, 0.05 mm
Reflector: 304
The retained configuration for the first prototype is based on the version presented at the FCC week in April 2016.
Internal electrode:
Copper, 6 mm wide
Ceramic insulation
Chimney for pressure measurement
End plate at both extremities

## Slide 31
Prototypes
Series vs prototype #1
Cooling channel:
316L,
3D printed + machined
Cooling channel:
P506 stainless steel
Extruded
Reflector:
P506 stainless steel
Extruded + finishing
Beam screen wall:
P506, 1.25 mm
copper colamination, 0.3 mm
Reinforcement:
P506
punching
Beam screen wall:
304L, 1. 5 mm
copper electrodeposition, 0.05 mm
Sub-component manufacturing:
Reinforcement:
304L
EDM or water jet cutting
Reflector:
304,
Machined + forming + finishing
Series
1st prototype

## Slide 32
Manufacturing procedure: prototypes
Assembly:
Beam screen wall
Cooling channel
Reflector
3D printing
Machining
Welding
Cu Coating
Machining
Forming
Heat treatment
Forming
Deburring
Welding
Reinforcement
Cutting
Welding
Welding
Coating
~ 40 cm long
Sheet
Sheet
Flat bar
Powder
Transition and special central pieces
Cutting
Machining
Coating
Machining
Forming
Machining
Deburring
Welding
polishing
Machining
End plate
Cutting
Sheet
Deburring
Machining (FP)

## Slide 33
Key technologies
Technology |  | Risk | Mitigation
3D printing |  | Leak | Leak tests of 100% of 3D printed parts
 |  | Deformation | Minimize the machining Dedicated tooling during welding
Laser cutting and welding |  | Metal projection | Tooling
 |  | Deformation | Tooling Additional forming
Sheet metal working and machining |  | Precision | Heat treatment Dedicated tooling
Coating | Electrodeposition | Peel off | Apply known procedures
 | Plasma and cold spray |  | Tests on dedicated representative samples
 |  |  | Thermal shock cycles

## Slide 34
Key technology validation
Copper cold sprayed strips on beam screen short prototype
Production of a 30 cm prototype
Main technologies have been validated by the production of two 30 cm long prototypes.
Different surface preparations have been assessed for the copper cold spray.

## Slide 35
Key technology validation
Electrode obtained by plasma and cold spray
Ceramic
Aluminium
Copper
Measurements of the electrodeposited copper thickness
Uniformity of the copper electrodeposition has been assessed along the 2 m long prototype.
The internal electrode has been produced by plasma and cold spray coating. Electrical insulation has been validated after thermal shock cycles (77K-~400K).
All 3D printed parts for the cooling channel have been leak tested at reception.
A few 3D printed parts

## Slide 36
Last news: 2 m long beam screen prototype manufacturing
Beam screen assembly before tack welding
Beam screen assembly after tack welding
Beam screen assembly after welding (today)
Next steps:
Cold sprayed copper rings
Fixed point machining
Instrumentation (temperature sensor) installation

## Slide 37
Long prototype to be installed at Anka
(see also other presentation by R. Kersevan)
Assembly:
Beam screen wall
Cooling channel
Reflector
3D printing
Machining
Welding
Coating
Machining
Forming
Machining
Forming
polishing
Welding
Reinforcement
Cutting
Welding
Welding
Coating
~ 40 cm long
Sheet
Sheet
Flat bar
Powder
Transition and special central pieces
Cutting

## Slide 38
Conclusions
A beam screen (BS) design capable of handling the ~30 W/m SR power generated by the 50 TeV protons in the FCC-hh has been conceived and designed;
A large number of ray-tracing montecarlo simulations, with realistic energy-, angle-, and material-dependent photon reflectivities have been carried out: they have allowed us to maximize the capture efficiency of the intense photon flux, and reduce the residual gas density along the path of the proton beam;
The effect of vertical misalignments between the orbit and the longitudinal slots has also been studied, and should not pose major problems, neither for the gas density nor for the SR power dissipation. This also includes the case of the SR fan generated at lower energies, which is wider vertically and can miss, in part, the opening of the slot (not discussed here, see FCC-hh General Meetings’ indico page)
A still open issue is the reliable calculation of the impedance generated by the presence of the double slot and, behind each slot, the evenly-spaced reinforcing ribs and pumping slots: randomizing their size and spacing seems difficult for this BS!
Ideally, the impedance of such an arrangement should be measured at cold temperatures (40-60 K);
Three 2m-long prototypes of the double-slot BS geometry are in an advanced stage of fabrication: the first one will be soon installed on a dipole radiation beam port of the 2.5 GeV ANKA light source, at KIT (see dedicated presentation, this workshop).
It will then be followed by a second one with integrated clearing electrodes, and a third one with laser-ablated surfaces.

## Slide 39
Acknowledgments
A large part of this presentation has been prepared by Paolo Chiggiato, head of CERN-TE-VSC;
Studies, CAD work, MC simulations, Thermal calculations, and more… have been carried out by C. Garion, J. Fernandez Topham, M. Gil Costa, I. Bellafont, R. Kersevan, with support from M. Ady for SYNRAD+ and Molflow+ code upgrades
Thank you for your attention 