## Slide 1
Beam Dynamics and Vacuum Issues in FCC
FCC
PS
SPS
LHC
Work supported by the European Commission under Capacities 7th Framework Programme project EuCARD-2, grant agreement 312453, and the HORIZON 2020 project EuroCirCol, grant agreement 654305, as well as by the German BMBF
Frank Zimmermann, CERN
EuCARD-2 XRING workshop, KIT, 8 March 2017
on behalf of the FCC design study team
many thanks to Michael Benedikt, Roberto Cimino, Stephane Fartoukh, Roberto Kersevan, Mayro Migliorati, Daniel Schulte,..

## Slide 2
colliders and discoveries
Standard Model
Particles and forces
powerful instruments for discovery and precision measurement
A. Ballarino
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 3
many open questions remain
    Standard Model describes known matter, i.e. 5% of the universe!
    what is dark matter?
    what is dark energy?
    why is there more matter than antimatter?
    why do the masses differ by more than 13 orders of magnitude?
    do fundamental forces unify in single field theory?
    what about gravity?
    is there a “world equation – theory of everything”? …
Dark Energy 68.3%
Known Matter 4.9%
Dark Matter 26.8%
galaxy rotation curves, 1933 - Zwicky
K. Borras
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 4
very large circular hadron collider - only feasible approach to reach 100 TeV c.m. collision energy in coming decades
access to new particles (direct production) in few-TeV to 30 TeV mass range, far beyond LHC reach
much-increased rates for phenomena in sub-TeV mass range → much increased precision w.r.t. LHC
energy frontier in the 21st century
hadron collider energy reach
Cf. LHC: factor ~4 in radius, factor ~2 in field  O(10) in Ecms
M. Mangano

## Slide 5
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as a possible first step
p-e (FCC-he) option, integration one IP, FCC-hh & ERL
HE-LHC with FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
Goal: CDR for European Strategy Update 2018/19
suggested
in 2010
HE-LHC

## Slide 6
CepC/SppC study (CAS-IHEP) 100 km (new baseline!) , e+e- collisions ~2028; pp collisions ~2042
Qinhuangdao (秦皇岛）
easy access
300 km east
from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
“Chinese Toscana”
100 km
50 km

## Slide 7
M. Koratzinos, HongKong
alternative CEPC sites

## Slide 8
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC – operation run 2
Construction
Physics
Design
HL-LHC - ongoing project
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
~20 years
Design
FCC – design study
must advance fast now to be ready for the period 2035 – 2040
milestone: CDR by end 2018 for next update of European Strategy
CERN Circular Colliders & FCC
2040

## Slide 9: hh peak luminosity scaling
shorter bunch spacing would help!!
(e.g. 25→ 5 ns increases nb 5x!)
with
beam-beam tune shift
limited hadron collider:
event pile-up limited
hadron collider:
FCC-hh vs LHC:
x700
x4
x8
x5?
x1 or x5?

## Slide 10
parameter | FCC-hh |  |  | HE-LHC | (HL) LHC
collision energy cms [TeV] | 100 |  |  | 25 | 14
dipole field [T] | 16 |  |  | 16 | 8.3
circumference [km] | 100 |  |  | 27 | 27
beam current [A] | 0.5 |  |  | 1.27 | (1.12) 0.58
bunch intensity [1011] | 1 (0.2) | 1 (0.2) |  | 2.5 | (2.2) 1.15
bunch spacing [ns] | 25 (5) | 25 (5) |  | 25 (5) | 25
IP b*x,y [m] | 1.1 | 0.3 |  | 0.25 | (0.15) 0.55
luminosity/IP [1034 cm-2s-1] | 5 | 30 |  | 34 | (5) 1
peak #events/bunch crossing | 170 | 1020 (204) |  | 1070 (214) | (135) 27
stored energy/beam [GJ] | 8.4 |  |  | 1.4 | (0.7) 0.36
synchrotron rad. [W/m/beam] | 30 |  |  | 4.1 | (0.35) 0.18
transv. emit. damping time [h] | 1.1 |  |  | 4.5 | 25.8
initial proton burn off time [h] | 17.0 |  | 3.4 | 2.3 | (15) 40
hadron collider parameters (pp)

## Slide 11
FCC-hh as A-A collider
J. Jowett, M. Schaumann
 | Pb-Pb | Pb-p
beam energy [TeV] | 4100 | 50
c.m. energy/nucleon pair [TeV] | 39.4 | 62.8
no. bunches / beam | 2072 | 2072
IP beta function [m] | 1.1 | 1.1
long. emit. rad. damping time [h] | 0.24 | 0.5
initial luminosity [1027 cm-2s-1] | 24.5 | 2052
peak luminosity [1027 cm-2s-1] | 57.8 | 9918
M. Schaumann, “Potential performance for Pb-Pb, p-Pb, and p-p collisions in a future circular collider, Phys. Rev. ST Accel. Beams 18, 091002 (2015).
A. Dainese et al., “Heavy ions at the Future Circular Collider,” contribution to forthcoming CERN Report on Physics at FCC-hh, http://arxiv.org/abs/1605.01389 .
based on existing LHC complex; fast radiation damping; secondary beams from IP require dedicated collimators,…

## Slide 12
FCC-hh layout
NEW LAYOUT NOV. 2016

## Slide 13
2 main IPs in A, G for both machines
asymmetric IR optic/geometry for ee to limit synchrotron radiation to detector
common layouts for hh & ee
11.9 m
30 mrad
9.4 m
FCC-hh/
ee Booster
Common
RF (tt)
Common
RF (tt)
IP
IP
0.6 m
Max. separation of 3(4) rings is about 12 m:
wider tunnel or two tunnels are necessary around the IPs, for ±1.2 km.
Lepton beams must cross over through the common RF to enter the IP from inside.
Only a half of each ring is filled with bunches.
FCC-ee 1, FCC-ee 2,
FCC-ee booster (FCC-hh footprint)
FCC-hh
layout
K. Oide
Notes: Check with Katsunobu to have latest layout.
Check with detector people if 9 m offset is acceptable for ee detector

## Slide 14
FCC-ee scope
physics programs / energies:
  Z (45.5 GeV) Z pole, ‘TeraZ’ and high precision MZ & GZ
  W (80 GeV) W pair production threshold, high precision MW
  H (120 GeV) ZH production (maximum rate of H’s)
  t (175 GeV): threshold, H studies
beam energy range from 35 GeV to 200 GeV
highest possible luminosities at all working points
possibly H (63 GeV) direct s-channel production with monochromatization
  (c.m. energy spread <6 MeV, presentation at IPAC’16)
beam polarization up to ≥80 GeV for beam energy calibration
A. Blondel, J. Ellis, C. Grojean, P. Janot,
et al.
possible 1st step of ~100 TeV hadron collider (FCC-hh)
JHEP 01 (2014) 164

## Slide 15
FCC-ee
Marica Biagini 2016
combining successful ingredients of recent colliders → extremely high luminosity at high energies
LEP:
high energy
SR effects
B-factories:
KEKB & PEP-II:
high beam
currents
top-up injection
DAFNE: crab waist
Super B-factories
S-KEKB: low by*
KEKB: e+ source
HERA, LEP, RHIC:
spin
gymnastics
FCC-ee & CEPC exploit lessons & recipes from past & present e+e- and pp colliders

## Slide 16: ee luminosity scaling
x4
x4.5
x1/25-1/50
<x2
FCC-ee vs LEP:
extremely high luminosity
x1.5-2

## Slide 17
FCC-ee key parameters
parameter | FCC-ee |  |  |  |  |  | CEPC | LEP2
energy/beam [GeV] | 45 |  |  | 120 | 175 |  | 120 | 105
bunches/beam | 30180 | 91500 |  | 770 | 78 |  | 50 | 4
beam current [mA] | 1450 |  |  | 30 | 6.6 |  | 19.2 | 3
luminosity/IP x 1034 cm-2s-1 | 207 | 90 |  | 5.1 | 1.3 |  | 2.0 | 0.0012
energy loss/turn [GeV] | 0.03 |  |  | 1.67 | 7.55 |  | 1.67 | 3.34
synchrotron power [MW] | 100 |  |  |  |  |  | 64 | 22
RF voltage [GV] | 0.4 |  | 0.2 | 3.0 |  | 10 | 2.1 | 3.5
rms bunch length (SR,+BS) [mm] | 1.2, 6.7 |  | 1.6, 3.8 | 2.0, 2.4 |  | 2.1, 2.5 | 2.7, 2.9 | 12, 12
rms emittance ex,y [nm, pm] | 0.2, 1 |  | 0.1, 1 | 0.6, 1 |  | 1.3, 2.5 | 1.3, 4.0 | 22, 250
longit. damping time [turns] | 1320 |  |  | 72 |  | 23 | 72 | 31
crossing angle [mrad] | 30 |  |  | 30 |  | 30 | 33 | 0
beam lifetime [min] | 94 |  | 185 | 67 |  | 57 | 110 | 434

## Slide 18
high level of synchrotron radiation (SR)
FCC-hh: 5 MW in cold environment, Eg~4 keV, cryogenics power, vacuum, impedance
HE-:LHC: 170 kW in cold environment, Eg~0.3 keV, vacuum, impedance, aperture
FCC-ee: 100 MW, Eg~1 MeV, high total power, high photon energies, detector background, impedance
performance - electron cloud / impedance / vacuum
  NEG coating? HTS coating?
cost-efficient construction
  vacuum chambers, thin-film Nb/Cu SC cavities
machine protection
  collision debris, collimation
dynamics, vacuum & material issues for FCC

## Slide 19
FCC-hh cryo -vacuum system
FCC-hh: ≈5 MW SR power
emitted in cold arcs
beam screen at 40—60 K
(LHC at 5—20 K) → better Carnot efficiency;
but higher resistance → res. wall instability
slits & wedge capture and hide photons → no
photoelectrons in beam pipe proper
surface treatment to reduce SEY?
R. Kersevan,
C. Garion,
O. Boine-Frankenheim,
V. Kornilov,
F. Petrov,
et al.
R. Kersevan et al.

## Slide 20
simulation of quench behaviour
F. Perez & CIEMAT team, et al.
FCC-hh cryo-vacuum system
FCC-hh beam screen prototypes
beam tests at KIT ANKA
R. Kersevan et al.

## Slide 21
G. Guillermo,
D. Sagan,
F. Zimmermann, IPAC16 (2016)
0.6 %
40 %
1 %
vertical orbit
error tolerance:
approx. 1 mm
(slot height 3 mm)
Synrad
absorption of synchrotron radiation
beam energy
slot height 5 mm
G. Guillermo

## Slide 22
picked 50 K for efficiency and beam stability
but for 4.5 K magnets can also consider 110 K
100MW
200MW
300MW
Ph. Lebrun
L. Tavian
V. Baglin
based on LHC screen
FCC-hh beam-screen temperature
D. Schulte
total
cryo
power

## Slide 23
SR mitigation – dreams & challenges
shaping the beam
DC beam does not radiate
suppression of shot noise to reduce radiation demonstrated at SLAC NLCTA, D. Ratner et al., PRST-AB 18, 050703 (2015)
1 D crystalline beam (acceleration by induction acceleration?)
tailoring the boundary
large bending radius + small chamber size provide shielding - effect seen at RHIC (published 2008)
HTS coating for small chamber?
hollow plasma channel shield? other ideas?
guiding the SR photons to warmer place(s)
proposal by R. Cimino

## Slide 24
ex. Reflectivity of Beam screen (RoB)
<50% on last
magnet
20 nm C coating might greatly reduce heat load at cryogenic temperature
R. Cimino

## Slide 25
Betatron side-bands
are at 1 kHz
SIBC impedance is valid down to 100 Hz and sufficient for FCC estimations.
High-frequency part requires 3D
simulations
At 3 TeV: resitive wall instability turns -> feedback (+ octupoles) required !
FCC-hh b.s. impedance
O. Boine-Frankenheim et al.
Beam pipe | 
Material | Cu, Ti
Cu thickness [μm] | 300

## Slide 26
HTS coating of beam screen?
goals: - drastically lower FCC-hh beam impedance
- allowing for higher beam-screen temperature
candidate materials:
Tl-1223 (promising performance, opens up >100 K temperature window, scalable coating, R&D with CNR-SPIN and TU-Vienna)
YBCO (proven performance, requires forming technology, R&D with ICMAB-ALBA-IFAE)
CC: coated conductor
HTS can have surface resistance lower than Cu
at T< 77 K and
f < 10 GHz
S. Calatroni

## Slide 27: )
Cu
YBCO
Wide tape
2mm tapes
f
Cu
YBCO
antechamber
HTS
coating
YBCO ()
coated
conductor
YBCO: Yttrium Barium Copper Oxide
HTS coating (YBCO, 𝑻𝒄=𝟗𝟕 K)
O. Boine-Frankenheim et al.
A (partially) HTS coated pipe would more or
less cancel the screen’s impedance contribution.
- two collaborations (S. Calatroni): YBCO/Tl-1223
- frequency, temperature, B-field dependance
- field distortion and hysteresis
- effect on SEY and photoelectron yield

## Slide 28
buildup simulations (pyCloud) indicate:
to run the machine without electron cloud and heat loads, sufficiently low SEY is required (<1.8 already OK), but
photoelectrons may be dangerous even for SEY ≤ 1, if no mitigation
L . Mether, FCC week, Rom (2016)
K. Ohmi et al, IPAC2015
3 TeV: ρe,th = 4.4 x 1010 m-3
50 TeV: ρe,th = 5.7 x 1011 m-3
build up in drift/dipoles
so far, the slits/absorbers were not included
in the e-cloud simulations !
FCC-hh e-cloud instability
O. Boine-Frankenheim et al.

## Slide 29
O. Malyshev,
R. Valizadeh,
et al.
LASE on a metal surface is a very viable solution for reducing the d < 0.6.
• even the initial (unconditioned) d = 0.93 for SS is low enough to suppress e-cloud in, e.g., the SPS, HL-LHC, or FCC, etc.
• SEY is reduced by a combination of two geometrical effects
• surface resistance measurements: shallow groove type with superimposed nano-sphere is preferable solution
e-Cloud Mitigation by Laser Ablation
Surface Engineering (LASE) ? …

## Slide 30
or open-cell metallic foams?
a typical open-cell metallic foam structure
Wearie-Phelan honeycomb cell (top left),
its constituent polyhedra (top right) and its
numerically simulated reticulated foam
low secondary emission yield
resisting eddy-current induced stresses
good pumping properties
but potentially much larger impedance than solid metals
(→ HTS coated foams, or backing beam screen slits with metallic foams?)
S. Petracca, et al.

## Slide 31
FCC-hh beam screen
pumping slots shielded,
much reduced # photoelectrons
experiencing beam field
(3) b = 13.2 mm, T=50 K
scaled LHC beam screen
with pumping slots,
and sawtooth structure
14
19
(1) b = 14 mm, T=20 K
(2) b = 14 mm, T=50 K
HE-LHC beam-screen options

## Slide 32
HE-LHC e-cloud build up
5 ns beam
25 ns beam
L. Mether
K. Ohmi
e-cloud inst. threshold |  | 25ns inj | 5ns inj
formula | re,th(m-3) | 1.4x1011 | 1.4x1011
simulation with B | re,th(m-3) | 3x1011 | 3-4x1011
simulation wo B | re,th(m-3) | 1-2x1011 | 1-2x1011
→
FCC type chamber efficient,
5 ns requires very low SEY

## Slide 33
SR flux spectra for FCC-ee
R. Kersevan

## Slide 34
Ref.: “Impact of synchrotron radiation in lepton collider arcs”,
F. Cerutti et al., FCC Kick-off Meeting, Univ. Geneva, Feb 2014
10.5 m dipole
Iron + plastic
25 mm
24 cm absorber
Lead
SR shielding for FCC-ee
F. Cerutti, L. Lari., R. Kersevan

## Slide 35
damaged spoiler, RF shield, BPMs,…
A. Novokhatski
HOM heating due to small gaps at PEP-II

## Slide 36
FCC-ee IR: HOMs, SR, vacuum
M. Sullivan

## Slide 37
M. Migliorati
FCC-ee NEG effect
TiN coated beam duct for KEKB
1 mm NEG
→ disaster
0.2 mm TiN
Perhaps
acceptable
NEG coating greatly increases
longitudinal impedance
→ microwave instability

## Slide 38
FCC-hh BDS & MDI
interaction region
beam delivery
System (BDS)
machine
detector interface
(MDI)
issue:
collision debris
hitting final
quadrupoles
radiation dose for final quadrupoles
I. Besana, F. Cerutti, D. Schulte, A. Seryi, et al.
Notes: Add one slide showing optics, possibly with some smaller plots on insertions?
Detailed optimisation on optics of each insertion within overall defined boundaries.

## Slide 39
contributions: beam screen (BS) & cold bore (BS heat radiation)
FCC-hh machine protection
stored energy 8.4 GJ per beam
  at least one order of magnitude higher than for LHC, equivalent to A380 (560 t) at nominal speed (850 km/h).
  collimation, control of beam losses and radiation effects (shielding) are of prime importance.
  injection, beam transfer and beam dump all critical
damage of a beam with an energy of 2 MJ
all machine protection issues to be addressed early on
D. Schulte

## Slide 40
collimators should avoid quenches of SC magnets (efficiency) and protect the machine in case of sudden failures (robustness)
first FCC efficiency studies
high losses in dispersion suppressor
heat load on primary collimators close to the limit
FCC-hh collimation
operational robustness improvements:
  - crystal collimation?
  - hollow electron lens?
M. Fiascaris,
J. Molson,
S. Redaelli,
D. Schulte

## Slide 41
Beam core
Collimator
Crystal
Halo
(1)
(1) angular scan: strong reduction of local losses in channeling compared to amorphous
~1/30
Beam losses at crystal [ a.u. ]
Crystal angle [ μrad ]
Loss rates in amorphous
Reduced losses in channeling
Example: scan at 450GeV
Secondary collimator position [ mm ]
Losses at collimator [ a.u. ]
Example: scan at 6.5TeV
(2) linear collimator scan: measures the profile of the channeled halo.
(2)
Channeled halo
Beam core
Offset at collimator
Phys.Lett. B758 (2016) 129-133
Measurement
Simulation model 1
Simulation model 2
important: achieved required angular control of <1 μrad (A. Masi et al.)
1st LHC crystal channelling at 6.5 TeV
S. Redaelli et al.

## Slide 42
sketch of the e-lens equipment to be installed in LHC
prototype of e-gun for hollow beam (Fermilab)
hollow e-lens for beam-halo collimation
L. Rossi, V. Shiltsev, et al.

## Slide 43
in-situ repairs?
M. Di Castro
T. Torims
laser cladding
monorail
prototypes
R&D at space agencies

## Slide 44
EU program ‘EuroCirCol’
European Union Horizon 2020 program
Support for FCC study
Grant agreement 654305
3 MEURO co-funding
Scope:
FCC hadron collider
Optics Design
Cryo vacuum design
16 T dipole design, construction folder for demonstrator magnets
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 45
16 T dipole options and plans
Cos-theta
Blocks
Common coils
down-selection of options end 2016 for detailed design work
model production 2018 - 2022
prototype production 2023 - 2025
Swiss contribution
via PSI
Canted
Cos-theta
M. Benedikt
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 46
US Magnet Development Program
Under Goal 1:
16 T cos theta dipole design
16 T canted cos theta (CCT) design
S. Gourlay

## Slide 47
R&D on Superconducting Septa
hybrid system: short overall length with high robustness & availability
SuShi concept:
SC shield creates a
field-free region inside strong dipole field
3 candidate technologies:
NbTi/Nb/Cu multilayer sheet
HTS tape
Bulk MgB2
superconductor
M. Atanasov, D. Barna

## Slide 48
RF system R&D lines
hh
≈ 16 cells per beam
≈ 100 per beam
(+ 100 for booster ring)
Z
W
≈ 210 per beam
(+ 210 for booster ring)
W
≈ 800 per beam
(+ 800 for booster)
≈ common 2600 cells for both beams
(+ 2600 for booster)
H
t
≈ 200 per beam
(+ 200 for booster)
400 MHz single-cell cavities preferred for hh and ee-Z (few MeV/m)
baseline Nb/Cu @4.5 K, development with synergies to HL-LHC, HE-LHC
R&D: power coupling 1 MW/cell, HOM power handling (damper, cryomodule)
400 or 800 MHz multi-cell cavities preferred for ee-ZH, ee-tt and ee-WW
baseline options 400 MHz Nb/Cu @4.5 K, ◄▬► 800 MHz bulk Nb system @2K
R&D: High Q0 cavities, coating, long-term: Nb3Sn like components
Notes: New slide from Olivier
Common design for hadron and lepton low energy-high currecnt system
Synergies HL-LHC, HE LHC, FCC-hh, FCC-ee Z pole

## Slide 49
20
Companies
30
Countries
102
Institutes
collaboration & industry relations

## Slide 50
First FCC Week
Conference
Washington DC
23-27 March 2015
http://cern.ch/fccw2015
468
Participants
24
Countries
168 Institutes
http://cern.ch/fccw2016

## Slide 51
FCC colliders offer plenty of R&D possibilities for vacuum, surfaces, and material plus their interactions with lepton and hadron beams
a few highlights:
  synchrotron radiation for hh & ee
  machine protection against damage, Pb & W masks,…
  cost-efficient designs (various coatings: TiN, NEG, a-C, HTS, Nb/Cu,…), and surface treatments (LASE)
  cost-effective production (additive manufacturing)
  novel approaches: e-lenses, foams, crystals, total photon reflection …
material properties matter! – SEY, conductivity, SR shielding, nuclear & el.-magn. stopping power, cost, efficiency,…
some conclusions