## Slide 1: SAMURAI
Superconducting Analyzer for Multi-particles from Radioisotope beams

## Slide 2: Overview
The SAMURAI spectrometer is designed for kinematically complete reaction measurements by detecting multiple particles in coincidence.
Superconducting dipole magnet
Heavy Ion detectors
Proton detectors
Neutron detectors
Large vacuum chamber
Rotatable base
SAMURAI consists of …
Large angular- and momentum-acceptance
Large pole gap
Wide horizontal opening of a yoke
The construction of the SAMURAI was completed in Feb. 2012.

## Slide 3: Requirements for Magnet
Requirements
  Large field integral --> for high precision momentum analysis
  Large pole gap --> for large vertical acceptance for neutrons
  No coil link --> for large acceptance in the horizontal direction
  Small fringing field --> for detectors around the target region and tracking detectors
  Flexibility --> for various experimental conditions
  Large momentum acceptance --> for heavy fragments and protons in coincidence
  High momentum resolution --> for deuteron-induced reactions
  Field Integral 7 Tm (dR/R ~ 1/700 @ 2.3 GeV/c for A/Z=3)
  --> mass separation sA=0.2 for A=100
  Large Gap (0.8 m --> vertical ±5 degrees)
  Large opening (3.4 m --> holizontal ±10 degrees)
  Small Fringing Field (< 50 gauss @ 50cm from magnet)
  H-type magnet with cylinder poles (2m in diameter)
  Magnetic field … about 3T at center by ~1.9MAT
  Field clamp
  Build-in vacuum chamber
  Rotatable base (from -5 to 95 deg, 0.1deg/sec)

## Slide 4: Versatile usage
Magnet can rotate around it’s center.
Flexibility of settings is one of the good properties of SAMURAI.
(g, n) reaction: neutron-rich side
(g, p) reaction: proton-rich side
(p,p’), (p,2p), (p,pn), …
pol. d-induced reaction
EOS measurement
0
90
30deg
90deg
45deg
30deg
0deg

## Slide 5: Photo
LHe reservoir vessels
target
upstream
side view
Vacuum chamber
* The magnet was rotated at an angle of 30o.
Field cramp

## Slide 6: Yoke
field clamp
hole
hole
880

## Slide 7: Yoke
cutaway view at median plane
pole (2m dia.)
side yoke
top view

## Slide 8: Yoke
70 stud bolts
M90, S45C
yoke = 58 slabs
The slabs weigh less than 15 tons due to the load limit of the crane.

## Slide 9: Specifications of the soft steel
Company: JFE Steel Corporation
Product name: Hot Rolled Steel Plate
Model: JFE-EFE 2003
SPEC: SUY-2 (defined in JISC2504)
Chemical components |  |  |  |  |  |  |  |  |  | 
 | C | Si | Mn | P | S | Cu | Cr | Mo | Al | N
[%](mass) | < 0.03 | < 0.20 | < 0.50 | < 0.03 | < 0.03 | (0.15) | (0.05) | (0.02) | (0.06) | (0.01)
Mechanical properties | 
0.2% proof stress | > 120 MPa
tensile strength | > 220 MPa
Elongation | > 20%
DC magnetic properties |  |  |  | 
H [A/m] | 300 | 500 | 1000 | 4000
B [T] | > 1.15 | > 1.30 | > 1.45 | > 1.60
coercive field strength | < 100 A/m @1.5 T |  |  | 

## Slide 10: Saturation of the Yoke
|B| [T]
|B| [T]
5.703051
5.0
4.0
3.0
2.0
1.0
0.0
5.703051
5.0
4.0
3.0
2.0
1.0
0.0
B(0)=3.08 T

## Slide 11: Field clamp
field integral
B=3.08T
Field clamp (W5400 x H740 x D250) was designed so as to obtain smaller fringe field.
2.2 < Z < 5.0
Thickness dependence
W5400 x H740 x D***
Width dependence
W**** x H740 x D250
field integral
2.2 < Z < 5.0
2.2 < Z < 5.0
field integral
Height dependence
W5200 x H*** x D250

## Slide 12: Super conducting wire
FURUKAWA ELECTRIC CO., LTD.
PVF insulation
NbTi/Cu

## Slide 13: SC wire

## Slide 14: SC wire

## Slide 15: SC wire
Ic @4.2K
Ic @5K
Ic @6K
Ic @7K
Load Line
563 A
5.4 T
Load factor : 60% @4.2K

## Slide 16: Specifications of the coil
NOT stabilized
Wet winding using the special epoxy resin

## Slide 17: Coil vessel
pre-stress
radially by welding
SUS316L
LHe
tube (f10x1t)
LHe: 57.4 L
2300
2800
total weight: 3 ton
coil: 1.8 ton
vessel: 1.2 ton
welding

## Slide 18: Coil
(A1050)

## Slide 19: Coil
I=563 A, B=3.08 T
|B| [T]
Fields at the coil surface
|B|max=5.4 T

## Slide 20: Cryostat
Cold mass (@4.2K)
coil: 1.8 ton
coil vessel: 1.2 ton
reservoir vessel+pipe: 0.5 ton
3.5 ton / coil
From RT to 4.2K …
LN2: 3000L/coil
LHe: 1500L/coil
3 weeks / 2coils
Amount of LHe
coil vessel: 57.4 L
reservoir vessel: 165.4 L
pipe: 10.9 L for upper coil
16.7 L for lower coil
~240 L/coil
Upper coil
57.4L
165.4L

## Slide 21: Cryostat
suspension rod
(GFRP)
support link
(GFRP)
(SUS304N2)
coil
cryostat
(SUS304)
80K shield
(A1050)
(A5083)
20K
(pure AL)
4.2K
coil vessel
(SUS316L)
GFRP
SUS304N2

## Slide 22: Estimated Heat load/coil
Place | Parts | Heat load | @ramping | @I=560 A | @I=0 A
In the cryostat + Chimney pipe | Thermal shield | Radiation | 0.40 | 0.40 | 0.40
 | Support | Conduction | 1.35 | 1.35 | 1.35
 | Coil | AC loss | 0.50 | 0.00 | 0.00
In the reservoir vessel (port) | Thermal shield | Radiation | 0.52 | 0.52 | 0.52
 | Support | Conduction | 0.04 | 0.04 | 0.04
 | Power leads | Conduction + Joule loss | 0.54 | 0.54 | 0.30
 | He gas | Conduction | 0.57 | 0.57 | 0.57
 | Bellows |  | 0.07 | 0.07 | 0.07
 | Signal leads |  | 0.12 | 0.12 | 0.12
Sum |  |  | 4.11 | 3.61 | 3.37
Place | Parts | Heat load | @ramping | @I=560 A | @I=0 A
In the cryostat | Thermal Shield | Radiation | 0.08 | 0.08 | 0.08
 | Support | Conduction | 4.88 | 4.88 | 4.88
Sum |  |  | 4.96 | 4.96 | 4.96
4K part
20K part
GM/JT 2.5W@4.3K x2
GM 4.2W@12K x2
( calculated for the lower coil )

## Slide 23: Estimated Heat load/coil
Place | Parts | Heat load | @ramping | @I=560 A | @I=0 A
In the cryostat + Chimney pipe | Thermal shield | Radiation | 23.79 | 23.79 | 23.79
 |  | Residual gas | 0.60 | 0.60 | 0.60
 | Support | Conduction | 53.83 | 53.83 | 53.83
Sum |  |  | 78.22 | 78.22 | 78.22
Place | Parts | Heat load | @ramping | @I=560 A | @I=0 A
In the reservoir vessel (port) | Vacuum chamber | Radiation | 10.99 | 10.99 | 10.99
 |  | Residual gas | 0.28 | 0.28 | 0.28
 | Support | Conduction | 0.47 | 0.47 | 0.47
 | Power lead | Conduction + Joule loss | 40.496 | 40.496 | 22.344
 | Bellows | Conduction | 1.708 | 1.708 | 1.708
Sum |  |  | 53.94 | 53.94 | 35.78
80K thermal shield
Power lead
GM 54W@40K x1
GM 100W@80K x2

## Slide 24: Heat load @4K
Heat load @4K /coil (estimation)
 | @Ramping [W] | @I=560 A [W] | @I=0 A [W]
4 K part | 4.11 | 3.61 | 3.37
LHe
pressure
1.25 L/h
Time [hour]
LHe [L]
Pressure in vessel [kPaG]
Upper cryostat
Time [hour]
LHe
pressure
2.05 L/h
LHe [L]
Pressure in vessel [kPaG]
Lower cryostat
Evaporation rate of LHe (measurement @I=0 A)
0.9 W
1.5 W
Two GM/JTs were prepared, but the measured heat load is smaller than the estimated value. Thus, just one GM/JT is used now.

## Slide 25: Cryocoolers
12 cryocoolers are equipped.
4K GM/JT
80K GM
20K GM
20K GM
80K GM
PL GM

## Slide 26: Temperature
monitor screen of the controller
(6 Sept. 2013)
 | Place | Upper coil [K] | Lower coil [K]
a | He vessel (outside of the wall) | 4.2 | 4.3
b | He vessel (port) | 7.1 | 7.1
c | 20K GM A | 11.8 | 11.9
d | 20K GM B | 11.6 | 11.2
e | 80K GM A | 40.9 | 43.3
f | 80K GM B | 41.6 | 40.6
g | 80K thermal shield | 45.1 | 47.5
h | 80K thermal shield (reservoir vessel) | 45.3 | 43.8
i | PL GM | 42.6 | 41.5
j | PL (+) | 42.9 | 41.6
k | PL (-) | 42.8 | 41.6

## Slide 27: Structural Analysis
FEM analysis: coil + coil vessel + support link
coil
Support link
Coil vessel
(SUS316L)
Fr=5x103 kN
(2000ton/coil)
Fy=1.5x103 kN
(600ton/coil)
coil
Fr
coil
Fy
Magnetic forces as a function of the azimuthal angle
GFRP(25mm)
20mm
Al(3mm)
25mm
GFRP(12mm)
GFRP(7mm)
Al(3mm)
20mm
20mm
GFRP(5mm)
integrate

## Slide 28: Structural Analysis
1.89
0.65
-0.18
-0.60
[mm]
Displacement of the coil
0o
90o
Displacement of the vessel
1.82
[mm]
0.97
-0.09
-0.72
0o
90o
90o
0o
Principal stress in the coil
95
[MPa]
7
51
66
29
Allowable stress=180MPa@RT
Von Mises stress in the vessel
0o
90o
[MPa]
205
105
5.2
55
155
Allowable stress=600MPa@4K
R-direction
Y-direction:0.22 mm
R-direction
Y-direction:0.19 mm

## Slide 29: Safety interlock
 |  |  | Action |  |  | 
 | Interlock | Condition | CUT OFF (DCCB open) | Quench back heater ON | Power supply OFF | Alarm
1 | Failure of power supply | Over voltage, Over current, Water leakage, Door open |  |  |  | 
 |  | Fuse break Cryo-controler down |  |  |  | 
2 | Water flow (PS) down | < 40 L/min |  |  |  | 
3 | Quench | Vdiff > 1 V Duration time > 0.5 s |  |  |  | 
4 | Power failure | Power failure |  |  |  | 
5 | Failure of the PL cryocooler | Stop |  |  |  | 
6 | Voltage of HTc-PL | VPL > 10 mV, VPL < -10 mV |  |  |  | 
7 | Temperature of HTc-PL 1 | T > 70 K |  |  |  | 
8 | Temperature of HTc-PL 2 | T > 75 K |  |  |  | 
9 | Lack of LHe | Level < 80% |  |  |  | 
10 | Pressure of the vessel 1 | P > 19 kPaG (120.3 kPa) |  |  |  | 
11 | Pressure of the vessel 2 | P > 40 kPaG (141.3 kPa) |  |  |  | 
12 | Emergency stop | Push emergency button |  |  |  | 
DCCB
PS OFF
cryostat
power supply
The coils are forced to quench. The current is discharged through the diodes in the cryostat and the coils.
The current is discharged through the diodes mounted in the power supply.

## Slide 30: Quench protection
1. The detector recognizes the quench. (1V, 0.5s)
2. DCCB open (Coils are cut off.)
3. Current flows to the heater layer on the outermost of the coil.
4. Backup heaters switch on within 50 ms.
5. Coils are forced to quench from the outer to inner layer.
6. Stored energy is dumped by the superconducting coils.
In the case …
cryo-conroler down
power failure
|VPL| > 10 mV
TPL > 75 K
emergency stop
Quench
Same procedure as the quench case will be done.

## Slide 31: Quench analysis
180
160
current
Vdiff
current
Vdiff (Vu-Vd)
change of Vdiff after quench
quench propagates longitudinal direction
vq =10 m/s
quench propagates transverse (radial) direction
vq =0.05 m/s (estimated from the value of KEK-SKS)
current
temperature (K)
current
temperature (K)
current
temperature at the outermost layer
Vdiff > 1V at 1.2 sec.
0.5 sec. before cut off
+
0.3 sec. delay before heater on
Total: 2 sec.
Temperature rise is moderate and acceptable

## Slide 32: Quench analysis
Induced voltage is moderate and acceptable
180
160
(a)
(b)
(c)
~700 V

## Slide 33: Coil protection
In the case …
1. Power supply is cut off
2. Stored energy is dumped by diodes in the power supply
3. Diodes are cooled by heat-sink and fan
from 560A to 0A : ~1 hour
decay const. : 0.25A/sec
over voltage
over current
door open
water leakage
water flow down
PL cryocooler failure
TPL > 70 K
LHe level < 80%
pHe > 40 kPaG

## Slide 34: Cryostat assembling
coil winding

## Slide 35: Cryostat assembling
reservoir vessel
cryostat chamber

## Slide 36: Cryostat assembling
Lower cryostat assembling
support link
coil vessel
part of 80K shield
part of cryostat chamber
support link

## Slide 37: Cryostat assembling
coil vessel
pipe for liq. He transfer
80K shield
80K shield
80K shield
20K GM head is attached here
support links

## Slide 38: Cryostat assembling
coil vessel
80K shield
suspension rod
(GFRP)
Upper cryostat
Upper cryostat
Lower coil

## Slide 39: Cryostat assembling
Upper cryostat
cryostat chamber
20K GM
80K GM

## Slide 40: Cryostat assembling
Upper cryostat
LHe
transfer port
current port
Lower cryostat
reservoir vessel
PL GM
4K GM/JT port

## Slide 41: Test in Toshiba factory
Excitation test (1st time)
GM for 80K
GM for 20K
GM/JT for 4K
reservoir vessel
GM for PL
magnetic shield for GM head
Upper cryostat
Lower cryostat
polarity check by applying 1 A
apply 10A -> cut off to check the protection sequence
excite to 518.4 A -> training quench happened @450 A
Excitation test (2nd time)
excite to 530 A -> success without quench
~4 T in the coil region
~624 ton

## Slide 42: On site assembling
Rails for rotatable base (11/13/2010)
Rotatable base with the first layer of the yoke
Magnet yoke with poles
Coils with cryostats, LHe reservoir vessels
Vacuum chamber
After day-one experiments (9/19/2012)

## Slide 43: Excitation test
May 2011, excitation test was performed.
A training quench happened in the lower coil at 561 A (3.07 T), which corresponds to 99.6% of the maximum operation current, 563 A (3.08 T).
During subsequent excitation testing after refilling of LHe, the current reached 563 A without quenching and the test was continued up to 573 A (3.10 T) successfully.

## Slide 44: Magnetic Field
They are determined in response to changes is the inductance of the coil so as to keep the induced voltage below 20 V, which is the maximum voltage of the power supply.

## Slide 45: Magnetic Field
Y
Z
Y
Z
X
model 1
model 2
The value of the central field is compared between measurements and calculations (TOSCA).

## Slide 46: Fringe Field
FDC2
B(0) dependence on |By|_max
By [Gauss]
distance [mm]
B(0) [T]
HODO
TOSCA
|By|_max [Gauss]

## Slide 47: Fringe Field
FDC2
B(0) dependence on |By|_max
HODO
TOSCA

## Slide 48: Fringe Field
By(center)=3.08T
TOSCA
measured
TOSCA
B(0)=3.0T
FDC2
HODO
Z
x
The calculated values and measured values agree well with each other. The fringe fields are smaller than 50 Gauss in the region more than 0.5 m distant from the edge of iron yoke, satisfying our experimental requirements.

## Slide 49: Summary
Large-acceptance spectrometer “SAMURAI” has been constructed at RIKEN RIBF.
The construction of the H-type superconducting dipole magnet was finished in June 2011.
Large pole gap (800mm effectively)
Wide horizontal opening (3400mm)
Central field =3.08T, BL=7.05Tm, I=563A, E=27.4MJ
The coils are cooled by liquid He.
Twelve cryocoolers are used to keep the temperature.
The first reaction experiments using SAMURAI were carried out in May 2012, and the second experiments were carried out in April 2013.