## Slide 1: MECHANICAL FRAME OF THE MVD
G. GIRAUDO
TORINO 16 June 2009

## Slide 2
G. GIRAUDO
TORINO 16 June 2009
The MVD will be suspended in position to the Central Frame.
The two systems must be independent:
    High Stiffness
    Good Machining of the interfaces
    Good Dimensional Control
Stress due to the assembly must be controlled:
    Simulation (stochastic analysis)
    ….minimized….

## Slide 3
G. GIRAUDO
Three bosses are embedded into the Central Frame.
Machining after assembly.
Two inserts are glued.
Survey of the inserts position and plane
geometry reached.
TORINO 16 June 2009
A PROPOSAL FOR MVD-CENTRAL FRAME COUPLING

## Slide 4
G. GIRAUDO
Three reference arms
are assembled on the
external MVD frame.
Dedicated tools are needed.
Three small surfaces are
machined: definition of
a bearing plane.
Housings of the spheres are
machined.
Spheres fixed.
Final survey.
TORINO 16 June 2009
A PROPOSAL FOR MVD-CENTRAL FRAME COUPLING

## Slide 5
G. GIRAUDO
Half MVD is suspended to
the Central Frame and fixed to
it with three springs.
TORINO 16 June 2009
A PROPOSAL FOR MVD-CENTRAL FRAME COUPLING

## Slide 6
G. GIRAUDO
TORINO 16 June 2009
NEXT …
Dimensional freezing
Material choice (FEM analysis)
  Environmental Behaviour
  Stiffness
Prototype (only geometry-stereo lithography)
Prototype for mechanical studies