## Slide 1: eTOF MRPC Production Status at Tsinghua University
Lyu Pengfei
Department of Engineering Physics,
Tsinghua University, Beijing, China
September 23rd, 2017
CBM-STAR Joint Meeting

## Slide 2: Outline
Mass production status of MRPC3a
  Conceptional design of MRPC3a
  MRPC3a production procedure
  Quality assurance results
Preliminary test results
  HV test
  Cosmic test based on TRB system
Plan and time line
Summary

## Slide 3: Conceptional Design of MRPC3a
The sectional sketch of the double-stack MRPC3a.
STAR eTOF
STAR module

## Slide 4: Conceptional Design of MRPC3a
MRPC3a prototype in SPS beamtest (Nov 2015).
30 GeV Pb beam on 1mm/2mm/3mm Pb.
Flux rate up to 10 Hz/cm2.
Performance in HV and threshold scan:
Time resolution: ~ 60 ps
Efficiency: > 98%
Cluster size: ~ 1.5
MRPC3a prototype in Heidelberg cosmic test.
From Ingo’s talk on July 5th

## Slide 5: MRPC3a Production Procedure
Quality check of glass & electrode production.
Electrode glass before spraying.
Sprayed electrode. 3 mm space on edge is for getting rid of edge effect.
Every piece of glass in each batch has been inspected.

## Slide 6: MRPC3a Production Procedure
Assembling PCB board & HV production.
HV connection to top & bottom board. This is to avoid discharge between HV & the nearest strip.
HV connection to middle board.
An installing module can fix the PCB board and honeycomb together exactly.

## Slide 7: MRPC3a Production Procedure
Stack assembling procedure.
Iron bricks are applied to press the first stack, while the pins are soldered.
Distance between the two PCBs is monitored during assembling.
The same procedure is repeated when assembling the second stack.

## Slide 8: Quality Assurance Results
Quality assurance of each type of materials and the assembling procedure is recorded.

## Slide 9: Quality Assurance Results
Quality assurance of each type of materials and the assembling procedure is recorded.
Detailed information can be found by scanning the QR code on it.
A website is developed to record all the QR information of each produced counter: http://hepd.ep.tsinghua.edu.cn/CBM_TOF/

## Slide 10: Quality Assurance Results
Thickness uniformity between each PCB has been measured at 8 points around the assemble counter.
The requirement is the thickness of two adjacent PCBs should be within ±0.2 mm of the nominal value.
The distance measured at the edge is not absolutely equal to the thickness in glass & gap region, but it could be a reference.

## Slide 11: HV Test
All the MRPC3a counters should be tested with HV.
The working gas is 90% C2H2F4, 5% i-C4H10 and 5% SF6. The flushing time is 60 hours (determined by 3 times of the gas box volume 72 L and gas flow 3.6 L/h).
The counter should be trained 10 hours at the nominal voltage of 5500V.
Dark current read out from HV crate should be no more than 50 nA, otherwise, it will be disassembled to look for the reason.
The qualified counters are ready for cosmic test.

## Slide 12: HV Test
Dark current and noise rate monitored in 170 hours since the MRPCs are trained.
Dark current < 50 nA √
Noise rate around 1 Hz/cm2
After 10 hours’ HV training, the counter is set to 5600 V, and the PADI’s threshold 300 mV.

## Slide 13: Cosmic Test Based on TRB System
MRPC setup in the gas box.
PADI 10
PADI power cable
PADI output
Interface board
HV connector
MRPC3a - 000
MRPC3a - 002
MRPC3a - 003
702
701
700
Gas box

## Slide 14: Cosmic Test Based on TRB System
TRB system setup.

## Slide 15: Cosmic Test Based on TRB System
Photo of the TRB system setup with MRPC3a test gas box.
Noisy and dead zones are found at both ends and middle line of each TDC.
Test gas box
LV supply
TRB board
FPGA TDCs

## Slide 16: Cosmic Test: Calibration & Analysis
Run: 24Aug1829: Dut: 701; Ref: 702; Sel2/BRef: 700.
Calibration mode: 701702700.
HV: ±5600 V; Threshold: -300 mV; Gas: 90% Freon + 5% C4H10 + 5% SF6
Unpacking
Calibration
calib_runs_batch.sh 24Aug1829 701702700 700
Analysis
ana_sets_batch.sh 24Aug1829 701702700_700 0.5 701 702 700
create_calib.C (1000000,"CbmTofThu_24Aug1829")
apply_calib.C (1000000,"CbmTofThu_24Aug1829")
init_calib_digi.sh
iter_calib_digi.sh
gen_calib_digi.sh
iter_ana_hits.sh
Analysis strategy:

## Slide 17: Cosmic Test: Calibration & Analysis
Unpacking:
MRPC3a - 000
MRPC3a - 000
MRPC3a - 002
MRPC3a - 003
MRPC3a - 002
MRPC3a - 003
TDC channel occupancy
TDC Leading edge time to trigger

## Slide 18: Cosmic Test: Calibration & Analysis
Unpacking:
Matching of left and right side of each MRPC. It can prove the mapping file we prepare is correct.
MRPC3a - 000
MRPC3a - 002
MRPC3a - 003

## Slide 19: Cosmic Test: Calibration & Analysis
pl_over_cluSel0_7_0_2
pl_over_cluSel1_7_0_1
Calibration: Dut: 701; Ref: 702; Sel2/BRef: 700

## Slide 20: Cosmic Test: Calibration & Analysis
tofAnaTestbeam->SetDXWidth(1.2);
tofAnaTestbeam->SetDYWidth(2.0);
tofAnaTestbeam->SetDTWidth(0.15;
tofAnaTestbeam->SetPosY4Sel(1*dScalFac);
tofAnaTestbeam->SetDTDia(0.);
tofAnaTestbeam->SetCorMode(iGenCor);
tofAnaTestbeam->SetMul0Max(400);
tofAnaTestbeam->SetMul4Max(20);
tofAnaTestbeam->SetMulDMax(20);
tofAnaTestbeam->SetHitDistMin(10.);
tofAnaTestbeam->SetDTD4MAX(6.);
tofAnaTestbeam->SetPosYS2Sel(1*dScalFac);
tofAnaTestbeam->SetChS2Sel(0.);
tofAnaTestbeam->SetDChS2Sel(100.);
tofAnaTestbeam->SetChi2Lim(5.);
tofAnaTestbeam->SetChi2Lim2(2.);
tofAnaTestbeam->SetEnableMatchPosScaling(kFALSE);
tofAnaTestbeam->SetCh4Sel(15);
tofAnaTestbeam->SetDCh4Sel(15*dScalFac);
pl_over_Mat04D4best
Analysis: Dut: 701; Ref: 702; Sel2/BRef: 700

## Slide 21: Cosmic Test: Calibration & Analysis
tofAnaTestbeam->SetDXWidth(1.2);
tofAnaTestbeam->SetDYWidth(2.0);
tofAnaTestbeam->SetDTWidth(0.15;
tofAnaTestbeam->SetPosY4Sel(1*dScalFac);
tofAnaTestbeam->SetDTDia(0.);
tofAnaTestbeam->SetCorMode(iGenCor);
tofAnaTestbeam->SetMul0Max(400);
tofAnaTestbeam->SetMul4Max(20);
tofAnaTestbeam->SetMulDMax(20);
tofAnaTestbeam->SetHitDistMin(10.);
tofAnaTestbeam->SetDTD4MAX(6.);
tofAnaTestbeam->SetPosYS2Sel(1*dScalFac);
tofAnaTestbeam->SetChS2Sel(0.);
tofAnaTestbeam->SetDChS2Sel(100.);
tofAnaTestbeam->SetChi2Lim(5.);
tofAnaTestbeam->SetChi2Lim2(2.);
tofAnaTestbeam->SetEnableMatchPosScaling(kFALSE);
tofAnaTestbeam->SetCh4Sel(15);
tofAnaTestbeam->SetDCh4Sel(15*dScalFac);
pl_over_Mat04D4best
Analysis: Dut: 701; Ref: 702; Sel2/BRef: 700
Efficiency: 96%
System time resolution: 100ps

## Slide 22: Cosmic Test: Calibration & Analysis
Dut | Ref | BRef/ Sel2 | Eff | Time Resolution/ps | Clustersize Dut | Clustersize Ref | Event number | Calibration mode
700 | 701 | 702 | 98.4% | 35.7 | 1.5 | 1.7 | 14414 | 700701702
700 | 702 | 701 | 97.6% | 35.5 | 1.6 | 1.7 | 15320 | 700702701
701 | 700 | 702 | 94.5% | 153.1 | 2.2 | 1.5 | 973 | 701700702
701 | 702 | 700 | 96.3% | 106.9 | 1.7 | 1.6 | 11976 | 701702700
702 | 700 | 701 | 84.0% | 153.8 | 2.0 | 1.6 | 1336 | 702700701
702 | 701 | 700 | 92.3% | 127.4 | 1.6 | 1.7 | 15078 | 702701700
The 3 MRPCs are supposed to have the same performance. However, their behaviors are not consistent under different calibration mode.
When 700 is Dut, unreasonably good time resolution is got. When 700 is Ref, we lost most of the entries, and the performance deteriorates.

## Slide 23: Cosmic Test: Calibration & Analysis
dis_hits.C(1,700701,1,"CbmTofThu_24Aug1829","700701702_702",702)
dis_hits.C(1,701700,1,"CbmTofThu_24Aug1829","701700702_702",702)
Tracking method is applied to find how most of the entries are lost in analysis class.

## Slide 24: Cosmic Test: Non SF6 Test
MRPC3a is required to work with non-SF6 gas mixture at STAR.
From Ingo’s talk
In Heidelberg’s test, MRPC3a composed of low-resistive glass reaches 86% efficiency at 4800V without SF6. Because of lower electric field, the time resolution worsens.

## Slide 25: Cosmic Test: Non SF6 Test
Similar non SF6 test is repeated in Tsinghua.
Threshold: -300 mV; Gas: 95% Freon + 5% C4H10.
The dark current of 701 (MRPC3a - 002) always stays at +0.01 μA / -0.01 μA with HV increasing.
The noise rate should be at same level to reach the same efficiency. So HV is increased to 5200 V to reach the nominal point.
Noise rate of 701 (MRPC3a - 002)

## Slide 26: Cosmic Test: Non SF6 Test
Dut: 701; Ref: 702; Sel2/BRef: 700.
Calibration mode: 701702700.
The working point without SF6 is 400V below that with SF6, with an efficiency of 96%, system time resolution below 100 ps and 1.5 clustersize.

## Slide 27: Plan and Time Line
Time line for the mass production of MRPC3a.
40 MRPC3a detectors will be shipped to Heidelberg in August 2017, by a conservative estimation according to the table of time line.
3 counters among the 6 are already packed and shipped to Heidelberg.

## Slide 28: Summary
The mass production of MRPC3a counters has begun, and the first batch 6 counters are produced.
All these counters meet the quality assurance requirement.
Three counters (00, 02, 03) have been tested at nominal voltage with dark current around 10 nA and noise rate around 1 Hz/cm2.
TRB system was established in Tsinghua lab. Data acquired from cosmic looks promising, but we are still debugging on the analysis.
MRPC3a counter is capable to keep the performance without SF6.
All 40 MRPC3a counters are expected to be ready and shipped to Heidelberg by the end of December this year.

## Slide 29: Thank You!
Lyu Pengfei
Department of Engineering Physics,
Tsinghua University, Beijing, China
September 23rd, 2017
CBM-STAR Day,
30th CBM Collaboration Meeting

## Slide 30: Backup

## Slide 31: Materials for one MRPC3a counter
Material | Length/mm | Width(Diameter)/mm | Thickness(Height)/mm | Quantity | Description
Low-resistive glass | 330 ± 0.2 | 276 ± 0.2 | 0.7 ± 0.02 | 10 | ~ 2×1010 Ωcm
HV graphite spray | 324 ± 0.5 | 270 ± 0.5 | 0.005 | 4 | < 10 MΩ/sq
Top PCB | 360 ± 0.2 | 338 ± 0.2 | 0.8 ± 0.05 | 1 | 
Bottom PCB | 360 ± 0.2 | 338 ± 0.2 | 0.8 ± 0.05 | 1 | 
Middle PCB | 360 ± 0.2 | 328 ± 0.2 | 1.6 ± 0.05 | 1 | 
Protective resistor | / | / | / | 128 | 200 kΩ, 0603
Honeycomb | 333 ± 1 | 310 ± 1 | 6 ± 0.2 | 2 | 
Block A | 23 ± 0.2 | 10 ± 0.2 | 4 ± 0.05 | 8 | PTFE
Block B | 14 ± 0.2 | 10 ± 0.2 | 4 ± 0.05 | 4 | PTFE
Mylar | 340 ± 0.2 | 286 ± 0.2 | 0.25 ± 0.02 | 8 | 
HV cable | 1000 | 3 | / | 3 | 
Fishing line | 26000 | 0.25 + 0.005 | / | / | 
M2.5 screw (nut) | 40 | 2.5 | / | 32 | Nylon
M4 screw (nut) | 40 | 4 | / | 16 | Nylon
2 × 9 connector | / | / | / | 16 | 
Pin | 19 | 0.6 | / | 100 | 
Carbon tape | 50 | 50 | 0.13 ± 0.02 | / | ~ 100 kΩ/sq
CAF4 for isolating, copper foil for HV making, absolute ethanol for cleaning are not included in this list.

## Slide 32: Materials: PCB Board
Design of top/bottom PCB:
① 32 readout strips on a 10 mm pitch with 3 mm interval.
② Transmission feedthrough.
③ Installing holes for HV.
④ Mounting holes.
⑤ Installing holes for fishing line columns.
⑥ Installing holes for blocks.
⑦ Copper foil.
Design of middle PCB:
⑧ Signal transmission pins from bottom/top readout PCBs.
⑨ 200 kΩ protective resistors.
⑩ 2×9 connectors for signal output to PADI.
Design values of these PCBs:
Copper foil thickness: 0.035 mm.
Dielectric constant: 4.6.

## Slide 33: Quality Assurance
Test module for glass inspection. Each batch of glass should be examined before they are applied into assembling of counters.

## Slide 34: Test and Analysis: Cosmic-Ray Test
The performance requirement of the MRPC3a counter in cosmic-ray test.
Without any cuts: 103 ps
The time resolution in cosmic-ray can’t be as good as that in beamtest (velocity correction not sufficient).
Run 01Mar2217 SPS Feb 2015 (no diamond):
Only with walk correction: 121 ps

## Slide 35: Cosmic Test: Calibration & Analysis
Comparison between calibration mode 700701702 and 701700702.
pl_over_cluSel1_7_0_1 701700702
pl_over_cluSel1_7_0_0 700701702

## Slide 36: Cosmic Test: Calibration & Analysis
Comparison between calibration mode 700701702 and 701700702.
pl_over_Mat04D4best 701700702
pl_over_Mat04D4best 700701702
All the products have been uploaded to Kronos under path:
/lustre/nyx/cbm/users/plyu/CbmTofThu_24Aug1829