## Slide 1
Project
Current Development Activities
System Integration
Read-out Electronics, Data Acquisition Chain
Silicon Microstrip Sensors
The Silicon Tracking System
The Compressed Baryonic Matter (CBM) experiment at FAIR
The Silicon Tracking System of the CBM experiment at FAIR Johann M. Heuser*, GSI Helmholtz Center for Heavy Ion Research, Darmstadt, Germany *J.Heuser@gsi.de, for the CBM Collaboration
Physics aim
Exploration of the QCD phase diagram at high net baryon densities and moderate temperatures
Starting with SIS100 projectile energies: 2÷11 GeV/nucleon / = 2.74.9 GeV, protons up to 29 GeV
Observables
Hadrons, electrons, muons, photons
Particle yields and multi-differential cross-sections
Rare diagnostic probes: strange mesons, light vector mesons (ρ, ω, φ), charm production
Recent paper: Challenges in QCD matter physics – The scientific programme of the CBM experiment at FAIR; arXiv:1607.01487v2 [nucl-ex] 24 Nov 2016
pile-up free track point determination in high-rate collision environment: 105  107/s (A+A), up to 109/s (p+A)
physics aperture : 2.5    25, 0.3 m  z  1.0 m
8 tracking stations
double-sided silicon microstrip sensors
hit spatial resolution  25 µm
self-triggering front-end electronics
time-stamp resolution  5 ns
material :  0.3 % – 1.2% X0 per station
momentum resolution: p/p  1.8% (p > 1 GeV/c, 1 Tm field)
p+C, 29 GeV
few charged particles/collision
central Au+Au, 8 GeV/nucleon
 350 charged particles/collision
central Au+Au, 25 GeV/nucleon
 700 charged particles/collision
UrQMD + GEANT + CbmRoot
285/320 ± 15µm thick
n-type silicon
double-sided segmentation
1024 strips of 58 µm pitch
strip length 2/4/6/12 cm
angle front/back: 7.5/0
read-out from top edge
double-metal routing on p-side
radiation tolerance 1014 neq/cm2, 1 Mrad
p-side
n-side
prototypes from CiS, Germany and Hamamatsu, Japan
0.5 mm/div
r/o electronics
8 stations, volume 2 m3, area 4 m2
896 detector modules in various lengths
    896 double-sided microstrip sensors
    ~ 1.8 million read-out channels
    ~ 16 000 r/o STS-XYTER ASICs
    ~ 16 000 ultra-thin r/o cables (550 cm long)
106 detector ladders with 8-10 modules
power dissipation: ~40 kW (CO2 cooling)
thermal enclosure: sensors at T = -5 C
front-end board
896 modules
8 tracking stations
18 mechanical half-units
C-frame
STS-XYTER ASIC | v2.0 (produced 2016) 2016 JINST 11 C02024
CMOS process | UMC 180 nm
channels | 128, polarity +/-
noise | < 1ke- at 20-50 pF load
ADC range | linear up to12 fC, 5 bit
clock | 250 MHz
power | < 10 mW/channel
timestamp | ~5 ns resolution
out interface | 5 × 500 Mbit/s LVDS
STS-XYTER ASIC 8 ×
  GBTx chip-set (CERN):
  3 GBTx, 1 VTRx, 1 VTTx, 1 SCA 42 E-links à 320 Mb/s
  3 GBT optical uplinks à 4.48 Gb/s
Front-End Board
Read-Out Board
Data Processing Board
time-slicing
STS-XYTER chips
à 1/2/5 LVDS E-links out
time-stamped data
data combining
optical link
copper link
FLES online event computing center
Power Boards
microstrip sensor with 1024 channels
self-triggering
prototype free-stream-ing DAQ system
ultra-thin r/o cables
sensor
read-out + power boards
Concept:
Module assembly:
Ladder assembly:
106 ladders
2013 – Technical Design Report*
2017-2018 – Production Readiness (Sensors, Electronics, System Integration)
Detector construction until 2021
*GSI Report 2013-4 (Aug. 2013)
Timeline:
GSI-FAIR, Darmstadt, Germany; JINR, Dubna, Russia; Univ. Tübingen, Germany; KIT, Karlsruhe, Germany;
AGH, Cracow, Poland; JU, Cracow, Poland; WUT, Warsaw, Poland.
Assembly Centers: GSI-FAIR, JINR -VBLHEP
Key Institutes:
tab-bonding of Al-polyimide cables between ASICs and sensor
mounting of modules onto low-mass carbon-fiber supports
Radiation hardness of sensors:
Front-end electronics:
Module performance test stand:
Quarter-unit demonstrator:
AFCK-DPB
FLIB
FLES node
test module, 128 channels on front and back sides
longitudinal cut – Silicon Tracking System in Dipole Magnet
ladder mounting
mechanical stability
electronics cooling
cable routing
powering
connectivity
cooling plate
STS-XYTER v2 test set-up
1:1
 5:1
under verification
under development
operated under beam test conditions
under development
 = 2 × 1014 neq cm-2 (2× end-of-life fluence) T= - 5 C
sensor type
off detector
presented at
Quark Matter 2017, XXVI International Conference on Ultra-Relativistic Heavy-Ion Collisions, Chicago, IL, USA, 6-11 February 2017
supported by EU-Horizon2020 project CREMLIN
Dipole
Magnet
Silicon
Tracking
System
Micro
Vertex
Detector
Muon
Detector
Ring
Imaging
Cherenkov
Detector
Transition
Radiation
Detector
Time of Flight Detector
Projectile
Spectator
Detector
DAQ/FLES HPC cluster
Beam Dump
Beam on Target
FLIB
8:1
neutron-irradiated sensors tested in the laboratory and with proton beam
set-up in muon-hadron configuration at SIS100
particle densities in STS up to  10/cm2