## Slide 1: FAIR – CBM – STS The Compressed Baryonic Matter Experiment at FAIR and its Silicon Tracking System
Johann M. Heuser, GSI Helmholtz Center for Heavy Ion Research, Darmstadt, Germany
Workshop on Detector Technologies for High-Energy Physics CiS Research Institute for Microsensor Systems, Erfurt, Germany, 28+29 November 2016

## Slide 2
Protons: 2 - 29/89 GeV
Ions: 2 – 14 GeV/u (SIS100) 10 – 45 GeV/u (SIS300) sNN= 1.9 - 4.5 GeV sNN= 4.2 - 9 GeV
Intensities: 1012/s @ Super-FRS, 109/s @ CBM
new international research laboratory to explore the nature and evolution of matter in the Universe
under construction in Darmstadt, Germany
Facility for Anti-Proton and Ion Research
Helmholtz Center for Heavy Ion Research

## Slide 3: Facility for Anti-Proton and Ion Research
Sweden
France
India
Finland
Germany
Poland
UK
Romania
Russia
Slovenia

## Slide 4: Facility for Anti-Proton and Ion Research
NUSTAR
Nuclear Structure & Astrophysics radioactive ion beams
PANDA
Hadron Physics
antiproton beams
  CBM
  QCD phase diagram, High-density nuclear matter
  relativistic nuclear collisions
APPA
Materials Science & Radiation Biology
ions, antiprotons
Sweden
France
India
Finland
Germany
Poland
UK
Romania
Russia
Slovenia

## Slide 5: Facility for Anti-Proton and Ion Research

## Slide 6: Facility for Anti-Proton and Ion Research
September 2016:
Formal approval by German Research Ministry to start civil construction of northern area; call for tender out: SIS100 tunnel plus connections.
Schedule for civil construction:
- concrete shell completed : 7/2020
- building ready for installation: 11/2021
- building ready for commissioning: 5/2022
Modularized Start Version
Experiments: FAIR phase 0 – before FAIR startup FAIR phase 1 – from 2023
FAIR phase 2 – by 2025, full operation
FAIR phase 3 – beyond MSV (SIS300, ...)

## Slide 7: Compressed Baryonic Matter
7
atom
atomic nucleus
proton/neutron
quarks
(10-10 m)
(10-14 m)
(10–15 m)
(<10-18 m)
(10-5 m)
electron
Baryonic Matter
made from particles composed of three quarks: proton (uud), neutron (udd)
Scientific questions
Why are there no free quarks?
Where does mass come from?

## Slide 8: Compressed Baryonic Matter
8
atom
atomic nucleus
proton/neutron
quarks
(10-10 m)
(10-14 m)
(10–15 m)
(<10-18 m)
(10-5 m)
electron
Baryonic Matter
made from particles composed of three quarks: proton (uud), neutron (udd)
Scientific questions
Why are there no free quarks?
Where does mass come from?
Approach
Break up matter, see it forming again, probe its properties during that process:
How does matter behave under extreme conditions?
  temperatures as in “Big Bang”
  densities as in cores of neutron stars
Study systematically energetic collisions of nuclear matter (“heavy ions”)

## Slide 9: Relativistic heavy-ion collisions
high density phase
Au
Au
+
transport models: ρmax ≅ 12ρ0
≈ 10-22 s (10 fm/c)
t
resonances
nucleons
mesons
high density and high temperatures are reached on a very short time scale:
 = 3.4∙1016 g/cm3, T = 1012 K
9

## Slide 10: Exploring the QCD phase diagram
Courtesy of K. Fukushima & T. Hatsuda
At high collision energies (> 200 GeV/nucleon): very high temperature
N of baryons  N of antibaryons  zero baryon density Situation similar to early universe
L-QCD finds crossover transition between hadronic matter and Quark-Gluon Plasma
Experiments: ALICE, ATLAS, CMS at LHC STAR, PHENIX at RHIC
10
“density”

## Slide 11: Exploring the QCD phase diagram
At colllision energies 4 – 45 GeV/nucleon: highest baryon density
N of baryons  N of antibaryons; Densities like in neutron star cores
L-QCD not (yet) applicable Models predict 1st order phase transition with mixed or exotic phases
Experiments: BES at RHIC, NA61 at CERN SPS,
CBM at FAIR, NICA at JINR
Courtesy of K. Fukushima & T. Hatsuda
11
“density”

## Slide 12: Experiments exploring dense QCD matter
high
net-baryon densities
12

## Slide 13: Particle yields in central Au+Au collisions
4 GeV/nucleon
multiplicity  branching ratio
motivating CBM experimental requirements in precision and rates
multiplicity  branching ratio
25 GeV/nucleon

## Slide 14
Time of Flight
Projectile
Spectator
Detector
DAQ/FLES HPC cluster
Dipole
Magnet
Silicon
Tracking
System
Compressed Baryonic Matter Experiment
Ring
Imaging
Cherenkov
Transition
Radiation
Detector
Muon
Detector
Micro
Vertex
Detector
HADES
p+p, p+A
A+A (low mult.)

## Slide 15: Silicon Tracking in CBM
p+C, 30 GeV
few charged particles
track identification + momentum determination
    from few charged particles in p+A collisions at SIS100
    to hundreds of charged tracks in A+A collisions at SIS100 and SIS300
    collision rates: 105 to 107/s (A+A), up to 109/s (p+A)
    no event pile-up, unambiguous time stamps
    momentum resolution of ~ 1.5 %
identification of decay topologies within STS aperture
central Au+Au, 8 AGeV
~350 charged particles
central Au+Au, 25 AGeV
~700 charged particles
UrQMD + GEANT + CbmRoot

## Slide 16: Silicon Tracking System
1 m
STS
2.5°
25°
beam
target

## Slide 17: STS integration
8 stations, volume 2 m3, area 4 m2
896 detector modules
    1220 double-sided microstrip sensors
    ~ 1.8 million read-out channels
    ~ 16 000 r/o STS-XYTER ASICs
    ~ 58 000 ultra-thin r/o cables
106 detector ladders with 4-5 modules
power dissipation: 42 kW (CO2 cooling)
896 modules:
4-5 modules per ladder
front-end board: 8 self-triggering r/o ASICs
sensor
8 tracking stations
106 ladders
18 half- units
ultra-thin r/o cables
material budget in physics aperture
[%X0]
C-frame

## Slide 18
MVD
STS
Ni+Ni @ 15 AGeV central collision
collision rates from 100 kHz to 10 MHz
beam on target
1T magnetic dipole field

## Slide 19
MVD
STS
Ni+Ni @ 15 AGeV central collision
collision rates from 100 kHz to 10 MHz
beam on target
1T magnetic dipole field
p
K+
+

## Slide 20: STS performance simulation
track reconstruction efficiency
momentum resolution
detailed, realistic detector model based on tested prototype components
CbmRoot simulation framework
using Cellular Automaton / Kalman Filter algorithms

## Slide 21: Silicon microstrip sensors
285/320 ± 15µm thick
n-type silicon
double-sided segmentation
1024 strips of 58 µm pitch
strip length 2/4/6/12 cm
angle front/back: 7.5/0 deg
n-side strip insulation: modulated p-spray
read-out from top edge
double-metal routing on p-side
rad. tol. w.r.t. NIEL: max. 1014 neq/cm2
rad tol. w.r.t. TID: max. O(10) kGy
p-side
n-side
0.5 mm/div
r/o electronics

## Slide 22: Microstrip sensor shapes
6.2 cm × 6.2 cm
6.2 cm × 4.2 cm
6.2 cm × 2.2 cm
few sizes
6.2 cm × 12.4 cm
fill gaps at beam hole
outer parts of large stations
standard sensors throughout the stations
geo v16a
STS 1
STS 8
900 modules altogether
strip length
260 x
60 x
252 x
324 x
20 x

## Slide 23: Prototype microstrip sensors
prototypes from CiS, Germany and Hamamatsu, Japan

## Slide 24: Front-end electronics
NIM A 568 (2006) 301–308
n-XYTER chip
- from a neutron imaging project
- used for current prototyping (v1, v2.0)
30 ns rise time
170 ns rise time
self-triggering: channels deliver stream of ADC values above threshold + timestamp
128 channels
STS-XYTER chip
- dedicated development for STS, now v2.0
per channel: two-stage internal trigger
adapted to high capacitive load
back-end GBT compatible
128 channels
30 ns
90 ns

## Slide 25: Read-out chain
STS-XYTER ASIC 8 ×
  GBTx chip-set (CERN):
  3 GBTx, 1 VTRx, 1 VTTx, 1 SCA 42 E-links à 320 Mb/s
  3 GBT optical uplinks à 4.48 Gb/s
  under development /production
Front-end Board
Read-Out Board
Data Processing Board
time-slicing
STS-XYTER chips
à 1/2/5 LVDS links out
time-stamped data
under development
STS-XYTER ASIC | v1.0 (2013), v2.0 (2016)
CMOS process | UMC 180 nm
channels | 128, polarity +/-
noise | < 1ke- at 20-50pF load
ADC range | linear up to12 fC, 5 bit
clock | 250 MHz
power | < 10 mW/channel
timestamp | < 10 ns resolution
out interface | 5 × 500 Mbit/s LVDS
data combining
optical link
copper link
FLES farm online event computing
Power Boards
sensor: 1024 channels

## Slide 26: Module assembly
Integration of:
silicon sensors,
front-end electronics,
read-out cables
 functional building block of the STS.
more than 70 components/module
non-reworkable assembly
high-yield components essential
 most work-intensive and critical part of STS construction effort:
896 modules required
Front-end Board
2 x 16 read-out cables
2 shielding layers 4 spacer layers
1 inter-strip cable
sensor
mounting legs

## Slide 27: Read-out cables
Aluminum-Polyimide technology (LTU Ltd, Kharkov, Ukraine)
signal layer: 64 Al lines of 116 µm pitch, 14 µm thick, on 10 µm polyimide, lengths up to 55 cm

## Slide 28: Module assembly
GSI-Detector Lab

## Slide 29: Module assembly
Assembly procedure established at both production centers:
GSI
JINR
dummy sensors, dummy FEBs

## Slide 30: Ladder assembly
prototype carbon-fiber ladders , JINR team/CERN
pre-series carbon-fiber ladders made in industry, GSI
ladder assembly tooling, under development at GSI
mock-up ladder, JINR-LTU
30

## Slide 31: System Integration
mechanical construction ladders, units, main-frame
component installation
cabling and powering
thermal insulation, cooling

## Slide 32: CBM-STS Project Timeline
http://repository.gsi.de/record/54798
Technical Design Report approved in 2013
Production Readiness of components in 2017  here: silicon microstrip sensors
Production of components 2017 - 2020
STS system assembly in 2019 – 2020
STS commissioning in lab in 2021
Installation in CBM cave in 2022/2023

## Slide 33
Germany
Darmstadt, Germany, GSI Helmholtz Center (GSI)
Karlsruhe, Germany, Karlsruhe Institute of Technology (KIT)
Tübingen, Germany, Eberhard Karls University (EKU)
Poland
Krakow, Poland, AGH University of Science and Technology (AGH)
Krakow, Poland, Jagiellonian University (JU)
Warsaw, Poland, Warsaw University of Technology (WUT)
Russia
Dubna, Russia, Joint Institute for Nuclear Research (JINR)
Ukraine
Kharkov, Ukraine, LED Technologies of Ukraine Ltd (LTU) * Partner
Kiev, Ukraine, Kiev Institute for Nuclear Research (KINR)
Core teams of the CBM-STS project

## Slide 34
The CBM Collaboration: 60 institutions, 530 members
Croatia:
Split Univ.
China:
CCNU Wuhan
Tsinghua Univ.
USTC Hefei
CTGU Yichang
Czech Republic:
CAS, Rez
Techn. Univ.Prague
France:
IPHC Strasbourg
Hungary:
KFKI Budapest
Budapest Univ.
Germany:
Darmstadt TU
FAIR
Frankfurt Univ. IKF
Frankfurt Univ. FIAS Frankfurt Univ. ICS
GSI Darmstadt
Giessen Univ.
Heidelberg Univ. P.I.
Heidelberg Univ. ZITI
HZ Dresden-Rossendorf
KIT Karlsruhe
Münster Univ.
Tübingen Univ.
Wuppertal Univ.
ZIB Berlin
India:
Aligarh Muslim Univ.
Bose Inst. Kolkata
Panjab Univ.
Rajasthan Univ.
Univ. of Jammu
Univ. of Kashmir
Univ. of Calcutta
B.H. Univ. Varanasi
VECC Kolkata
IOP Bhubaneswar
IIT Kharagpur
IIT Indore
Gauhati Univ.
Korea:
Pusan Nat. Univ.
Romania:
NIPNE Bucharest
Univ. Bucharest
Poland:
AGH Krakow
Jag. Univ. Krakow
Silesia Univ. Katowice
Warsaw Univ.
Warsaw TU
Russia:
IHEP Protvino
INR Troitzk
ITEP Moscow
Kurchatov Inst., Moscow
LHEP, JINR Dubna
LIT, JINR Dubna
MEPHI Moscow
Obninsk Univ.
PNPI Gatchina
SINP MSU, Moscow
St. Petersburg P. Univ.
Ioffe Phys.-Tech. Inst. St. Pb.
Ukraine:
T. Shevchenko Univ. Kiev
Kiev Inst. Nucl. Research
  http://www.fair-center.eu/for-users/ experiments/cbm.html
  “Challenges in QCD matter physics – The scientific programme of the Compressed Baryonic Matter experiment at FAIR”
    arXiv:1607.01487 [nucl-ex] https://arxiv.org/abs/1607.01487 v2, 24 November 2016

## Slide 35
Backup slides

## Slide 36: STS design constraints
Coverage:
  from center-of mass to close to beam rapitidies
  aperture 2.5° <  < 25°
Momentum resolution
  δp/p  1%
  field integral 1 Tm, 8 tracking stations
  25 µm single-hit spatial resolution
  material budget per station 0.3 – max. ~1% X0
  No event pile-up
  interaction rates 0.1 - 10 MHz
  self-triggering read-out
  timestamp resolution < 5 ns
  signal shaping time < 20 ns
Efficient hit & track reconstruction
  close to 100% hit efficiency
  > 95% track eff. for p > 1GeV/c
Minimum granularity
  at hit rates < 20 MHz/cm2:
  maximum strip length compatible with hit occupancy and S/N performance
  largest read-out pitch compatible with the required spatial resolution
Radiation hard sensors
  compatible with CBM physics program:
  1 × 1013 neq/cm2 (SIS100)
  1 × 1014 neq/cm2 (SIS300)
Integration, operation, maintenance
  compatible with the confined space in the dipole magnet
  efficient cooling for electronics
  cooling of sensors
  system design including target chamber, MVD, beam pipe
  extraction possible for maintenance
36

## Slide 37: Module test stand
AFCK-DPB
4x FLIB
2x mFLES node
to be set up with new acquisition chain
questions to be addressed:
  S/N as function of micro cable length
  ...
Functional test module, 128 channels front and back

## Slide 38: Contributions to STS construction
JINR VB-LHEP, Dubna:
sensor procurement
assembly of 400 modules and 46 ladders for STS stations 1-4
GSI, Darmstadt:
sensor procurement
read-out chain
LV and HV powering
detector controls
procurement of micro-cables
production of carbon-fiber ladder supports
assembly of 500 modules and 50 ladders for STS stations 5-8
mechanical integration
system assembly
KIT (GSI contract):
module assembly
Univ. Tübingen:
sensor QA
module QA
cooling systems
AGH, Crakow :
production of STS-XYTER ASICs
production of front-end electronics boards
JU, Crakow :
STS-XYTER ASIC QA
Tech. Univ. Warsaw:
ASIC data protocol
all STS teams :
commissioning
38

## Slide 39: CBM-STS assembly flow

## Slide 40: Assembly center at GSI – QA site Tübingen
GSI Detector Laboratory
realized in GSI + JINR cooperation with BMBF-JINR funding (2015)
clean rooms, Solid State Section
sensor QA optical
sensor QA electrical
modules, ladders, system

## Slide 41: Assembly site at KIT-Karlsruhe
Institute for Data Processing and Electronics https://www.ipe.kit.edu/english/index.php
modules

## Slide 42: Assembly site at JINR VB-LHEP
modules, ladders

## Slide 43: Baryon densities in central Au+Au collisions
I.C. Arsene et al., Phys. Rev. C 75, 24902 (2007)
5 A GeV
10 A GeV
8 ρ0
phase
coexistence
5 ρ0

## Slide 44
arXiv:1111.5475v2 [hep-ph] 13 Mar 2012