Selection of hardware platform for CBM Common Readout Interface
W.M.Zabołotnya, G.H.Kasprowicza, A.P.Byszuka, D.Emschermannb, M.Gumińskia, K.T.Poźniaka, R.Romaniuka
aInstitute of Electronic Systems
Warsaw University of Technology
bGSI-Helmholtzzentrum für Schwerionenforschung GmbH
Presenter: Wojciech M. Zabołotny

---
Original concept of the CBM readout
CBM service
building
CBM detector cave
Computer center
~100 m
~700 m
Timeslice Builder
and FLES
FEB
FEE
CROB
FEB
FEB
DPB
Optical link
Data
Data
CROB
FEB
GBT links
FEB
CROB
FEB
TFC
ECS
FLIB
Clock, Synchro-
nization, Control
commands
Status, Command
responses, Data
Clock, Synchro-
nous commands,
„busy” status
Setup and Control
Commands,
Commands res-
ponses
FLES input
node
FLES computing
node
InfiniBand

---
STS-XYTER tester
The DPB firmware blocks were tested in the STS-XYTER tester. The tester uses the black-box model of the GBTx and E-Links and IPbus-based readout with limited bandwidth.
AFCK FPGA
STS
CMD
Tx
E-Link
black-
box
model
STS
Rx
CLK
DO
DI
DI
DI
DI
DI
STS/MUCH-XYTER2 Interface Core
Slide presented on the CBM Collaboration meeting 03.2017
STS CMD Processor
LVDS Interface
LVDS Interface
STS/MUCH-
XYTER2
model
STS Readout
FIFO
IPbus
Controller
1Gbps Ethernet Interface

---
Integration of the tester with GBT
- To test the operation of the GBTX ASIC in modes needed in the STS/MUCH readout (160 Mb/s „GBT frame” for downlink and 320 Mb/s „wide bus” for uplink), the dedicated AFCK-GBT-tester has been created.
- The tester firmware uses the GBT-FPGA IP Core from CERN (currently version 5.0.0)
- Testing using both – interactive mode and complex routines was possible due to the addition of Forth CPU – J1B with SwapForth to the firmware.
AFCK FPGA
Chipscope
GBTx
on
VLDB
Slide presented on the CBM Collaboration meeting 03.2017
HDMI
connectors
4.8 Gb/s link
J1B Forth CPU
USB UART interface
J1B I/O
registers
GBT-FPGA
J1B I/O
registers

---
Hardware used for GBT testing
- Test setup based on the AFCK board supplemented with the FM-S14 board and the „e-Link FMC”.
- Two HDMI cables with HDMI-micro to HDMI-mini adapters.
- Shifted clock routed via separate coaxial cable to the U.FL connector on the AFCK (required disabling of Si570 though!)
Slide presented on the CBM Collaboration meeting 03.2017

---
Current state of the GBT-based STS-XYTER tester
AFCK FPGA
STS
CMD
Tx
GBTx
STS
Rx
STS/MUCH-XYTER2 Interface Core
STS CMD Processor
LVDS Interface
4.8 Gb/s link
STS/MUCH-
XYTER2
model
STS Readout
FIFO
IPbus
Controller
1Gbps Ethernet
Interface
GBT-compatible
controller
GBT-FPGA
FADE
Interface
10 Gbps Ethernet
Interface

---
Previous concept of the CBM readout
CBM service
building
CBM detector cave
Computer center
~100 m
~700 m
Timeslice Builder
and FLES
FPGA!
FEB
FEE
CROB
FEB
FEB
DPB
Optical link
Data
Data
CROB
FEB
GBT links
FEB
CROB
„PC”
FEB
TFC
ECS
FLIB
Clock, Synchro-
nization, Control
commands
Status, Command
responses, Data
Clock, Synchro-
nous commands,
„busy” status
Setup and Control
Commands,
Commands res-
ponses
FLES input
node
FLES computing
node
InfiniBand

---
New concept of the CBM readout
Computer
center
CBM detector
 cave
CBM service building
~700 m
~100 m
FPGA!
Timeslice
 Builder
and FLES
FEB
FEE
CROB
FEB
InfiniBand
Optical link
FEB
CRI
PCIe
Data
Data
CROB
FEB
GBT links
„PC”
FEB
CROB
FEB
„PC”
ECS
TFC
Clock, Synchro-
nization, Control
commands
Status, Command
responses, Data
Clock, Synchro-
nous commands,
„busy” status
Setup and Control
Commands,
Commands res-
ponses
FLES computing
node
Ethernet

---
Requirements to the CRI board
- Handling of the required number of GBT links to receive the data from the CROBs
- Providing the sufficient PCIe bandwidth to send the received data to the FLES input node
- Providing the sufficient amount of logical resources to concentrate the data

---
CROB board
x
x
(STS)
(TRD)
ROB-3
A ROB-3 will interface to 3 MGTs on the DPB.
Based on the slide presented by David Emschermann @ CBM ASIC workshop in Darjeeling 22.02.2017

---
Available optical transceivers
Source: https://www.finisar.com/optical-transceivers/ftl410qd2c
QSFP+: Finisar FTL410QD2C 22 with approximate price of $300 for 4 duplex channels.
12-channel - Foxconn MiniPOD 23 modules with the approximate price of $360 for simplex channels (either Tx or Rx).
12-channel - Foxconn MicroPOD 24 modules with the approximate price of $130 for 12 Tx channels and $280 for 12 Rx channels.
Source: Foxconn
Source: Foxconn
24-channel - Finisar FBOTD10SL1C00 25 with the approximate price of $860 for 24 duplex channels. The RX only FBRTP10SL1C00 modules are also available.
Source: Foxconn

---
Optical input possibilities
- It seems that the best cost per channel may be achieved with the 12-channel MicroPOD modules. The smallest configurations with a reasonable utilization of optical channels are the following:
  - With two 12-channel receivers and one 12-channel transmitter, we can connect 8 CROBs to a single CRI. In this case, we waste 4 transmit channels (may be used as spares).
  - With three 12-channel receivers and one 12-channel transmitter, we can connect 12 CROBs to a single CRI. In this case, we fully utilize optical channels.

---
Input data bandwidth analysis
- The number of handled CROBs defines also the required PCIe bandwidth
  - Worst case analysis: 4.48 Gbps/GBT link, 13.44 Gbps/CROB,
    108 Gbps for 8 CROBs, 162 Gbps for 12 CROBs
  - Optimistic analysis: 9.41 Mhit/s/SMX2 chip, 20 bits of non-aggregated data/hit, 40 SMX2 chips/CROB, 7.53 Gbps/CROB,
    60.22 Gb/s for 8 CROBs, 90.34 Gb/s for 12 CROBs.

---
PCIe bandwidth analysis
- PCIe 3.0 or 3.1: 7.877 Gbps/lane, UltraScale+ devices may use up to 16 lanes.
  - For pessimistic assessment:
    - we need 16 lanes for 8 CROBs (bandwidth 126 Gb/s - margin of 14%)
    - we need two links each with 16 lanes for 12 CROBs (bandwidth of 252 Gb/s - margin of 36%).
  - For optimistic assessment:
    - a single link with 8 lanes should be sufficient for 8 CROBs (bandwidth of 63 Gb/s) but the margin of 4% is probably too low, and therefore the 16-lanes link will be needed (margin over 50%).
    - The same link will be needed in case of 12 CROBs (margin of 28%).
- The PCIe 4.0: 15.752 Gbps/lane, UltraScale+ devices may use up to 8 lanes.
  - For pessimistic assessment:
    - one 8-lanes link for 8 CROBs
    - two 8-lanes links for 12 CROBs
  - For optimistic assessment
    - one 8-lanes link both for 8 and 12 CROBs

---
Required MGT resources
#CROBs	#GBTs	#lanes PCIe 3		#lanes PCIe 4
		opt.	pess.	opt.	pess.
8 CROBs	24	16	16	8	8
12 CROBs	36	16	32	8	16

---
Total number of required MGT resources (+1 for TFC)
#CROBs	For PCIe 3		For PCIe 4
	opt.	pess.	opt.	pess.
8 CROBs	41	41	33	33
12 CROBs	53	69	45	53

---
Available FPGAs
	KU11P	KU15P		ZU11EG	ZU17EG		ZU19EG
System Logic Cells	653,100	1,143,450		653,100	926,124		1,143,450
Block RAM Blocks	600	984		600	796		984
UltraRAM Blocks	80	128		80	102		128
Enclosure	FFVE 1517	FFVE 1517	FFVA 1760	FFVC 1760	FFVC 1760	FFVD 1760	FFVC 1760	FFVD 1760
Number of transceivers GTH+GTY	32+20	32+24	44+32	32+16	32+16	44+28	32+16	44+28
Total number of transceivers	52	56	76	48	48	72	48	72
Example price	ca. $3500	ca. $4600	ca. $7900 / $5000?	ca. $3900	ca. $4400	ca. $4900	ca. $4900	ca. $5400

---
Cost analysis
- The estimated cost per CROB (assuming $130 for MicroPOD Tx and $280 for MicroPOD Rx):
  - (2 · $280 + $130 + $3500) /8CROBS ≈ $524 in case of 8-CROB version with XCKU11P in FFVE1517 enclosure.
  - (3 · $280 + $130 + $4600) /12CROBS ≈ $464 in case of 12-CROB version with XCKU15P in FFVA1517 enclosure (optimistic assessment).
- For ZynqMP chips:
  - (2 · $280 + $130 + $3900) /8CROBS ≈ $574 in case of 8-CROB version with ZU11EG in FFVC1760 enclosure.
  - (3 · $280 + $130 + $4900) /12CROBS ≈ $489 in case of 12-CROB version with ZU17EG in FFVD1760 enclosure.

---
Available FPGAs
	KU11P	KU15P		ZU11EG	ZU17EG		ZU19EG
System Logic Cells	653,100	1,143,450		653,100	926,124		1,143,450
Block RAM Blocks	600	984		600	796		984
UltraRAM Blocks	80	128		80	102		128
Enclosure	FFVE 1517	FFVE 1517	FFVA 1760	FFVC 1760	FFVC 1760	FFVD 1760	FFVC 1760	FFVD 1760
Number of transceivers GTH+GTY	32+20	32+24	44+32	32+16	32+16	44+28	32+16	44+28
Total number of transceivers	52	56	76	48	48	72	48	72
Example price	ca. $3500	ca. $4600	ca. $7900 / $5000?	ca. $3900	ca. $4400	ca. $4900	ca. $4900	ca. $5400

---
Availability of resources
- Preliminary analysis of resources defines number of BRAMs (for data sorting): 320 BRAMs for 8 CROBs, 480 BRAMs for 12 CROBs
- Consumption of other resources will be assessed after the first CRI firmwares are created.
- Upgrade possibilities (in case of unsufficient resources, in the same package):
  - XCKU11P → XCKU15P
  - ZU11EG → ZU17EG
  - ZU17EG → ZU19EG

---
Distribution of time and fast control
- The CROB modules (and further FEB boards) require precise synchronization
  - Time synchronization (PPS)
  - Reference clock signal
  - synchronous control commands.
- Possible solutions:
  - Support for White Rabbit or similar protocol in every CRI board. The clock is received from the optical signal from the SFP transceiver.
  - Dedicated receiver board use of a standard WR node in the form of a PCIe card. The clock and timing signals distributed via pear-to-pear or daisychain connectors (e.g. miniSAS).
  - Delivery of both clock and control messages using dedicated optical or copper links to each CRI board from external distribution unit (e.g. by the TTC-PON system developed at CERN)
- Selected FPGAs may implement all those options, but additional hardware (e.g. the jitter cleaner must be provided by the board)

---
Is it reasonable to use ZynqMP?
- We get quad-core ARM almost for free!
- DDR4 RAM must be mounted – 2400MT/s throughput not sufficient to pass the data through the RAM even for 64 bit data width
- Use of ARM core for control
  - Without the DDR4 RAM – in „bare metal” configuration with 1MB L2 memory
  - With slow 32-bit LPDDR memory – even under control of Linux OS
- Usability of ZynqMP chips must be evaluated

---
Visualization of the possible CRI board

---
Conclusions
- It is possible to create the CRI board supporting 8 or 12 CROBs in a PCIe card form factor, based on new UltraScale+ FPGAs from Xilinx
- The 12 CROB version, gives sligthtly lower cost/channel (12%) but is more technologically challenging
- Information from the team responsible for FLES input nodes also suggest to use the 8 CROB version
- Final decision will be possible after the protype firmware is implemented.

---
Thank you for your attention!