## Slide 1: mCBM@SIS18 – a CBM full system test-setup at GSI
Christian Sturm et al. , GSI Helmholtz Center
for the CBM Collaboration
mCBM@SIS18 - a test facility for the
CBM FLES
(HK 15.1,J. de Cuveland
HK 63.6, D.Hutter)
CBM free-streaming DAQ System
(HK15.4,D. Emschermann)
Introduction and status of the project:
Motivation and Concept
Present Design
Preparations
green cube
FLIB

## Slide 2: CBM experimental challenges
Central Au+Au at 25 A GeV / UrQMD+GEANT4:
160 p, 400 π+, 400 π+, 44 K+, 13 K-
Identification
of leptons and hadrons
Determination of
(displaced) vertices (σ  50 m)
Perform measurements at unprecedented reaction rates
105 - 107 Au+Au reactions/sec
→ fast and radiation hard detectors
→ free-streaming read-out electronics
→ high speed data acquisition and
high performance computer farm for online event selection
→ 4-D event reconstruction

## Slide 3
The CBM experiment
Dipol
Magnet
Micro
Vertex
Detector
Silicon
Tracking
System
Ring
Imaging
Cherenkov
Transition
Radiation
Detector
Time of Flight
Detector
Projectile
Spectator
Detector
Muon
Detector
DAQ/FLES HPC cluster
ECAL
HK 30.1, J. Lehnert

## Slide 4: Motivation and Concept
detector prototypes at θlab ≈ 15° - 20°
straight tracks, no B-field
high resolution TOF (t0 – TOF stop wall)
event characterization with PSD prototype
mCBM@SIS18 - a CBM full system test-setup in high-rate
nucleus-nucleus collisions at GSI/FAIR, 2017 – 2021
with focus on the
free streaming data transport to a mFLES or FLES
online reconstruction
offline data analysis
controls
permanent test-setup at the host lab
test of final detector prototypes

## Slide 5: Present design of mCBM@SIS18
mMVD
mSTS
mMUCH
mTRD
mTOF
2.5m
side view

## Slide 6: Present design of mCBM@SIS18
top view
mMVD
mSTS
mMUCH
mTRD
mTOF
UrQMD event:
Ag+Ag 1.65 AGeV
central collision
First results from
simulation: < Mtrack > ≈ 7

## Slide 7: mCBM - contributions by subsystems: STS and MUCH
mSTS
mSTS: 2x stations
1st: 2x2 modules
2nd: 3x3 modules
= 5 half-ladders
= 13x 6x6 cm² sensors
all components available
... except FEB-8
mMUCH: 3x layers
3x M2 GEM modules
18x FEBs per module (STS-XYTER)
used during CERN beamtest 2016
mMUCH
SPS2016

## Slide 8: mCBM - contributions by subsystems: TRD and TOF
mTRD
SPS 2016
mTRD: 4 layers
TRD modules (Frankfurt/Münster)
incl. read-out from CERN test beam
Nov./Dec. 2016
mTOF:
3x STAR modules
3x MRPC counter / module
read-out scheme is identical
to the STAR setup
mTOF

## Slide 9: Present GSI SIS18 Facilities

## Slide 10: Zoom-in: Present SIS18 Target Hall
HADES
R3B
BioMat

## Slide 11: Cave C and HTD Test Stand
HTD
Cave C
R3B

## Slide 12: mCBM Cave - HTD at present
March 24th, 2017

## Slide 13: mCBM – support infrastructure
gas area
counting house
DAQ container
mCBM
cave
Green Cube

## Slide 14: Sketch of the mCBM Cave – Test Stand HTD

## Slide 15: Radiation level simulation at top SIS18 energies and CBM collision rates
FLUKA simulation

## Slide 16: Radiation level simulation at top SIS18 energies and CBM collision rates
FLUKA simulation

## Slide 17: Additional shielding required
Additional iron and concrete layer
radiation level simulation
optimization ongoing

## Slide 18: 1st Preparation Meeting
Tuesday, March 20, 2017

## Slide 19: Summary and Outlook
mCBM@SIS18 – a CBM full system test at GSI
A test facility for the
High-performance free-streaming DAQ system
FLES
Final detector prototypes
2016 – 2018 design and construction phase
2018 – 2021 permanent test-setup incl. beam tests with high-rate A+A collisions
Next steps
Design freeze of the
Contributions by subsystems
HTD cave
Preparation of the installation site

## Slide 20: GSI core team
D. Emschermann
J. Frühauf
W. Niebur
P-A. Loizeau
A. Senger
F. Uhlig
C. Sturm